## Slide 1: BIC Test beam results & simulation validation
Henry Klest

## Slide 2: Test beam goals
Verify simulated performance of BIC
  Particularly hadronic showers, which can be tricky to simulate
Use the Baby BCAL as a proxy of the BIC SciFi
  Pb+SciFi Matrix design is mechanically identical to BIC
  Kuraray double-clad fibers
  Older generation SiPMs
  Less longitudinal segmentation than BIC
  15.1 X0 at normal incidence
Extract energy resolution of Baby BCAL
Measure electron/pion separation capabilities

## Slide 3: Test beam Setup

## Slide 4: Fermilab test beam facility
Nominal beam is 120 GeV protons from main injector
Secondary hadron/electron beam from sending 120 GeV protons on a 30 cm thick aluminum target
Scintillators provided by FTBF along beamline for trigger
Two Cherenkovs for PID
BIC

## Slide 5: Cherenkov Detectors
Downstream Cherenkov
Upstream Cherenkov
Downstream Cherenkov
Inner PMT
Downstream Cherenkov
Outer PMT
Upstream Cherenkov
Downstream Cherenkov
Inner PMT
Downstream Cherenkov
Outer PMT
Electron event
Pion event

## Slide 6: datasets
Due to heat issues at FNAL, only ran for ~30% of our allotted week
DAQ was limited to ~7 kHz due to full waveform readout
120 GeV protons
  Mostly parasitic overnight
  Large dataset, few million events
10 GeV e/pi
  Also large dataset, but mostly taken with FADC jumpers set in the wrong positions, so gain is 2x higher than it should be
  Took 1.5 hours (540k events) with FADC jumpers repositioned
10 GeV mu/pi
  Taken with a lead sheet in the beam to absorb electrons
  Provides a large MIP calibration dataset
Energy scan e/pi
  4 GeV (1.4M), 6 GeV (440K), and 8 GeV (320K)
  Took a larger 4 GeV because pions are rarer at low energies

## Slide 7: Beam Δp
An important factor in understanding the energy response is the beam momentum spread
This term enters as a constant term on the energy resolution
Quoted beam spread is 2.7% at low energies, improving to 2% at 120 GeV
  However, statement from Joe at FTBF: ”Every calo group is telling me it looks like the momentum spread is higher than the website indicates it should be.” – does this tell us something about the beam or the “optimism” of calorimeter experts?
This number depends on beam tune, which can vary from run to run
We see the 4 GeV beam is physically wider, which suggests it also has a larger momentum spread

## Slide 8: Beam profile
For calo analysis, want to know the profile of the beam in the vertical direction
  Determines amount of leakage
Not much info from FTBF detectors
  MWPCs were out of gas
  SWICs showed poor performance for secondary beams
Have AstroPix & Calo information
  Thanks to Bobae and Manoj for taking nice AstroPix data for us 
Both detectors agree beam widens at lower energy, both agree the beam center is vertically below the center of the calorimeter
Vertically down
Vertically up
Vertically up
Vertically down

## Slide 9: Calibration
Employ two complementary calibration techniques
MIP technique – use MIP peak to align all channels
  Pro: Each channel has an independent calibration constant, one single solution
  Con: MIP sampling fraction is different from electrons! Needs an additional sampling fraction correction.
Electron technique – minimize difference of sum of all channels with respect to a known input electron energy
  Pro: Better energy resolution achievable
  Con: No unique solution, 16 (or 32) unknowns and one known, different combinations of calibration constants can give the same result

## Slide 10: Electron energy
MIP & Electron give very similar results!

## Slide 11: Linearity

## Slide 12: Comparison to simulation
Simulation using FTBF cited beam momentum smearing
  Peaks are narrower than data
  Shapes of distributions are similar
  Tail in data is well-reproduced by simulation

## Slide 14: Pion data
Compare data to simulation
  Observed offset in beam energy, attempt to include in simulation
Data and simulation agree for 6 GeV pions
  4 GeV pions in data deposit more energy than simulation
  8 GeV pions in data deposit less than simulation

## Slide 15: Pion data
Tried various different simulation variants to try to understand the discrepancy at 4 GeV
Birks’ constant has a nominal value of 0.132 mm/MeV
  Only very large changes in Birks’ constant produce substantial changes
Would need Birks’ to be be somewhere between 2 and 4 times smaller than nominal to explain the data

## Slide 16: Pion data
Physics lists made only minor differences

## Slide 17: Pion data
Beam energy would have to be 400-500 MeV higher than requested
  4 GeV beam quality was poor, so this isn’t impossible
  Last magnet is horizontal bending dipole and baby BCal is very long
Beam position spread at the face of the calorimeter also had only minor effects
  Would have substantially larger effects without containment cuts

## Slide 18: separation
Measured energy distributions of events with Cherenkovs firing (electrons, orange) and Cherenkovs not firing (pions, blue)
Electrons and pions well separated, but both have tails
  Electron tail: showers upstream, horizontal leakage
  Pion tail: electron misID, pileup

## Slide 19: separation
The tail of the electron distribution is an artifact of the measurement setup
  Predict the true performance by fitting crystal ball or gaussian to the electron peak

## Slide 20: separatioN
All things considered, separation is pretty good
  Even with beam momentum spread, upstream material, & some leakage
Random forest is a ML algorithm that includes shower shape information
  Still has to contend with the messy tails on E/p, manages to handle them well
Presented methods in various degree incorporate artifacts of the test beam setup: beam momentum smearing, effects of upstream material, possible pileup, and beam profile variations
Including longitudinal energy profile (4-sections only in Baby BCAL) helps significantly with separation (even with low energy electron tail)
Affected by dp/p: impact on both measured electron and pion energy resolution
(edited)

## Slide 21: conclusion
Electron and pion response measured
Energy resolution extracted (measurement limitation: 2-3% dp/p at FTBF)
Good constraining power over the constant term ~1.5 ± 0.4%
Simulations describe the electron and pion data reasonably well
  Slight discrepancy for 4 GeV pions, unsure if source is FTBF or simulation
e/pion separation extracted within the full system in the test beam environment
  Affected by FTBF beam conditions including Δp spread
  Results described in more detail:
  https://arxiv.org/abs/2504.03079
Thanks to our test beam team for making our campaign a success!

## Slide 22: daq
Used 3x 16 channel JLab 250 MHz fADCs in full waveform readout mode
Sent analog signals from the “north” and “south” sets of 16 baby BCal channels into two blades of fADC, remaining blade used for FTBF detectors, cosmic ray paddles, AstroPix analog signal