## Slide 1
The Evolution of Nuclear Detectors
Alexander Ngo
Prairie View A&M

## Slide 2
Wilson Cloud Chamber
  Inventor: Charles Wilson, 1911
  Materials: Alcohol vapor, supersaturated environment, sealed container, dry ice or cooling system.
  How it works: Vapor in a sealed chamber condenses along the paths of ionizing radiation, making tracks visible.
  Cost (est.): ~$500–$2,000 (modern educational versions)
  Power usage: Minimal; dry ice or Peltier coolers
  Experiment examples: Observing alpha/beta particle tracks, cosmic ray trails
Geiger-Muller Counter
  Inventors: Hans Geiger and Walther Müller, 1928
  Materials: Metal tube, low-pressure gas (argon, neon), thin mica window, central wire anode
  How it works: Detects ionizing radiation via gas ionization inside a metal tube, producing electric pulses.
  Cost (est.): ~$100–$1,000 (modern)
  Power usage: ~1–5W
  Experiment examples: Background radiation surveys, radioactive decay detection
Early Beginnings (1900s-1930s)

## Slide 3
Bubble Chamber
  Invented by Donald Glaser, 1952
  Materials: Liquid hydrogen/neon, large containment vessel, cameras, magnetic fields
  How it works: Superheated liquid forms bubbles along ionizing tracks when particles pass through.
  Cost (est.): $5M–$15M depending on size
  Power usage: High; cryogenics, camera arrays, magnet systems
  Experiment examples: Neutrino detection at Fermilab; pion-proton interactions
Scintillation Detector
  Inventors: Work by researchers at MIT, Los Alamos, and Philips in the 1940s–1950s
  Materials: NaI(Tl) crystals, plastic scintillators, photomultipliers
  How it works: Incoming radiation excites scintillating material which emits light; photomultiplier tubes convert light into an electrical signal.
  Cost (est.): $2,000–$50,000
  Power usage: ~20–100W
  Experiment examples: Radiation dosimetry, gamma spectroscopy, Manhattan Project applications
Mid-20th Century Advances (1940s-1960s)

## Slide 4
Solid-State Detectors Rise (1970s-1990s)
Silicon Strip Detector
  Developer: CERN, SLAC, and other labs
  Materials: High-resistivity silicon, metal contacts, readout electronics
  How it works: Tracks particles via charge collected in silicon diodes segmented into strips.
  Cost (est.): ~$50,000–$500,000/module
  Power usage: ~10–50W/module
  Experiment examples: LEP (Large Electron–Positron Collider), RHIC (Brookhaven)
High-Putirty Germanium Detector
  Developers: ORTEC, Canberra, and national labs
  Materials: HPGe crystal, vacuum cryostat, cooling system (liquid nitrogen or electric)
  How it works: Detects gamma rays via ionization in ultra-pure germanium at cryogenic temperatures.
  Cost (est.): $40,000–$150,000
  Power usage: ~500W (with cryo system)
  Experiment examples: Neutrino-less double beta decay (GERDA), environmental monitoring

## Slide 5
Large-Scale Detector Systems (2000s-Present)
ATLAS & CMS Detectors
  Developers: International collaborations (3,000+ scientists), led by CERN
  Materials: Silicon pixel detectors, liquid argon calorimeters, superconducting magnets
  How they work: Combine layers of tracking, calorimetry, and muon detection to reconstruct high-energy collisions.
  Cost (est.): ~$1B each (build phase)
  Power usage: ~3–7 MW each
  Experiment examples: Higgs boson discovery (2012), supersymmetry searches
STAR Detector (RHIC)
  Developer: Brookhaven National Lab, STAR collaboration
  Materials: Gas chamber, electric fields, readout pads
  How it works: Time Projection Chamber (TPC) measures charged particle paths and energy loss in heavy ion collisions
  Cost (est.): ~$100M (phased upgrades)
  Power usage: ~500 kW–1 MW
  Experiment examples: Quark-gluon plasma studies, gold ion collisions

## Slide 6
Specialized Global Detectors
KamLAND
  Developers: Japanese/US collaboration
  Materials: 1,000 tons of liquid scintillator, photomultiplier array
  How it works: Detects neutrinos via inverse beta decay in a large liquid scintillator tank
  Cost (est.): ~$15M
  Power usage: Moderate (~100 kW)
  Experiment examples: Reactor neutrino oscillation
Super-Kamiokande
  Developer: University of Tokyo and KEK
  Materials: 50,000-ton water tank, 11,000+ PMTs
  How it works: Detects Cherenkov radiation from neutrino interactions in water
  Cost (est.): ~$100M
  Power usage: ~500–750 kW
  Experiment examples: Solar and atmospheric neutrino detection, proton decay searches

## Slide 7
Specialized Global Detectors (Continued)
FAIR (Facility for Antiproton and Ion Research)
  Status: Under construction (Germany)
  Use: Heavy-ion collisions and exotic nuclei studies
  Estimated cost: €3B (entire complex)
  Power usage: High (est. several MW)
  Planned experiments: CBM, PANDA, NUSTAR

## Slide 8
Detectors in Space & Medical Applications
AMS-02 (Alpha Magnetic Spectrometer)
  Developer: CERN and international teams; installed on ISS in 2011
  Materials: Silicon trackers, permanent magnet, RICH detector, transition radiation detector, ECAL.
  How it works: Measures cosmic rays with silicon trackers, transition radiation detectors, and magnet spectrometers
  Cost (est.): ~$2B
  Power usage: ~2.5 kW
  Experiment examples: Dark matter searches, cosmic antimatter studies
PET Scanners
  Developers: Siemens, GE, Philips, national research hospitals
  Materials: Scintillation crystals (e.g., LSO), photodetectors
  How they work: Detect gamma photons from positron annihilation in medical imaging
  Cost (est.): ~$1M–$3M/unit
  Power usage: ~1–3 kW
  Applications: Oncology, neurology, cardiology imaging

## Slide 9
The Current & Future of Nuclear Detectors
Quantum Sensors
  Developers: NIST, Harvard, D-Wave, NASA QDIT
  Materials: Trapped ions, NV centers in diamond, ultracold atoms
  How they work: Use quantum states (e.g., superposition) to detect minuscule field or radiation changes
  Cost (est.): Experimental; tens of millions in R&D
  Power usage: Varies (low for sensors, high for cryogenics)
  Experiment examples: Gravitational wave follow-ups, dark matter detectors
AI/ML in Detection
  Use: Pattern recognition, real-time data filtering, noise suppression
  Example: LHCb’s real-time trigger system upgrade
Emerging Ideas:
  Space-based arrays for cosmic ray studies
  Perovskite-based sensors for flexible, low-cost detection
  Modular AI-driven detectors for planetary missions
  Quantum-enhanced PET scanners
Predicted Costs:
  Highly variable; research stage to $100M+ for deployment
Power Sources:
  Solar power, nuclear RTGs, advanced batteries
Planned Experiments:
  Lunar/planetary surface radiation analysis, long-baseline neutrino detection (DUNE)

## Slide 10
  https://www.physics.wisc.edu/outreach/wonders-of-physics-outreach-fellows/activities/wilson-cloud-chamber/
  https://americanhistory.si.edu/collections/object/nmah_700205
  https://www.livescience.com/how-a-geiger-counter-works.html
  http://national-radiation-instrument-catalog.com/new_page_144.htm
  https://senate.universityofcalifornia.edu/_files/inmemoriam/html/DonaldArthurGlaser.html
  http://national-radiation-instrument-catalog.com/historical_ads.htm
  https://www.psi.ch/sites/default/files/import/lmu/DevPsdEN/history_Si_pixel_detect.pdf
  https://www.nuclear-power.com/nuclear-engineering/radiation-detection/semiconductor-detectors/high-purity-germanium-detectors-hpge/
  https://sites.uci.edu/energyobserver/2012/11/26/introduction-to-the-atlas-detector-at-the-lhc/
  https://www.researchgate.net/figure/Schematic-overview-of-ATLAS-and-CMS-detectors_fig1_256423227
  https://www.sciencedirect.com/science/article/pii/S0168900202019605
  https://www.researchgate.net/figure/KamLAND-Zen-detector-In-the-center-of-the-detector-there-is-the-inner-balloon-IB_fig1_319948177
  https://www.researchgate.net/figure/Schematic-view-of-the-Super-Kamiokande-50-kiloton-water-Cherenkov-detector-in-Japan_fig3_45863929
  https://www.nature.com/articles/d41586-024-02221-y
  https://www.symmetrymagazine.org/article/july-2015/underground-plans?language_content_entity=und
  https://www.researchgate.net/figure/The-Facility-for-Antiproton-and-Ion-Research-FAIR-at-the-GSI-Helmholtzzentrum-fuer_fig1_346656100
  https://www.science.org/content/article/wanted-1-billion-troubled-german-nuclear-physics-facility
  https://www.nasa.gov/alpha-magnetic-spectrometer/
  https://www.iaea.org/newscenter/news/advancing-radiation-detection-instruments-for-nuclear-security
Work Cited