## Slide 1: Framework for the Development of Virtual Accelerator Models for Machine Learning Applications
October 27, 2025
Adwaith ravichandran
Postdoctoral Appointee
Argonne National Laboratory
Brahim mustapha
Accelerator Physicist
Argonne National Laboratory

## Slide 2: outline
ATLAS AI/ML Interface – Current online capabilities
Virtual Accelerator Aim – Offline experiments, train operators, support online tuning
Virtual Model Requirements – Mimics the machine in all aspects
Virtual Model Development – Example: ATLAS PI-Booster beamline
Virtual Accelerator Application – Example: Offline MHB experiment prior to online test
Potential Application to the EIC: Common techniques that can be transferred

## Slide 3: ATLAS: Argonne tandem linear accelerator system
World’s first superconducting accelerator for ion beams
Ion beams ranging from hydrogen to uranium
Energies as high as 10 MeV/u for the heaviest ions
National User Facility serving ~ 400 users per year
Switch ion beam every 3-4 days requiring rapid tuning
PII-BOOSTER BEAMLINE
ATLAS EXIT-PRE TARGET BEAMLINE

## Slide 4: The atlas ai-ML Dashboard interface

## Slide 5: ATLAS AI/ML Interface:
ATLAS AI-ML Interface [Dash module backend] used for Online accelerator interfacing
The Dash Interface is being used for online beam tuning and optimization, by expert operators
Virtual Accelerator with TRACK simulation added, Common input controls & output visualization

## Slide 6: Example - Online optimization of both beam transmission and profiles
This video shows comparison between 2 online experimental tests performed with and without profile width optimization in addition to transmission
When profile information is considered, higher transmission is achieved quicker

## Slide 7: virtual accelerator framework & development

## Slide 8: Virtual accelerator Requirements:
Accurate 3D physical representation using operationally validated beam dynamics software (TRACK in our case)
Match real machine behavior; Same control, diagnostics/observables experience for user:
Statistical simulated particle profiles match profile monitor reading
Statistical simulated particle timing/energy match silicon barrier detector spectra
Same control channel names, operating range/units
Compatible backend calibration for beamline elements:
Quadrupole Magnetic field → Control current
Radio frequency quadrupole Chassis voltage → Inter-vane voltage
Steering magnet bending angle → Control current [using beam rigidity-based scaling]
Cavity Field level → Control
Model extended, reused, adapted for many configurations, components, future designs

## Slide 9: Virtual accelerator Development:
Sample procedure to transform TRACK-based Simulation Model Virtual Accelerator
Experiment data collected for 40Ar beam at 52 MeV
PII-Booster line b/n two accelerating sections 7 quadrupole & 2 steering magnets
Bayesian inference for finding quadrupole misalignments, minimizing simulation error
Bayesian inference to obtain optimized synthetic input beam parameters
Eventually realistic input beam distribution will be measured from Pepper pot meter
Error drops from ~20% to ~6% after accounting for misalignments; to ~2% after fitting for input beam parameters
Following agreement, reduced-order modeling (ROM) / machine learning surrogates will be used to replace full-scale heavy simulations
Server [ac047] hosts control system emulator; Surrogate model will be integrated here

## Slide 10: Error minimization btw model & experiment

## Slide 11: Virtual accelerator Applications
Profile optimization with prior experiment data
Energy Change using Resonators
Newly proposed experimental methods can be tested in virtual model
Input settings for Quadrupole, Steering magnets, Resonators, Solenoids & Multi harmonic bunchers can be changed
Output observables like beam profile, beam current, bunch length and exit energy measured
Bunch length optimization
Profile optimization without prior experiment data

## Slide 12: Virtual accelerator Demonstration [PROFILE OPT]:

## Slide 13: Virtual accelerator Demonstration [mhb OPT]:

## Slide 14: Experimental tests
Resonator/Solenoid
control voltage [V]
Resonator
phase [deg]
Optimizing for fixed beam energy [fine tuning]
Optimizing for Transmission
Optimizing Transmission using prior experiment data
Optimizing for bunch length [fine tuning]
Same interface used to repeat virtual model tests in real machine
Experimental observables for objective function: > Faraday cup [beam current/transmission]; > Time of Flight measurement [beam energy]; > Silicon barrier detector [bunch length]
Each test ends with optimized element settings corresponding to optimal objective
These are compared with virtual model recommendations

## Slide 15: Summary of progress & highlights
The ATLAS AI-ML Dashboard Interface is fully developed and currently being used for online beam tuning and optimization by expert operators, working on full deployment…
Developed Virtual Accelerator models for different sections of the ATLAS linac based on beam simulations using TRACK code
Model predictability was significantly improved through fine-tuning by adding misalignment and steering effects as well as initial beam parameters inferred from data
For PII-to-Booster beamline, the difference in beam transmission between experiment and simulation reduced from ~46% down to ~16% after adding steering, down to 6% after including misalignments, and down to ~2% after including initial beam parameters
Using the described model tuning procedure, a highly accurate virtual model is now at the core of the ATLAS AI-ML Dashboard Interface, model already being used for experimental preparations
Future work
  Developing a surrogate to the full TRACK simulation model for speed
  Deploying the virtual accelerator online, bidirectional data flow Virtual ↔ Physical
  Developing virtual models for other sections of the linac

## Slide 17: Back up / Additional slides