## Slide 1: Compress by Importance and more
AI4EIC
10-27-2025

## Slide 2
Task:
Compress Tracking Detector data
Examples:
TPCs at sPHENIX and EIC
Baseline:
Do it accurately
Restrictions:
Do it on On-Time
Note: In fact, I become less and less worried about the throughput constraint recently, because the fast development in novel AI hardware. As an example, I just learned this past weekend that FPGA can handle convolution. Amazing, right!

## Slide 3
Encoder
Code
Decoder
Autoencoding as a Natural Solution to Data Compression
?
Since we are dealing with image data, the encoder and decoder are designed using convolutional neural network
Then, the reconstruction is compared with the input. While the difference between them is minimized with gradient descent, we get a good encoder/compressor with its matching decoder/decompressor.

## Slide 4
Channel dimension
Spatial dimensions
Compression by Size
(and what’s wrong with it TPC data)
Convolution is great at changing the size of the input

## Slide 5
Inductive bias of CNN: Spatial Homogeneity.
Convolution is mixing locally. Hoping a model based on homogeneous convolution to work is almost like hoping mixed color could be separated properly again
Although we may assume macro spatial homogeneity, the TPC data is NOT homogeneous on a micro level.

## Slide 6
input
Reconstruction by the compression-by-size approach
Difference
Bruised reconstruction

## Slide 7
Moreover
Compression-by-size produces
fixed size output, even if there is no signals in the input
Used the same amount of the time to compress, even if there is no signals in the input

## Slide 8
Can We Compress in a Different Way?
Anyway, we just need to save the data with fewer bytes…
It can be achieved by shrinking the input, but it can also be accomplished by saving only part of the input…

## Slide 10
Then, I determined to be lazy…
I just let my encoder to do nothing but to drop signals randomly…
MSE dropped from ~220 to ~19 with only 50% randomly selected signals
And to ~90 with 25% randomly kept signals
What if, the encoder can choose signals smartly to keep?

## Slide 11
Can We Compress by Importance

## Slide 12
1
2
3
4
5
6
7
8
9
10
Voxels ids:
Encoder that is an importance score assigner
.42
.35
.93
.01
.57
.88
.71
.89
.95
.99
Scores:
Now, we need to determine voxels to keep, but how?
By choosing a threshold, of course!
Threshold = 8.15484548538

## Slide 13
3
6
8
9
10
Voxel ids
.93
.88
.89
.95
.99
Scores
Threshold = 8.15484548538
Decoder
1
2
3
4
5
6
7
8
9
10
This is good, but how can we compress?
We penalize too high a sum of scores. So, only a small fraction of voxels will be saved.
1
2
3
4
5
6
7
8
9
10
Construction accuracy
Gradient Back propagation

## Slide 14
Data type | occupancy |  | PSNR | precision | recall | Retention ratio | Compression ratio
Au + Au (sPHENIX) | 0.108 | 0.112 | 21.4 | 0.934 | 0.936 | -- | 31
 |  | 0.0284 | 26.0 | 0.996 | 0.988 | 0.133 | 34
p + p (EIC) | 0.024 | 0.0073 | 28.7 | 0.994 | 0.985 | 0.109 | 185
Data type | occupancy |  | PSNR | precision | recall | Retention ratio | Compression ratio
Au + Au (sPHENIX) | 0.108 | 0.112 | 21.4 | 0.934 | 0.936 | -- | 31
 |  | 0.0284 | 26.0 | 0.996 | 0.988 | 0.133 | 34
p + p (EIC) | 0.024 | 0.0073 | 28.7 | 0.994 | 0.985 | 0.109 | 185
Compression by importance works
for both Au + Au and p + p collision
Additionally, compression by importance achieves variable compression ratio!
With the Sparse Convolution Engine, Compression by Importance can also achieves higher throughput on sparser data

## Slide 15
input
Reconstruction by the compression-by-importance approach
Difference
Better reconstruction

## Slide 16
From a Reviewer:
Can we use the importance score as a sliding bar to control how much data to save?
Implication:
The higher the cutoff, the fewer data to save, the lower the reconstruction quality. The lower the cutoff, the more data to save, the higher reconstruction quality to achieve.
Tunability after Training!

## Slide 17
Threshold = 8.15484548538
1
Score
Count
The Encoder is not motivated at all to produce any number between 0 and the threshold.
And the infinitely possible scores are wasted!
An absolutely arbitrary nonsense!

## Slide 18
1
Threshold
Density
1
Random Threshold
1
.42
2
.71
Kept:
3
.99
Random threshold
Random threshold
Random threshold

## Slide 19
1
Threshold
Density
1
Random Threshold
viv
.71
Now, we get rid of absolutely arbitrary nonsense! But will it work?
1.0
Random thresholding can push truly important voxels, and only truly important voxels, to high scores.

## Slide 20
1
Scores
Count
Will random thresholding use the full range of the scores?
Not really!
I really hope it to be a triumph story, but …

## Slide 21
Cumulative distribution of the scores
score
score
Distribution of the scores
Log scale

## Slide 22
Limited control by importance score
Cumulative distribution of the scores
Importance score
A sliding bar
Have you ever used a faucet that goes from trickling to a gushing when you rotate it by 0.1 degree? Well, we have it here.
Very narrow tunable range

## Slide 23
Cumulative distribution of the scores
score
A sliding bar
The sliding bar can help us achieve the following effect (we hope):
Harder sample low threshold more voxels saved acceptable reconstruction
Easier sample high threshold less voxels saved acceptable reconstruction
If we must fix a uniform threshold for all samples:
High threshold (less kept)
  Harder sample worse reconstruction
  Easier sample acceptable reconstruction
Low threshold (more kept)
  Harder sample acceptable reconstruction
  Easier sample wasted space

## Slide 24
Let us accept the fact that the tunable range of the fraction of kept voxels can only be this small.
But can we at least get what we hope?
Recall
Precision
Nope!
More voxels saved doesn’t guarantee better performance!
?
?

## Slide 25
A model that is not Trained to be flexible will not have flexibility after training
But how do you train the model to be flexible?
We can tell the model that if more voxels are going to be saved, I am going to request a better reconstruction. But if less voxels are saved, I won’t penalize you too much for a bad reconstruction.

## Slide 26
How to Train a Model to be Flexible
1
Threshold
Density
Random Threshold
For each input, generate a random number as the harshness of the voxel filter. Then, we map by
For this input, the reconstruction error will be weighted by

## Slide 27
1
Threshold
Density
harshness
Loss weight
1
harshness
mean
1
Threshold
Density
1
mean
harshness
Loss weight
Loss weight

## Slide 28
Recall
Precision
A Model trained to be flexible indeed exhibit flexibility after training – more voxels saved leads to better reconstruction accuracy!
?

## Slide 29
Summary
For sparse data, we can compress by importance for
  A variable compression ratio
  A higher throughput with proper software support
Tunability after training is possible but still a major challenge
Dataset: https://zenodo.org/records/14064045
GitHub repo: https://github.com/BNL-DAQ-LDRD/NeuralCompression_v3