## Slide 1: Setup for tile testing
Y. Khyzhniak, M. Stefaniak, M. Lisa, D. Brandenburg

## Slide 2: LFHCAL tiles
CALICE AHCal inspired SiPM-on-tile approach
Tiles and SiPM from Oak Rige for initial tests
Concave tile

## Slide 3: SiPM on PCB board
S14160-1315PS
Photosensitive area (mm): 1.3 × 1.3
Number of pixels: 7284
Breakdown voltage (V): 38 ± 3
Typical pulse shape

## Slide 4: How is the SiPM physically connected to the tile?
In this configuration there is no physical connection between SiPM and tile
The spherical hollow acts like an optical lens
It causes photons that scatter inside the tile to be redirected downward toward the SiPM located underneath
This design increases the probability that light generated far from the SiPM still reaches it, helping recover signal from across the tile
Incident light

## Slide 5
In this configuration there is no physical connection between SiPM and tile
Unwrapped Tile on top of the SiPM
Wrapped Tile on top of the SiPM
How is the SiPM physically connected to the tile?

## Slide 6: Why is the spherical hollow visible in the unwrapped tile you hold in your hand not visible in the photo with the different tile sizes / thicknesses?
As tile size increases, the SiPM-on-tile approach becomes less effective due to:
  Uniformity degrades with larger tiles
  The optical features become less prominent in large tiles due to longer photon travel paths and increased internal scattering
As alternative we going to test different SiPM placement

## Slide 7: Wrapping: alternative
Even small tiles are difficult to wrap perfectly, often leaving gaps at the corners and air gaps, folds, or wrinkles which can scatter light unpredictably
Edge artifacts can lead to position-dependent signal variations → worse uniformity
Over time, adhesive tapes can peel or degrade, especially with temperature changes or humidity
Larger tiles make this problem worse, creating bigger unwrapped areas
Instead of foil wrapping, a white reflective paint can be used, for example
  Four SiPMs are attached to flex cables, which are glued into grooves at the tile corners for optical readout.

## Slide 8: Is the controlling board an explicit component of the sketch Maria showed last Tuesday, page 5 of the slides uploaded to the nHCal indico? Is it shown in any of the photos of the muon telescope?
No, here is the more right way to show it
Also, there is no fibers+PMT → instead we have SiPM-on-tile
SiPM-on-tile + controlling bard

## Slide 9: SiPM control board
The black 3D-printed housing holds a scintillator tile with reflective coating
The purple PCB next to the tile hosts the SiPM socket and initial signal routing
Hamamatsu Readout Module (C11204-01)
  SiPM bias voltage generator
  Amplifier chain: SiPM current pulses to voltage signals
  Analog output (SMA): connector sends analog signal to scope/DAQ
  USB control
  Flat ribbon cable interface

## Slide 10: SiPM control board
The black 3D-printed housing holds a scintillator tile with reflective coating
The purple PCB next to the tile hosts the SiPM socket and initial signal routing
Hamamatsu Readout Module (C11204-01)
  SiPM bias voltage generator
  Amplifier chain: SiPM current pulses to voltage signals
  Analog output (SMA): connector sends analog signal to scope/DAQ
  USB control
  Flat ribbon cable interface

## Slide 11: SiPM control board
The black 3D-printed housing holds a scintillator tile with reflective coating
The purple PCB next to the tile hosts the SiPM socket and initial signal routing
Hamamatsu Readout Module (C11204-01)
  SiPM bias voltage generator
  Amplifier chain: SiPM current pulses to voltage signals
  Analog output (SMA): connector sends analog signal to scope/DAQ
  USB control
  Flat ribbon cable interface

## Slide 12: Initial testing: the idea
Cosmic ray testing setup
A simple muon telescope:
  Two scintillators placed above and below the test tile
Trigger condition:
  A valid event occurs only when both scintillators detect a signal in coincidence
If there is no coincidence:
  Ignore the event as background
Scintillator
Scintillator
Trajectory of a cosmic ray particle

## Slide 13: Setup: muon telescope
Background Data

## Slide 14: Oak Rige tiles testing
Cosmic ray testing setup
A simple muon telescope:
  Two scintillators placed above and below the test tile
Trigger condition:
  A valid event occurs only when both scintillators detect a signal in coincidence
When a coincidence is detected:
  Open the gate to read out the signal from the concave test tile
If there is no coincidence:
  Ignore the event as background
Scintillator
Scintillator
Concave tile
Trajectory of a cosmic ray particle

## Slide 15: Setup: muon telescope
Putting SiPM-on-tile in between triggering scintillators → data from tile
Background Data

## Slide 16: Electronics
Scintillator on Top → PMT → Discriminator
Scintillator on the Bottom → PMT → Discriminator
→ Coincidence (AND logic)
→ Gate signal
→ CAMAC ADC integration window

## Slide 17: Electronics
Scintillator on Top → PMT → Discriminator
Scintillator on the Bottom → PMT → Discriminator
→ Coincidence (AND logic)
→ Gate signal
→ CAMAC ADC integration window

## Slide 18: Electronics
Scintillator on Top → PMT → Discriminator
Scintillator on the Bottom → PMT → Discriminator
→ Coincidence (AND logic)
→ Gate signal
→ CAMAC ADC integration window

## Slide 19: Electronics
Scintillator on Top → PMT → Discriminator
Scintillator on the Bottom → PMT → Discriminator
→ Coincidence (AND logic)
→ Gate signal
→ CAMAC ADC integration window

## Slide 20: Electronics
Scintillator on Top → PMT → Discriminator
Scintillator on the Bottom → PMT → Discriminator
→ Coincidence (AND logic)
→ Gate signal
→ CAMAC ADC integration window

## Slide 21: Electronics
Delayed (by purpose) signal from SiPM-on-tile

## Slide 22: Plan
Cosmics → Sr-90 source
  Half-life: 29.1 years
  Mode of decay: Beta radiation
E < 0.546 MeV
E < 2.28 MeV
Can penetrate ~1cm of plastic

## Slide 23: Plan
Vary tile size (5×5 cm², 10×10 cm²)

## Slide 24: Plan
Vary tile thickness (4,6,8 mm)

## Slide 25
Vary SiPM placement (center, corner, edge)

## Slide 26
Vary SiPM placement: with wavelength shifting bars, fibers

## Slide 27: Plan
Cosmics → Sr-90 source
  Vary tile size (5×5 cm², 10×10 cm²)
  Vary tile thickness (4,6,8 mm)
  Vary SiPM placement (center, corner, edge), with wavelength shifting bars, fibers
  Tile coating (wrapping, painting)
Check performance:
  Light yield per MIP
  Signal uniformity
  Long range plan: timing resolution, optical cross-talk (if relevant; configuration-dependent)
Target timeline: ~2 months, aiming for completion by July 11 (ideally)