## Slide 1: Wire-Cell Updates
Haiwang Yu for the Wire-Cell team
SBND CM @ The University of Sheffield
2025-06-04

## Slide 2: Wire-Cell Event Reconstruction
3D imaging
clustering
charge-light matching
3D trajectory & dQ/dx fitting
cosmic muon tagger
TPC simulation
noise filtering
signal processing
multi-track fitting
DL-3D vertexing
particle identification
JINST 13 P05032 (2018) JINST 16 P06043 (2021)
Phys. Rev. Applied 15, 064071 (2021)
JINST 17 P01037 (2022)
JINST 12 P08003 (2017) JINST 13 P07006 (2018) JINST 13 P07007 (2018) JINST 16 P01036 (2020)
Part 1: Sim-NP-SigProc
Part 2: Img-Clus-QLMatching-nu-select
Part 3: 3D PatRec
Sep. 2025
End 2025

## Slide 3: Progress:
SBN Team
  Part 1 – Lynn, Moon, Prabhjot
    Baseline Sim/Noise Filtering/SigProc deployed in production
    DNN-ROI production ready – Moon, Avinay, Gray
  Part 2
    Imaging, clustering – evaluation and validation – Ewerton, Prabhjot
    QL-Matching – initial version – Lynn, Haiwang
BNL Team
  Part 2:
    Multi-apa/face generalization – Xin, Brett, Haiwang
    Other Infrastructure updates
      IO design for ql-matching results – Brett
        For using Lynn's QL-Matching work
      uboone QL-Matching file reader – Brett
        For development validation
      Retiling: fill gaps in 3D – Xin, Brett
        Prepare for Part 3
Lynn's talk, Reco. 1
Moon's talk, Reco. 1
This talk
Notes: Add description of part 1
echo other talks: link, plots
less technical language
links to SBND

## Slide 4: Plan
SBN Team
  Part 1
    Wrap up DNN-ROI – production, paper – Moon, Avinay, Gray, Haiwang
  Part 2
    DL-nu-clustering – targeting NC pi0 – Avinay, Prabhjot, Haiwang
    Initial generic nu selection – Haiwang, Prabhjot, etc.
  Part 3
    validation, optimization, deployment
BNL Team – Xin’s summary of rest works
  Rest of Part 2
    Cosmic taggers
  Part 3
    Single/multi trajectory fitting
    NeutrinoID PatRec
    PatRec
    Track & Shower separation
    Vertex related
      Sparse-RCNN
    EM Shower related
This talk
Moon's talk, Reco. 1
Notes:     Tagger & Kinematics Info
      RNN
less technical language
links to SBND
discuss the production timeline
physics analyses for nu2026
April 2026
DetVar sample? Wire mod or hit mod?

## Slide 5: Multi-apa/face generalization
Add apa/face information
  wpid in Facade, standalone
Add alternative scope
  T0 x correction
Update lower-level utility functions
Update higher-level algorithms
Update configurations
Test for PDHD – 4APA/8Faces
Notes: why use PDHD
easy to adapt to SBND

## Slide 6: Using PDHD to show the multi-apa effect
https://www.phy.bnl.gov/twister/bee/set/6f9a9a6f-1a87-465c-b427-56374ab2a534/event/0/
Dummy T0 correction applied
Configuration for SBND is straight fowrad
Working on merging with Lynn's QL-Matching work
APA crossing tracks

## Slide 7: Potential improvements from uboone
https://www.phy.bnl.gov/twister/bee/set/d620d2d4-0608-47b9-a5aa-169b9d743c4d/event/291/
Isochronous events
  include more 2D information
Neutrino Vertexing
  improving the Sparse-RCNN-Vertexing
Prolonged signal
  DNN-ROI
Clustering failure
  important for photon related analysis
  separate gammas are not clustered together for NCpi0  important for SBND (Lee)
    try AI/ML clusgtering
Clustering failure

## Slide 8: Wire-Cell 3D information: 3d points, point-point edges and blobs
BEE link
BEE:
DUNE-FD-VD, numu, one APA
torch_geometric.data
visualization: plotly
https://github.com/HaiwangYu/sbnd-dl-clustering
3d points, point-point edges
Zoom in to show blobs

## Slide 9: Labling of Wire-Cell 3D points
SBND Simulation - Avinay

## Slide 10: Towards generic neutrino selection
MicroBooNE generic neutrino selection
3D Imaging
Clustering
QL-Matching
Through-going muon tagger (TGM)
  SCE corrected FV boundaries
Stopping muon tagger (STM)
  track direction
SBND adaptation
QL-Matching alone is enough?
  much higher neutrino event fraction, ~30 times w.r.t. uboone (Michelle’s slides)
  SCE, track direction still needed for down stream PatRec
In uboone, other reconstruciton paradigms used wire-cell generic neutrino tagger
  could be useful in SBND?
    if so we can port that information to LArSoft together with the 3D points
Notes: https://sbn-docdb.fnal.gov/cgi-bin/sso/RetrieveFile?docid=40270&filename=maths.pdf&version=2

## Slide 11: Rejecting Through-Going Muons (TGM)
Z (beam direction)
Y
TGM: cosmic-ray muons go all way through the active TPC volume
Identification: the two endpoints of TPC cluster at/outside the effective detector boundary
SCE correciton is needed
Charge-light matching
TGM rejection
Neutrino:Cosmic-ray in MicroBooNE
1 : 6.4
1 : 0.9
Improved by factor of 6
Fiducial volume used in analysis: 3 cm inside the effective boundary
Effective detector boundary because of space charge effect
Notes: With the charge-light matching, the main background is the cosmic muon in random coincidence with the beam spill.
Within which, The dominated one is the through-going muons that cross through the active TPC volume.
This kind of background can be identified by examining if the two end points of the TPC clusters are outside the effective detector boundary.
After rejecting this kind of through-going muon background, we improve the neutrino signal to noise ration from 1:6.4 to about 1:1.

## Slide 12: Rejecting Stopping Muons
Y
X (drift direction)
STM: cosmic-ray muons enter and stop inside the active volume
Identified by directionality: from outside to inside
  Tracks from neutrino activities will go out of detector from inside
  Tracks from background will enter the detector from outside
Trajectory and dQ/dx fitting  Bragg peak  directionality
dQ/dx vs. residual range is also important for the particle identification for tracks
Charge-light matching
TGM rejection
1 : 6.4
1 : 0.91
STM rejection
1 : 0.36
Improved by factor of ~3
Improved by factor of >6
Additional Cuts
1 : 0.20
Neutrino:Cosmic-ray in MicroBooNE
Notes: The second largest background is the random-coincident cosmic-ray muon stopped inside the detector. The topology of this kind of background is very similar to the case where you have a neutrino interaction, and the muon exiting the detector.
This kind of background can be rejected by identifying the direction of the track:
tracks from neutrino activities start from inside and end outside
while the bkg. stopping muons start from outside and end inside.
The direction of the track, can be determined by searching for the Bragg peak near the stopping point. At the same time, the charge per unit distance: dQ/dx vs. the residual range is also important to perform particle identification for tracks.
To achieve this, Wire-Cell invented a new algorithm to fit the track trajectory as well as the dQ/dx.

## Slide 13: Summary
The multi-apa/face generalization work setup foundation for future PatRec porting works
  Also took us a lot of time
Lynn's initial QL-Matching results showed promissing results and establish foundation for generic nu selection
The Wire-Cell 3D information and labling is almost ready to use
  e.g., DL neutrino clustering
The BNL team is actively working on porting the rest PatRec – targeting end of 2025
The SBND team is working on adaptation/validation of ported algorithms and new developments
If we have users that are interested in the Wire-Cell 3D points or the generic nu selection, we can include that in the Sep. 2025 production

## Slide 14: backups

## Slide 15: Test for PDHD – 4APA/8Faces
3 Clusterings: per-face; per-apa; all-apa
https://github.com/HaiwangYu/wcp-porting-img/blob/main/pdhd/wct-clustering.jsonnet
per-face: single volumn
per-apa:
deghosting needs both faces
all-apa: using T0 corrected points

## Slide 16
Matching Hypotheses
Clustering
3D Image
Light Reconstruction
Hypotheses Selection
4.8 ms drift window
20-30 TPC activities
All possible hypotheses
One cluster  at most one flash (inefficiency in the light system)
One flash  many or zero TPC clusters within corresponding active volume (activities in inactive volume)
Light signal proportional to (reconstructed 3D) charge
Known light acceptance given position
Predicted vs. Measured light pattern with Compressed Sensing
Many-to-many QL-Matching
JINST 16 P06043 (2021)
Notes: Here is how this algorithm works. We have 20-30 TPC charge activities.
At the same time, we have 40-50 PMT light activities.
First, we perform a charge clustering algorithm to group all reconstructed 3D charge into separate clusters, each cluster represents a possible particle or physics activity.
Then, all possible hypotheses of charge-light matching pairs are calculated in P_ijk.
Then 3 extra constrains are added
1, each TPC cluster can be only used once;
2, some light may won't match due to e.g., TPC activities outside the active volume;
and 3, L1 regularization for compressed sensing.
This animation shows one charge-light matching result by showing individual TPC clusters, the predicted PMT pattern in green and the measured PMT pattern in red.
Given the matched charge-light pair, if we cut on the light signal in coincidence with the beam, we can select the neutrino interaction candidate.

## Slide 17: Rejecting Stopping Muons
Y
X (drift direction)
STM: cosmic-ray muons enter and stop inside the active volume
Identified by directionality: from outside to inside
  Tracks from neutrino activities will go out of detector from inside
  Tracks from background will enter the detector from outside
Trajectory and dQ/dx fitting  Bragg peak  directionality
dQ/dx vs. residual range is also important for the particle identification for tracks
Notes: The second largest background is the random-coincident cosmic-ray muon stopped inside the detector. The topology of this kind of background is very similar to the case where you have a neutrino interaction, and the muon exiting the detector.
This kind of background can be rejected by identifying the direction of the track:
tracks from neutrino activities start from inside and end outside
while the bkg. stopping muons start from outside and end inside.
The direction of the track, can be determined by searching for the Bragg peak near the stopping point. At the same time, the charge per unit distance: dQ/dx vs. the residual range is also important to perform particle identification for tracks.
To achieve this, Wire-Cell invented a new algorithm to fit the track trajectory as well as the dQ/dx.

## Slide 18: Principle of the Fit
Come up with a 3D track hypothesis (3D trajectory points and dQ/dx)
Predict the deconvolved signals on all projection views
Minimize the difference between the observation and prediction
V view
U view
W view
Notes: Here is the principle of the fit. First, we need to come up with a 3D track hypothesis, which includes the 3D trajectory and their associated dQ/dx.
Then, we can predict the deconvolved signal on each of the projection view. The minimization of the difference between the observation and prediction would help us to find the best 3D track hypothesis.

## Slide 19: Simplified Prediction of the Deconvolved Signal
dQ/dx at generation
diffusion
Electron at anode plane
Induced current on wires
Convolve with field res.
Convolve with elec res.
Digitized amplified current
Signal Processing Chain
Deconvolved signal
At signal processing stage, we have two additional effects:
Software filters (time and wire dimension)
Usage of position-averaged overall response function
Simplified model
Pixel # in 2D Projections
Charge
Full process of signal formation and signal processing is complex  significant burden in computation
A simplified model was developed
Notes: One key of this technique is to be able to make prediction of the deconvolved signal based on each track hypothesis. This is challenging, given the long chain in TPC signal simulation and signal processing.
Since we spent a long time studying the signal formation/processing, we come up with a simplified model based on smearing, which allows us to quickly and accurately model the deconvolved signal.

## Slide 20: Trajectory and dQ/dx Fitting
Unknowns
Measurements
Charge-light matching
TGM rejection
Neutrino:Cosmic-ray
1 : 6.4
1 : 0.91
STM rejection
1 : 0.36
Improved by factor of ~3
Improved by factor of >6
Additional Cuts
1 : 0.20
Notes: The minimization is achieved through a two-step process. The first step focuses on the 3D track trajectory positions, and the second step focuses on the dQ/dx extraction.
With this technique, we reliably reconstruct the track trajectory and dQ/dx, which allow us to identify Bragg peak. After rejecting the stopping muons and some additional background, we achieved a signal to background ratio of 5:1.

## Slide 21: Preselection
Generic neutrino detection powered by many-to-many charge light matching and additional cosmic taggers to reject in-time coincidence cosmic-ray muons
  99.999% cosmic-ray muon background rejected
    Start with 1:20,000 neutrinos to cosmics
    End with 5.2:1 neutrinos to cosmics
  90% efficiency for νeCC and 80% efficiency for νµCC
  νeCC purity ~0.4% at this stage
Phys. Rev. Applied 15, 064071
Notes: With all these tools together, we achieved a generic neutrino setection. 99.999% of cosmic muon background are rejected.
Started with 1:20,000 neutrinos to cosmic ratio, we achieved a 5.2:1 ratio after the preselection.
At this stage, we still maintain a 90% and 80% efficiencies for nueCC and numuCC, respectively.
But for nueCC, the purity is still low due to the FermiLab booster neutrino beamline configuration.

## Slide 22: DL-Clustering data preparation
Sim/SP/Img
artROOT
MCParticle in .root or .json?
trackID?
Clus
sampling -> 3D points (KDTree, PCA, Hough)
physics-informed graph
ITensons in .npz
Points or Graph
graph2file utility function
Post processing
Labeled data
SimEnergyDepo in .json
trackID?
CellTree_module
Notes: additional labeling whether a track is out of box without correction

## Slide 23: save out reco.
Facade::Grouping -> boost::multi_array<float, 2> -> WireCell::Stream::write() (.npz)
a Facade::Util function that is called at the end of MABC
  similar like a BEE dumper
meta data: run, subRun, eventNum
blob:
[blob_idx], q, qp0 (uq), dqp0 (duq) ..., wind_min_dp0 (wind_u_min) ...,
ncorners, corner0_x, corner0_y, corner0_z, ... corner11_z [max 12 corners]
points:
[pt_idx], x, y, z, q, blob_idx, qp0 (uq), dqp0 (duq) ...
point_graph:
head (pt_idx), tail, weights (pp-dist.)
light?
Notes: add the existing clustering information

## Slide 24: Another Identified Problem
Another problem identified
  Clustering of NCpi0 parts …
  Multiple activities, not be able to clustered together ….
  Clustering problem (before Q-L matching)
https://www.phy.bnl.gov/twister/bee/set/d620d2d4-0608-47b9-a5aa-169b9d743c4d/event/291/
Separate gammas are not clustered together for NCpi0  important for SBND (Lee)

## Slide 25
Sep: generic nu-selection, user of this?
neutrino2026:
Lynn, Pandora, inclusive nueCC xsec
  use WC QLMatching?
  PID?
Moon, 1mu1p
Prabhjot, img-clus-match-nu-sel
Avinay, end of this year with high chance of extension
  physics analysis on photon
  reach out to Lee

## Slide 26: DL-Clus

## Slide 28: issue with SimChannel IDE

## Slide 29: Avinay-mar, z-offset 0.5cm
https://www.phy.bnl.gov/twister/bee/set/80364363-b233-43d8-8bee-be394a0260ee/event/0/

## Slide 30: max_distance=4cm

## Slide 31: Scaling up for production
LArSoft env:
wcls-img-clus.fcl -> g2f-apa?-face?—r-s-e.npz
  blobs
  points: x,y,z,q,blob_idx
  ppedges
celltree_sbnd.fcl -> celltree-apa?—face?-r-s-e.json
python env (sklearn, etc):
label.py -> g2f-label-apa?-face?—r-s-e.npz with per point tags
  points: x,y,z,q,blob_idx,isnu
train python env (torch, torch_geometric)
load g2f arrays which can be used as torch_geometric.data

## Slide 32: Generic nu selection

## Slide 33: Thoughts on resolving this issue
https://www.phy.bnl.gov/twister/bee/set/826f2384-5551-4926-9863-37829ef3a175/event/1008/
match first or merge (two apa info) first?
merge first let us use all possible information
  consider chi2 for two apas
can we handle overlapping TPC activities?
  rm front/back porch first?
caveat: random coincidence merging?

## Slide 34: PDHD stages:
per-face
per-apa
all-apa

## Slide 35: Potential approach
MABC
per-face clus
MABC
no-t0-corr stitching
MABC
per-face clus
light for all apa
ql-matching
MABC use t0-corr Scope

## Slide 36: backups

## Slide 37
DL-clus data – Avinay etc
merge apply-pc to master
link larwirecell with wct for the IO
generic nu selection
  outline the requirement, status of the tagger
  TGM – HY etc
  STM tagger – BV, XQ
  tagged 3d points to larsoft (spacepoint)
    have the user first
Technical
SigProc paper
DNN-ROI paper
imaging-clustering-qlmatching generic nu selection
Physics
nue x-sec
End of 2025:
Full WC without nue BDT tagger
2026: more DL

## Slide 38
Wire-Cell SBND group:
BV, XQ, etc:

## Slide 39
Hanyu: Plan to port back general nu selection
LEP. reco., blip protection