## Slide 1: MPGD Endcap Tracker Interconnection Structures and Integration
C. Ammendola, R. Ammendola, M. Bondì, A. D’Angelo, R. Di Salvo, A. Fantini, L. Lanza, S. J. Lee, G. Nobili, E. Sidoretti, L. Torlai
July 28th 2025 – Infrastructure and Integration Meeting
Stefano Gramigna (sgramigna@roma2.infn.it) on behalf of the ECT group:

## Slide 2: Issues with Current ECT Integration
ECT quadrants overlap, either internal clearance in Z (limiting for ECT) or precise alignment will be necessary for the installation of PST’s top half

## Slide 3: Issues with Current ECT Integration
We can bypass the problem by installing the modules frontally, with the PST already closed and the beam pipe in place
NOT HERE
BUT HERE

## Slide 4: Principles
Glued pins handle module to module interfaces
Possible materials are brass, SS 316, PEEK, and PERMAGLAS (+ SS HeliCoil)
Threaded standard
Through standard
Through low profile
Threaded spacer
Threaded spacer
reversed

## Slide 5: Principles
The detector’s back panel acts as reference, pins are glued in a 1.5 mm deep counterbore, the head of the pin sticks out 0.5 mm (standard)

## Slide 6: Principles
This ensures that interfaces are not affected by errors accrued when gluing the detector stack
Glued stack
A nominal detector thickness of 16 mm is assumed
Actual thickness should be closer to 15.7 mm
Standard pins stick out 0.5 mm at each side w.r.t. the nominal detector thickness
Spacer pins add 2 mm in a chosen direction
SPACER PIN

## Slide 7: Principles
A second counterbore on the front panel provides a glue reservoir for epoxy sealing

## Slide 8: Principles
FEBs and service inlets/outlets will not be accessible once all the modules are in position
Cables and service lines (up to the patch panels) must remain connected to the modules

## Slide 9: Principles
No fine mechanical alignment is pursued
Software alignment with data from magnet-off runs should provide better results anyway
Golden tracks from the silicon tracker will be used as reference
Overlapping portions of the quadrants could be used for alignment if needed (4 points per track in these regions)

## Slide 10: Starting Point
No. 4 mounting brackets already mounted on PST at 0°, 90°, 180°, 270°
(Nothing prevents a 45° rotation of the whole detector at present)

## Slide 11: Mounting Brackets Preliminary Design
No. 2 designs for mounting brackets (mirrored across the vertical plane)
Just a placeholder proposal until PST design is frozen

## Slide 12: Integration procedure
First quadrant installed is top-right

## Slide 13: Integration procedure
Fixed to the mounting brackets with a single M4x16 screw at each corner
(M4 in Ø4.3 for the time being, subject to changes)

## Slide 14: Integration procedure
The second quadrant installed is bottom-left, similarly fixed to the mounting brackets (temporary supports might be useful at this stage)

## Slide 15: Integration procedure
A two-part interconnection ring (PERMAGLAS) is pre-assembled around the beam pipe and then fixed to the quadrants with M4 screws (brass, SS 316, or PEEK)

## Slide 16: Integration procedure
The third quadrant installed is top-left, fixed first at the mounting brackets …

## Slide 17: Integration procedure
… Then to the other quadrants near the central cavity …

## Slide 18: Integration procedure
… and finally to the bottom level quadrants again where the spacer pins are located. 2 mm separate the two levels of modules

## Slide 19: Integration procedure
Bottom-left quadrant is similarly installed to complete the first disk

## Slide 20: Integration procedure
A two-part interconnection pipe (PERMAGLAS) is pre-assembled around the beam pipe

## Slide 21: Integration procedure
A two-part interconnection pipe (PERMAGLAS) is pre-assembled around the beam pipe

## Slide 22: Integration procedure
And then fixed to the interconnection ring and to the top-level quadrants with M4 screws

## Slide 23: Integration procedure
The second row of mounting brackets can now be installed

## Slide 24: Integration procedure
The module’s mounting sequence repeats itself. Top-right quadrant is secured to the mounting brackets and to the interconnection pipe with M4 screws

## Slide 25: Integration procedure
The bottom-left module is similarly installed

## Slide 26: Integration procedure
Then top-left

## Slide 27: Integration procedure
Low-profile screws are used to secure the top-level modules of the second disk These are the only special screws in the assembly

## Slide 28: Integration procedure
The installation of the bottom-right module follows next, concluding the assembly

## Slide 29: Changes to FEB Form Factor
FEB PCBs had to be shrunk by 2 mm to accommodate the interconnection structures and maintain a 5 mm clearance between facing boards

## Slide 30: Screw-by-screw Video of the Procedure

## Slide 31: Conclusions
A first proposal for structures interconnecting the ECT modules on the lepton side is presented
An integration sequence only requiring frontal access and applicable with the beam pipe already in place was developed in accordance
Mechanical interfaces are rendered independent from the glued detector stacks (which are prone to accumulating errors)
FEB form factor had to be adjusted, now consisting of two 110x52.5 mm2 PCBs
Hadron side geometries are more complex due to the asymmetric central cavity, but the same solutions can be applied