## Slide 1: Efficient Programming on Heterogeneous Accelerators
Peipei Zhou

## Slide 2
2025/09/12, New York Scientific Data Summit 2025 Peipei Zhou, Assistant Professor
Research:
Teaching:
Architecture: FPGA, AI ASIC, GPU, Chiplet, etc.
Abstraction: Compiler Support
Application: Artificial Intelligence, Genome (Medical), etc.
G: Reconfigurable Computing, 2022 Spring, 2023 Spring, 2024/2025 Fall
UG: Computer Organization and Architecture, 2022 Fall, 2023 Fall, 2024 Spring
UG: Embedded System Design, 2023 Spring; UG: VLSI Design, 2025 Spring
Peipei Zhou’s Group
https://peipeizhou-eecs.github.io/
Experience:
2008-2012: ECE B.Sc. @ Southeast University
2012-2019: CS Ph.D. @ UCLA with Prof. Jason Cong
2019-2021: Staff Software Engr. @ Enflame, AI ASIC Startup
2021/09-2024/08: Assistant Professor @ Pitt-ECE
2024/09/01-Now: Assistant Professor @ Brown

## Slide 3
Based on Fred Pollack (Intel) and Michael Taylor (UW)
Adapt the architecture to application domain
i386
i486
Pentium®
Pentium Pro®
nuclear reactor
Pentium II®
Pentium III®
Pentium® 4
hot plate
rocket nozzle
sun’s surface
Parallelization
Customization
1.5µ
1.0µ
0.7µ
0.5µ
0.35µ
0.25µ
0.18µ
0.13µ
0.10µ
0.07µ
1
10
100
1000
Watts/cm2
Power doubles every 4 years
Why Customized Computing?
Challenge with Processor Design – Power Barrier:
From Parallelism to Customization and Specialization
“New Microarchitecture Challenges in the Coming Generations of CMOS Process Technologies”, Fred J. Pollack (Intel Fellow)
3
Notes: Muhuan: figure from Michael Taylor, UCSD; data is from Intel
https://pdfs.semanticscholar.org/6a82/1a3329a60def23235c75b152055c36d40437.pdf

## Slide 4
Source: I. Kuon, R. Tessier, J. Rose. FPGA Architecture: Survey and Challenges. 2008.
FPGA (Field Programmable Gate Arrays)
  Energy efficiency, 10-100X than CPUs
  Domain-Specific Accelerators (DSA) for various applications: genomics, image/video, GNN, etc.
Customized Computing on FPGAs
Stencil for Image/Video Processing [ICCAD’18 SODA]
Genomics Acceleration [FPGA’21 Mocha]
Use of FPGAs trade-off performance for design cost, flexibility, and time-to-silicon

## Slide 5
Energy Efficiency (GOPS/Watt)
Chart: 
| DeiT-T | DeiT-160 | DeiT-256 | LV-ViT
GPU T4 (12nm) | 35.4 | 21.84 | 36.4 | 26.9
FPGA U250 (16nm) | 17.04 | 12.57 | 18.27 | 15.32
GPU A10G (8nm) | 48.37 | 34.98 | 66.78 | 45.19
Re-examine FPGA vs. GPU vs. CPU: Deep Learning Inference
Vision Transformer, INT8 inference, batch = 6
Energy efficiency comparison
Why FPGA becomes the most inefficient platform in deep learning inference?

## Slide 6
Re-examine FPGA vs. GPU vs. CPU: Deep Learning Inference
B
A
B’
C
D
C’
A -> B, Volta GPU introduces Tensor Core
B’-> C, Tensor Core Upgrade
C’-> D, Tensor Core Upgrade
What if “FPGA + Tensor Core”?

## Slide 7
Energy Efficiency (GOPS/Watt)
Chart: 
| DeiT-T | DeiT-160 | DeiT-256 | LV-ViT
GPU T4 (12nm) | 35.4 | 21.84 | 36.4 | 26.9
FPGA U250 (16nm) | 17.04 | 12.57 | 18.27 | 15.32
GPU A10G (8nm) | 48.37 | 34.98 | 66.78 | 45.19
SSR(Ours) | 453.32 | 360.9 | 423.89 | 360.04
“Game Changer” in Deep Learning Inference
Vision Transformer, INT8 inference, batch = 6
Energy efficiency comparison
“X FPGA”

## Slide 8
“X FPGA” => Versal ACAP Architecture
AMD ACAP
Heterogeneous SoC
FPGA + AI Tensor Cores + CPU
Combine the best of both worlds? How?
Can we generalize this?
Notes: Versal ACAP Architecture Overview

## Slide 9
Secret Sauce => Partition & Compose
Image Classification: Vision Transformer
768 Layers
Monolithic Programming Model: 49.5 GFLOPS
Partition & Compose : 1609 GFLOPS
32.5x
B0L0
B0L1
B0L2
B0L3
Scheduling
ACC0
ACC1
ACC2
ACC3
Batch 0
B0L0
B0L1
B0L2
B0L3
B1L0
B2L0
B3L0
B1L1
B2L1
B3L1
B1L2
B2L2
B3L2
B1L3
B2L3
B3L3
-3
ACC0
L0
L1
L2
L3

## Slide 10
0
0
AIE Array
PLIO
AIE
Monolithic Programming Model
25.6 GB/s
1.2 TB/s
PL
NOC
Processor System
(ARM)
DMA
Sender
Receiver
LHS
RHS
Output
DDR4
DDR Space
Sending
Matrix With Large Size
1
2
3
5
6
7
4
0
1
2
3
0
5
6
7
4
LHS
RHS
VLIW
Processor
32KB
Mem

## Slide 11
0
0
AIE Array
PLIO
AIE
Monolithic Programming Model
PL
NOC
Processor System
(ARM)
DMA
Sender
Receiver
LHS
RHS
Output
LHS
RHS
DDR4
DDR Space
Matrix With Large Size
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
2
3
5
6
7
4
0
1
2
3
0
5
6
7
4
1
0
2
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
0
2
Sending
0
1
25.6 GB/s
1.2 TB/s
VLIW
Processor
32KB
Mem

## Slide 12
AIE Array
PLIO
AIE
Monolithic Programming Model
PL
NOC
Processor System
(ARM)
LHS
RHS
Output
LHS
RHS
DDR4
Matrix With Small Size
DDR Space
Valid Data
Padding
Invalid communication
Invalid Computation
DMA
Sender
Receiver
VLIW
Processor
32KB
Mem

## Slide 13
Matrix Multiply on 384 AIEs
Huge computation resources in one monolithic accelerator vs. MM layers of small sizes
Monolithic Programming Model

## Slide 14
Chart: 
| one | two | thirty | dog | cat | bird | year | month
One Monolithic Acc | 0.41 | 3.27 | 24.9 | 172.23 | 1083.15 | 1606.73 | 1649.92 | 2821.14
64 128 256 512 1K 1.5K 2K 3K
10-1
104
103
102
101
100
Throughput (GFLOPs)
Huge computation resources in one monolithic accelerator vs. MM layers of small sizes
X
A
2821.14 GFLOPS
X
B
0.41 GFLOPS
Explore data reuse by allocating large on-chip buffers
Shape mismatch, waste on both computation and communication
Square Matrix Size
Monolithic Programming Model

## Slide 15
Composing Diverse Accs
PLIO
AIE
VLIW
Processor
32KB
Mem
NOC
Processor System
(ARM)
DDR4-DIMM
DMA
Buffer
PLAIE
Accelerator 0
AIE Array
PL
DDR Space
Matrix With Both Large and Small Size
Partition & Compose Programming Model

## Slide 16
Composing Diverse Accs
DDR Space
Matrix With Both Large and Small Size
PLIO
AIE
VLIW
Processor
32KB
Mem
NOC
Processor System
(ARM)
DDR4-DIMM
DMA
Buffer
PLAIE
Accelerator 0
DMA
PLAIE
Buffer
Accelerator 1
Partition & Compose Programming Model

## Slide 17
Secret Sauce => Partition & Compose
Image Classification: Vision Transformer
768 Layers
Monolithic Programming Model: 49.5 GFLOPS
Partition & Compose : 1609 GFLOPS
32.5x
B0L0
B0L1
B0L2
B0L3
Scheduling
ACC0
ACC1
ACC2
ACC3
Batch 0
B0L0
B0L1
B0L2
B0L3
B1L0
B2L0
B3L0
B1L1
B2L1
B3L1
B1L2
B2L2
B3L2
B1L3
B2L3
B3L3
-3
ACC0
L0
L1
L2
L3

## Slide 18
Applications
Experiment Results
Bert-Large (Natural Language Processing)
Vision Transformer (Classification)
Multilayer Perceptrons (Regression, Classification)
Neural Collaborative Filtering (Recommendation)

## Slide 19
Applications Characteristics
Experiment Results
MLP
NCF
BERT
96 Layers
ViT
768 Layers
Large layers Dominate the Application
Obvious Shape Variance
Even Larger Shape Variance

## Slide 20
Chart: 
| Bert | ViT | NCF | MLP
One Monolithic | 276.8 | 49.5 | 1736 | 2936.7
One Specialized | 515.4 | 217.1 | 1736 | 2936.7
Two diverse | 1464.2 | 1609 | 1730.9 | 2386.1
8 duplicate | 534.2 | 382.2 | 671 | 696
Best_Config | 1464.2 | 1609 | 1736 | 2936.7
Experiment Results
Throughput Comparison Among Different CHARM Strategies
Composing Diverse Accelerators
BERT ViT NCF MLP
Throughput (GFLOPS)
BERT: 1.46 TFLOPS, 5.3x gain over one monolithic design
ViT: 1.61 TFLOPS, 32.5x gain over one monolithic design
NCF: 1.74 TFLOPS for one accelerator design
MLP: 2.94 TFLOPS for one accelerator design
5.3x
32.5x

## Slide 21
Nvidia A10
CTC Ratio
Throughput (TOPS)
Chart: 
| 0 | 52 | 120
y | 0 | 31.2 | 31.2
app1 | 0 | 37.44
app2 | 0 | 37.44
Apply this to Other Platforms, GPUs?
Provided spatial flexibility, combine communication-bound MM with computation-bound MM
Vertical and horizontal kernel fusion in GPU.
1.37x Gain

## Slide 22
Apply this to Other Platforms, GPUs?
Shall we introduce FPGA or reconfigurable architecture in broader GPU architecture to improve latency?
If FPGA is too fine-grained, what is the least reconfigurability needed in future architecture to balance performance and adaptability?  <=> Microarchitecture support to enable flexible mapping & execution model
Can we design “GPU” better than current GPU?

## Slide 23
Collaboration with Domain Experts: ART: Accelerator Customization in Real-Time System for Autonomous Driving
Collaboration with the CAR Lab (University of Delaware NSF IUCRC Center), Wayne State University
Before ART, accelerators can not guarantee to meet the task deadline, causing severe safety concerns.
After ART, meeting the task deadline is guaranteed, & performance is optimized
Notes: adaptive compute acceleration platforms (ACAPs)
Efficient Number Theoretic Transform
NSF #2213701: Collaborative Research: CCRI: New: A Scalable Hardware and Software Environment Enabling Secure Multi-party Learning NSF #2217003: Collaborative Research: PPoSS: LARGE: Co-designing Hardware, Software, and Algorithms to Enable Extreme-Scale Machine Learning Systems

## Slide 24
Collaboration with Domain Experts: Real-Time Flaw Detection in Additive Manufacturing (3D printing)
US Navy Naval Engineering Education Consortium (NEEC) Fund: “Enabling Real-Time Flaw Detection in Laser Powder Bed Fusion Using In-Situ Infrared Monitoring by Integrating Image Processing, Machine Learning, and Hardware/Software Co-Design”, Collaboration with Prof. Albert To (PITT)
Notes: There is no denying that camera-based facial recognition technology enhances public places’ security and reduces the cost of manual surveillance, but the widespread use of facial recognition technology has raised privacy concerns around the world
Changes in the physical or chemical parameters around the fiber can modify the properties of the guided light, such as its intensity, phase, or wavelength. By detecting and analyzing the changes in these light properties, the information about the environment around the optical fiber can be measured. DAS is a type of fiber-optic sensor that achieves distributed vibration measurement by interrogating a special sensing fiber with pulsed light.
After the preliminary test, the sensing area in this work is configured to 3 meters, and the reflectivity of the sensing fiber is represented in Figure 5. This fiber contains six Rayleigh enhancement points, collectively constituting five individual fiber-optic sensors, and each sensor has its sensing area. This distributed arrangement enables precise and comprehensive monitoring of ground vibrations, facilitating the system’s capability to recognize and analyze various environmental disturbances.

## Slide 25
Collaboration with Domain Experts: FiberFlex: FPGA-based Intelligent & Distributed Fiber Sensor System for Pedestrian Recognition
ACM TRETS’ 2024: FiberFlex: Real-time FPGA-based Intelligent & Distributed Fiber Sensor System for Pedestrian Recognition Collaboration with Dr. Nageswara Lalam (DOE National Energy Technology Laboratory), Prof. Kevin Chen (PITT)
Open-source framework on GitHub
Python APIs, ready to use
9x perf gain, 91x energy effi. gain over CPU+GPU
Reduced impact on personal privacy, No limitations on line-of-sight detection, Lower cost in mass surveillance situations
Notes: There is no denying that camera-based facial recognition technology enhances public places’ security and reduces the cost of manual surveillance, but the widespread use of facial recognition technology has raised privacy concerns around the world
Changes in the physical or chemical parameters around the fiber can modify the properties of the guided light, such as its intensity, phase, or wavelength. By detecting and analyzing the changes in these light properties, the information about the environment around the optical fiber can be measured. DAS is a type of fiber-optic sensor that achieves distributed vibration measurement by interrogating a special sensing fiber with pulsed light.
After the preliminary test, the sensing area in this work is configured to 3 meters, and the reflectivity of the sensing fiber is represented in Figure 5. This fiber contains six Rayleigh enhancement points, collectively constituting five individual fiber-optic sensors, and each sensor has its sensing area. This distributed arrangement enables precise and comprehensive monitoring of ground vibrations, facilitating the system’s capability to recognize and analyze various environmental disturbances.

## Slide 26: Technology Core Areas (Peipei, Ben, Haneesh, Kimani)
AI-powered interactive Avatar AI-enabled embedded computing platforms (Zhou lab) (courtesy: A. Blumenthal)
Kinematic sensors (Kesari lab)
Optical wearable sensor (Toussaint lab)
Sandbox features will include:
Wearable sensors, AI-powered technologies
Approved multiyear “general” IRB to provide constant participant feedback
Input from partner communities, e.g., medicine, public health, computer science, and data science
Computer vision (Kimia lab)

## Slide 27: Health Innovation Sandbox Lab Space
105
EHR

## Slide 28
NSF Projects: POSE: Phase I: Enabling Open-source Ecosystem for Rapid System-on-Chip Design and Programming
Notes: adaptive compute acceleration platforms (ACAPs)
Efficient Number Theoretic Transform

## Slide 29
NSF Project: MRI Consortium: Track 1: Development of SPECTRUM: An Evolutionary Rapid-Prototyping Testbed for Low Latency Multi-Domain Computing
Notes: adaptive compute acceleration platforms (ACAPs)
Efficient Number Theoretic Transform

## Slide 30: Thank you & Questions?

## Slide 31
Impacts
NSF #2213701: Collaborative Research: CCRI: New: A Scalable Hardware and Software Environment Enabling Secure Multi-party Learning NSF #2217003: Collaborative Research: PPoSS: LARGE: Co-designing Hardware, Software, and Algorithms to Enable Extreme-Scale Machine Learning Systems
Impacts (Application): Smart Health, Smart Transportation, AIoT & IoS,
Impacts (Architecture): Heterogeneous Domain Specific Architecture
Impacts (Programming): GitHub Open-source, No.1 Downloaded (>4100) Paper in FPGA’23
Collaboration with the CAR Lab, University of Delaware, Wayne State University
ART: Accelerator Customization for Safety-Critical Autonomous System
Notes: adaptive compute acceleration platforms (ACAPs)
Efficient Number Theoretic Transform

## Slide 32
C/C++
Polygeist
Affine
Vector
MemRef
Loop IR Level
HeteroCompose IR
Loop.opt
Hetero.opt
GPUs
FPGAs
Graph.opt
Different HW backend
MLIR IR
Passes
Tensorflow
Pytorch
Stencil + GEMM IR
e.g.
Exploit general optimizations across-kernel
Ongoing Research: MLIR-based HeteroCompose Compilation Framework
ACAPs
CPUs
CGRAs
PIMs
HW-related IR
New

## Slide 33
Supercomputing 25 Just Accepted Paper: GPU+SSD -> What are Next Steps?
https://arxiv.org/pdf/2504.19365

## Slide 34
Customized Computing on FPGAs Deployed in Cloud Scale
Microsoft programmable hardware/software "fabric" on more than 5,760 Microsoft datacenter servers running Intel Xeon processors and Altera FPGA chips.
Apps: Bing Search, Azure Machine Learning, SmartNIC
ISCA’14, IEEE Micro’15, MICRO’16, NSDI’18, NeurIPS’20

## Slide 35
Customized Computing on FPGAs
Can Every Programmer Easily Design DSAs?
Yes! We can create circuits from C/C++ with high-level synthesis (HLS)
Example Code:
Use of FPGAs trade-off performance for design cost, flexibility, and time-to-silicon

## Slide 36
Advanced Computing - Software and Hardware - from Edge to Datacenter
AMD Versal ACAP
VCK5000
Nvidia GPU RTX 5000 Ada
Dell R750 with 512GB memory
QSFP
QSFP
Network Switch

## Slide 38
0
10
20
30
40
50
60
70
80
Chart: 
| Category 1
Series 2 | 77
Series 3 | 25.6
FPGAs
16nm
7nm
Bandwidth (GB/s)
U250
VCK190
DDR Bandwidth
76.8
25.6
Chart: 
| FP32
U250 (300MHz) | 1.5
VCK190 (1GHz) | 6.4
FPGAs
0
1
2
3
4
5
6
7
16nm
7nm
FP32 Performance
U250 (PL:300MHz)
VCK190 (AIE:1GHz)
Throughput (TFLOPS)
Challenge 1
6.4
1.47
4.3x
The computation scaling vs. off-chip communication scaling
3.0x
1.0x

## Slide 39
High level complexity
Increasing Programming Efforts
900 LOC
AIE C/C++
1000 LOC
HLS C/C++
Host C/C++
300 LOC
Challenge 3
DDR4-DIMM
AIE Array
IO
AIE
25.6 GB/s
Programmable Logic
BRAM
URAM
CLB
DSP
NOC
Processor System
(ARM)

## Slide 40
Challenges
CHARM: Composing Heterogeneous Accelerators for Matrix Multiply on Versal ACAP Architecture
Solutions
Off-chip bandwidth doesn’t scaling as fast as computation
Hugely explore the on-chip reuse
High parallelism makes one-size-fit-for-all solution inefficient
Two-step Accelerator Composing Algorithm
Heterogeneity makes it non-trivial to program a system like Versal with good performance
White-box open-sourced Framework
https://github.com/arc-research-lab/CHARM

## Slide 41
CHARM Input and Output
Input 1) MM-based AI Model ; 2) Profiling of Off-chip Bandwidth ; 3) Hardware resource constrains ;
CHARM Compilation Flow
Output 1) Bitstream Running on the AIE and PL (AIE/V++ Compiler) 2) Executable Running on ARM CPU (GCC Cross Compilation)
XCLBIN
EXE
AI Models
DDR-Profiler
Hardware Constraints
RAM
PLIO
AIE

## Slide 42
XCLBIN
EXE
CHARM Framework Overview
①
②
③
④
① Single Accelerator Design Space Exploration ② Diverse Accelerator Composer
③ Runtime Configuration
④ Automatic Code Generator
CHARM Components
AI Models
DDR-Profiler
Hardware Constraints
RAM
PLIO
AIE

## Slide 43
CHARM Framework Overview
① Single Accelerator Mathematical-Modeling Based Design Space Exploration 1) Fully-pipelined AIE Processor Design 2) Hugely IO Reused AIE Array Design
3) On-chip Buffer Reused PL Design
CHARM Components
XCLBIN
EXE
①
AI Models
DDR-Profiler
Hardware Constraints
RAM
PLIO
AIE

## Slide 44
Acc0
L1
L2
CHARM Framework Components
Single Accelerator Analytical Model
EST: 2.8 TFLOPs
URAM: 384, 83%
BRAM: 764, 80%
AIE: 384, 96%
PLIO Strategy:
A=6, B=4, C=16
Throughput
Hardware Configuration
EST: 1.2 TFLOPs
URAM: 192, 41%
BRAM: 256, 26%
AIE: 192, 48%
PLIO Strategy:
A=6, B=4, C=8
RAM
PLIO
AIE
Platform
RAM
PLIO
AIE
Acc 0
L0
L1
L2
① Single Accelerator Design Space Exploration

## Slide 45
CHARM: Diverse Accelerator Composing
Two-step Search Algorithm
How to assign M layers in one AI Model to N accelerators?
①
②
L0
L1
L4
L2
L3
2 ACCs
ACC0
ACC1
URAM
AIE
PLIO
BRAM
LUT
5 layers
1st Step: Workload Assignment
2nd Step: Hardware Resource Partitioning

## Slide 46
CHARM: Diverse Accelerator Composing
Two-step Search Algorithm
L4
L1
L0
L2
L3
ACC0
ACC1
URAM
AIE
PLIO
BRAM
LUT
URAM
AIE
PLIO
ACC0
URAM
AIE
PLIO
ACC1
Single Accelerator Analytical Model
EST: 2.5 TFLOPs
URAM: 200
BRAM: 500
AIE: 256, 64%
PLIO Strategy:
A=4, B=4, C=16
EST: 0.4 TFLOPs
URAM: 16
BRAM: 32
AIE: 32, 8%
PLIO Strategy:
A=2, B=4, C=4
L4
L1
L0
L2
L3
URAM
AIE
PLIO
ACC0
URAM
AIE
PLIO
ACC1
Overall
1.8 TFLOPs
How to assign M layers in one AI Model to N accelerators?
①
②
1st Step: Workload Assignment
2nd Step: Hardware Resource Partitioning
5 layers
2 ACCs

## Slide 47
URAM
AIE
PLIO
ACC0
URAM
AIE
PLIO
ACC1
CHARM: Diverse Accelerator Composing
Two-step Search Algorithm
L4
L1
L0
L2
L3
URAM
AIE
PLIO
ACC0
URAM
AIE
PLIO
ACC1
Single Accelerator Analytical Model
EST: 2.9 TFLOPs
URAM: 256
BRAM: 384
AIE: 288, 72%
PLIO Strategy:
A=4, B=4, C=18
EST: 0.8 TFLOPs
URAM: 64
BRAM: 64
AIE: 64, 16%
PLIO Strategy:
A=4, B=4, C=4
Record Optimized Solution
Overall
2.0 TFLOPs
How to assign M layers in one AI Model to N accelerators?
①
②
1st Step: Workload Assignment
2nd Step: Hardware Resource Partitioning
5 layers
2 ACCs

## Slide 48
“X FPGA” => Versal ACAP Architecture
AMD ACAP
Heterogeneous SoC
FPGA + AI Tensor Cores + CPU
Composing Diverse Accs for Matrix Multiply -> Throughput Optimal [FPGA’23 CHARM]
Composing Diverse Accs for End-to-end Applications, Latency-Throughput Pareto [FPGA’24 SSR]
Notes: Versal ACAP Architecture Overview

## Slide 49: End-to-end Deep Learning, e.g., Transformer
Transpose
Element-wise & Non-linear Kernels (CTC <=1)
Non-MM kernels <1% total FLOPS, ~ 50% execution time in GPU

## Slide 50
Matrix-Multiply (MM)
Batch MM
Computation-Intensive Kernels
End-to-end Deep Learning, e.g., Transformer

## Slide 51: Latency & Throughput Driven Scenarios
Latency-Driven
Throughput-Driven
…
Google
Autonomous Driving
Video Conferencing
Data Center Services

## Slide 52: Motivation: Sequential or Spatial Arch?
Sequential-only Accelerator  Hardware Under-utilization
0
1
2
3
Directed acyclic graph (DAG)
ACC0
Timeline
Scheduling
Corresponding Workloads
8 : 4 : 4 : 16
Vector Processors
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Mismatch between shape of the layers & size of the accelerator

## Slide 53: Motivation: Sequential or Spatial Arch?
Vector Processors
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Sequential-only Accelerator  Hardware Under-utilization
0
1
2
3
Directed acyclic graph (DAG)
Corresponding Workloads
8 : 4 : 4 : 16
L0
ACC0
Timeline
Scheduling Layer 0
Mismatch between shape of the layers & size of the accelerator
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Padding  Invalid Computation

## Slide 54: Motivation: Sequential or Spatial Arch?
Tiled Architecture
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Sequential-only Accelerator  Hardware Under-utilization
0
1
2
3
Directed acyclic graph (DAG)
Corresponding Workloads
8 : 4 : 4 : 16
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
ACC0
Timeline
Scheduling Layer 1-2
L0
L1
L2
Mismatch between shape of the layers & size of the accelerator

## Slide 55: Motivation: Sequential or Spatial Arch?
Sequential-only Accelerator  Hardware Under-utilization
0
1
2
3
Directed acyclic graph (DAG)
Corresponding Workloads
8 : 4 : 4 : 16
Vector Processors
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
ACC0
Timeline
Scheduling Layer 3
L0
L1
L2
L3
Mismatch between shape of the layers & size of the accelerator

## Slide 56: Motivation: Sequential or Spatial Arch?
0
1
2
3
B0L0
B0L1
B0L2
B0L3
Timeline
Scheduling
ACC3
ACC2
ACC1
ACC0
0
1
2
3
Spatial-only Accelerator  Longer Latency (Multiple batches)
Directed acyclic graph (DAG)
Corresponding Workloads
8 : 4 : 4 : 16
Vector Processors
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
ACC0
ACC1
ACC2
ACC3
Batch 0
B0L0
B0L1
B0L2
B0L3
B1L0
B2L0
B3L0
B1L1
B2L1
B3L1
B1L2
B2L2
B3L2
B1L3
B2L3
B3L3
-3

## Slide 57: Motivation: Sequential or Spatial Arch?
B0L0
B0L1
B0L2
B0L3
Scheduling
ACC0
ACC1
ACC2
ACC3
Batch 0
B0L0
B0L1
B0L2
B0L3
B1L0
B2L0
B3L0
B1L1
B2L1
B3L1
B1L2
B2L2
B3L2
B1L3
B2L3
B3L3
-3
ACC0
L0
L1
L2
L3

## Slide 58: Solution: Sequential + Spatial Hybrid
0
1
2
3
Timeline
Scheduling
ACC0
ACC1
0
1
2
3
SSR-Hybrid  Pareto front in Latency throughput tradeoff
Directed acyclic graph (DAG)
Corresponding Workloads
8 : 4 : 4 : 16
Vector Processors
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Batch 0-1
ACC0
ACC1
B0L0
B0L1
B1L0
B0L2
B0L3
B1L1
B1L2
B1L3

## Slide 59: SSR-Hybrid Solution
0
1
2
3
Timeline
0
1
2
3
SSR-Hybrid  Pareto front in Latency throughput tradeoff
Directed acyclic graph (DAG)
ACC0
ACC1
0
1
2
3
Sequential
Spatial
Hybrid
B0L0
B0L1
B0L2
B0L3
ACC0
ACC1
ACC2
ACC3
B0L0
B0L1
B0L2
B0L3
B1L0
B2L0
B3L0
B1L1
B2L1
B3L1
B1L2
B2L2
B3L2
B1L3
B2L3
B3L3
ACC0
L0
L1
L2
L3
B0L0
B0L1
B1L0
B0L3
B1L3
B0L2
B1L1
B1L2
High Throughput
High Latency
Latency-Throughput
Tradeoff
Less execution time in each stage
Low latency
Low throughput
Longer time

## Slide 60: SSR Architecture, Designs & Software
Challenges
Solutions
Non-linear & elementwise kernels takes Non-negligible time
Feature: Enable Inter-Acc aware on-chip data forwarding and fine-grained pipeline
The large design space & heterogeneity of ACAP motivates an automation tool
SSR two-phase DSE tool & automatic workflow for implementation on ACAP https://github.com/arc-research-lab/SSR
Spatial-Only  High Latency
Sequential-Only  Low Throughput
Feature: Multi Spatial Accelerators; Apply hybrid architecture to explore latency throughput tradeoff

## Slide 61: SSR Design Methodology
SSR Architecture
Network-on-Chip
DDR4-DIMM
AIE Core
PLIO OUT
FIFO
Stream
DDR
Access
PLIO IN
Cascade
PL Region
A Spatial Accelerator
PLIO Interface
HMM Unit
SSR-HCE
PLIO Interface
HMM Unit
SSR-HCE
PLIO Interface
HMM Unit
SSR-HCE
AIE0
AIE1
AIE2
AIE3
AIE4
AIE5
AIE6
AIE7
PLIO Interface
…
3D-Parallelism on two hierarchy: 3D-AIE Array (A, B, C), 3D-SIMD Instruction (PI, PK, PJ)
AIE Region
Layernorm
Softmax
Transpose
Control Logic
Layernorm
Softmax
Transpose
Control Logic
AIE0
AIE1
AIE2
AIE3
AIE4
AIE5
AIE6
AIE7
PLIO Interface
Local
RAM

## Slide 62: SSR Design Methodology
SSR Programming Model & Dataflow
Network-on-Chip
DDR4-DIMM
AIE Cores
PLIO OUT
FIFO
Stream
DDR
Access
PLIO IN
AIE Region
PL Region
PLIO Interface
MM 1
Non-MM 1
PLIO Interface
MM 0
Non-MM 0
A Spatial Accelerator
PLIO Interface
MM 2
Non-MM N
0
1
2
0
1
2
0
1
2
Chained Graph
Batch 0
Batch 1
Batch 2
0
0
1
2
0
R

## Slide 63: SSR Design Methodology
Fine-grained pipeline for element-wise and non-linear kernels
Non-linear Kernels
Line-buffers
+
/
x
Σ(x)
u
x
x
u
+β
AIE0
x
HMM
u
Avg
Var
LN
Dependency
HMM
Avg
Var
LN
x
SRAM
(Store for later use)
u
(Load SRAM)
Final
Sequence Length
Embed Dim
……
X0, X1, …Xn
X0, X1, …Xn
Element-wise Kernels
HMM
Transpose
Dequan
…
…
Efficiently and conveniently done by PL than using VLIW instructions

## Slide 64: Experiment Results
Latency & Throughput Tradeoff Analysis of DeiT-T across Different Strategies
Throughput (TOPS)
Latency (ms)
Chart: 
| 0.22 | 0.44 | 0.66 | 0.87 | 1.0900000000000001 | 1.3
 | 10.9 | 11.05 | 11.09 | 11.12 | 11.1 | 11.17
 | 5.66 | 10.42 | 14.92 | 19.37 | 22.99 | 26.7
SSR-Hybrid (Including Spatial & Sequential)
BS = 6 0.54ms, 26.7 TOPS
BS = 6
1.3ms, 11.2TOPS
Spatial-only
Sequential-Only
BS = 1
0.22ms, 10.9TOPS
BS = 1 0.43ms, 5.66TOPS

## Slide 65: Experiment Results
Latency & Throughput Tradeoff Analysis of DeiT-T across Different Strategies
Throughput (TOPS)
Latency (ms)
Chart: 
| 0.22 | 0.44 | 0.66 | 0.87 | 1.0900000000000001 | 1.3
 | 10.9 | 11.05 | 11.09 | 11.12 | 11.1 | 11.17
 | 5.66 | 10.42 | 14.92 | 19.37 | 22.99 | 26.7
SSR-Hybrid (Including Spatial & Sequential)
BS = 6 0.54ms, 26.7 TOPS
BS = 6
1.3ms, 11.2TOPS
Spatial-only
Sequential-Only
BS = 1
0.22ms, 10.9TOPS

## Slide 66: Experiment Results
Latency & Throughput Tradeoff Analysis of DeiT-T across Different Strategies
Throughput (TOPS)
Latency (ms)
Chart: 
| 0.22 | 0.44 | 0.66 | 0.87 | 1.0900000000000001 | 1.3
 | 10.9 | 11.05 | 11.09 | 11.12 | 11.1 | 11.17
 | 5.66 | 10.42 | 14.92 | 19.37 | 22.99 | 26.7
 | 18.56
SSR-Hybrid (Including Spatial & Sequential)
BS = 6 0.54ms, 26.7 TOPS
BS = 6
1.3ms, 11.2TOPS
Spatial-only
Sequential-Only
BS = 3 0.39ms, 18.6TOPS
BS = 1
0.22ms, 10.9TOPS

## Slide 67: Experiment Results
SSR (ours) vs TensorRT on GPU A10G
Throughput (TOPS)
Latency (ms)
Chart: 
| 0.22 | 0.44 | 0.66 | 0.87 | 1.0900000000000001 | 1.3
 | 10.9 | 11.05 | 11.09 | 11.12 | 11.1 | 11.17
 | 5.66 | 10.42 | 14.92 | 19.37 | 22.99 | 26.7
 | 18.56
 | 3.0885 | 5.2848 | 6.8601 | 8.3445 | 9.077 | 10.1199 | 10.8099 | 11.2576 | 11.3246
SSR-Hybrid (Including Spatial & Sequential)
GPU-TensorRT
BS = 6
BS = 6
BS = 1
BS = 1
BS = 9
Spatial-only
Sequential-Only
BS = 6

## Slide 68: Experiment Results Further Analysis
SSR (ours) vs TensorRT on GPU A10G
Multiple Spatial Accs -> Improve tensor core utilization
On-chip Forwarding & Fine Grained Pipeline ->
Overlap execution of MM & non-MM kernels