## Slide 1
The hpDIRC Simulation Status
Greg Kalicy
July 15th, 2025
ePIC Collaboration Meeting

## Slide 2
Stand-alone Geant4 Simulation
  Realistic optics, geometry, and material properties – based on prototypes and experimental data, wavelength-dependent material properties and processes
  Validated with test beam data
  Used for design optimization studies and to test novel design options
Full ePIC Simulation:
  Functionality of Stand-alone simulation imported and integrated
  Repeat physics background and detector impact study in the full software stack
Reconstruction and PID methods:
  Geometrical (BABAR-like), robust and fast method based on Look-Up Tables, delivers Cherenkov angle per particle and Single Photon Resolution (useful for calibration and in prototype tests), does not depend on precise time measurement
  Time Imaging (Belle II TOP-like), uses Probability Density Functions (analytical or simulation-based), makes optimum use of precision of position and time information
  Machine Learning based – in preparation, using Foundation Model
Pythia events in hpDIRC simulation
hpDIRC Simulation

## Slide 3
Recent hpDIRC related studies:
  Confirmed robust performance in magnetic field, using physics events (Pythia) to include backgrounds, multiple tracks per bar (WSU)
  Adopting hpDIRC reconstruction methods into full ePIC Simulation Stack (WSU)
  Performance with latest ePIC angular track resolution maps (GSI) → High-precision angular resolution crucial for reaching required hpDIRC performance.
  Verifying optimal sensor coverage (CUA, GSI)
  Study of the impact of bar imperfections on the hpDIRC performance relevant for the BaBar bar refurbishment (GSI)
  Impact of bar/lens misalignments on performance (Jazan)
  Machine Learning approach to reconstruction and generating PDFs (W&M)
  Preparation for hpDIRC full chain test setup operation at CRT (SBU, GSI, ODU)
hpDIRC Simulation
time imaging reconstruction
0.5 mrad tracking, 100 ps photon timing
π/K separation power at 6 GeV/c
Geant4
→ Performance requirements reached: ≥ 3 s.d. π/K separation at 6 GeV/c for all angles
Simulation studies performed with
Stand-alone Geant4 simulation
Single particles from particle gun
1.7T magnetic field, no other ePIC subsystems
0.5 mrad tracking resolution
100ps time resolution
Roman Dzhygadlo (GSI)
Bill Llope (WSU)

## Slide 4
Recent hpDIRC related studies:
  Confirmed robust performance in magnetic field, using physics events (Pythia) to include backgrounds, multiple tracks per bar (WSU)
  Adopting hpDIRC reconstruction methods into full ePIC Simulation Stack (WSU)
  Performance with latest ePIC angular track resolution maps (GSI) → High-precision angular resolution crucial for reaching required hpDIRC performance.
  Verifying optimal sensor coverage (CUA, GSI)
  Study of the impact of bar imperfections on the hpDIRC performance relevant for the BaBar bar refurbishment (GSI)
  Impact of bar/lens misalignments on performance (Jazan)
  Machine Learning approach to reconstruction and generating PDFs (W&M)
  Preparation for hpDIRC full chain test setup operation at CRT (SBU, GSI, ODU)
hpDIRC Simulation
Bill Llope (WSU)
hpDIRC in stand-alone and ePIC simulation

## Slide 5
Recent hpDIRC related studies:
  Confirmed robust performance in magnetic field, using physics events (Pythia) to include backgrounds, multiple tracks per bar (WSU)
  Adopting hpDIRC reconstruction methods into full ePIC Simulation Stack (WSU)
  Performance with latest ePIC angular track resolution maps (GSI) → High-precision angular resolution crucial for reaching required hpDIRC performance.
  Verifying optimal sensor coverage (CUA, GSI)
  Study of the impact of bar imperfections on the hpDIRC performance relevant for the BaBar bar refurbishment (GSI)
  Impact of bar/lens misalignments on performance (Jazan)
  Machine Learning approach to reconstruction and generating PDFs (W&M)
  Preparation for hpDIRC full chain test setup operation at CRT (SBU, GSI, ODU)
hpDIRC Simulation
π/K separation power at 6 GeV/c
Roman Dzhygadlo (GSI)
Matt Posik (TU)
Geant4
time-based imaging reconstruction

## Slide 6
Recent hpDIRC related studies:
  Confirmed robust performance in magnetic field, using physics events (Pythia) to include backgrounds, multiple tracks per bar (WSU)
  Adopting hpDIRC reconstruction methods into full ePIC Simulation Stack (WSU)
  Performance with latest ePIC angular track resolution maps (GSI) → High-precision angular resolution crucial for reaching required hpDIRC performance.
  Verifying optimal sensor coverage (CUA, GSI)
  Study of the impact of bar imperfections on the hpDIRC performance relevant for the BaBar bar refurbishment (GSI)
  Impact of bar/lens misalignments on performance (Jazan)
  Machine Learning approach to reconstruction and generating PDFs (W&M)
  Preparation for hpDIRC full chain test setup operation at CRT (SBU, GSI, ODU)
hpDIRC Simulation
Roman Dzhygadlo (GSI)
Imran Hossain (CUA)
Kris Cleveland (JLab)
Backplane of hpDIRC readout box
Two arrangements of 5x4 array of sensors

## Slide 7
Recent hpDIRC related studies:
  Confirmed robust performance in magnetic field, using physics events (Pythia) to include backgrounds, multiple tracks per bar (WSU)
  Adopting hpDIRC reconstruction methods into full ePIC Simulation Stack (WSU)
  Performance with latest ePIC angular track resolution maps (GSI) → High-precision angular resolution crucial for reaching required hpDIRC performance.
  Verifying optimal sensor coverage (CUA, GSI)
  Study of the impact of bar imperfections on the hpDIRC performance relevant for the BaBar bar refurbishment (GSI)
  Impact of bar/lens misalignments on performance (Jazan)
  Machine Learning approach to reconstruction and generating PDFs (W&M)
  Preparation for hpDIRC full chain test setup operation at CRT (SBU, GSI, ODU)
hpDIRC Simulation
Roman Dzhygadlo (GSI)

## Slide 8
Recent hpDIRC related studies:
  Confirmed robust performance in magnetic field, using physics events (Pythia) to include backgrounds, multiple tracks per bar (WSU)
  Adopting hpDIRC reconstruction methods into full ePIC Simulation Stack (WSU)
  Performance with latest ePIC angular track resolution maps (GSI) → High-precision angular resolution crucial for reaching required hpDIRC performance.
  Verifying optimal sensor coverage (CUA, GSI)
  Study of the impact of bar imperfections on the hpDIRC performance relevant for the BaBar bar refurbishment (GSI)
  Impact of bar/lens misalignments on performance (Jazan)
  Machine Learning approach to reconstruction and generating PDFs (W&M)
  Preparation for hpDIRC full chain test setup operation at CRT (SBU, GSI, ODU)
hpDIRC Simulation
Afaf Wasili (Jazan)
Horizontal bar misalignment
Bar rotation

## Slide 9
Recent hpDIRC related studies:
  Confirmed robust performance in magnetic field, using physics events (Pythia) to include backgrounds, multiple tracks per bar (WSU)
  Adopting hpDIRC reconstruction methods into full ePIC Simulation Stack (WSU)
  Performance with latest ePIC angular track resolution maps (GSI) → High-precision angular resolution crucial for reaching required hpDIRC performance.
  Verifying optimal sensor coverage (CUA, GSI)
  Study of the impact of bar imperfections on the hpDIRC performance relevant for the BaBar bar refurbishment (GSI)
  Impact of bar/lens misalignments on performance (Jazan)
  Machine Learning approach to reconstruction and generating PDFs (W&M)
  Preparation for hpDIRC full chain test setup operation at CRT (SBU, GSI, ODU)
hpDIRC Simulation
James Giroux (W&M)
Cristiano Fanelli (W&M)

## Slide 10
Recent hpDIRC related studies:
  Confirmed robust performance in magnetic field, using physics events (Pythia) to include backgrounds, multiple tracks per bar (WSU)
  Adopting hpDIRC reconstruction methods into full ePIC Simulation Stack (WSU)
  Performance with latest ePIC angular track resolution maps (GSI) → High-precision angular resolution crucial for reaching required hpDIRC performance.
  Verifying optimal sensor coverage (CUA, GSI)
  Study of the impact of bar imperfections on the hpDIRC performance relevant for the BaBar bar refurbishment (GSI)
  Impact of bar/lens misalignments on performance (Jazan)
  Machine Learning approach to reconstruction and generating PDFs (W&M)
  Preparation for hpDIRC full chain test setup operation at CRT (SBU, GSI, ODU)
hpDIRC Simulation
Nathan Shankman (SBU)
Jaydeep Datta (SBU)
Carlos Ayerbe Gayoso (ODU)

## Slide 11
Stand-alone hpDIRC simulation, validated in particle beams in 2018, still essential for many studies
Important progres in understanding realistic tracking resolution and its impact on hpDIRC performnce
Effort on finishing integrstion of hpDIRC into the ePIC simulation software restarted
Summary

## Slide 12
Expected hpDIRC Performance vs. Tracking
π/K separation power at 6 GeV/c
Geant4
time-based imaging reconstruction
→ High-precision angular resolution crucial for
reaching required hpDIRC performance.
Simulation studies performed with
Stand-alone Geant4 simulation
Single particles from particle gun
6 GeV/c momentum
1.7T magnetic field, no other ePIC subsystems
100ps time resolution
Impact of tracking angular resolution on hpDIRC performance
π/K Cherenkov angle difference at 6 GeV/c: ΔΘc≈3 mrad
Yellow Report tracking requirement: 0.5 mrad resolution at 6 GeV/c

## Slide 13
Photosensors
hpDIRC sensor requirements
Single photon sensitivity in ePIC magnetic field: 106 gain at ~ 1T
Fast timing for single photons: timing precision (rms) < 100 ps
Large active area ratio for tiled sensors: goal > 75%
High PDE in visible range: goal > 25% at 400 nm
Small pixels: anode pixel size < 3.5 mm
Tolerance for high photon rates: goal > 0.5 MHz/cm2
Tolerance for high occupancies: up to 200+ photoelectrons per particle, need DC-coupled anodes
Long lifetime: goal > 10 C/cm2
Photek MAPMT 253
6 μm pores 8x8 anodes (PANDA)
S. Krauss, RICH2022
PHOTONIS XP85012-S
10 μm pores 8x8 anodes (PANDA)
Expected number of photoelectrons per particle per 12 cm x 12 cm sensor
Geant4 single particles