## Slide 1: Electronics & DAQ WG
Fernando Barbosa (JLab)
24 July 2025

## Slide 2
  News
    Collaboration meeting 14 – 18 July 2025
  CALOROC 64 ch or 32 ch
    Technical aspects - Norbert
    Cost impact estimate – Fernando
    Concurrence from collaboration TBD
  AOB
Welcome & News

## Slide 3
Cost impact estimate from CALOROC 64 ch (nominal) to 32 ch
Si area usage:
Frontend (1) ~70% area
Backend (2,3,4) area will remain ~ the same regardless of the 64 or 32 [72 or 36 ch] implementation
  Area (64) ~ 1.7 x Area (32)
Current design submission has 36 ch

## Slide 4
Cost impact estimate from CALOROC 64 ch (nominal) to 32 ch (cont)

## Slide 5
Cost impact estimate from CALOROC 64 ch (nominal) to 32 ch (cont)
Ch/CALOROC | #ASICs/Wafer | #Wafers | Total #Ch | #Packages
64 | 480 | 5 | 153,600 | 2,400
32 | 816 | 6 | 156,672 | 4,896
  Cost Delta = 1 x $4k (additional Wafer) + 2,496 x $7.5 (additional 2,496 packages) = $22,720
    Cost of 32 ch version is higher by ~$25k
  There are additional costs for the additional packaged devices:
    Testing
    PCB assembly
  Total additional costs are not excessive:
    The current submission has 32 ch – 64 ch requires an additional design and submission cycle.
    Decision should primarily be determined on technical merits.
  Quantities needed: 97k channels
  Area (64) ~ 1.7 x Area (32)