## Slide 1: sLDO Serial Chain Test
Parameters around testing a serial chain of sLDO’s simulating power control of a group of 4 LAS’s.
Roy Wastie, B. Todd Huffman

## Slide 2: sLDO Serial chain test
4 sLDO’s in a serial chain
  Mimic a LAS group
Each sLDO will be at its own local VSS
  4 Controllers will need their own supplies (GND) tried to the SLDO VSS
    Need VSS relative to local ground.
    4 floating supplies needed
    Every chip has capacitor 100uF from local VSS to ‘current IN’
      Roy discovered in simulations of chain
1.6v across the sLDO
Current Source for the sLDO 10v 2A
  Why a current Source? – stability against voltage fluctuations
Use the sLDO carrier board
sLDO controls required:-
  Test shunting each one or in combinations
  Changing settings on individual sLDO’s in the chain

## Slide 3: sLDO Serial chain test
Start-up tests from MODE 0
Variable loads for each sLDO
  Does partial shunting work as expected in a chain?
  Current fluxuations/spikes as shunting takes effect?
Test chips have No over-voltage protection!
  Don’t let the magic smoke out!
Active load need to buy? https://www.keysight.com/us/en/products/dc-electronic-loads/n3300-series-modular-dc-electronic-loads.html