## Slide 1: SLDO Failure Modes and Operation
WP1 Designer’s Meeting
Roy Wastie, Iain Sedgwick

## Slide 2: Introduction
Failure Modes
  How the SLDO avoids the most likely failures?
Overvoltage Protection
  How the OVP helps avoids the most likely failures?
Start-up
  How to start the 5 SLDOs without explosion using the OVP?
Simulations
  Results from full stave simulations with OVP
Builds on Iain’s existing work on one AncASIC powering
  Iain’s talk June 23rd 2025 WP1 Designer’s Meeting
  https://indico.bnl.gov/event/28508/#43-powering-discussion
Conclusion
  What next?

## Slide 3: SLDO Failure Modes

## Slide 4: Failure modes of SVT SP chain with SLDO
A SLDO behaves as an open circuit
A SLDO develops a short
The load develops a short
Over-voltage Protection is required to service the failure modes.
From Iain Sedgwick

## Slide 5: Failure modes 1
From Iain Sedgwick
Failure 1: SLDO fails in an open circuit fashion
  The input current needs to redistribute between the other SLDO  Pass and shunt transistor of SLDO are sized to take extra current from failing SLDO(s) in parallel
  More current in the remaining SLDOs will raise the voltage across the module; if needed, the overvoltage protecion circuit will clamp this to the max V
   No interruption of current flow to other modules in the chain

## Slide 6: OVP with Global digital SLDO open mode 1
OVP shunt I
V SLDO
SLDO output OFF

## Slide 7: Failure modes 2
From Iain Sedgwick
Failure 2: SLDO develops a short circuit
  For a constant current supply from a current source, the current continues to flow
  If a voltage source is used, then the voltage applied will need to split between n-1 modules, which might trigger the OVP; this should be corrected at the voltage supply
   No interruption of current flow to other modules in the chain

## Slide 8: OVP with Global digital SLDO short mode 2
OVP shunt I
V current source
SLDO output shorted

## Slide 9: Failure modes 3
From Iain Sedgwick
Failure 3: Load overcurrent
  This corresponds to a reduction of the current being shunted
  The undershunt current protection activates putting the SLDO in a high impedance state, situation equivalent to failure 1
   No interruption of current flow to other modules in the chain

## Slide 10: Overcurrent Protection
Over-current protection
  Change from that described in this paper
    Detect under-shunt condition
    Voltage limit by output voltage reduction
    Still some short circuit current
  Use more traditional LDO overcurrent protection
    Detect under-shunt condition
    Short pass transistor
    Effectively make output high impedance, and shunt behaves like an open circuit
    Some transient immunity

## Slide 11: Overcurrent Protection
Over-current protection
  Use more traditional LDO overcurrent protection
    Detect under-shunt condition
    Short pass transistor
    Effectively make output high impedance, and shunt behaves like an open circuit
    Some transient immunity
    Locks into overcurrent state until reset
    TMR protection
    Pull-ups for default operation
Overcurrent Detection
Transient Protection
TMR
Defaults
Voltage buffer
Register
PT Short

## Slide 12: Overcurrent Protection
Filters transients of up to 100us
Over-current protection
  Disable signal is triggered by detection of overcurrent condition
  This is delayed by an RC buffer chain.
  Resulting signal samples the original disable and triggers a shutdown if it is still high.
  In this way small transients are filtered.

## Slide 13: Start-up and Overcurrent Protection
Over-current protection
1. Top left trace, supply ramping up.
2. Outputs come on as the supply ramps, but they start disabled, so once things start to become active, they shut down.
3. Then we turn them on one by one.
4. Bottom red trace is a simulated overcurrent condition on the serialiser supply.
5. Serialiser supply shuts down, then the current disappears because we have shut down the supply voltage.

## Slide 14: Over Voltage Protection

## Slide 15: Motivation for the OVP
Over-voltage Protection is required to service all failure modes.
SLDO Absolute Max input voltage is 1.8V currently (may affect lifetime)
  XFAB PELVT and NELVT FETs also have an absolute max voltage of 1.8V
  SLDO is mostly 2 FETs in series, giving a nominal of 3V MAX Input Voltage
  Start-up Block has the lowest limit of 1.6V
  Hence, OVP will limit at 1.6V
  One OVP per SLDO set.
Vmax
OVP operates if all 4 stave SLDO shorted on a neighbour or Stave going open or SLDOs are OFF

## Slide 16: OVP Design
Over-Voltage protection
  Monitor voltage across SLDO
    Detect over-voltage condition
    Turn on shunt transistors
    Effectively lower the SLDO impedance
    Clamping the voltage across the SLDO
Set OVP Threshold
1.6v to 2v 0.1 steps
Current Shunt
Input V
Vref
Comparator

## Slide 17: OVP Test Bench
Current
Source PSU
Stave SLDO + OVP
Enable Controls
Loads

## Slide 18: OVP Test Bench
Current
Source PSU
Stave SLDO + OVP
Loads
SLDO V drop set resistors
Enable Controls

## Slide 19: OVP shunt set to 1.6V
Shunt Current
Shunt Voltage
LDO Vout

## Slide 20: OVP disabled
Shunt Current
Shunt Voltage
LDO Vout

## Slide 21: SLDO Start-up

## Slide 22: The Problem
How to start-up the SLDO?
  MOSAIX requires power sequencing:
    GSVDD, GAVDD,GDVDD, TXVDD
  AncASIC needs to be on at start-up to control this
  How to achieve?
  What are the problems?

## Slide 23: Model
10th EIC DAC Meeting, June 11th – 13th 2025
Each SLDO can be represented as a resistance with equivalent resistance as shown.
So the total system is as shown in diagram.
Each SLDO takes a different current and has its R3 configured so that all 5 develop the same voltage across them.
The challenge in start up is that currents and SLDOs cannot be stepped simultaneously, so what happens when they are misaligned?
GDVDD is a particular challenge due to its value and position in the sequence.
R
R
R
R
R
AncBrain
GSVDD
GDVDD
GAVDD
TXVDD
Table 1
Table 2

## Slide 24: SLDO – Features for Startup
MODE 0
MODE 1
Can start in two modes:
  Mode0: Output is off by default, and enabled by command
  Mode1: Output is on by default and disabled by command
Mode is selected by single pin, which can have pull-up or down resistor to enforce default condition
Also Over-Voltage Protection (OVP). More later…

## Slide 25: Simulations

## Slide 26: Simulation configuration
Assumptions I have made:-
  Stave configuration of 4 LASs 4 AncAsics + 1 OVP per LAS
  4 AncAsics are serial powered by a non ideal current source.
  Supply Rail Loads as table 1 on page 23
  AncAsic SLDO needs to be ON as power comes up. SLDO Mode 1.
  The AncAsic controller will sequence the supplies for the LAS:
    GSVDD, GAVDD,GDVDD, TXVDD
    4 SLDOs for these will be in Mode 0.
    350us interval between each SLDO turn ON.
    950us interval between each AncAsic turn ON.
    2ms current ramp to 2.2A
  Nominal parameters no corners yet

## Slide 27: First Simulation Results – Full Current with OVP
Large spike > 580mv
AncBrain1 supply
GS GA GD GTX
GS GA GD GTX
GS GA GD GTX
GS GA GD GTX
LAS0
LAS1
LAS2
LAS3
I Current Source

## Slide 28: Simulation Results..
First Results show large spikes on the AncBrain supply, but particularly when Global Digital is turned ON.
AncBrain1 supply has the biggest spikes when LAS 0 is turned ON.
LAS turn ON sequence 0 to 3 or reverse doesn't effect the spikes.
ANB1 580mV

## Slide 29: Simulation Results..
Not the real picture:-
  VSS is bouncing
  Look at the difference between Supply and VSS
  AB1 has the highest spike
  AB3 has the lowest spike
  Still quite large spikes 338mV
AB1 338mV
AB3 316mV

## Slide 30: Simulation Results.. with capacitors…
Reduce spikes with capacitor across AncAsic Current supply:-
  Tried a range of capacitors 10uF to 660uF used real models from TDK and Murata
AB1 10uF 185mV

## Slide 31: Simulation Results with 100uF Murata
Reduce spikes with capacitor across AncAsic Current supply:-
  100uF 4v Murata is optimal 0805
AB1 100uF 28mV

## Slide 32: Simulation Results with 100uF Murata…
Reduce spikes with capacitor across AncAsic Current supply:-
  100uF 4v Murata is optimal 0805
AB1 100uF 28mV

## Slide 33: 100uF Murata
  To get >= 100uF
  Requires a 220u 4v 1206 to give 144uF

## Slide 34: Simulation Results with OVP
OVPs take excess current during start-up protecting the SLDO from overvoltage.
OVP0
OVP2
OVP1
OVP3
1.97A to 33mA

## Slide 35: Conclusion

## Slide 36: Conclusion
Builds on Iain’s existing work on one AncASIC powering
  Iain’s talk June 23rd 2025 WP1 Designer’s Meeting
  https://indico.bnl.gov/event/28508/#43-powering-discussion
The OVP function enables the SLDO to operate under fault conditions and also allows start-up of the serial chain with full operation current (Max 3A) successfully.
Upgrades to the next version:-
  Improve the pre-reg to be more immune to overvoltage.
  Provide an OVP triggered status to the AncBrain
  Change the Temperature specification of the AnCAsic to 10°C to 60°C