## Slide 1: Electron-Ion Collider Design Readiness
Resource Review Board Meeting November 4, 2025
Sergei Nagaitsev
EIC Technical Director

## Slide 2: Outline
Requirements
Design changes
Present concept
Summary

## Slide 3: EIC Accelerator Performance Drivers
wide center-of-mass energy √s: 20 – 140 GeV :
map the out nucleon and nuclei structure from high to low x
polarized electron and hadron (p, He-3) beams:
access to spin structure of nucleons and nuclei
Spin vehicle to access the spatial and momentum structure of the nucleon in 3d
Full specification of initial and final states to probe q-g structure of NN and NNN interaction in light nuclei
nuclear beams: d to Pb
accessing the highest gluon densities  saturation
quark and gluon interact with a nuclear medium
high luminosity 1033-1034 cm-2s-1 :
mapping the spatial and momentum structure of nucleons and nuclei in 3d
access to rare probes, i.e. Ws
large acceptance (0.2 – 1.3 GeV) through forward focusing IR magnets
spatial imaging of nucleons and nuclei
gluon emission
?
=
gluon recombination

## Slide 4: EIC Accelerator Performance Requirements
EIC peak luminosities (CDR)
5x41
5x100
10x100
10x275
18x275
Bunch charges: 28 nC (10 GeV, e) and 11 nC (275 GeV, p)
Center-of-mass energies: ~20 to ~140 GeV (e-p)
High degree of beam polarization (P): ~70%
Availability of ion beams: from proton to Pb
Luminosity (L): 1033 – 1034 cm-2sec-1
Possibly more than one IR
Figure of merit: to
The EIC design and performance parameters address the requirements established by the U.S. Nuclear Science Advisory Committee (NSAC) Long Range Plans (2015 & 2023)

## Slide 5: EIC Design Changes since the CDR (2021)
Main changes highlighted on right:
1. Optimized location of 41 GeV bypass
2. Optimized location
  of the HSR injection
3. Added low-energy cooler; removed CeC cooler
4. Optimized electron
  injector concept
1
2
3
4
Conceptual Design 2023
Conceptual Design 2025
Implemented design changes effectively addressed identified technical uncertainties and risks without affecting the performance or cost objectives.

## Slide 6: Preparing the Accelerator Design for Performance Baseline in 2026
Date | Milestone/Progress
2019 | DOE EIC Mission Need Statement (MSN)
2021 | EIC Conceptual Design Report
2023 | EIC Global Requirements
2023-2024 | Design changes reviewed by Machine Advisory Committee and documented by TCCB, CCB, RoDs, System Requirements
2025 | Design Converged EIC Global Parameters List (draft) – now under version control
2026 | Draft Preliminary Design Report posted for August 2025 IPR Final version will be released by Summer 2026
The EIC Accelerator design is stable.
We have a well-defined vision of what is required to build the EIC!

## Slide 7: Collider Layout
1
3
5
7
1
3&7
5
IR6 and EPIC

## Slide 8: Subproject Interfaces in Sector 5
RHIC Q10
Short Spin Rotator
ASR
IR
Detector
IR
Subproject interfaces are well-defined.

## Slide 9: Subproject Interfaces in Sector 7
RHIC Q10
(fixed)
Short Spin rotator
IR
IR
ASR
Detector
DR8
Rear SC magnets
Subproject interfaces are well-defined.

## Slide 10: Key EIC Accelerator Concepts Proposed in the CDR
The following core design principles enable the EIC to achieve luminosity of ~1034 cm-2s-1 and to maintain high polarization at collisions over a broad range of CoM energies.
Ribbon-like (flat) hadron beam (11:1 transverse emittance & beam size ratio)
Large beam crossing angle (25 mrad)
Collisions at beam-beam tuneshift limits for both beams (0.1 e/ 0.01 p)
Spin preservation from source to collisions (protons and electrons)
Very high bunch intensities and circulating beam currents (1 A (p), 2.5 A (e))
Recent design updates have not altered these foundational concepts.
Note: HERA(1992-2007) peak luminosity: ~5x1031 cm-2s-1

## Slide 11: Luminosity Performance Meets the Established Requirements
“Flat” proton bunches allow for high initial luminosity.
CoM Energy (GeV) | Average Lumi (x1033 cm-2s-1) (per 4-hour store)
105 | 3
63 | 1.2
45 | 1
140 | 0.44
29 | 0.13
EIC peak luminosities (CDR)
5x41
5x100
10x100
10x275
18x275

## Slide 12: Polarization Performance Meets the Established Requirements
Frequent swap-out injection of bunches with high initial polarization of 85%
  Bunch spacing is ~10 ns
Initial polarization decays towards P∞
At 18 GeV, every bunch is replaced (on average) after 2.2 min with RCS cycling rate of 1Hz
B P
Refilled every 1.2 minutes
B P
Refilled every 3.2 minutes
Pav=80%
Pav=80%
Re-injections
P∞= 30%
(conservative)
Re-injection
HSR proton polarization
performance also meets
the requirements.
Present RHIC proton
polarization is 60%

## Slide 13: From RHIC to EIC
Protons: ~40 – 275 GeV
Electrons: 5 – 18 GeV
RHIC
RHIC
EIC
Ion species:
proton – Uranium
60% p polarization

## Slide 14: From RHIC (Yellow Ring) to EIC HSR
EIC HSR to be composed of existing arcs of the Yellow RHIC ring (remove unused magnets)
Insert sleeves coated with copper and amorphous carbon into superconducting magnet beam pipes to improve conductivity and reduce secondary electron yield (-> electron cloud)
Add new RF cavities
Add hadron cooling to create flat beam
Add crab cavities, new IR SC magnets
Add a collimation system
Add extra ‘snakes’ for spin control
Tripled beam current, shorter bunch length, shorter bunch distance, ‘flat’ beams with small vertical emittance
Superconducting Radio Frequency Cavity

## Slide 15: RHIC Magnets Conversion to EIC
Existing RHIC cold bore beam pipes are stainless steel
  High surface resistance -> Excessive resistive wall heating
  High secondary electron yield (SEY) -> Electron cloud formation
New parameters required for EIC
  High stored beam current (.72 A vs .27 A)
  Reduced bunch length (60 cm vs 600 cm)
  Short bunch spacing (10 ns vs 108 ns)
  High bunch charge (1.2x1011 ppb)
Actively Cooled Beam
Screen
CD3A procurement

## Slide 16: Magnet Interconnect Assembly
Extraction bushing
Helium jumper line
Anti-rotation extraction flange
Fixed extraction flange
Interconnect module
Extraction bushing
Strain relief bracket
Existing magnet cold bore
Thermal strap
Beam position monitor
Existing magnet cold bore
Flexible RF bridge
Gold plated contact ring
Spring ring
Pumping slots

## Slide 17: a-Carbon Coating
Proof of principle coating system
  Cycle time meets production requirements
Design of full length (11m) system completed
  Assembly in process
Clean tent area for production nearing completion
Ultrasonic cleaning equipment (11m) commissioned
Cleaning facility
Coating Facility
Graphite target inside beam screen
POP horizontal coating system

## Slide 18: EIC Electron Storage Ring
Electron Storage Ring (ESR) consists of six FODO-cell arcs, and six straight sections (IRs)
High-intensity (28 nC), short (7 mm) bunches
add many interesting accelerator challenges
Circulating beam current ~2.5 A and the synchrotron
radiation power of ~10MW
HSR
EIC needs nearly constant (20 to 24 nm) emittance from
5 to 18 GeV for optimum luminosity, but equilibrium
emittance in an electron storage ring depends on beam energy.
We will use ‘super bends’ (reverse bends) for emittance
control below 10 GeV

## Slide 19: ESR Chamber Detail
Beam channel 80mm x 36mm [3.15” x 1.42”]
Chamber material: OFS copper (C10700)
Water cooling channels joined by e-beam or laser welding
Internal surfaces are NEG coated
Photon absorber formed at end of chambers
CuCrZr flanges with combination RF-vacuum seal
36mm
80mm
Heater wire groove
BPM mount
Pump port
Integrated photon absorber
RF shielded pump ports
CuCrZr flange

## Slide 20: ESR Chamber Status
Both copper profiles in hand
Engineering Validation Unit in process
  Samples of laser welding cooling tubes to main profile
  Integrated photon absorber forming
  Will include BPM and pump ports
  NEG coating on interior vacuum surfaces
New flange and gasket geometry testing in process
  5 thermal cycles to 250C (with hot leak check)
  5 gasket changes (durability test)
Full penetration laser weld
ESR chamber profiles
Silver plated gasket
Seal impression
Flanges post 250°C bake

## Slide 21
EIC IR Layout
High Luminosity:
  25 mrad crossing angle
  Small β* for high luminosity
  with limited IR chromaticity contributions
  Large final focus quadrupole aperture
  Machine Detector Interface
  Large detector acceptance
  Forward spectrometer
  No magnets within - 4.5 / +5 m from IP
  Space for luminosity detector, neutron detector, “Roman Pots”

## Slide 22: Electron Injector

## Slide 23: Electron Injector
Function: Deliver electron bunches of up to 28 nC at a 1 Hz repetition rate for injection into the ESR at various energies of 5 – 18 GeV.
RCS magnet assembly
Vacuum chamber: stainless steel, copper coated (50 um)
Polarized Electron Gun
1-nC, 30 Hz
RCS SRF Cavity, 591 MHz
Beam Accumulator Ring
750 MeV, 40 m
S-band linac, 750 MeV, 30 Hz, 1 nC single bunch
RCS
750 MeV – 18 GeV
28 nC, 1 Hz
85% polarization
1.4 km
Concept modeled after the ANL APS-U injector

## Slide 24: Present EIC Concept (2025)
Accelerator Status at a glance:
Polarized ion/proton source
Ion injection and initial acceleration systems – Linac (200 MeV), Booster (1.5 GeV), AGS (25 GeV)
Hadron Storage Ring (40-275 GeV) – HSR
Electron Pre-Injector (750 MeV linac)
Beam Accumulation Ring (750 MeV) – BAR
Electron Rapid Cycling Synchrotron (0.75 GeV – top energy) – RCS
Electron Storage Ring (5 GeV – 18 GeV) – ESR
Interaction Region(s) – IR
Hadron Cooling System
Ultimate EIC Performance Parameters:
High Luminosity: L= 1033 – 1034cm-2sec-1
Highly Polarized Beams: 70%
Large Center of Mass Energy Range: Ecm = 28 – 140 GeV
Large Ion Species Range: protons – Uranium
Large Detector Forward Acceptance and Low-Background Conditions
Possibility to Implement a Second Interaction Region (IR)
24
Protons: ~40 – 275 GeV
Electrons: 5 – 18 GeV

## Slide 25: Summary
EIC is a unique, high-energy, high-luminosity, polarized beam collider that will be one of the most challenging and exciting accelerator complexes ever built – the only new collider in the next decades.
Since the publication of the 2021 CDR, the project has implemented several design changes to advance design maturity and reduce risk, without affecting the established preliminary performance and cost objectives.
The EIC design is stable and complete.
Subproject scope is well developed, designs are mature, long-lead procurements are ready to be executed.
We now have a well-defined vision of what is required
to build the EIC!