## Slide 1: BHCal Mechanical Modifications
Dan Cacace

## Slide 2: Current Interference
The magnet chimney needs a cutout in the HCal for the phase separator to be mounted on the OD.
The three top sectors of the HCal are already unique from sPHENIX due to a similar issue.
The modifications would be made to these three sectors.
3 Chimney Sectors
Normal Sectors
Endcap
Magnet Phase
Separator
Magnet Chimney

## Slide 3: Proposed Modifications
We need to cut short the three chimney sectors, such that the interference is eliminated, and we maintain the full HCal structure
All chimney tiles would be eliminated, but all full tiles would remain intact.
This attempts to minimize the modifications needed and impact on the structure.
Possibly can regain some tiles in extensions, but will be more complicated/work/expensive.
Maintain HCal
Splice-Plate Structure
Cutout For Chimney
Extend Sector
for structure
Adapt splice plates to
support top sector

## Slide 4: HCal Sectors
Normal HCal Sector
Chimney HCal Sector
Modified Chimney HCal Sector