## Slide 1
1. The FMC adaptor
20 pieces were received
Five pieces were tested;
Most of them do not have the SMA connectors and the I2C connector, so that the board can fit into single-width slots;

## Slide 2
2. The clock test setup
This Si5395 is in LOL_holdover mode, (system clock source)
This Si5395 is in “DAM” mode, with fiber input (19.7 MHz)

## Slide 3
2. The clock test
The phase of the two Si5395 outputs:
13.6842 ns ± 1 ps
FWHM: ~5 ps
2 ps

## Slide 4
3. Some pico/micro/miniDAQ related information
The price of ALINX’s boards:
AXAU15: $556
The ACAU15 SOM ($334) is included.

## Slide 5
3. ACAU25-JL SOM
ACAU15: $334
ACAU25-JL co-design
AMD UltraScale+ Artix XCAU15P-2FFVB676I
AMD UltraScale+ Artix XCAU25P-2FFVB676I
XCAU15P
XCAU25P

## Slide 6
4. Fiber RDO thought
ALINK.COM price:
ACKU15$2781
AMD Ultrascale+ Kintex:
Xcku15p-2FFVE1517i
 | ACKU15 SOM | XCKU15P FPGA | ACKU11 SOM
GTH/GTP | 32/24 | 44/32 | 32/20
price | $2781 | $9K (A1760) (~$4K special) | ?
Aggregation capability | 52 : (1-4) | 72 : (1-4) | 48 : (1-4)

## Slide 7
4. The FIBER RDO ideas
The GTU base board
4* PCIe +12V power
EIC common platform inputs
GTU user interface (1000BaseT)
ATX power
+3.3V, +5V, +12V
AMD
ZU19EG
MPSOC
AMD
KU15P
SOM#2
AMD
KU15P
SOM#1
3* dedicated Clock fanout
18* optic transceiver adaptor boards (to DAM)
Clock (phase)
Monitor plugin
40 GBE
/ 4*RDO
2* DAM
Generic IO
Cooling fan (12V)
Optic transceivers

## Slide 8
4. Fiber RDO thought
Rough estimates:
Cost: $4K per board ($5K including the optic transceivers),  $500K for 5k streams (plus fibers)
Rackspace: < 40 U
  limited by the MTP fiber connectors
  And NO fiber patch panel
  The rack can be very short (12”)