## Slide 1: Recent Developments in SAMMY
January 2026
D. Wiarda, J. Brown, M. Pigni, J. McDonnell, C Chapman, Goran Arbanas
Oak Ridge National Laboratory
Notes: Accessing Title Slide Options The standard ORNL presentation template includes five branded title slide layouts:
  Title | Standard. The preferred layout for lab-wide and general presentations. Features a default aerial photograph of the lab.
  Title | Custom Image. Allows replacement of the default background with a custom full-slide image (16:9 or 4:3 landscape format).
  Title | Custom Portrait Image. Supports inclusion of a custom 4:3 portrait image positioned next to the introductory text.
  Title | Custom Landscape Image. Supports inclusion of a custom 16:9 landscape image positioned next to the introductory text.
  Title | Text Only. Offers additional space for longer titles and multiple presenters.
Additional Lab-approved title slides specific to directorates and user facilities are available in PowerPoint under the following folders: Custom Title Slides and User Facility Templates, located in Presentation Templates.
Custom Title Slide Guidelines
  Image Rights. Any custom images, graphics, or photography must be owned by ORNL or used with documented permission from the original creator or source.
  Appropriate Image Use. Select images that work well with the layout. Ensure the focal point of the image is not obscured by the title text and white overlay box.
  Relevance and Impact. Visuals are a key element of effective communication. Whenever possible, use imagery that enhances the message of your presentation and reflects ORNL’s mission and values.
  Quality and Clarity. Use high-resolution images for clarity on large screens. Avoid overly complex or dark images that may conflict with the title text.
  Text-Only Option. If no appropriate or approved imagery is available, or if imagery is not permitted for the subject matter, the Title | Text Only layout provides a clean, professional alternative.
Learn more about ORNL presentations
  https://ornl.sharepoint.com/sites/branding/SitePages/presentations.aspx

## Slide 2: Outline
Improved ENDF reading
Improved SAMMY API
Updated SAMMY models for use in fitAPI
Cleaner program flow under the hood
Improved treatment of integral experiments
Very early alpha version of python bindings

## Slide 3: Improved ENDF file reading (RR only)
Used as SAMMY par file: #file fe_elemental.js Examples can be found in samtry/tr102
Covariance data are read from File 32 and parameters are flagged depending on what is in File 32
Abundance adjustments are controlled via the json file
All allowed ENDF formats are supported (URR not supported as ENDF uses different algorithm in the URR than SAMMY)
58Fe
File 2
File 32
57Fe
File 2
File 32
56Fe
File 2
File 32
55Fe
File 2
File 32
54Fe
File 2
File 32
{
"n-026_Fe_058.endf":[
{"mat":”2637", "abundance":"0.028",
"adjust":"true","uncertainty":"0.002"}
],
"n-026_Fe_056":[
{"mat":"3625", "abundance":"0.91",
"adjust":"true","uncertainty":"0.04"}
],
…
}

## Slide 4: Better SAMMY C++ Api – RR only
A new C++ class SammyInstance (takes as input a file containing the names of input, parameter and data file and a prefix, i.e get prefix.LPT instead of SAMMY.LPT).
  It just calls the fortran initializing function that still has a lot of global fortran parameters. Thus, need to run all SAMMY inputs in sequential mode.
Get the initial u-parameter (user input parameters converted to a form suitable for adjustment). Before or after conversion to different incoming particle if using.
Allows to update and/or retrieve parameters before or after adjustment. Adjustment can be skipped if using an external fitting program
Write final output if desired
We plan to update this API to be usable for integral data and the URR. As we eliminate more of the global parameters, parallel runs will become available.

## Slide 5: Make a SAMMY model for external fitting (RR only)
For use in our external fitAPI package:
  A SAMMY model for one input/par/data file combination. It allows to read the input files names from a json file or from the command line.
  Functions exist to calculate chi or to get experimental data and or the theory, as well as to set updated parameters.
For use with Minuit (minimally tested) and a Metropolis-Hasting algorithm.
  Test case for the later is in fitAPI/test/metropolisRegression, controlled by the json input file mhSammy.inp
{
"fitMethod": "metropolis",
"sammyInp":[
"trunc-gtt.inp",
"u233-endf.par",
"trunc-gtt.twenty",
""
],
"rrrinputfile": "interactive-inp",
"numberSamples": 500,
"parDistMultiplier": [
0.003,
…

## Slide 6: Make a SAMMY model for external fitting (RR only), cont.
A SAMMY model that can take several SAMMY runs for use in Dakota. Runs are performed sequentially. All resonance parameter must be the same for all runs. Change to inverse reaction is allowed. Experimental corrections and desired reactions can vary.
A method to only get the u-parameters, for use in creating a Dakota input file.
A mode to have Dakota call it during its run.
Examples are in tr001, convertToInverse, and changeExpInfo in the samtry directory.
This allows to get cross experiment covariances if Dakota produces them.
Dakota is a framework used for Uncertainty Quantification (UQ) and Sensitivity Analysis developed by Sandia National Laboratory.
{
"fitMethod":"dakota",
"dakotaInput":"myData",
"defaultLower":"1000.0",
"defaultUpper":"1000.0",
"inputs":[
{
"prefix":"run6",
"printLst":"yes",
"sammyInp":[
"../bair_an.inp",
"../o17-alpha.par",
"../bair_an.twenty 0000000.0 4500000.0",
""]
},
{
"prefix":"run7",
"printLst":"yes",
"sammyInp":[
"../cierjacks_ntot.inp",
"../o17-alpha.par",
"../cierjacks_ntot.twenty 0000000.0 6000000.0",
""]
}
]
}

## Slide 7: Internal program flow updates
All formalism (MLBW, CRO and XCT) now fill the same 0K cross section object for spin group and channel dependent cross section.
New classes have been added to calculate the desired reactions, like total, capture, eta, etc. This is especially helpful if the final reactions is the ratio of several reaction like eta or alpha ratios (see next slide).
These new classes allow to use different abundances (by isotope, by sample (if self-indicating experiment), by l-value for detector efficiency), without cluttering the 0K R-Matrix calculation.
Therefore, the internal program flow has a cleaner separation between R-Matrix calculations and experimental corrections.
Previously certain experimental results or corrections were only supported with one algorithm. Except for angle-differential data this is no longer true.

## Slide 8: Internal program flow updates, cont.
Created a C++ class (CalculationInfo) new Fortran class, SetupCrossInfo to fill CalculationInfo, to set up the calculations required for the current experiment, i.e.
  What cross sections need to be calculated (for example fission and absorption) for eta
  What abundances need to used be used (for example different ones for the sample and the self-indicating sample)
  To what temperature(s) do we need to broaden the 0K data
  What corrections (scattering, background, ..) need to be applied.
Created a C++ class (CombineCrossData) to combine the data to calculate eta or alpha ratios or any other combined cross section.
This information is filled in at the beginning of each SAMMY run.
(Currently under review and not yet available on the public facing SAMMY web-site)

## Slide 9: Internal program flow updates, cont.
Consolidate the flow for experimental corrections:
  The function doppler_and_resolution_broadening now controls the application of all experimental corrections and ratio calculations.
Previously this was controlled by each doppler and resolution broadening module, i.e. once Doppler broadening was performed a global flag determined which and if resolution broadening was to be done.
Thus, the changes needed where actually more intrusive to the underlying SAMMY code than expected.
It allowed us to add an alpha ratio calculation to SAMMY, which is currently under review.
(Currently under review and not yet available on the public facing SAMMY web-site)

## Slide 10: Improved treatment of integral experiments (currently under review)
Ensure that integral quantities can be calculated by isotope or total sample. (Input allowed that, but calculation didn’t).
Ensure that after calculation, fitting procedure do not need to know that integral data are calculated.
This allows to use integral data just like any other supported reaction.
(Currently under review and not yet available on the public facing SAMMY web-site)
Integral data (totally made up) for pretend FE
0 [= sum over all nuclides]
THABS 7.89 1.0 [Thermal absorption]
MXABS 6.5 0.9 [Maxwellian absorption]
2 [= isotope (nuclide) number, as in PAR file
THABS 4.2 1.0 [Thermal absorption]
MXABS 3.7 0.7 [Maxwellian absorption]
4 [= isotope (nuclide) number, as in PAR file
THABS 0.8 0.04 [Thermal absorption]
MXABS 0.71 0.07 [Maxwellian absorption]

## Slide 11: Very Early Alpha version Python interface to SAMMY
Enable python bindings using -DSAMMY_PYTHON=ON on the cmake configure
Currently only works for resolved range data
An example can be found in samtry/tr001/ctest_c.py
  Provide the usual SAMMY input files
  Retrieve the result data using the standard SAMMY output structures
We are planning to extend this to allow better access to the the user input
Please provide any feedback or suggestion to us, so we can make this a useful user feature. Available as is on master in the publicly facing SAMMY web site.

## Slide 12: Future plans
Ensure that the URR is using the same C++ class to hold the data as the RR. This will make all the improvements available for the RR also available for the URR.
  This will include adding the improvements made by Alec Golas (RPI) to SESH and updated self-shielding and the updates by Justin Lorin (UTK) to the fitting of the level spacing.
Move to a more modern input (json file) for SAMMY, levering the C++ SammyInputInfo class currently used to hold many of the input information along with the classes that hold the experimental correction information.
Add numerical differentiation to the RR resonance calculation. This will allow for much easier testing of new R-Matrix algorithms, which is currently made harder as the analytical derivatives also need to be given.
Improve the interaction with external fitting programs such as MINUIT and Dakota.
Move the SAMMY fitting algorithms into fitAPI, so that all adjustment is done through that API, while still giving the same good SAMMY results as before.
Create an HDF5 file containing all covariance and theory information instead of the current ODF file and binary covariance file. LST files (written from the HDF5 informtion) will be available as before.

## Slide 13
SAMMY is available from https://code.ornl.gov/RNSD/SAMMY