## Slide 1: International Nuclear Data Evaluation Network (INDEN) Updates on 233U, 239Pu, 54,56Fe, 50,53Cr, and 19F
Roberto Capote
Deputy Section Head, NDDU head
CSWEG November 2024, Brookhaven National Laboratory, Upton, NY

## Slide 2: International Nuclear Data Evaluation Network (INDEN)
https://www-nds.iaea.org/INDEN

## Slide 3
Outlook
U-233: Brooks & Leal-Cidoncha data, PROFIL
Pu-239: EUCLID crit. experiments, NIFFTE TPC
Fe-54,56: New elastic/inelastic data by
Gkatis et al (EC JRC Geel)
Cr-50,53: New capture data by
Maroto et al (CNA Sevilla, Spain)
F-19: Quasidiff. RPI data (G. Siemers et al)
“It doesn't matter how beautiful your theory is,
it doesn't matter how smart you are.
If it doesn't agree with experiment, it's wrong.”
Richard Philips Feynman, Nobel Prize in Physics 1965

## Slide 4
U-233 below 2eV (thermal systems)
New RRR fit needed for En<2eV!
α=σγ/σf

## Slide 5
U-233 fission XS (from U3/U5 ratios)
B8.1 = JENDL-4 = JENDL-5 fission XS
(n,f) data in good agreement,
-> problems in capture

## Slide 6
U-233 (URR & fast)
JENDL-5 eval (URR) agrees with CEA PROFIL data
JEFF-3.3 (B71) and B81 in disagreement with PROFIL
α=σγ/σf
J. Tommasi and G. Noguere, Nucl. Sci. Eng. 160, 232 (2008) - PROFIL
(adopted by JEFF-3.3)

## Slide 7: Pu-239 updates

## Slide 8
239Pu(n,f)/235U(n,f) NIFFTE (2021,2024)
Provided by Pronyaev
Snyder L et al, Nucl Data Sh. 178 (2021) 1–40. https://doi.org/10.1016/j.nds.2021.11.001
Dongwi D.H. et al, https://doi.org/10.48550/arXiv.2409.18279 (2024)

## Slide 9
Provided by Pronyaev
239Pu(n,f)/235U(n,f) NIFFTE (2021,2024)
Snyder L et al, Nucl Data Sh. 178 (2021) 1–40. https://doi.org/10.1016/j.nds.2021.11.001
Dongwi D.H. et al, https://doi.org/10.48550/arXiv.2409.18279 (2024)
+2%

## Slide 10
exp_6001a = TPC 2021 (TPC 2024 not used yet)
exp_1029a = Lisowski exp_609a = White
5 10 15
Latest fit (with USU), 10/24
0.9 0.95 1.0 1.05 1.1
+2%
239Pu(n,f)/235U(n,f) NIFFTE (2021,2024)
Correlations TPC2024 - TPC2021 being assessed!

## Slide 11: 239Pu(n,f)/235U(n,f) impact on SACS-STD
SACS fission cross sections | SACS meas. (*) evaluation (2023) | STD 2017 (B-VIII.0) | Difference to SACS eval (%) | Latest 10/2024 (MCMC) (*) | Difference to SACS eval (%)
235U(n,f) | 1.221 (0.91%) | 1.227 (1.2%) | 0.5% | 1.225 | 0.3%
239Pu(n,f) | 1.826 (1.03%) | 1.798 (1.3%) | 1.5% | 1.826 | 0.0%
238U(n,f) | 0.327 (1.06%) | 0.322 (1.3%) | 1.5% | 0.325 | 0.6%
239Pu/235U ratio | 1.495 (1.7%) | 1.465(1.2%) | 2.1% | 1.49 | 0.3%
238U/235U ratio | 0.268 (1.8%) | 0.262(1.2%) | 2.2% | 0.265 | 1.1%
Updated SACS(Cf) experimental database (*)

## Slide 12
J. Hutchison et al, EUCLID: A New Approach to Constrain Nuclear Data via Optimized Validation Experiments using Machine Learning,
EPJ Web of Conferences 284, 15006 (2023)
J. Hutchison et al, Reaction Rate Ratios for Recent Fast Metal Experiments withLarge Plutonium Masses, Nucl. Sc. & Eng. 2024
https://doi.org/10.1080/00295639.2024.23431181

## Slide 13
EUCLID sensitivities: Jezebel, 3x2, 8x1
J. Hutchison et al, EUCLID: A New Approach to Constrain Nuclear Data via Optimized Validation Experiments using Machine Learning,
EPJ Web of Conferences 284, 15006 (2023)
J. Hutchison et al, Reaction Rate Ratios for Recent Fast Metal Experiments withLarge Plutonium Masses, Nucl. Sc. & Eng. 2024
https://doi.org/10.1080/00295639.2024.23431181

## Slide 14
EUCLID design: 3x2, 8x1 (+Jezebel)

## Slide 15
EUCLID + Jezebel for trials
e81b2 ~ e80 ~ INDEN p57 (3x2->8x1 drop ~ -200pcm)
e81b2Puan9 (INDEN p57 with JEFF-3.3 INL and EL recalculated)
=> Lower inelastic and (corresp) higher elastic XS strongly favored

## Slide 16: Summary: EUCLID & analysis
Two new critical experiments were especially designed to be sensitive to compensating errors in elastic/inelastic XS
Simulation results favor lower inelastic and higher elastic than in current ENDF/B libraries
JEFF-3.3 gives better (but not perfect) results
New file using JEFF-3.3 INL confirmed improvement. Improved modelling required
J. Hutchison et al, EUCLID: A New Approach to Constrain Nuclear Data via Optimized Validation Experiments using Machine Learning,
EPJ Web of Conferences 284, 15006 (2023)
J. Hutchison et al, Reaction Rate Ratios for Recent Fast Metal Experiments withLarge Plutonium Masses, Nucl. Sc. & Eng. 2024
https://doi.org/10.1080/00295639.2024.23431181

## Slide 17: 239Pu coupling scheme: New OMP 2420
Important octupole band (built on ½- state) coupled with SRM:
½-  (core exc) 0-  ½+ (single-particle GS)
better physics lead to better nuclear data
Uexc(MeV)

## Slide 18: Pu239(n,inl): SRM vs Rigid OMP
SRM lead to significant reduction of the CN cross section below 2 MeV !

## Slide 19: Iron updates

## Slide 20: Fe-54 inelastic cross sections

## Slide 21: Chromium updates

## Slide 23
jefdoc-2269: T. Ligonnet et al (2023)
T. Ligonnet et al, presented at JEFF meeting. November 2023, jefdoc-2269

## Slide 24
PETALE: Cr reflector (preliminary)
“Near thermal” range: Au-197(n,g) In-115(n,g)
fast range: In-115(n,n’) fast range: Ni-58(n,p)
T. Ligonnet et al, presented at JEFF meeting. November 2023, jefdoc-2269

## Slide 25: Fluorine updates

## Slide 26
RPI quasi-diff. test on Teflon
G. Siemers et al, RPI, analysis for the ENDF/B-VIII.1 paper (2024)

## Slide 27: SUMMARY
U-233: New RRR fit, new URR (PROFIL)
Pu-239: New OMP with soft-rotor model multi-band coupling to reevaluate the fast neutron range (elastic , inelastic )
Check with EUCLID 1x8 & 3x2 + PMF001
Fe-54,56: Gkatis data to be considered
Cr-50,53: RRR reevaluation (Maroto & PETALE)
F-19: To improve 2nd-6th (n,n’) XS & ang. distrib.
Additional work on O-16, Pb, Zr, Ni, Cu (covar)

## Slide 28: Thank you!
Notes: Thank you!