## Slide 1: Berkeley Group Nuclear Data Measurements Program (mostly GENESIS)
Lee A. Bernstein
Department of Nuclear Engineering
University of California - Berkeley
Nuclear Science Division
Lawrence Berkeley National Laboratory
https://nucleardata.berkeley.edu

## Slide 2: I’m going to present a short sample of some of our nuclear data measurements for applications
LBNL/UCB Measurements Program
DOE-Nuclear Energy
Energy
National Security
DOE-NNSA
NASA
DOE-IP
NorthStar
Pharmaceutical
Medical Isotopes (Voyles, Apgar)
Google
(Time Permitting)
DOE Nuclear Physics
Atomic-Nuclear interaction & RSF
MDA
Gamma-rays
Natural
Radioactivity
Cosmic rays
Fast neutrons
Space Exploration
Notes: Replace figures as appropriate

## Slide 3
D-beam
Thick target Deuteron Breakup Neutron Source
GENESIS
We built the Gamma Energy Neutron Energy Spectrometer for Inelastic Scattering (GENESIS) to measure coincident (n,xng) cross sections
Chart: DTOF 14 MeV D on C
Chris Brand
“GENESIS 2.0”
Josh Brown
The combination of HPGe, neutron detectors and an energy-limited neutron spectrum provides differential + integral tests of all parts of a nuclear reaction model (OMP, gSF, NLD…)

## Slide 4: Our initial effort with GENESIS was a proof-of-principle studying 56Fe(n,n’g)
Our initial work has focused on nuclei for advanced reactors and nonproliferation: 56Fe, 238U, 35Cl and 23Na
J.M. Gordon
56Fe(n,n’g)
gated on prompt neutrons
Gamma-rays up to 10 MeV measured for incident En from 10 keV to 20 MeV
Priority | Elements
First | C, N, O, Na, Al, Si, Fe, Cu, Pb, W, U, Pu
Follow-up | He, Li, Be, B, Cl, Cr, Mn, Ni, Ge, Br, Cd, I, Cs, La
Remaining | F, Mg, P, S, Ar, K, Ca, Ti, As, Kr, Mo, Sn, Sb, Xe, Gd, Bi, Np, Am, Tm
S. McConchie, et al., Technical Report No. ORNL/TM-2021/1900, 2021.
Nn(En,qn) gated on the
1238 keV
“GENESIS: Gamma Energy Neutron Energy Spectrometer for Inelastic Scattering.” J.M. Gordon et al., NIM A 1061 (2024) 169120.
*https://doi.org/10.1016/j.nima.2024.169120

## Slide 5: We use a forward fit process to determine optimal reaction modeling parameters for multiple incident neutron energies
GENESIS sg/n’(En,qn’)
sg/n’(En,qn’) from Talys
Publication
c2
minimization
Joey Gordon
c2/dof=1.6
Realistic values were obtained for all parameters except neutron OMP using only g-ray partial cross sections
Next Step included the neutron spectral data Nn(En ,qn )
Spectrometer
Simulation
Input: ENSDF, NLD, RSF, OMP
Calculate g-ray, neutron observables
Contributions from all beam pulses were well-modeled
J.M. Gordon Ph.D. dissertation, December 2023. https://escholarship.org/uc/item/3mm226cb

## Slide 6: We use a forward fit process to determine optimal reaction modeling parameters for multiple incident neutron energies
GENESIS sg/n’(En,qn’)
sg/n’(En,qn’) from Talys
Publication
c2
minimization
Joey Gordon
c2/dof=1.6
Spectrometer
Simulation
Input: ENSDF, NLD, RSF, OMP
Calculate g-ray, neutron observables
This approach isn’t limited to observed channels
sElastic was successfully predicted as well
J.M. Gordon Ph.D. dissertation, December 2023. https://escholarship.org/uc/item/3mm226cb

## Slide 7: The actual minimization approach involves three steps
c2 for avadjust
1238 keV
c2 for s2adjust
Joey Gordon
J.M. Gordon Ph.D. dissertation, December 2023. https://escholarship.org/uc/item/3mm226cb
Notes: 847 keV Mn-56

## Slide 8: The final values
Neutrons
Gammas
Joey Gordon
J.M. Gordon Ph.D. dissertation, December 2023. https://escholarship.org/uc/item/3mm226cb
Notes: 847 keV Mn-56

## Slide 9: We also performed a 3-part 35Cl(n,x) measurement for MCFRs
D-beam
Neutron Source
Integral Experiment #1
Production of 35S and 32P via 35Cl(n,p) and 35Cl(n,a) on a NaCl tablet (Ni monitor foil)
Differential Experiment #3
35Cl(n,p) and 35Cl(n,a) relative to 6Li(n,t)a from a CLYC (Ce:Cs2Li6YCl6) Active Target
Differential Experiment #2
35Cl(n,xg) & 35Cl(n,g) using a NaCl tablet
Experiments performed in 2021 & 2022
Tyler Nagel

## Slide 10: We also used GENESIS to perform simultaneous energy differential and integral measurements of the 35Cl(n,p), (n,a) and (n,n’g) cross sections
Neutron Source
Tyler Nagel
g-ray energy (keV)
Counts
D-beam
35Cl(n,n’g)
23Na(n,n’g)
35Cl(n,pg)35S
35Cl(n,p0)
6Li(n,⍺)t
6Li(nth,⍺)t
CLYC-6 @ 4.5 m
CLYC-6 @ 9 m
6Li(n,⍺)t
35Cl(n,p0)
35Cl(n,pɣ)
“Measurement of energy-differential 35Cl(n,p0)35S cross section via ratio with 6Li(n,α)t.” T. Nagel et al., Phys. Rev. C 110, 034612 (2024)

## Slide 11: We’ve been working to determine isotope production rates at different beam energies using the stacked target method
Beam
VERY thick Al Degraders
(lowers the beam energy)
Foil of Interest
Monitor Foils
g-ray
detector
Irradiate a stack of foil that includes monitor targets that where the reaction rates are known and targets we want to determine the production rate on and “beam degraders” which lower the beam energy.
Put the targets in front of the g-ray detector after the experiment to measure the decay of the radioactive products formed during irradiation.
This allows the production rate of the unknown target to be determined relative to the known targets.
Notes: Beam current and energy measured using activation monitors and beam-current integrators. High current (≤1500 W) and modest beam energies allow for very short irradiations and quick sample extraction facilitating the measurement of activities with t-1/2 ≥ 10 min.

## Slide 12: We’ve developed a high-power target for intense neutron bombardments of materials for fusion & single event effects
Target tested in August 2024, with sponsorship from MDA and NorthStar
J.T. Morrell, PRC 108, 024616 (2023)
*Assumes 20 µA beam and 0°
40 MeV deuterons*
=1.4x1011 n/s/cm2 @ 1 cm
=2.0x1010 n/s/cm2 @ 10 cm
=2.2x105 n/s/cm2 @ 10 m
50 MeV deuterons*
=7.5x1012 n/s/cm2 @ 1 cm
=1.2x1011 n/s/cm2 @ 10 cm
=6.7x105 n/s/cm2 @ 10 m
The intense fast, forward-focused neutrons from TTDB at the LBNL 88-Inch Cyclotron is a powerful capability for measuring:
gas production & materials damage in high-temp superconductors
final-stage optics for ICF
neutron shielding & single-event effects for space applications

## Slide 13: Onto Isotope Production! We performed (p,x) measurements at 50 MeV (LBNL), 100 MeV (LANL) and 200 MeV (BNL) on 121,123Sb
93Nb 100%
Over 200 nuclei populated with 16 independent + 10 cumulative excitation functions measured for natSb(p,x)
Isomer ratios for 119,121Tem,g show that r(J) and that neutron optical model parameters need adjustment..wait for the paper…
Catherine Apgar

## Slide 14: Catherine Apgar saw evidence of significant secondary neutron production in natSb(p,x) data at Ep=200 MeV
1C. Apgar, PhD Thesis, UCB (2024)
2M.B. Fox, PRC 104, 064615 (2021)
Secondary neutrons are a challenge and an opportunity for isotope production
BNL
(200 MeV)
123Sb(p,pn)122Sb
+123Sb(n,2n)122Sb
BNL
(200 MeV)
121Sb(p,pn)120mSb
+121Sb(n,2n)120mSb
121Sb(p,p5n)116mSb
+121Sb(n,6n)116mSb
BNL
(200 MeV)
It turns out we saw this as well in our 2021 As data as well2
75As(p,pn)74As
+75As(n,2n)74As
Catherine Apgar
LANL
(100 MeV)
LANL
(100 MeV)
LANL
(100 MeV)
LBNL (50 MeV)
LBNL (50 MeV)
LBNL (50 MeV)

## Slide 15: We’re establishing a Berkeley/Oslo/INFN-SPES-Legnaro collaboration to resolve discrepancies in reaction modeling
M.B. Fox, PRC 104, 064615 (2021)
C. Apgar, PhD Thesis, UCB (2024)
Single-foil and stacked-target irradiations will provide insight into secondary neutrons at high-Ep facilities
Sc(p,x)44Ti →44Sc PET generator
Ag(p,x)107Cd for Auger therapy
Deformed → near-spherical enriched Nd, Eu, Sm targets for improved reaction models (collaboration w/ A. Koning)
Data analysis by UiO students
Andrew Voyles
Mathis Wiedeking

## Slide 16: Our group has performed a series of measurements, reaction modeling and decay studies related to the production of radionuclides near the PET imaging nucleus 86Y
SrCO3 target enriched 86Sr (96.4%) irradiated with proton and deuteron beams at 88-inch cyclotron, LBNL, and BC1710 cyclotron, FZJ, Jülich.
Medical Isotope production cross sections
Decay studies
   emission probability
   emission probability
Reaction dynamics
  (p,xn)
  (d,xn), (d,x)
(p,n)
86Sr(p,n)86m,gY
86Sr(p,2n)85m,gY
(d,xn)
86Sr(d,n)87m,gY,
86Sr(d,2n)86m,gY
86Sr(d,3n)85m,gY
(d,x)
86Sr(d,a)84m,gRb,
86Sr(d,an)83Rb
86Sr(d,a2n)82mRb
7 Publications since 2020:
2020Ba30: Phys.Rev. C 101, 064619 (2020)
2020Ud01: Radiochim.Acta 108, 747 (2020)
2022Ud01: Molecules 27, 768 (2022)
2022Ud02: Eur.Phys.J. A 58, 67 (2022)
2022Ud03: Radiochim.Acta 111, 81 (2022)
2024Ud01: Eur.Phys.J. A 60, 128 (2024)
2024UdAA: PRC (submitted)
This is all part of a long and fruitful collaboration with
Prof. S. Qaim (FZJ-Julich), and Dr. M.S. Uddin (BAEC-Bangladesh)
M.S. Basunia

## Slide 17: We’ve developed target fabrication capabilities to support current and future measurements
Vacuum Deposition
10 µg/cm2 Au
20 µg/cm2 C
70 µg/cm2 Au
2 mg/cm2 As (Electrodeposition)
Computer Vision based areal density measurement tool1
[1] https://github.com/avoyles/ArealDensityCam
Other Capabilities:
Thin-Foil Rolling, Pressed Pellets, Sedimentation
Actinide Targets (229Th, 241Am, 240Pu) - coming soon!
Andrew Voyles

## Slide 18: We have been using ultra-high flux (1028+ e/cm2/s) e’s and g’s from a fs laser to perform photoexcitation measurements
80gBr (17.7 m)
80mBr (4.4 h)
79Br
QC
Use a LaBr detector for use as a 79,81Br active target.
Install adjustable Bremsstrahlung converter (energy selection via geometry, few pC/MeV expected)
Use both photons and electrons to populate 79mBr, 80gBr and 80mBr
LaBr “active target”
Dispersion
Magnet
Electron
Beam
Target Chamber Floor
Energy/Charge Scintillator
Laser
15-35 MeV Electrons
Active Detector
The isomer on population ratio depends on both r(Ex ) & F(Eg )
80gBr
(stable)
Magnet
Brem. Converter
15-35 MeV photons
Electrons are ≈4 times as effective at changing J

## Slide 19: CY2023-2024 BAND Ph.D. Dissertations
“Simultaneous Measurements of Secondary Gamma Rays and Neutrons from Fast Neutron Scattering on 56Fe with GENESIS”
  Joseph Gordon – December 2023 UCB Post-doc
“Techniques in Live Neutron Spectroscopy”
Christopher Brand – December 2023 – LLNL Staff
“Isomer Population Control in Solid-Density Targets using Compact Laser-Plasma Accelerators”
  Robert E. Jacob– May 2024 LBNL Postdoc
“Production of 117mSn and 119mTe via Proton Bombardment on Natural Antimony: Applications for Charged Particle Reaction Modeling and Theranostics”
  Catherine Apgar– May 2024 LANL Postdoc
“35Cl(n,x) Cross Section Measurement”
  Tyler Nagel– May 2024 LANL Postdoc
Future Colleagues - Our most valuable product

## Slide 20: Collaborators and Sponsors
GENESIS
J.A. Brown1, C. Brand2, D.L. Bleuel2, J.M. Gordon1, B.L. Goldblum1,3 Catherine E. Apgar1*, T. Laplace1, Amanda M. Lewis1**, Jon Morrell1*, T. Nagel1***
Isotope Production via (p,x), (d,x) reactions
Andrew S. Voyles1, Catherine E. Apgar1***, M.S. Basunia2, Jon C. Batchelder1, Eva R. Birnbaum4, Cathy S. Cutler5, Morgan B. Fox1, Arjan Koning5, Amanda M. Lewis1**, Dmitri Medvedev5, Jon Morrell1*, Ellen O’Brien4, S.M. Qaim6, Michael A. Skulski4, M.S. Uddin7, Etienne Vermeulen4, M. Wiedeking3
Isomer manipulation @ BELLA
J.A. Brown1, C. Geddes2, R. Jacob2, T. Ostermayr2, C. Schroeder2,1, D.H.G. Schneider2
1 University of California-Berkeley Dept. of Nuclear Engineering
2Lawrence Livermore National Laboratory
3 Lawrence Berkeley National Laboratory
4 Los Alamos National Laboratory
5 Brookhaven National Laboratory
5 International Atomic Energy Agency
6Forschungzentrum Jülich
7Bangladesh Atomic Energy Agency
*Now at Brookhaven National Laboratory
**Now at UT-Knoxville
***Now at Los Alamos National Laboratory