## Slide 2: Ta181 Covariances and Integral Experiments
CSEWG 2025
J. Hutchinson, P. Brain, T. Cutler, N. Gibson, N. Kleedtke, R. Little, I. Michaud, D. Neudecker, M. Rising

## Slide 3
Ta nuclear data needs
Until 2022, there was 1 experiment sensitive to Ta.
5 new cases were added in 2022.
Ta is a refractory metal with high melting point and high corrosion resistance.
  Useful for plutonium processing operations
All processes with significant quantities of fissionable material must follow ANSI/ANS-8 series standards:
  ANSI/ANS-8.1: “Where applicable data are available, subcritical limits shall be established on bases derived from experiments…”
Criticality safety evaluations utilize predictive simulations
  Relies on codes to be correct and for nuclear data to be accurate
  Critical and subcritical experiments are required for validation
The International Criticality Safety Benchmark Evaluation Project (ICSBEP) contains over 5000 cases
  But, for many nuclides such as Ta, there are no experiments
  And often those same nuclides can lead to large uncertainties for applications

## Slide 4
Thales project goals
Thales project
  Explore Ta nuclear data sensitivity/uncertainty for applications
  Designing integral experiments to provide additional validation data for nuclear criticality safety of Ta reflected Pu applications
In addition, this project will
  Help identify other nuclear data uncertainty drivers of subcritical margins for criticality safety applications.
  Improve machine learning as applied to design of criticality experiments.
Thales experiment will take place at the National Criticality Experiments Research Center (NCERC)
Comet critical assembly machine at NCERC
NDML
ARCHIMEDES
EUCLID
Thales
Named after Thales of Miletus

## Slide 5
Ta181 has been a high DOE-NCSP priority for years
J. Brown, “Ta-181 URR Covariance”, CSEWG 2024.
Previous benchmarks
  PU-MET-FAST-045-006
  PU-MET-MIXED-003-001
Previous Thales work:
  Application down-selection: ANS Winter 2024
  Experiment design: NCSD 2025
  Nuclear data sensitivity, uncertainty, and similarity metrics: NCSD 2025
This work focuses on comparing 7.1 (with 7.1/BLO covariances) to 8.1

## Slide 6
Investigation of Ta-181 Correlations
7.1/BLO
ENDF/B-VIII.1
Energy
Energy
Notes:
More cross-reaction correlations in ENDF/B-VIII.1

## Slide 7
Investigation of Ta-181 Correlations
Max 𝜌 = 1.0000000000000002
Min 𝜌 = -0.9926
Max 𝜌 = 9.8552
Min 𝜌 = -2.3940
7.1/BLO
ENDF/B-VIII.1
Notes:
BLO covariances have very minor round-off issues
Many ENDF/B-VIII.1 covariances have major issues making them unusable

## Slide 8
Investigation of Ta-181 Relative Uncertainties
7.1/BLO
ENDF/B-VIII.1
Energy
Reductions across the board, but a bit hard to see when looking at all reactions

## Slide 9
Capture comparison
This is NOT a direct comparison
Based on available data
  7.1/BLO: 44 groups
  8.1: 51 groups
The important comparisons, however are:
  General shape of cross-sections at top
  Fact that relative uncertainties are much smaller for 8.1 (as expected)
8.1 correlation plot
7.1/BLO correlation plot

## Slide 10
Experiment design models
From V3 build (Brain NCSD 2025)
Models vary by
  Amount of Ta reflector
  Material in axial region
  Number of Pu plates (adjusted for criticality)
Model name | Ta thickness (in) | Ta thickness (cm) | Material in axial region
Nominal_0_31_Crit | 0.125 | 0.3175 | Ta
Nominal_0_63_Crit | 0.25 | 0.635 | 
Thales_Nominal_1_27_Crit | 0.5 | 1.27 | 
Thales_Nominal_2_54_Crit | 1 | 2.54 | 
Thales_Nominal_5_8_Crit | 2 | 5.08 | 
Thales_Nominal_8_89_Crit | 3.5 | 8.89 | 
ZOIDED_MAX_0_63_00_Crit | 0.25 | 0.635 | Void
ZOIDED_MAX_1_27_00_Crit | 0.5 | 1.27 | 
ZOIDED_MAX_2_54_00_Crit | 1 | 2.54 | 
“Zoided” = Z-axis voided
Colors are darker as the total Ta mass increases
Axial void will be provided by Al spacers

## Slide 11
keff sensitivities
Applications/experiments with thick Ta are (not surprisingly) very sensitive to Ta181 scattering
All sensitivity is in the fast energy range
elastic
n,gamma
inelastic

## Slide 12
Results: nuclear data unc
The unc in keff due to Ta181 nuclear data dramatically decreased from the BLO covariance library to ENDF/B-VIII.1
  Expected due to the VIII.1 work on Ta181
That being said, the uncertainty for Ta181 is still >700 pcm for VIII.1
This drastic change in the covariance data means that ck results will shift compared to future work
  Also true for other metrics that use covariance data
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_22_e80_e81JSON_51_nof_noi
Nuclide | Reaction | BLO | ENDF/B-VIII.1
73181 | elastic | 861 | 364
73181 | inelastic | 2509 | 307
73181 | n,gamma | 497 | 65
94239 | elastic | 268 | 202
94239 | fission | 337 | 504
94239 | inelastic | 409 | 366
94239 | n,gamma | 116 | 33
94239 | total nu | 1239 | 424
Total |  | 3013 | 917
Thales_App_01

## Slide 13
Results: ck
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_22_e80_e81JSON_51_nof_noi
Shift in ck results from BLO (left) to VIII.1 covariances (right)
1 3 5 7 8 9 2 4 6
1 3 5 7 8 9 2 4 6
Most Ta
Least Ta
ck is generally lower for VIII.1
These numbers go from 1 (least Ta mass) to 9 (most Ta mass)

## Slide 14
Conclusions
Nuclear data uncertainties and similarity metrics were investigated for the Thales design
Nuclear data uncertainties decrease dramatically from BLO to ENDF/B-VIII.1 covariances
  But Ta181 is still a large contributor to total nuclear data uncertainty
Similarity metrics were utilize to down-select among proposed experiment design files
  Four configurations can be utilized to have good performance for all of the metrics

## Slide 15
Future work
Procure all materials
Perform experiments at NCERC!

## Slide 16
Many ENDF/B-VIII.[0,1] ND Covariances Need Fixing
Before successful usage in NCS/Whisper applications, correlations in ND covariances should only exist between -1,1.
  Some numerical round-off issues are typically not concerning
  Nearly half of the ENDF/B-VIII.[0,1] covariances are likely unusable by Whisper as is
Number of Isotopes with Inappropriate Correlations | Whisper-1.1 (407) | ENDF/B-VIII.0 (246) | ENDF/B-VIII.1 (266)
# 𝜌 < -1 # 𝜌 > +1 | 23 (5%) 162 (40%) | 136 (55%) 241 (98%) | 149 (56%) 264 (99%)
# 𝜌 < -1.00015 # 𝜌 > +1.00015 | 0 0 | 136 (55%) 127 (52%) | 149 (56%) 140 (53%)
# 𝜌 < -1.1 # 𝜌 > +1.1 | 0 0 | 130 (53%) 125 (51%) | 145 (55%) 137 (52%)

## Slide 17
Acknowledgments
NCERC is supported by the DOE Nuclear Criticality Safety Program, funded and managed by the National Nuclear Security Administration for the Department of Energy.
Los Alamos National Laboratory is operated by Triad National Security, LLC, for the National Nuclear Security Administration of the US Department of Energy under Contract No. 89233218CNA000001.

## Slide 18
Backup

## Slide 19
Investigation of Ta-181 Relative Covariances
7.1/BLO
ENDF/B-VIII.1
Energy
Energy
Notes:
More reactions and smaller uncertainties in ENDF/B-VIII.1

## Slide 20
Inelastic comparison
8.1 correlation plot
7.1/BLO correlation plot

## Slide 21
Elastic comparison
Also a dramatic reduction for 8.1
8.1 correlation plot
7.1/BLO correlation plot

## Slide 22
Similarity metric results
From previous work:
ck for the 40 applications.
Actually a 40x40 matrix.
Values along the diagonal are 1 by definition.
A01 has ck>0.99 for A04 and A05.
Application A02 has ck<0.99 compared to other applications.
A03 has ck>0.99 for A06-A40.
A maximum of three application models (A01, A02, and A03) are needed.
  One could argue that 0.99 is too strict.
  If so, maybe only 1 model is needed.
Results of filtered ck (only 181Ta elastic or inelastic) are not shown:
  >0.99 between each pair of the 40 applications.
All values with ck>0.99 are shown in green.

## Slide 23
Methodology
Note that these three metrics are really only applicable if the sensitivity vectors are filtered
  You can still compute it using all reactions, but the results won’t make sense
  So all of these equations are assuming the vectors are filtered (to Ta181 scattering)
Additional nomenclature notes:
  1 and 2 are the L1 and L2 norms
  E refers to energy
Taxicab geometry, Wikipedia
A
B

## Slide 24
Results: summary

## Slide 25
Results: Esum
Esum is not very interesting since nearly all values are >0.99
Note that PMF045-006 has values of >0.99 for all three applications
These results include all nuclide/reaction pairs and the results are being dominated by Pu239
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_22_e80_e81JSON_51_nof_noi

## Slide 26
Results: WSS (Ta181 inelastic)
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_21_e80_e81JSON_51_Ta181in_noi
Filtered on Ta181 inelastic

## Slide 27
Results: WSS (Ta181 elastic)
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_23_e80_e81JSON_51_Ta181el_noi
Filtered on Ta181 elastic

## Slide 28
Ta need documented by LANL NCS
Slide at right is from a presentation in May 2023: A. Smiley, J. Alwin, “LANL Nuclear Criticality Safety Needs for Experimental Data,” TEX2.0 Meeting, LA-UR-23-24612.
Presented to a workshop with criticality safety professionals across the DOE complex.
Conclusions slide states:
  Highest priorities:
    Intermediate Pu PARADIGM
    Ta reflection Thales
    Chlorine CWS

## Slide 29
Ta need also documented by SRS
Slide at right is from a presentation in May 2023: A. Szasz, “Savannah River Site Input for TEX 2.0,” TEX2.0 Meeting.
The bottom right shows all of the high priority needs established at the meeting across the complex.
High |  |  | 
SNM | Reflectors | Absorbers | Other
Pu239 int | Ta fast | Cl, Li | Poly PNDA
U235 int and epithermal | Be thermal |  | Lucite PNDA
MOX all energies |  |  | 
HALEU all energies |  |  | 
High-priority list identified at TEX 2.0 meeting in May 2023

## Slide 30
Sensitivity results
Sensitivity to 181Ta scattering.
This figure includes the application A01 (largest Ta scattering sensitivities).
Also includes PU-MET-FAST-045-006 and PU-MET-MIXED-003-001.
These are the specific cases with highest 181Ta inelastic scattering.
Series labeled P03 is a simple proposed design.
  Pu cuboid with Ta reflection.

## Slide 31
Methodology
Similarity metrics are useful at comparing two models
  Traditionally an application and a benchmark
  Also applications to each other (see previously slide)
  And applications to proposed experiment designs (focus of this work)
All similarity metrics in this work utilize sensitivities (Sk,x) of the system keff to a nuclear data (x) calculated via
  x can be a nuclide reaction cross-section, ν, etc.
The uncertainty in keff due to nuclear data uncertainty:
  S is a vector of sensitivities
  T is the transpose of the vector
  C is the nuclear data covariance matrix

## Slide 32
Methodology
Esum similarity metric
  A and B are two models
  Esum is a measure of the shared sensitivities
ck similarity metric
  A measure of the shared nuclear data uncertainty
For all similarity metrics, the sensitivity vectors and covariance matrix can be filtered to only include reactions of interest
  For this work, isolated data of Ta181 elastic and inelastic scattering are investigated
  There are other similarity metrics that can also be of use, especially when utilizing filtered data

## Slide 33
Methodology
There are many distance metrics in mathematics
Manhattan distance (M)
  Sum of absolute value of difference in vector elements
  Red, blue, and yellow in image at right
Euclidean distance (ED)
  Sum of squares of the vectors
  Green in image at right
Weighted sum of squares (WSS)
  Similar to ED, but imposes a weight of the geometric mean
  For this work the results are scaled to
Taxicab geometry, Wikipedia
A
B

## Slide 34
Methodology
What is a good match between two models?
For all metrics used here, higher numbers mean a better match
  Might seem non-intuitive for M and ED, but I did some normalization
For all but WSS, 1 is a perfect match
  For WSS, there is no upper limit, but higher is better
For ck, criticality safety applications often say that a value of 0.9 or higher is a “good” match
Metric | Perfect match
Esum | 1
ck | 1
M | 1
ED | 1
WSS | N/A, higher is better

## Slide 35
Results: ck
PMM003-001 has ck values slightly below 0.9
  Still very useful for validation!
PMM045-006 also has high ck values
  But there are reasons why this benchmark might not be the best for validation
As expected, designs with lower Ta thickness (<1.27 cm) have lower ck for Thales_App_01
  As thickness increases, it reaches 0.95 and seems to plateau
Thales_App_02 is highest when 1.27 cm thick Ta or less is present
Thales_App_03 falls between the other two applications
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_22_e80_e81JSON_51_nof_noi
1 3 5 7 8 9 2 4 6
These numbers go from 1 (least Ta mass) to 9 (most Ta mass)

## Slide 36
Results: D Opt
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_21_e80_e81JSON_51_Ta181in_noi
Using 8.1 covariances
Shows importance of case with most Ta
Also shows that any of the cases have a fairly large D Opt by themselves
Large drop-off in cumulative D Opt after first experiment

## Slide 37
Results: summary
Many of the metrics yielded similar results, so not shown
  Available in backup slides
At right is the best configuration for each metric
  Red are the four configurations that were selected: “zoided” 1.27, “zoided” 2.54, nominal 5.08, nominal 8.89 cm
Best configurations (cm Ta thickness) for each metric

## Slide 38
Results: summary, App 1
Another way to think of the results:
  Plot at right has value for each metric
  Compare:
    Blue to orange: how high is the down-selected configurations compared to the best value of all models run?
    Blue to green: how much better is the down-selected configurations compared to existing benchmarks?
  Note: results were normalized for WSS

## Slide 39
Results: summary, App 2
Another way to think of the results:
  Plot at right has value for each metric
  Compare:
    Blue to orange: how high is the down-selected configurations compared to the best value of all models run?
    Blue to green: how much better is the down-selected configurations compared to existing benchmarks?
  Note: results were normalized for WSS

## Slide 40
Results: summary, App 3
Another way to think of the results:
  Plot at right has value for each metric
  Compare:
    Blue to orange: how high is the down-selected configurations compared to the best value of all models run?
    Blue to green: how much better is the down-selected configurations compared to existing benchmarks?
  Note: results were normalized for WSS

## Slide 41
Results: Manhattan distance (Ta181 inelastic)
Filtered on Ta181 inelastic
Shows that for Thales_App_01, thick Ta reflection is best
As expected, thin Ta for Application 2 and moderate amount for Application 3
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_21_e80_e81JSON_51_Ta181in_noi
Filtered on Ta181 inelastic
1 3 5 7 8 9 2 4 6
Run 21 + 23 but for BLO

## Slide 42
Results: Manhattan distance (Ta181 elastic)
Filtered on Ta181 inelastic
Shows that for Thales_App_01, thick Ta reflection is best
As expected, thin Ta for Application 2 and moderate amount for Application 3
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_23_e80_e81JSON_51_Ta181el_noi
Filtered on Ta181 elastic

## Slide 43
Results: Euclidean distance (Ta181 inelastic)
Same findings as Manhattan distance
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_21_e80_e81JSON_51_Ta181in_noi
Filtered on Ta181 inelastic

## Slide 44
Results: Euclidean distance (Ta181 elastic)
\\slip.lanl.gov\NCERC\Software\whisper-tk\Output\Thales_23_e80_e81JSON_51_Ta181el_noi
Filtered on Ta181 elastic