## Slide 1: Activation Library Use in Target Design and Analysis for Radioisotope Production
November 6, 2025
January 9, 2026 | Nuclear Data Week “2025”
William (B.J.) Marshall
Radioisotope Science and Technology Division

## Slide 2: Outline
HFIR description and operations
Radioisotopes produced at HFIR
Codes, tools, and data
Conclusions

## Slide 3: High Flux Isotope Reactor (HFIR) description and operations
HFIR is a unique research reactor
  Central flux trap intended for transplutonium production
  Beryllium reflector with numerous irradiation facilities
  Beam tubes for neutron scattering
Cylindrical core approximately 2’ (~60 cm) tall and 15” (~38 cm) outer diameter
  5” (12.7 cm) OD for central flux trap
85 MW thermal power, ~23 day cycles
  Peak thermal flux ~2 × 1015 n/cm2 s in flux trap
  Thermal flux in the reflector ranges from about 5 × 1014 to 1 × 1015 n/cm2 s

## Slide 4: Radioisotope products
252Cf: Part of the original and still primary mission of HFIR for the DOE Isotope Program
  Generated in the flux trap from Cm target material provided by Savannah River
238Pu: Heat source for NASA RTGs
  237NpO2 feed material from INL originally generated at Savannah River
  Irradiation for multiple cycles in the Be reflector
Anything else DOE Isotope Program desires
  Industrial sources for radiography and other applications
  Medical sources for therapy, diagnostics, or both

## Slide 5: Target design, analysis, and qualification radiation transport tools
TCOMP
  Prediction of 252Cf production
  Nuclear data have been tuned to give accurate predictions based on past campaigns
ISOCHAIN
  Simplified, user-friendly code for approximate activation and decay calculations
  Nuclear data derived from “Lockheed Martin” Chart of the Nuclides or input by user
These tools do not directly use released, evaluated nuclear data.
MCNP/ORIGEN
  Flux tally from static MCNP calculation input to ORIGEN for activation and decay calculation
  LANL-generated ACE data for MCNP and ORNL-generated AMPX data for ORIGEN
HFIRCON
  Coupling of MCNP with ORIGEN to do cycle simulation including depletion, activation, decay, heat generation
  In both standalone ORIGEN and HFIRCON, the JEFF-3.0 activation library is the primary source of nuclear data for depletion and activation.
“Fit-for-purpose” or “Low-fidelity” tools
“General purpose” or “High-fidelity” tools

## Slide 6: Conclusions
Radioisotope production calculations would benefit from a new activation library, especially if it is consistent with ENDF data used in transport calculations
ORNL radioisotope production predictions and measurements may be helpful in providing validation for activation library evaluations
Other HFIR users may also be able to provide feedback
  Neutron activation analysis laboratory
  Fuel irradiation
  Other materials irradiations

## Slide 7: Thanks for your time and attention!