## Slide 1: Status of ENDF/B-VIII.0/b4 for Light-Element Evaluations
G. M. Hale and M. W. Paris
Group T-2
Los Alamos National Laboratory
May 4, 2017
Mini-CSEWG
4-5 May 2017
Los Alamos National Laboratory
LA-UR-16-28727

## Slide 2: n+p:
Changes from VII.1 for 0 ≤ En ≤ 20 MeV are within uncertainties
New data are fit well
Small change in thermal capture cross section had large effect on solution criticals
R-matrix analysis presently goes to 100 MeV
Still to do: Covariances on differential cross sections (c.m. and lab); Extend analysis to at least 200 MeV

## Slide 3: n+9Be:
Still to do:
Improve description of (n,2n)2a breakup cross section in R-matrix analysis using hyper-spherical coordinates
Covariances

## Slide 4: n+6Li:
Fitted (unsmoothed) GMA standard cross section in place of (n,t) data
Still to do: Covariances, capture cross section

## Slide 5: n+12,13C:
n+C elastic cross section about 2% higher than VII.1 near 2 MeV
Seems to have little effect on benchmarks
Still to do:
  Covariances
  Improve 13C(n,g) xs
  Add 13C(n,n’g) files
Notes: Need to plot revised cross sections from soln 10e

## Slide 6: n+10B:
Fitted (unsmoothed) GMA (n,a) cross sections in place of data up to 1 MeV
Made extensive changes in (n,a) and total cross sections above 1 MeV
Still to do: Covariances

## Slide 7: n+16O:
All data well represented
Little change in critical benchmarks
Capture cross section improved (? need astrophysics feedback)
Still to do: covariances (calculated up to 7 MeV, but not formatted)
5/3/17 | 9
Los Alamos National Laboratory

## Slide 8: Analyses for the Light-Element Standards
n-p scattering: N-N analysis goes up to 100 MeV; plan to to extend it to 200 MeV.
6Li(n,t): 7Li analysis gives excellent fits (c2/n=1.36) to data up to 4 MeV.
10B(n,a): 11B analysis gives excellent fits (c2/n=1.14) to data up to 1 MeV.
Natural carbon: sel increased ~2% at 2 MeV, as already shown.