## Slide 1: Coupling Analysis in LtB
Lucy Lin
3rd AI/ML for EIC Hadron Pre-injectors Collaboration Meeting
Oct 20-22, 2025

## Slide 2
OPPIS (Optically Pumped Polarized Ion Source) Since 2000, H- ion source has been upgraded several times to higher intensity and polarization.
Prior to Run-13(2013), the ECR-type source was used to generate the primary proton beam. The ECR-source was originally developed to operate on DC current and placed inside a super conductive solenoid (SCS).
In 2013, the ECR-source was replaced with a high-brightness source “Fast Atomic Beam Source” (FABS) operating in a pulsed mode. The FABS-source improved source parameters such as beam current density, angular divergence and stability.
In 2022, We reduced the LEBT portion of the beam line by about 5feet, modify polarization part of OPPIS (He-cell, Rb-cell and Na-cell) and the extractor-transformer system.
Optically Pumped Polarized Proton Source
D. Raparia 25/06/18

## Slide 3: Optically Pumped Polarized Ion Source
to LEBT
OPPIS produces 3-5 mA Polarized H- ion pulse current
81-84% polarization @200 MeV , 0.5 mA
D. Raparia 25/06/18
Notes: General Introduction of the OPPIS source.
All three main blocks of the OPPIS were developed with either minor or major upgrades

## Slide 4: Polarization Transfer Technique
He-cell
Rb-cell
SC-solenoid
Sona-transition with 3 corr. coils in it
Na-jet
&
Solenoid
H0
H-
Polarized light
Polarized electron
Polarized proton
Production of circular polarized tunable wavelength (~795nm) laser beam
Polarization of the outer electron of Rb-atom by laser
Ionization of hydrogen atom at He-cell
Production of electron spin polarized hydrogen atoms by capture electron from Rb
Polarization transfer from electron to proton by “Sona-transition” technique
Ionization of hydrogen atoms by capture of second electron in Na-jet for acceleration
D. Raparia 25/06/18
Solenoid scan

## Slide 5
OPPIS
RHIC, NSRL
500 A, 400 s, 0.15 -1 Hz
85% polarization
Word highest intensity pol. H- source
Polarization Direction Manipulation
OPPIS
Magnetron S-2
Magnetron S-1
To RFG
23.7 deg. dc dipole magnet
RFQ
Slits for energy discrimination
Spin Rotator
Switching Magnet
Chopper
D. Raparia 25/06/18
The Low Energy Beam Transport (LEBT) lines combine three beams. The first line is the polarized OPPIS beam-line and the second and third are the high-intensity unpolarized beam-line.
Magnetron S-1,2
BLIP, NSRL
135 mA, 1000 s, 6.67 Hz
Word highest peak intensity H- source
LEBT

## Slide 6: OPPIS / LEBT / MEBT
Corrector scan

## Slide 7: MEBT corrector scan
Found that polarities of lmt-th1 and lmt-tv1 were reversed in MEBT

## Slide 8: MEBT corrector scan
Turn solenoid in Na-cell off and on, not significant change in behavior

## Slide 9: MEBT corrector scan
Weird behavior of lmt-th2 and lmt-tv2? No real explanation as of now

## Slide 10: MEBT corrector scan
Turn solenoid in Na-cell off and on, not significant change in behavior

## Slide 11: HEBT / LtB
Q7 + Q17 scan
profile observed

## Slide 12: Linac to Booster (LtB)
Takes 200 MeV H- from Linac
Three main sections:
  1) HEBT to start of 126 bend
  2) 126 bend (DH2 – DH5)
  3) end of 126 bend to C5
Fully stripped protons after foil after C5

## Slide 13: HEBT quad scan

## Slide 14: HEBT quad scan

## Slide 15: HEBT quad scan

## Slide 16: HEBT quad scan

## Slide 17: HEBT / LtB
Q9 + Q8 scan
profile observed

## Slide 18
LtB quad scan

## Slide 19
LtB quad scan

## Slide 20
LtB quad scan
Traditional emittance calculation gives very different answers at MW99 and MW107 for horizontal
Dispersion? Coupling? Experiment to measure?
Skip parabola fitting which uses thin lens approximation, use full transfer matrix from currents (accuracy of transfer function? Distances in model? Etc.)
Dispersion here

## Slide 21
LtB quad scan
MW | alpha | beta | gamma | emittance
99 | -1.20 | 5.80 | 0.42 | 1.65
107 | 12.98 | 9.25 | 18.33 | 154.6

## Slide 22
LtB quad scan
MW | alpha | beta | gamma | emittance
99 | 5.57 | 12.66 | 2.53 | 0.46
107 | 4.96 | 14.18 | 1.81 | 0.41