## Slide 1: Reinforcement Learning in AGS Bunch Merge
Cornell Collaboration Meeting
10/20/2025
Yuan Gao

## Slide 2: AGS Bunch Merging
Before transferring to AGS, beam bunch is split longitudinally to reduce the space charge effect: -> reduce emittance -> improve polarization
Bunches are later merged before AGS extraction;
Requires expert tuning of many parameters:
  Prone to drift over time;
  Time consuming;
Method: Reinforcement Learning (RL)
Soft Actor-Critic (SAC)
Controls: RF voltages, phases
Goal: Obtain a “good” merged bunch profile:
  Emittance preservation:
    No particle lost; Gaussian shape;
    No “baby” bunches;
  Stable final bunch profile:
    Not shifting left to right; Not bouncing up and down;
    Merged in the center;
RF voltage and phase during merge
Merge signals are captured by the Wall Current Monitor (WCM) which generates voltage vs time signal and displayed in a scope.
Each of the mountain range data traces is separated in time by N cycles vertically.
end of squeeze & start of merge
end of merge
start of squeeze

## Slide 3: Reinforcement Learning in Bunch Merge
Reinforcement learning is a machine learning paradigm where an agent learns to make decisions by interacting with an environment and receiving rewards for its actions, aiming to maximize cumulative reward over time.
For this bunch merge experiment:
  State:
    Final bunch’s center position;
    Final bunch length;
    Bunch center variation;
    Bunch length variation;
  Action: RF voltages to set
  Reward: Weighted sum of bunch length, center variation and bunch length variation. The smaller the sum, the higher the reward.
Require many training data at the beginning
Quick inference time, good for online continuous control

## Slide 4: Simulation Results
A Julia simulator was build using the Run 22 data
Action: Two RF functions with 6 control points.
2000 initial random samples, trained 40 k steps.
After training, the average reward is around 0.7
Voltage
Time after AT0
Agent learned RF functions similar to the ones used in the actual system

## Slide 5: Bunch Merge Operations
Merge operations happens from 910 ms – 1630 ms after AT0, on the AGS “flattop”.
Cavities used for 2 to 1merge: B, BC, and C are used for h=12 and JK and K for h=6.
Each group of cavities takes the same phase and voltage functions.
WCM signal monitor range is 650 ms – 2050 ms, covers the entire process (squeeze, merge and rebucket):
  Contains 80 traces, each trace is a bunch profile;
  Trace interval is 17.5 ms, shows how the bunch shape evolves with time.
Need a way to handle the merge traces data.
AGS Scope Data
80 traces, 17.5 ms interval
Merge in the AGS “flattop”

## Slide 6: Saving the WCM Signals
Signals shown in WCM are configured by the scope settings: where to start, how long the sequence, etc.
Those settings are copied to a local scope to ensure the same sequence will be focused.
scopelecroy6100Man will get triggers to save the local scope data to files, also log some statistics.
pet: /AGS/Instrumentation/wcm/Scope
Copy settings
Local scope
AGS scope
Triggers
scopelecroy6100Man

## Slide 7: Processing Bunch Data
80 arrays, each contains around 50k points.
The useful data is ~ 1%.
Some useful preprocessing steps: smoothing and down sampling.
……
Extract: center pos, bunch len, center variation, bunch len variation
Last trace

## Slide 8: Experiment Workflow
The observable is the WCM signals, which is saved to files on every AGS cycle.
Each file contains 80 traces (arrays) with 50k points each. The last ten traces are used to extract the merge information.
Based on the information, the agent send a set of RF voltages to the machine and then collect information from the WCM signals for the next action.
RF settings:
5 cavities with 6 voltages
Accelerator system
RL Agent
RMS bunch length,
Center variation,
Bunch length variation
WCM signals
Saved to files on every cycle
Generate

## Slide 9: Experimental Results
Initial
RL settings
Operation settings
Final bunch length
Bunch length variation
System logging bunch data during the RL optimization
The RL agent was able to quickly correct the merge and maintain it
We first intentionally break the merging process to test
Comparable to operational merges

## Slide 10: RL Agent Action and Optimization
The RL agent was able to locate the optimal solution in one step and maintain it.
All actions converge in one step
Both the bunch length and bunch variations were optimized effectively.

## Slide 11: Incentives for a Beam Property Manager
The goal is to publish beam parameters, such as bunch length, dpp, emittance, etc., in real time, for any beam.
Those parameters will also be logged, so they can be accessed later for further analysis.
Also give some options to explore the “what if” scenarios.

## Slide 12: Incentives for a Beam Property Manager
The goal is to publish beam parameters, such as bunch length, dpp, emittance, etc., in real time, for any beam.
Those parameters will also be logged, so they can be accessed later for further analysis.
Also give some options to explore the “what if” scenarios.
Accelerator system
ML Agent
Can see the evolution of the bunches
It’s also useful have those parameters available to check, especially when there is beam experiments.
For ML applications
Manager
Settings
Get data

## Slide 13: Two Calculation Methods
Measure Synch Freq
Read from systems:
Particle species, charge, energy, RF volt, Rev freq, B dot, etc.
Explore different setups:
Input different RF volt
Calculate & Publish:
Corrected RF volt, Emittance, dpp, etc.
Calculate & Publish:
Synch Freq, Emittance, dpp, etc.

## Slide 14: Two Calculation Methods
Measure Synch Freq
Read from systems:
Particle species, charge, energy, RF volt, Rev freq, B dot, etc.
Explore different setups:
Input different RF volt
Calculate & Publish:
Corrected RF volt, Emittance, dpp, etc.
Calculate & Publish:
Synch Freq, Emittance, dpp, etc.

## Slide 15: Examples: 4 – 2 – 1 Merge
Number of bunches
Bunch length
Emittance
Momentum spread
Two methods agree with each other

## Slide 16: Examples: 3 – 1 Merge
Number of bunches
Bunch length
Emittance
Momentum spread
Two methods agree with each other

## Slide 17: Examples: General Beam
Bunch length
Number of bunches
Emittance
Momentum spread

## Slide 18: Acknowledgement
Kevin Brown, Vincent Schoefer, Keith Zeno, John Morris, Andrei Sukhanov, Michael Costanzo, Shruti Tajne, Md Latiful Kabir, Weijian Lin
Georg Hoffstaetter de Torquat, Jonathan Unger, Eiad Hamwi, Matthew Signorelli, David Sagan
Auralee Edelen, Ryan Roussel
Malachi Schram, Armen Kasparian, Kishan Rajput
Yinan Wang

## Slide 19: Backup Slides

## Slide 20: RF Phase Control
The RF system regulates the phases in such a way that the geographic phases differences among cavities are handled.

## Slide 21: Proton Merge Phase Scan
Emittance
Center position
Bunch length
Bunch variations