## Slide 1: AGS Horizontal Resonance Strength Correction (With special attention to low energy)
3rd AI/ML for EIC Hadron Injectors Collaboration Meeting
10/21/2025
V. Schoefer, with help from E. Hamwi

## Slide 4
Archaeological evidence of an ancient BNL-Cornell
collaboration

## Slide 5: Outline
Polarization and resonances in the AGS
Polarization measurements and the difficulty of optimization
Indirect lines of improvement
  Optics and improvement of corrections
  Locating unknown sources of depolarization
  Improved timing of corrections (later talk)
Measurements at low energy
  Single, slow resonance crossing

## Slide 6
RHIC Accelerator Complex
Tandem van de Graaff
~1.2 km
 | Au | Pol. Protons
Linac (H-) | -- | 1.1*
Booster | 1 | 2.3
AGS | 10 | 23.8
RHIC | 100 | 255
Typical Top Energies [Total, GeV/N]
 | Circumference [m]
Booster | 201
AGS | 807
RHIC | 3833
Accelerator Rings
6
Heavy Ions | Protons
E-beam Ion Source (EBIS) | OPPIS (polarized)
Tandem van de Graaf | High-intensity H- (unpolarized)
* The “200 MeV” Linac give 200 MeV kinetic energy

## Slide 7: RHIC Polarized Beam Complex
PHENIX
AGS
LINAC
BOOSTER
Pol. H- Source
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
2 Siberian Snakes/ring
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR
AGS Polarimeter
Spin flipper
 | Max Energy [GeV] | Pol. At Max Energy [%] | 
Source +Linac | 0.2 | 82-84 | 
Booster | 2.5 | ~80-84 | 
AGS | 23.8 | 67-70 | p-Carbon
RHIC | 255 | 55-60 | Jet, full store avg*
 | Relative Ramp Polarization Loss (Run 17, full run avg)
AGS | 17 %
RHIC | 8 %
* Includes both ramp loss and store decay

## Slide 8
Depolarizing resonances in AGS
Frequency of particle motion in the focusing magnets is (mostly) ENERGY INDEPENDENT
Precession frequency of spin motion is in general ENERGY DEPENDENT
If particle sample fields with a frequency equal to the spin precession frequency: spin motion
“Snakes”, helical dipoles, help manipulate the spin motion with local rotations to avoid that condition (at the cost of complicated fields/optics distortion)
Injection
Extraction
Spin tune gap
Hor resonance crossings
Tune
jump
(pause tune jump near transition)

## Slide 9
Depolarizing resonances in AGS
Spin tune gap
Hor resonance crossings
Tune
jump
HORIZONTAL resonances are still active, most recent efforts focus on improving these weak but numerous resonances
VERTICAL resonances are stronger and are completely avoided by the snakes + high vertical tune (or are they?....)

## Slide 10: Partial snake resonance suppression with betatron coupling
BUT:
There are 82 such linear algebra problems to solve
AND:
Phasing between skew quadrupole terms and snake terms varies wildly resonance to resonance
AND:
Correction vectors are frequently parallel, especially near strong vertical intrinsic resonances
We have 15 skew quad ‘knobs’ to form independent corrections at each energy
Skew quad correction vectors (last six hor resonances)
Phase offset chosen so that snake drive term is purely real
Red circle marks the same skew quad in each frame, phase changes rapidly from resonance to resonance
In principle minimizing resonance strength (calculated with SPRINT) and coupling (two complex numbers) takes 4 skew quads

## Slide 11: Calculated correction waveforms
Pulsing the skew quads with 1 ms rise, 1.3 ms flattop and 1 ms fall allows changing currents quickly to accommodate new correction vectors every resonance
  Also avoids having skew fields during strong vertical intrinsics (tracking showed small polarization losses at these with skew quads powered)
Calculated resonance strength reducible to zero at almost every resonance
  Tune shift from coupling < 0.005
11
1.3 ms
1.0 ms
Each trace= 1 skew quad
1.0 ms

## Slide 12: Ramp implementation and Polarization
Correcting only resonance above transition
Skew quad current
Early attempts:
  High energy pulses only (avoids difficult low energy optics)
  Omitting several pulses with too large orbit excursions
  Within statistical error of model in terms of gain factor over uncorrected polarization
Each trace= 1 skew quad

## Slide 13: Low energy resonance correction
Benefit from low energy pulses (GƔ < 15) expected to be ~3-4%
Measured benefit ~1%
In some cases negative, less reliable correction
Intentionally omit
Near transition
Correcting scaling, full cycle
Skew quad currents
Orb correction also enables broader scans
Each trace= 1 skew quad

## Slide 14: What’s wrong with low energy?
Model error is highest at low energy
  Snakes
  Orbit feed-down effects
    Huge orbit excursions (+/- 2 cm, non-negligible sextupoles)
    Not that great at higher energy (+/- 1 cm)
Qx closer to Qy: residual coupling from errors will change the drive term addressed by the skew quads
Near GƔ = 9 =0+Qy, very small correction strengths required
  Implies structurally easy to provoke a strong resonance
Sample horizontal orbits (at BPMs)
High energy (ɣ=25)
Low energy (ɣ=5)
Tunes
Correction currents

## Slide 15: Orbit effects
AGS Hor Orbit Corrector Currents
Before correction
After correction
C20
G20
NO ROUTINE GENERALIZED ORBIT CORRECTION IN AGS OR BOOSTER
Centering using orbit steerers accomplished to <2 mm at 13 of 15 locations
Correction objective only at skew quad locations
Outliers at C20 and G20: too demanding on orbit correctors (omitted from most corrections)
Global orbit (at BPMs) not significantly better
Correction in the model above 99% still possible without C,G20
Survey measurement completed last year Magnet realignment planned for long shutdown after end of RHIC run
Discussing adding correctors, upgrading existing correctors

## Slide 16: Orbit effects
Targeted correction implemented in Run 24
  ONLY horizontal
  ONLY to center in skew quads (insufficient strength for global correction
  ONLY at mid-to-high energies
    Avoided model complications at low energy
    Operational difficulty defining and moving to a ‘design’ orbit
Horizontal orbit offsets cause
  beam loss during skew quad pulses
  beta-beat from sextupoles
VERTICAL excursions in sextupoles lead to additional unknown horizontal resonance terms from coupling
  Not at all accounted for in the correction
  Spin esonance drive from feed-down is energy dependent
    (i.e. some resonances might be untouched, others could be highly reinforced

## Slide 17: Single resonance crossing, high energy
At nominal acceleration rate (dGɣ/dθ =4.7 x 10-5), max polarization loss from a single resonance is 0.1-0.5%
  too small to to measure individually
Configure a crossing at fixed energy: just above nominal extraction, with ramped horizontal tune and very slow ramp rate (>100x longer)
Parameter | Value
Gɣ | 45.74
dp/p (full base) | 1x10-3
Chrom ξx | 4
ΔQx | 0.08
Tune ramp length [ms] | 200
Crossing rate (⍺) | 1.7 x 10-7
Resonance crossing
Slow crossing gives measurable 20-25% relative polarization loss

## Slide 18: Single resonance crossing, high energy (Gɣ = 45.74)
Select three skew quads with good relative phasing
K07 in phase with snakes
E05 180o from K07
B07 orthogonal to snake drives
Skew quad arrow length is full current range of supply (arrow head is positive)
B07
K07
E05
Snake drive
Resonance ‘portrait’ at Gɣ = 45.74
Polarization response to skew strength
At high energy, single crossing shows GOOD AGREEMENT WITH SPRINT MODEL for small resonance strengths, worse with increasing strength
Phasing of skew quads is as expected
  Correcting current is accurate
Demonstration of total correction
Pf/Pi (uncorrected)
0.79 +/- 0.02
|ε|meas = (7.9+/-0.4)x10-5
|ε|mod = (7.6+/-0.5)x10-5
|ε| = Res strength
Measured uncertainty is statistical
Model uncertainty is systematic from uncertainty in emittance
Skew quad current (A)

## Slide 19
Single resonance crossing, Low energy, (Gɣ = 7.24)
Energy here chosen to be Ggamma = 7.24
BELOW first major depolarizing resonance (Ggamma = 9)
Advantage is that polarization is maintained even without snakes, so snake on/off comparisons can be made
Analyzing power of polarimeter is unknown
  Results reported in terms of raw asymmetry (proportional to polarization, good for relative measurements)
  Tune sweep of 0.08 units in 200 ms
Qx
Time
AGS MM B-field (kG)
GƔ=45.5
GƔ=7.24

## Slide 20: Skew quad scans, low energy, SNAKES ON
Scan two skew quad strengths expected to be:
K07 -> In phase with snake term
I07 -> out of phase with snake term
Comparison with full Bmad tracking (with idealized “flat” orbit)
Reasonably good:
Accurately predicts maxima (so the phases are well predicted)
Disagrees (for K07) when resonance drive is large
  More depolarization predicted by model
  Might be driven by orbit effects via feed-down
Parameter | Value
Gɣ | 7.24
ΔQx | 0.08
Tune ramp length [ms] | 200
Crossing rate (⍺) | 1.7 x 10-7
Hor emit | 2 um (rms, norm)
Long. emit | 0.5 eVs
COMPARISON WITH Bmad
Bmad = Full 6D tracking simulation of res crossing

## Slide 21
Skew quad scans, low energy, SNAKES ON
21
Comparison with SPRINT predictions shows basically 90° phase error
Effects of K07 and I07 look swapped
It’s the MODELs that don’t agree with each other
  Bmad agrees with data
  SPRINT calculation doesn’t
In SPRINT code
Absolute phase is not defined
Response matrix determined by numerical differences from small changes in each skew quad (forms the response matrix), possible this is buggy
Resonance calculation itself is probably OK
Model of snake optics implemented in SPRINT is very crude, worst at low E
COMPARISON WITH SPRINT
Heads up SPRINT-to-Bmad comparisons need to be made over full energy range (simple, single skew quad only over full energy, then snakes e.g.)
Previously only done near top energy (Bmad AGS was not mature)
SPRINT = resonance strength calculation  Froissart-Stora estimate of depolarization

## Slide 22: Resonance crossing without snakes
Snakes off in both Bmad and AGS
Residual drive principally from sextupole feed-down of vertical orbit
Bmad closed orbit fit to realistic measured orbit using only the orbit steerers (not survey misalignments)
Operational chrom currents
H,V = (38 A, 31 A)
Model appears to accurate predict closed orbit effects (at least in the absence of snakes)
Horizontal
Vertical
Bmad spin tracking
Measured depolarization is 4% +/- 1%
Good agreement with orbit fit model

## Slide 23: Individual sextupole offsets
Local vertical bump at location of individual sextupole shows measurable effect on the crossing efficiency
Polarization transmission gets both worse and more erratic when the drive term is made larger
Local bump at G13 sextupole, snakes are on, so change is relative to the snake drive term: +/- 5 mm range limited by p.s.
Difference orbit (local G13 bump)

## Slide 24: AI, ML, Polarization and their difficulties
One polarization measurement takes ~5 minutes for a 2% precision (precision is proportional to sqrt(time of measurement)
In general polarization measured at end of ramp, after all resonances crossed
Setup of individual resonance crossings one by one is time consuming
  If errors are time dependent (over days,weeks), repeated optimizations are prohibitively expensive
Direct AI/ML based attack on polarization seems unlikely
Effort could be put on attacking the elements of the problem
  Orbit and optics effects (Lucy’s talk re: orbit response)
  Refinement of model inputs: snake and main magnet models (Eiad’s talk)
AGS orbit, tune and chrom controls is archaic in implementation and (in the case of the orbit) insufficient to efficiently maintain a full developed polarized beam program
  Ripe for digital twin effort
  What to do?

## Slide 25: AGS Model/Digital Twin: necessary elements
Most efforts so far have been to refine model inputs
Not a lot of effort on model infrastructure and control capability
  we shouldn’t wait for a perfect model to implement control
Current model is sufficiently precise to implement orbit control: will improve model agreement just to eliminate feedown
What do we have to consider:
  Implement design/trim functionality in control software of orbit/optics elements: orbit correctors, BLWs, tune and chrom supplies, snake compensation quadrupoles
  Define a design orbit as a function of time in cycle: design orbit defined by BLWs (injection, snake compensation, extraction), “design” component of correctors, radial steering function
    Radial steering either needs to be calibrated and included, or subtracted out (subtracted out is RHIC approach).
  Complicated by diversity of controls: sometimes (x,y) pair functions, sometimes, trigger+amplitude. Gamma-jump is gauss time, not real time
  Will require considerable re-tuning and re-optimization for polarized protons: present setup is accumulation of 20 years of unconstrained individual tweaks
ANY effort to improve overall control or modeling will be significantly hampered by present state of orbit control in the AGS (as evidence I offer every effort so far)

## Slide 26: Parameters of an AGS Model
Particle | Design Optics | Design orbit
Z | Tune quads (2) | Inj BLW (2)
A | Chrom sext (2) | Csnk BLW (3)
Ɣ | Snake quads (7) | Xtrcn BLW (2)
E0 | Ɣ-jump quads (6) | Rad steering (1)
 | Ɣ-jump time | Correctors [design component] (up to 96=48x2 planes)
 | Helical dipoles (2) | 
6 scalar values
17 design optical functions
8 design orbit function + 96 correctors
Trim elements
Stop-band corrector (N-poles) ~5-10
Coupling skew quads (1)
Spin res skew quads (15)
Correctors [trim component] (up to 96=48x2 planes)
~20 functions + 96 correctors
+ Slow extraction elements for HEET
Red are scalar
Black are functions
“Function” = linearly interpolated (x,y) pairs except Ɣ which is combo of cubic and linear
RF elements
RF voltages (12)
Harmonic table: governs changes of h in each cavity

## Slide 27: Are horizontal resonance all that’s left? (Hint: probably not)
Nominally, every vertical resonance is avoided*
These kinds of resonances produce a polarization “profile”, less polarization on the transverse outside of the beam
If they were GONE, the profile would be flat
--- it isn’t
*the few early crossings *can* be avoided, polarization benefit too small to measure, intensity suffers
Polarization profile
Transverse position
Intensity profile
Polarization

## Slide 28: AGS Vertical Polarization Profile Comparisons
(Simulation by Yann)
JQ off
JQ on
The vertical polarization profile is developed between Gγ=13.5 and 31.5, across 12+, 36- and transition.
Acceleration with purely horizontal resonances and no betatron coupling would develop ONLY a horizontal profile
Vertical profile could develop from
Uncorrected vertical resonances
Horizontal resonances + mixing of hor profile into vertical via coupling
  But we don’t observe significant emittance swapping
Development of vertical profile is a totally open question
“Ry” is a measure of profile steepness: 0 = flat, no resonances

## Slide 29: Remaining depolarization: where does it go? Misalignments?
Resonance associated with vertical motion probably still important
AGS Magnet survey/realignment effort
  all 240 AGS main magnets are combined function (dipole + quadrupole)
  No global realignment since the 90’s (smaller targeted effort in 2012)
  Needs simulation assessment of impact on depolarizing resonances (ongoing)
  Also puts orbit closer to reach of existing (or moderately upgraded) correction magnets
  Realignment planned for post Run 25
Could use tools from EIC/HSR efforts
  Resonance “portraits” have been useful in optimizing lattice design for HSR
  Could be used to study impact of machine error on resonance structure
Qy
EIC HSR Lattice optimized to reduce resonance lines (3He)
AGS Main magnet misalignments
(HSR modeling by Eiad Hamwi)

## Slide 30: Instrumentation and Beam control upgrades
Turn-by-turn BPMs
  Fast turnaround optics measurements
  Driving term localization (e.g. linear coupling)
  Complementary to ORM
Tune meter Baseband tune (BBQ) pickup
  Much higher signal to noise
  Important for horizontal precision (high chrom, low signal)
  Possibility of feedback/feedforward stabilization
  Used to great effect at RHIC
RHIC TBT Beta Function Measurement
Standard TBT BPM
BBQ signal

## Slide 31: Brookhaven Accelerator Complex Scheduling
End of RHIC physics program nominally: Dec 2025
Possible extension of (up to) order 6-8 weeks (very ambiguous)
Extended operation all involved polarized protons in the AGS
Linac (polarized protons) become available for studies early-mid Nov (independent of RHIC run extension)
Last extended running for a while
Likely to be very tightly packed schedule (”no snake” studies are much easier to work in)
The Middle Ages (the period between RHIC shutdown and start of EIC)
NSRL operations in Booster continue as normal (study time negotiable)
AGS planned to operate (on average) two months a year
  Longer operations with longer shutdowns probably preferable (4 months every 2 years, e.g).
  EIC related priorities are demonstrating
    polarized He-3
    general polarized beam developments
  Other programs proposed but not yet planned: HEET, AtR test beams

## Slide 32: Summary
Remaining sources of depolarization in AGS are likely:
Incomplete correction of low energy horizontal resonances
Disagreement between Bmad and SPRINT needs followup
Not-well-understood development of vertical polarization profile
Closed orbit feed-down effects are low-hanging fruit for correction efforts
Direct removal of depolarizing drive terms (sextupole feed-down)
Simplifies every modeling effort going forward
AGS seems for implementation of Digital Twin infrastructure (at least up to the point of orbit control)