## Slide 1: The successful partnership between C-AD and STAR to fully leverage RHIC’s versatility
STAR 25-year celebration
17 December 2025
Wolfram Fischer Deputy Associate Lab Director for Accelerators, Nuclear and Particle Physics Chair, Collider-Accelerator Department
Notes: 30 min, ~20 slides

## Slide 2: Ingredients to a successful partnership
Ambitious goals drives performance
  Luminosity
  Polarization
  Large range of species combinations / energies
  Beam Energy Scan
From early days consistent STAR support for Machine Development and APEX
  Machine development for short-term performance increases
  APEX for longer-term performance increases
Good communication
  C-AD understood STAR goals, STAR understood what RHIC can do

## Slide 3: Contents
Design – ions, polarized protons, flexibility
Performance evolution
Accelerator Science and Technology legacy

## Slide 4: Life cycle of a large accelerator facility
RHIC (this talk)
EIC
Pre-project R&D [few decades]
Operation annual ops cost ~10% construction cost [few decades]
Re-use for next facility or shut-down
Construction [~decade]

## Slide 6: RHIC Design

## Slide 7: ISABELLE collider proposal
Early 1970 studies for 200+200 GeV proton-proton collider superconducting magnets (enough to see W, Z – discovered at SppS with 270+270 GeV in 1983)
3.8 km circumference, 6 intersections, AGS as injector
At the same time Fermilab started working on the Tevatron
Tunnel, office building, He cryo plant built (updated and still in use today)
Only one working dipole prototype (Mark V) – sc cable issues
1983 canceled in favor of SSC (itself canceled in 1993)
BNL quickly build a heavy ion physics program with AGS Ions from Tandem Van de Graaff, transfer line to AGS 1986
Ernest Courant 1920-2020
[Ernest D. Courant, “Accelerators, colliders, and snakes”, Annu. Rev. Nucl. Sci. 2003. 53:1-37]

## Slide 8: Relativistic Heavy Ion Collider
1984 began to think about heavy ion collider
~100 GeV/nucleon, dipoles ~3.5 T (5 T for ISABELLE)
transfer line from Tandem, develop heavy ion beams in AGS, with heavy ion experiments
1991 construction begins
12 Jun 2000 First collisions =>
[Ernest D. Courant, “Accelerators, colliders, and snakes”, Annu. Rev. Nucl. Sci. 2003. 53:1-37]
Satoshi Ozaki
Mike Harrison
Tom Ludlam

## Slide 9: Relativistic Heavy Ion Collider – main parameters
RF
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
(s)PHENIX
(PHOBOS) Electron lenses
Polarized Jet Target
(BRAHMS) Electron cooling
EBIS
BLIP
TPL
Start operation : 2000
Circumference : 3.8 km
Max dipole field : 3.5 T Energy : 255 GeV polarized p : 100 GeV/nucleon Au
Species : ph to U (incl. asymmetric) Experiments : BRAHMS, PHOBOS, pp2pp, AnDY, RHICf, PHENIX (complete) STAR, sPHENIX
<= Only experiment from first to last day

## Slide 10: RHIC Design Manual
reached Lavg = 88×1026 cm-2s-1 (44x design)
reached Lavg = 24.8×1031 cm-2s-1 (25x design) with Pavg = 57%

## Slide 11: RHIC Design Manual (July 1998)
IR design with beam splitting DX dipoles first
DX dipole
D0,Q1—Q3
DX dipoles
Lmag = 3.7 m, Bmax = 4.3 T
large aperture (18 cm coil ID)
only magnets that need training (~5 for IR6/8 only)
 Interaction Point
Notes: MAKE REAL CALCULATION FOR DX MOVE

## Slide 12: Transition crossing – with sc magnets
[M. Harrison, S. Peggs, and T. Roser, “The RHIC accelerator”, Annu. Rev. Nucl. Sci. 2002. 52:425-369]
Did limit intensity for some time:
Initially no gamma-t quads
Electron clouds
Instabilities

## Slide 14: Configuration Manual Polarized Proton Collider, 2006
reached Lavg = 2.5×1032 cm-2s-1
reached Pavg = 57% (avg. over 3D distribution and time)
Notes: A little sloppy with 10% effects

## Slide 15
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper
Special devices for polarized protons: source, polarimeters, snakes, rotator, flipper

## Slide 16: RHIC performance evolutions
Au+Au luminosity at 100 GeV/nucleon
p+p luminosity and polarization (100 and 255 GeV)
Medium heavy (Cu+Cu, O+O)
Asymmetric collisions (p+Au, d+Au, h+Au, Cu+Au)
U+U (non-spherical), Zr+Zr / Ru+Ru (same A = 95, max different DZ = 4)
Au+Au luminosity at 3.85 to 9.8 GeV/nucleon (Beam Energy Scan, including a fixed target program)
only ion combination shared between
RHIC and LHC are O+O and p+p (polarized in RHIC)

## Slide 17
RHIC Au+Au / U+U operation at full energy
can now be done in 1/2 day (200x faster)

## Slide 18: Performance limits – RHIC ions, high energy
Bunch intensity Nb, limited by injectors EBIS, bunch merges in Booster and AGS transition instability luminosity lifetime aim for >2x109 in store
Intrabeam scattering => stochastic cooling
Lattice with small b* and large off-momentum dynamic aperture with hourglass factor ≈0.5 at end of store, need large b* reduction any lattice change must not result in additional beam losses dynamic b* reduction after emittance decreased by cooling
Goal is to have burn-off as the dominant beam loss mechanism.

## Slide 19: RHIC Run-14 Delivering RHIC-II luminosity
2007, Beginning of RHIC-II upgrade
2014, End of RHIC-II upgrade
Increase in initial luminosity result of larger bunch intensity
Increase in luminosity lifetime result of 3D bunched beam cooling, >90% burn-off

## Slide 20: Early interest in cooling for RHIC
Simon Van der Meer, 1984

## Slide 21: 3D stochastic cooling for heavy ions
M. Brennan, M. Blaskiewicz, F. Severino, PRL 100 174803 (2008); K. Mernick PRSTAB, PAC, EPAC
longitudinal kicker cavity (half side with waveguides)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Notes: Frequency range: 5-8 GHz transverse, 6-9 GHz longitudinal

## Slide 22: Operation at burn-off limit in U+U
97% of intensity burned off at Lmax
Burn-off dominated operation allows for determination of total U+U cross section – and comparison with calculation (mostly QED) (published in Phys. Rev. C) =>

## Slide 23: How did stochastic cooling change heavy ion collider operation?
Increased in luminosity lifetime from ~2.5 h Au+Au up to infinite
Allowed for increase in bunch intensity L ~ Nb2
Increased optimum store length from 4 to 8 h for Au+Au, resulting in more time in collision, less time refilling
Can tolerate emittance growth during acceleration (from IBS, transition instabilities) as long as no intensity is lost
Operation close to burn-off limit, full use of accelerated intensity
Allowed flat luminosity for alternating species (Ru+Ru/Zr+Zr)

## Slide 24: Run-18 Zr+Zr/Ru+Ru – same A, different Z (CME) Zr-96/Ru-96
Extraordinary help from DOE, ORNL, RIKEN for source material and preparation
Ru isotopes

## Slide 25: Run-18 Zr+Zr/Ru+Ru at 100 GeV/nucleon
Run Coordinator: Greg Marr paper: IPAC 2019
Zr+Zr
Ru+Ru
Zr+Zr
Ru+Ru
Ru+Ru
Zr+Zr
Ru+Ru
Zr+Zr
CeC PoP dedicated
scheduled maintenance
Store-by-store species change and flat luminosity of 21.5×1026 cm-2s-1
20 h nominal store length (WEEK: 30-Apr-18 to 07-May-18)

## Slide 26: Low-Energy RHIC electron Cooling (LEReC) for the Beam Energy Scan I and II (BES-I, II)
[2015 NSAC Long Range Plan for Nuclear Science]
BES-I in 2010/11/14
BES-II: 10x increase in the number of events
Au+Au collisions down to 3.85 GeV/n (40% of CoM energy at nominal injection)
Luminosity really low:
Space charge
Intrabeam scattering
Magnetic field errors (also time dependent)
Large beam with losses
BES-II goal of 4x luminosity over 3.85 – 9.8 GeV/n (highest energy is nominal injection)
=> Designed cooler for 2 lowest energies
Notes: Picture from 2015 NSAC long-range plan

## Slide 27: LEReC Accelerator (100 meters of beamlines with the DC Gun, high-power fiber laser, 5 RF systems, including one SRF, many magnets and instrumentation)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
ERL solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity

## Slide 28: Low Energy RHIC electron Cooler
A.V. Fedotov et al., “Experimental demonstration of hadron beam … “, PRL 124, 084801 (2020)]
LEReC operational electron cooler:
  utilizes RF-accelerated electron bunches
  uses non-magnetized electron beam (no magnetization at the cathode and no continuous solenoidal field in cooling section)
LEReC approach to cooling is directly scalable to high-energies – pre-cooler in EIC at injection

## Slide 29: BES-I vs BES-II luminosity
Run Coordinator: Chuyu Liu (Run-19 to 21)
3rd year
1st year
2nd year
Goal was
Lavg (BES-II) = 4x Lavg (BES-I)

## Slide 30
RHIC p+p operation at 100 / 255 GeV
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper

## Slide 31
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper
Special devices for polarized protons: source, polarimeters, snakes, rotator, flipper

## Slide 32: Final Run-25 Au+Au
[mb-1]
damaged 69 kV power line
repair shut off Central Cryo Plant
required managing helium inventory
15 days
unsynchronized beam abort
Yellow abort vacuum repair
14 days
Run Coordinator: Travis Shrey
short in superconducting bus
repair required partial warm-up
opened several cryostats
65 days

## Slide 33: Run-25 STAR and sPHENIX event rates
Maintenance day
STAR 0 mrad crossing angle
sPHENIX 1 mrad crossing angle
Oct/Nov 2025

## Slide 34
L design
nominal injection
L design
Used stochastic or electron cooling in 1 or 2 beams

## Slide 35: Ingredients to a successful partnership
Ambitious goals drives performance
  Luminosity
  Polarization
  Large range of species combinations / energies
  Beam Energy Scan
From early days consistent STAR support for Machine Development and APEX
  Machine development for short-term performance increases
  APEX for longer-term performance increases
Good communication
  C-AD understood STAR goals, STAR understood what RHIC can do

## Slide 36: RHIC’s 25 years …
Good design – allowed for significant upgrades
Evolving physics program, strong community and funding agency support – DOE NP
Full energy Au+Au Lavg = 44x design New: bunched-beam stochastic cooling
Only p+p collider, Lavg = 1.3x design, P ~ 57% (70% design) New: p polarization preservation to high energy
12 species combinations (incl. asymmetric), 18 center-of-mass energies, low-abundance isotopes New: built-in flexibility, high-intensity high-brightness ion/p sources
Extended energy range slightly above; and significantly below nominal injection New: electron cooling with RF accelerated e-beam
RHIC operation to end in January 2026 Most of RHIC complex will be re-used for the Electron-Ion Collider Hadron injectors, RHIC tunnel, Yellow ring (part of Blue), Technical Infrastructure, New technologies listed above
Nominal injection
[APS DPB Newsletter on RHIC: https://engage.aps.org/dpb/resources/newsletters/25-newsletter/2025-f7]

## Slide 37
It was a great pleasure to work with the STAR collaboration over the last 25 years.

## Slide 39
Relativistic Heavy Ion Collider
New York City

## Slide 40
[Y.Y. Lee, ”50 years of the BNL AGS”, 14th Intl. Conf. on Accelerator and Beam Utilization, Gyeongju, Korea (2010).]
No 200 MeV Linac yet (1970) No 1.5 GeV Booster yet (1990)
1959: CERN PS

## Slide 41: Heavy ion program at AGS
RF
Tandem Van de Graaff
Completed in 1970 for NP studies
RHIC pre-injector until 2011 (now EBIS)
2 electrostatic accelerators
32 MV (= 2x16 MV) voltage
>40 ion species p to Au
Fixed target experiments (~100x lower intensity than SIS100) AGS vacuum system not baked
Heavy Ion Transfer Line (HITL), operational 1985
Notes: No EBIS, NSRL, AtR, Tandems pic

## Slide 42
Claudia Ratti,
University of Houston
RHIC CDR, 1986

## Slide 43: Au bunch intensity evolution
main limits: - injectors output - e-cloud in RHIC
- transition instability in RHIC
Today, Run-25
AGS 12g6g2 merge
EBIS, Booster 4g2g1, AGS 8g4g2 merge
scrubbing with protons
111 bunches
43 bunches
gt-jump, octupoles at transition

## Slide 44: p bunch intensity and polarization
FOM = LP4 ~ Nb2P4
main limits: - injectors output - polarization - e-cloud in RHIC - beam-beam in RHIC
beam-beam compensation
polarized source upgrade with Atomic Beam Source
AGS tune jumps, RHIC 9 MHz RF
AGS cold snake
polarized source upgrade with sc solenoid
AGS warm snake
A. Zelenski, H. Huang, K. Gardner, K. Zeno, RF, et al.
(double-spin experiments)

## Slide 45: Head-on bb compensation
tune distribution measured with BTF and p+Al collisions proton beam: (Qx,Qy) = (.685,.695); Al beam: (Qx,Qy) = (.685,.695); DQx, DQy >> x => no coherent modes
no bb
2x bb
DQ reduction from e-lens
Can only reduced BB tune spread (black curve is limit)
Tune footprint compression with a Gaussian electron beam
[W. Fischer, et al., ”Operational head-on beam-beam compensation with electron lenses in the Relativistic Heavy Ion Collider", Phys. Rev. Lett. 115, 264801 (2015).]