## Slide 1: LDRD-C 25-043 project conclusion Tunable Neutron Beam through Deuteron Disassociation
December 18th, 2025
Xiaodong Jiang

## Slide 2
Tunable Neutron Beam through Deuteron Disassociation
Results of a beam test (Sept. 3rd, 2025), with deuteron and proton beams 100 MeV/u
Conclusion and next steps.
deuteron
p
n
n
p
n
p
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
B field
Goal: once “mono-energetic” neutron is demonstrated, a tunable neutron beam (15-200MeV) is achievable with existing technology, reaching 1010 neutrons/cm2/sec.
Approved for FY2025 (LDRD-C $75k, covers 8hr beam time at NSRL, engineer time, etc.).
1cm Be
2.22 MeV binding energy
Method: (1947) disassociation reaction strips the loosely-bounded deuteron into (p + n) pair with similar energies, ~2% possibility for 100 MeV/n deuteron on a 1 cm Be.
This work focused on deuteron 100 MeV/u.

## Slide 3
Applications of neutron technology are limited by the available neutron sources:
Reactors neutrons (thermal): Ekin << 1 MeV.
Fusion neutrons (Deuteron-Deuteron, Deuteron-Tritium): Ekin =2.5 MeV, 14.1 MeV.
Accelerator based proton-spallation neutrons: wide energy not easily selectable.
Why Fast Neutron (Ekin = 15MeV - 200MeV) ?
It’s well-known since 1940s that deuteron disassociation on a light nuclear target produces mono-energetic neutrons, a practical fast-neutron beam with tunable energies has never been demonstrated.
Fast neutron beam (Ekin = 15MeV-200MeV) with selectable energy is not currently available to satisfy the needs of:
Isotope production.
Aviation Industry: neutron induced radiation damages in electronics.
National Security:
  fast-neutron cross-sections for weapons design and simulation.
  imaging of subcritical nuclear material in high-energy and high-density states.

## Slide 4
R. Serber, Phys. Rev. 72, 1008 (1947)
“…The yield of neutrons from a 1/2-inch Be target (in which the energy loss for 190-Mev deuterons is 20 Mev) is nearly 2 percent.”
This work focused on deuteron@100 MeV/u, on 1 cm Be target

## Slide 5: Deuteron Beam in the NSRL beam line (Booster R-line)
deuteron beam 100 MeV/u
injected from EBIS
set for Q/M=1/2
EBIS deuteron -> Booster -> R-line
NSRL
This work focused on deuteron@100 MeV/u
set for Q/M=1/2
The first time EBIS deuterons delivered to the Booster R-line.

## Slide 6: Proton beam in the NSRL beam line (Booster R-line)
molecular H2+
100 MeV/u injected from EBIS
0.25 mil AL foil
set for Q/M=1
EBIS molecular H2+ beam
Booster -> D6 foil
R-line 20o bend
proton beam in NSRL
set for Q/M=1/2
NSRL
The first time EBIS protons (from H2+) delivered to the Booster R-line.

## Slide 7
NSRL Target Room
Beam

## Slide 8
S3
~6m
Beam
1cm Be
S1
S2
Calorimeter
(Scintillator Block)
. . . . . .
. . . . . .
Dipole Magnet
p
n
n
p
n
p
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
B field
1cm Be
neutron detection through (n,p) interactions.
charge veto
Test Setup
(1947) disassociation reaction strips the loosely bounded deuteron into p + n with similar energies, with a ~2% possibility for 100 MeV/n deuteron on a 1 cm Be target.
10cm x 10cm x 20cm thick
Trigger: (S1+S2)+Calorimeter
scintillator S1, S2, S3: 5”x5”x1/4”
deuteron

## Slide 9
Dipole Magnet
B=0.475 tesla, L=12”
BdL ~ 0.145 Tesla.meter
center clearance:0.75”
Stephen Brooks

## Slide 10
100 MeV/u deuterium beam, a 10x10cm square shown as a reference
Beam camera screen: ~ 130cm from center of magnet
Magnet IN
Magnet OUT
primary beam displacement: ~5 cm

## Slide 11
100 MeV/u deuteron beam through the magnet.
At the Strip-Chamber (1” pitch) behind the Calorimeter (~650cm from magnet-center),
Primary deuteron beam displacement: ~10” (25.4cm)
Calorimeter size:
scintillator block
(10cm x 10cm) x 20cm thick
Magnet works
At downstream:
the primary deuteron beam is kicked far away from the calorimeter

## Slide 12
proton Ekin = 100 MeV/u
magnet out
pass through 1cm Be
proton Ekin ~ 78 MeV/u
magnet out
Calorimeter ADC
~ch530
~ch800

## Slide 13
deuteron Ekin = 100 MeV/u
magnet out
pass through 1cm Be
deuteron Ekin ~ 89 MeV/u
magnet out
Calorimeter ADC
~ch1550
~ch1740

## Slide 14
deuteron Ekin = 100 MeV/u
pass through 1cm Be
magnet IN
Calorimeter ADC
~ch1550
~ch530
deuterons
Scaler Rates (4.8 sec per spill):
(S1+S2): 200k/spill
S3 : 1200/spill
Calorimeter: 270/spill
Trigger (S1+S2)+Calorimeter: 90/spill

## Slide 15
Calorimeter_ADC vs S3_ADC all events
~ch1550
most event have S3 hit
any neutrons ?
triggered events appeared to be charge particle background

## Slide 16
Calorimeter Flight-Time
Calorimeter Flight-Time vs ADC
deuterons
any neutrons ?

## Slide 17
Calorimeter Flight-Time
deuteron Ekin =100 MeV/u
1cm Be, magnet out
proton Ekin =100 MeV/u
1cm Be, magnet out
peak1
peak2
peak3
any neutrons ?

## Slide 18
Calorimeter_ADC vs S3_ADC with Flight-Time Cuts
most event have S3 hit
peak2
peak1
peak3
triggered events appeared mostly charge particle background

## Slide 19
deuteron Ekin = 100 MeV/u
pass through 1cm Be
magnet IN
Calorimeter ADC
~ch1550
all events
possible neutron signal ?
events with S3ADC<500
Not expecting neutron conversion (n,p) reaction lead to protons with well-defined energy
events with S3ADC<500

## Slide 20
It’s well-known since 1940s that deuteron disassociation on a light nuclear target produces mono-energetic neutrons, a practical fast-neutron beam with tunable energies has never been demonstrated.
Conclusions
BNL has all the facilities/technologies to make such a tunable neutron beam possible:
EBIS provides deuteron beam (and proton through H2+).
Booster and slow extracted beam, for deuteron up to 1000 MeV/u.
NSRL beam line and the Target Room.
We conducted a beam test: did not pinpoint neutron signal, triggered events appeared mostly from background.
Improvements Planned (LDRD-C proposal submitted for FY2026):
An open-slot dipole magnet: to clearly sweep away all primary beam deuterons and the breakup protons.
Tag the breakup proton with scintillator strip detectors.
A neutron telescope detector: multi-layer segmented scintillators.
(charge-veto + flight-time, combined with a range-telescope)
Next Step:
Event-by-event tagged neutrons as a clear demonstration.

## Slide 21
p
n
n
p
n
p
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
. . . . . . . .
B field
Next Step: event-by-event tagged neutron
primary deuteron beam
multi-layer segmented scintillators
proton-tag scintillator in the trigger
deuteron