## Slide 1: Power cables
IBs to PP
Georg Viehhauser with lots of help from Nico Rotolo (Oxford)

## Slide 2: Geometry
Service installation up to the PPs will be responsibility of SVT
  Installed as part of the SVT half-barrel integration
    Service supports need to be present for that
  Will need to pivot inside for TOF and cymbal installation (which is after SVT insertion) at the blue arrows
    Service supports need to allow for that
    Angle will need to be defined
Lengths (courtesy Roland):
EPP
HPP
Forward (Hadron) Side | Length [cm]
End of L1 to HPP | 245
Point 1, end of L2 to HPP | 250
Point 2, end of L3 to HPP | 225
End of L4 to HPP | 195
Point 3, HD4 to HPP | 100
Backward (Electron) Side | 
Point 4, end of L3 to EPP | 350
End of L4 to EPP | 320
Point 5, ED4 to EPP | 225

## Slide 3: What we know (sort off)
Connectors at both ends
  Low material and size at FIB end (pair of conductors)
  PP connector needs to convert from AWG18 to AWG10
Length between 1 and 3.5 m
Max. current 2A, max. voltage 48 V (same cable for serial powering chains and control boards)
Total number about 1300 pairs
AWG18 Cu-clad Aluminium
Twisted pairs – one pair per FIB
  Need to decide on the number of pairs in one cable
Need some form of cladding for mechanical protection
  We don’t know yet whether we need shielding on the power cables
  We suspect no, as we are supplying current, but that needs some more thinking. Input welcome
Inside the SVT, multi-core cable will need to fan out to individual FIBs
Cables need to satisfy NEC 2021 NFPA 70 based standards

## Slide 4: Schematics
FIB
HPP
EPP
FIB
FIB
18AWG copper-clad Aluminium
What is smallest conduit cross-sectional area?
What is sharpest conduit bend radius?
FIB
C1-M
C1-F
C2-M
C2-F
Patch Panel
(is this a PCB board
or just a faceplate with
connectors mounted on it?)
Overall length between 1 and 3.50 m
Branch length XX mm
2 wires (a twisted pair)
C1-M
18AWG aluminium
10AWG copper
Faceplate (PP)
C1-F
How do you do the transition from 18awg to 10awg
do you create a PCB with two different connectors
or do you use the same connector that can accommodate
both wire sizes with the same crimp terminal?
D-Sub power connector terminal can do the transition
2 wires (a twisted pair)
2 wires (a twisted pair)
2 A constant current
2 wires (a twisted pair)
10AWG copper
SVT
Cable trays

## Slide 5: Discussion with supplier
We have started communication with Axon
  We have worked with Axon on cables for ATLAS (much more complicated, different wire gauges and pins in cables and connectors)
  They are aware of the constraints and technical and financial aspects of PP projects
Pricing will be decided after the design is finalised and depending on quantities and other factors such as the sourcing of third party components such as the wire themselves and the low mass cable screen
Most of the process is done in-house
  In this case insulation, stranding, overbraiding and jacketing
  For Copper conductors they plate, draw and strand most variants themselves, but Aluminium conductors they buy in
Copper-clad Al cores were surprisingly the most expensive for them to procure with the silver-plated copper-clad Al in the middle and silver-plated Cu the cheapest
  Difference in the final assembled cable cost between all three should be <20% and for final assemblies <10%
They offer cables rated for 300 Mrad (as in ATLAS), we need ~ 10 krad

## Slide 6: Some examples: cable option 1
Lynxeo Catalogue Aeronautique.pdf

## Slide 7: Some examples: cable option 2
axon-space-ESA-Axalu_cg.pdf

## Slide 8: Some examples: connector option 1
livebook.pdf
Standard D-Sub connectors from Harting

## Slide 9: Some examples: connector option 2
eaton-souriau-robust-metal-shielded-connector-UTO-catalog-en-eu.pdf or UTG series | Eaton

## Slide 10: Some examples: connector option 2 cont’d
With the use of the ‘PCB contacts’ the connectors can be mounted on a PCB,
but note, no right-angle contacts
Connector available from 4 to 48 or 61 contacts

## Slide 11: Some examples: connector option 3
axon-micro-D-connectors-rectangular_cg.pdf
Micro-D connectors with ‘power pins’ to accommodate 18AWG wire
Note, Micro-D connectors come pre-wired with wire ‘pigtails’, there are no separate crimp terminals

## Slide 12: Some examples: connector option 4
Harwin Hi Rel Brochure July 25 v3.indd

## Slide 13: Some examples: connector option 5
io_dsub_brochure.pdf
Amphenol, D-Sub Mixed and Full Power DW Series

## Slide 14: Further comments from Axon
One of the questions that came up in the discussion with them was whether the connector material must be non-magnetic
  In ATLAS this was a requirement (although never quantified), and this has been solved by using metal-coated PEEK connector housings
For the FIB connector:
  ‘Combo Micro-D C8/P8’, do you have a plastic version of it? Do you have anything similar to ‘Harwin M300’ connectors?
    Whilst not a catalogue part they can make PEEK versions of Combo P8 and other similar connectors shown in our catalogue
    Have used custom 1-way, 2-way and 6-way connectors before
    The M300 connectors will only come with the standard options so if we need <200nT this is likely not to be suitable whereas they can adapt/customise their design to meet tighter requirements
PP connector:
  ‘Souriao UTG (or UTO)’ series of multi-way circular connectors - Do you have anything similar?
    Again this is not a catalogue option but they have made Circular Micro-D with combo style inserts utilising the same larger gauge contacts from their combo Micro-Ds
    There may be other inherently low-mag options off-the-shelf

## Slide 15: Some examples: Low-mass shielding
330185-Micro-Coax-datasheet-41316139.pdf
This is used in ATLAS power cables

## Slide 16: CB to FIB

## Slide 17: Specifications
We currently think a 25-way nano-D connector will be sufficient
Current geometry:
  Surface mount, right-angle connector on the CB
  Through-hole, straight connector on the FIB
Connected with a multicore cable of the required 25 wires with common shield
  Signals are not particularly fast
  Material is again copper-clad aluminium
  Each wire a maximum of 30AWG (nano-D cannot fit larger)
    Cable with different diameters possible, cables will be customised anyway, standard procedure for Axon (and other suppliers)
  ARACON low mass shielding
Cable assembly will be terminated at both ends with connectors
  Nano-D connectors cannot be terminated by user

## Slide 18: Open questions
How many assemblies?
What is the estimated maximum length of the assembly?
Calculation of the voltage drop along the wires may be needed because it is a very thin (30AWG) aluminium wire
Any preference for the gender of the connectors on the boards?

## Slide 19
‘AXON cable’ nano-D connectors
A link to the datasheet\catalogue axon-nano-D-connectors_cg.pdf

## Slide 20
Connector for the CB board ND2A 2 25 S SMH P G 1 ?
Connector for the FIB board
ND2A 2 25 P BS P G 1 ?

## Slide 21
Connector for the FIB board
ND2A 2 25 S BS P G 1 ?
Connector for the CB board ND2A 2 25 P SMH P G 1 ?

## Slide 22
Cable to be ordered as ‘jumper cable’
plug with jackscrews at one end
and receptacle with jackscrews at other end
likely identification code:
ND2A
2
25
S
P
EMI (custom spec, ARACON, clamp, not soldered)
Connections (D, pin1 to pin1, custom?)
Wire code (custom spec, 30 AWG AXALU wire)
L
Wire Length in cm
R
R
Note: orient the connectors on the boards so that the cable is not twisted when connected
CABLE ASSEMBLY

## Slide 23
Wire for the cable
AXALU® silver plated aluminium conductor, thickness of silver plating is 2um
A Link to datasheet\catalogue here: axon-space-ESA-Axalu_cg.pdf
Note: it is not Copper Clad Aluminium wire, but if necessary, AXON should be able to source them
Note: wire gauge of the standard catalogue product is 24 AWG, but AXON should be able to custom produce a 30 AWG gauge wire
Note: wires to be made into a custom made cable
Note: insulation of the standard catalogue product is ‘Extruded crosslinked ETFE’ which is not LSZH but they can custom produce the wire with a radiation resistant and LSZH insulation, see below for available wire insulation types.
A link to datasheet\catalogue here: axorad-radiation-resistant-cables_cg.pdf
wire
insulation
Insulation for the wire

## Slide 24: Further material

## Slide 25: Outside cable lengths
External cables have to run around dRICH service boxes
  Will get split into 6 runs as evenly as possible around those 6 boxes
Cable lengths from PPs to power supplies will depend on
  Phi of cable exit from ePIC
    3 o’clock position versus 9 o’clock position is about an 8 m difference
  Rack allocation
    Closer racks cable lengths would be 4 m to 12 m
    Far away racks cable lengths would be 10 m to 18 m
    Electron side versus Hadron side doesn’t really matter for this

## Slide 26: CB-to-FIB cable wires
3 x diff pair for FPC S/Cs (6 wires)
VTRx+ power (2V5 domains could be supplied by 1 source, GND could be shared for all domains) (3-6 wires)
  1V2 Tx domain (VCCT1V2)
  2V5 Tx domain (VCCT2V5)
  2V5 Rx domain (VCCR2V5)
  GND needed
VTRx+ I2C (share GND with power domains?) (2-3 wires)
  SCL
  SDA
Laser driver controls (2 wires)
  Reset
  Disable
RSSI (Rx current monitor) (1 wire)
VTRx+ thermistor (2 wires)
  2 terminal interface
Voltage sense (for VTRx+ domains) (3-4 wires)
  1V2 domain
  Shared or separate 2V5 domains?
  GND sense (to account for V-shift on both rails)
Minimum only includes 1 x GND wire (we probably want more)! Minimum is 19, we go for 25