## Slide 1
MPW2-SLDO:
Initial tests
WP2 Sensor and AncAsic characterization
20251216
andrew.hill@stfc.ac.uk

## Slide 2: Outline
Test systems distribution.
Initial tests on MWP2-sLDO.
Serial Powering.
Conclusion.
MPW2-SLDO

## Slide 3: Distribution and test plan
Distribution:
Bham: 1 DUT + 1 DAQ, J.Glover, L.Li;
Brun : 1 DUT + 1 DAQ, L.Teodorescu, L.Ranatunge;
DL : 2 DUT + 3 DAQ, A.Hill;
DL : Spare: 1 unpopulated DUT carrier PCB;
[DUT assembly @ Bham]
Test:
Smoke testing of DAQ set-up; [A.Hill]
Smoke testing of DUT; [A.Hill]
Chip characterisation; [Shared Bham, Brun, DL]

## Slide 4: Smoke testing of DAQ set-up
Micro-controller
Ethernet port
DUT carrier card
DAQ card
Successfully commissioned w/o DUT

## Slide 5: DUT interconnection on carrier PCB
A total of 4 DUTs were mounted and wirebonded to 4 carrier PCBs.

## Slide 6: Smoke testing of DUT-TW1
Powered up the DUT (nominal values) and performed a DAC Scan: Scan DAC codes. Record the value of Vout and plot against the code.
The DUT output voltage successfully responded to commands.

## Slide 7: Chip characterisation
Focus on standalone sLDO.
Evaluation of performance against specified range of
parameters.
Bham -> perform all characterisation at +27C and -20C, +105C;
Brun -> perform all characterisation at +27C and +60C;
DL -> select sub-set of tests for irradiation [repeat
before/during/after irradiation][+27C and +60C(TBC)]

## Slide 8: Test setup

## Slide 9: DUT-TW1: 40mA region of interest (ROI)
PSU V_OUT = 1.65V
V_IN = 1.646V : V_DROP = 0.004V

## Slide 10: DUT-TW1: 500mA ROI
PSU V_OUT = 1.65V
V_IN = 1.623V : V_DROP = 0.027V

## Slide 11: DUT-TW1: 900mA ROI
PSU V_OUT = 1.75V
V_IN = 1.706V

## Slide 12: DUT-TW1: 900mA ROI (V_in = 1.75V @ Chip)
PSU V_OUT = 1.883V
V_IN = 1.75V : V_DROP = 0.133V

## Slide 13: Serial powering – sanity check
Test Set Up.
Both set to 40mA ROI
PSU V_OUT 3.2V 0.05A CC Mode
Board 1 V_IN =1.556V
Board 2 V_IN = 1.641V
Overall V_Drop = 0.003V
No Load test::-
Board 1 Dac set to 0  V_out = 1.416V
Board 2 Dac set to 0  V_out = 1.479V
PSU V_out = 3.2V 0.06A CC Mode
Board 1 Dac set to 31  V_out = 0.984V
Board 2 Dac set to 31  V_out = 1.055V
PSU V_out = 3.2V 0.06A CC Mode
With Load test:-
Board 1 Dac set to 0  V_out = 1.414V
Board 2 Dac set to 0  V_out = 1.478V
PSU V_out = 3.2V 0.06A CC Mode
Board 1 Dac set to 31  V_out = 0.985 V
Board 2 Dac set to 31  V_out = 1.058V
PSU V_out = 3.2V 0.06A CC Mode

## Slide 14: Conclusion

## Slide 15
Thanks for your time
Any questions