## Slide 1: Electron Storage Ring Polarimeter
Polarimeter Components:
RF-pulsed laser system (under development)
Position sensitive detectors (diamond strips) for scattered electrons and backscattered photons
Calorimeter for backscattered photons
Beam energy | PL | PT
5 GeV | 99.1% | 13.2%
10 GeV | 96.5% | 26.2%
18 GeV | 89.0% | 45.6%
Polarization components at Laser IP
Crab cavity
Photon Detector
(30 m from Laser IP)
*
D4EF
qB=1.5 mr
Q9EF
D5EF
qB=1.5 mr
D6EF
qB=12 mr
Q10EF
Q8EF
Q7EF
Q6EF
Q5EF
Q4EF
Q3EF
D3EF
qB=13 mr
D2EF
Electron Detector
Laser IP​
74 m upstream of IP-6

## Slide 2: ESR Information Needed for Compton Polarimeter
Beam position at laser IP and just before electron detector
  Position “lock” at laser IP possible? Maybe AI based incorporating detector rates?
Beam current/charge information
  Track correlation of polarization with bunch charge
Magnet currents/BdL between laser IP and electron detector
  Needed to map asymmetry vs. position at detector
Spin rotator settings upstream of laser IP, magnet currents/BdL
  Monitor spin direction
Bunch identifier, polarization state

## Slide 3: Other Controls
Controls that don’t interface with the beam
  Laser system
    Seed laser, amplifier
    Remote stages (rotation, mirrors)
    Readback of power meters, photodiodes and quad-photodiodes
  Photon detector  remote motion control to center detector on backscattered photon cone
  Electron detector  remote motion control

## Slide 4: RCS Compton Polarimeter
Compton polarimeter will also be used in RCS
Will use commercial, low-duty laser, operate in multi-photon mode
Photon detector only – no electron detector
Similar beam information needed:
Beam position information at laser (and position lock?)
Bunch intensity
Due to vertical polarization, don’t need as much information about magnet currents, fields