## Slide 1: Slow control EIC Hadron Polarimetry Frank Rathmann
EIC, Slow Controls workshop
November 13, 2025

## Slide 2: Two primary polarimeter systems
HJET
pC

## Slide 3
HJET subsystems
H. Kleines et al. , NIM A 560 (2006) 503
ABS (Atomic Beam Source)
  Vacuum and interlock
  Gas supply system H2, O2, N2
  RF dissociator
  PID loops for temperature and chopper control
  RF Transition units
    WFT and SFT
  Holding field magnet control
BRP (Breit-Rabi Polarimeter)
  Vacuum and interlock
  QMA (Quadrupole mass analyzer)
    H1 and H2 transverse beam profiles (xy)
    Rest gas analysis at target
    Stepper motor control
  RF Transition units
    WFT and SFT
  Chopper control
  Ion gauge signal detector

## Slide 4
Structure HJET control system
H. Kleines et al. , NIM A 560 (2006) 503

## Slide 5
pC subsystems
pC polarimeter
  Positioning of C targets in beam
    Stepper motor control
  QMA (future)
    Rest gas analysis of chamber vacuum
  Temperature readout
    C targets (in progress, difficult)
    Holders (future, easy)
Vacuum transfer chamber
  Vacuum and interlock
  QMA (Quadrupole mass analyzer)
    Rest gas analysis to ensure C targets are clean
  Stepper motor control linear drive

## Slide 6
HJET
  Total number of HJET process variables (PV) logged in EPICS ~ 500
  Most of these PVs are slow -> 0.1s update
  All PVs go to EPICS database
  CS Studio application for HJET
  Some subsystems require fast feedback loops (e.g., SFTs)
  Valve control to ring interlocked with ring vacuum
  Polarization + detector system info -> EPICS
    Info time stamped
Comments
pC
  Control system will get a similar architecture as HJET
  Focus on stepper motor control for C target movement
    Valve control for target transfer interlocked with ring vacuum
  Total number of PVs around 200
  CS Studio application for pC
  Polarization + detector system info -> EPICS
    Info time stamped
EIC control room talks to polarimetry equipment
Convenient to communicate directly via PVs through EPICS
  need to provide specific timing sequences for certain tasks