## Slide 1: TOF Test Beam Campaign 2026
Satoshi YANO
Hiroshima University

## Slide 2: AC-LGAD Time-of-Flight at ePIC
AC-LGAD TOF is used for PID, Tracking and background rejection at mid-rapidity and forward-rapidity
Timing resolution of 35ps and 25ps, positioning resolution of 30um and 30um for BTOF and FTOF, respectively, with installing in <8 cm thickness space are required
0.64 m
-1.33<η<1.74
1.84<η<3.61
60 cm
10.5 cm
~1.4 x 2 m = ~2.8 m
ePIC Tracking System
Barrel-TOF (BTOF)
Forward-TOF (FTOF)

## Slide 3: Challenge of AC-LGAD Test Beam
AC-LGAD requires high-precision waveform measurement
  Rise time for timing
  Height for hit position reconstruction
High performance digitizer or oscilloscope must be used
  High band-width, high sampling rate, data-taking rate: ~1GHz, 10 GS/s, O(100) Hz data taking
    CAEN DT5742: 500 MHz, 5GS/s, 16ch
    LeCroy WaveRunner8204HD: 2 GHz, 10GS/s, 8ch
    LeCroy WavePro804HD: 8 GHz, 20GS/s, 4ch
Three sensors or fast device are used for the timing measurement
  E.g. Photek PMT240 (MCP-PMT): σT ~ 10ps

## Slide 4: Challenge of AC-LGAD Test Beam
AC-LGAD requires high-precision waveform measurement
  Rise time for timing
  Height for hit position reconstruction
High performance digitizer or oscilloscope must be used
  High band-width, high sampling rate, data-taking rate: ~1GHz, 10 GS/s, O(100) Hz data taking
    CAEN DT5742: 500 MHz, 5GS/s, 16ch
    LeCroy WaveRunner8204HD: 2 GHz, 10GS/s, 8ch
    LeCroy WavePro804HD: 8 GHz, 20GS/s, 4ch
Three sensors or fast device are used for the timing measurement
  E.g. Photek PMT240 (MCP-PMT): σT ~ 10ps

## Slide 5: Challenge of AC-LGAD Test Beam
AC-LGAD requires high-precision waveform measurement
  Rise time for timing
  Height for hit position reconstruction
High performance digitizer or oscilloscope must be used
  High band-width, high sampling rate, data-taking rate: ~1GHz, 10 GS/s, O(100) Hz data taking
    CAEN DT5742: 500 MHz, 5GS/s, 16ch
    LeCroy WaveRunner8204HD: 2 GHz, 10GS/s, 8ch
    LeCroy WavePro804HD: 8 GHz, 20GS/s, 4ch
Three sensors or fast device are used for the timing reference
  E.g. Photek PMT240 (MCP-PMT): σT ~ 10ps

## Slide 6: Test Beam Campaign in 2025
Strip-type sensor has been tested at JLab in July
  First full-size sensor test (variable pitch sensor)
  Unfortunately, only 30um strip-type sensor has been tested
  CAEN DT5742: 500 MHz, 5GS/s, 16ch
Full-size strip-type and pixel-type sensor have been tested at DESY in December
  First real full-size strip-type sensor (BTOF sensor) has been tested
  Full-size pixel-type sensor (variable pitch) has been also tested
  Data was taken with several HV configuration (HV-scan)
  CAEN DT5742: 500 MHz, 5GS/s, 16ch
FCFDv1.1 test at DESY in August
  First FCFDv1.1 with strip-type AC-LGAD test
  Small prototype sensor (50um) with FCFDv1.1 (6ch analog block)
  LeCroy WaveRunner8204HD: 2 GHz, 10GS/s, 8ch

## Slide 7: Test Beam Campaign in 2025
Strip-type sensor has been tested at JLab in July
  First full-size sensor test (variable pitch sensor)
  Unfortunately, only 30um strip-type sensor has been tested
  CAEN DT5742: 500 MHz, 5GS/s, 16ch
Full-size strip-type and pixel-type sensor have been tested at DESY in December
  First real full-size strip-type sensor (BTOF sensor) has been tested
  Full-size pixel-type sensor (variable pitch) has been also tested
  Data was taken with several HV configuration (HV-scan)
  CAEN DT5742: 500 MHz, 5GS/s, 16ch
FCFDv1.1 test at DESY in August
  First FCFDv1.1 with strip-type AC-LGAD test
  Small prototype sensor (50um) with FCFDv1.1 (6ch analog block)
  LeCroy WaveRunner8204HD: 2 GHz, 10GS/s, 8ch

## Slide 8: Test Beam Campaign in 2025
Strip-type sensor has been tested at JLab in July
  First full-size sensor test (variable pitch sensor)
  Unfortunately, only 30um strip-type sensor has been tested
  CAEN DT5742: 500 MHz, 5GS/s, 16ch
Full-size strip-type and pixel-type sensor have been tested at DESY in December
  First real full-size strip-type sensor (BTOF sensor) has been tested
  Full-size pixel-type sensor (variable pitch) has been also tested
  Data was taken with several HV configuration (HV-scan)
  CAEN DT5742: 500 MHz, 5GS/s, 16ch
FCFDv1.1 test at DESY in August
  First FCFDv1.1 with strip-type AC-LGAD test
  Small prototype sensor (50um) with FCFDv1.1 (6ch analog block)
  LeCroy WaveRunner8204HD: 2 GHz, 10GS/s, 8ch

## Slide 10: Results From 2025
Strip-type sensor has been tested at JLab in July
  30um thickness result has been presented
  σt~63 ps and σx~32 um
Full-size strip-type and pixel-type sensor have been tested at DESY in December
  Analysis is on going
FCFDv1.1 has been tested with small-size strip-type sensor (eRD112 FY23 sensor) at DESY in August
  σt~40 ps and σx~15 um
    Sensor + PCB board was ~35 ps

## Slide 11: Results From 2025
Strip-type sensor has been tested at JLab in July
  30um thickness result has been presented
  σt~63 ps and σx~32 um
Full-size strip-type and pixel-type sensor have been tested at DESY in December
  Analysis is on going
FCFDv1.1 has been tested with small-size strip-type sensor (eRD112 FY23 sensor) at DESY in August
  σt~40 ps and σx~15 um
    Sensor + PCB board was ~35 ps

## Slide 12: Results From 2025
Strip-type sensor has been tested at JLab in July
  30um thickness result has been presented
  σt~63 ps and σx~32 um
Full-size strip-type and pixel-type sensor have been tested at DESY in December
  Analysis is on going
FCFDv1.1 has been tested with small-size strip-type sensor (eRD112 FY23 sensor) at DESY in August
  σt~40 ps and σx~15 um
    Sensor + PCB board was ~35 ps

## Slide 13: Test Beam Campaign in 2026
KEK-PS, electron @ ~6.5 GeV (Fortunately obtained by chance, parasite)
  Fixed: Feb. 19th ~ 25th
  Primary Goal
    20um and 30um pixel-type sensor test
    20um, 30um, 50um strip-type sensor test
Tohoku-RARiS, electron @ 800 MeV (main)
  Fixed: Mar. 3rd ~ 6th
  Primary Goal
    New geometry strip-type sensor (20um, 30um, 50um) test
    Homework of previous beam tests
CERN-SPS, proton @ 120 GeV (main)
  May/Eary June (Requested)
  Primary Goal: Test of EICROC1 with full-size pixel sensor (under discussion)
KEK-PS, electron @ ~6.5 GeV (main)
  Oct. to Dec (We will request the beam-time)
  Primary Goal: BTOF sensor + FCFDv1.2 and the first full-chain test
Using oscilloscope (8 GHz, 20GS/s)
Using oscilloscope (8 GHz, 20GS/s)

## Slide 14: Backup

## Slide 15: Multiple Scattering Effect @ RARiS
The new board with a hole under sensor has been developed
  Δθ ~ 0.94 mrad @ 800 MeV

## Slide 16: Plan-B Sensors
Larger-Gap and Shorten Strip Sensor
  Geometry: 2x64=128ch → 4x32=128ch
  Strip length: 10mm x 50um → 5mm x 50um
  Strip Pitch: 500um → 1000um
Double-Layer Strip Sensor
  Second metal layer is implemented to readout perpendicular direction

## Slide 17: Multiple Scattering Effect @ RARiS

## Slide 18
8
Board#4
WaveRunner#2
8
8
8
3
3
Scintillator#0
Scintillator#1
External Clock
WaveRunner#1
WavePro#1
2
2
2
2
2
FAN I/O
3
WaveRunner#3
MPC-PMT
Storage
PC
WaveRunner#0
Trigger Enable Signal
Board#0
Board#1
HV
WavePro#0
AUX OUT
AUX OUT
AUX OUT
AUX OUT
AUX OUT
AUX OUT
Board#2
DUT
Board#3
EXT TRIG
EXT TRIG
EXT TRIG
EXT TRIG
EXT TRIG
EXT TRIG
Coincidence
Ref-In
Ref-In
Ref-In
Ref-In
Ref-In
Ref-In
Network
Switch
Scintillator#2
Discriminator
FAN I/O
Switch
Control
PC
Control Room
Beam
Hall
HV
DT1471ET

## Slide 19
DIGITIZER
TLU
DIGITIZER
COINCIDENCE
TRIGGER
TRIGGER
EUDRBs
Telescope DAQ PC
DUT DAQ PC
Scintillator
AC-LGAD
AC-LGAD
AC-LGAD
Scintillator
Scintillator
BUSY

## Slide 20: Baseline Strip Sensors
Five sensors have been bonded
Classified by voltage value at which leak current reaches 1μA
  4 Class-S (1μA @ BV>=190V)
  1 Class-C (1μA @ 160<BV<170V)
Class-C
Class-S
Class-S
Class-S
Class-S

## Slide 21: Statistics of Test-Beam @ DESY 2025
Statistics for Strip (Triggered Event)
  Nominal HV Run
    5.6 GeV
    3 Class-S Sensors: 10ch/10ch/10ch (Pattern-2)
    All 185V: ~2x106
  HV Scan Run
    5.6 GeV
    3 Class-S Sensors: 10ch/10ch/10ch (Pattern-2)
    Side 185V + Middle 175V/160V/150V: ~2x106 each
  Positioning Measurement Run
    5.6 GeV
    2 Class-S Sensors: 15ch/15ch (Pattern-3)
    185V: ~2x106
  Class-C Sensor Run
    5.6 GeV
    3 Class-S Sensors: 10ch/10ch/10ch (Pattern-2)
    160V: ~2x106
  Low Energy Run
    3.6 GeV
    3 Class-S Sensors: 10ch/10ch/10ch (Pattern-2)
    All 185V: ~12 x106
  Low Energy HV 200V Run
    3.6 GeV
    3 Class-S Sensors: 10ch/10ch/10ch (Pattern-2)
    All 200V: ~12 x106
Statistics for Pixel (Triggered Event)
  Small Pixel Nominal HV-1 Run
    5.6 GeV
    Small-Pixel: 20um/30um
    HV: 110V/150V ~6x106
  Small Pixel Nominal HV-2 Run
    5.6 GeV
    Small-Pixel: 20um/30um
    HV: 100V/130V ~6x106
  Big Pixel Nominal HV-1 Run
    5.6 GeV
    Small-Pixel: 20um/30um
    HV: 100V/160V ~6x106
  Big Pixel Nominal HV-2 Run
    5.6 GeV
    Small-Pixel: 20um/30um
    HV: 80V/140V ~6x106
+ADC Calibration Run
Inject Pulse: 10/20/30/40/50/60/70/80/90/100/150/200/250/300mV
Into all channels