## Slide 1: NASA Space Radiation Laboratory Workshop Summary
12 May 2026 2026 RHIC/AGS Annual Users' Meeting & RHIC Science Symposium
Trevor Olsen Jessica Gasparik

## Slide 2
NSRL's first participation in RHIC/AGS Users' Meeting Showcasing four speakers from across the facility's multi-disciplinary user community
Radiobiology – Robert Schwartz, M.D. Electronics Testing – Andreas Waets
ML & Accelerator Physics – Eiad Hamwi Nuclear Data Measurements – Patrick Peplowski

## Slide 3: Introduction to NSRL

## Slide 4: NASA’s Terrestrial Analog for Space Radiation Studies
As NASA sets its eyes towards Mars, understanding the risks and uncertainties from the space radiation environment is crucial:
“In space, astronauts are exposed to ionizing radiation that is quantitatively and qualitatively different from terrestrial radiation. This environment includes protons and high-Z, high-energy ions together with secondary radiation, including neutrons and recoil nuclei that are produced by nuclear reactions in spacecraft materials or tissue.”
- Risk of Radiation Carcinogenesis (2016)
NASA HRP Space Radiation Element

## Slide 5
Source Machines Linac, EBIS & Tandem Van de Graaff
High Energy Beam Lines NSRL & HEET (proposed)
Low Energy Beam Lines Tandem VDG

## Slide 6: NSRL Beam Capabilities
Adapted from M. Sivertz
“Snowmass Workshop on Calibration and Test Beams”
Projectiles Options
  Protons, Deuterons, H2
  18 heavy ions between 2 ≤ Z ≤ 83
  Uncharacterized neutron beam possible through deuteron breakup
Beam Energy
  50 – 2500 MeV for protons
  50 – 1500 MeV/n for heavy ions Z ≤ 26 (Iron)
  Reduced peak energy for Z > Fe… 380 MeV/n for Bi
  Stopping beams, 10 MeV and below possible using polyethylene degrader
Flux (spills ~ 400 ms)
  1000 to 2x1011 protons per spill
  10 to 2x109 Fe ions per spill
Bismuth @ 360 MeV/u
20 cm

## Slide 8
Ions Delivered to NSRL
past & present
+ 2H

## Slide 9: Rapid Beam Switching via Laser Ion Source + EBIS
NASAs “GCR Sim”: 7 different ions in 33 beams within 1h
Pulse-to-Pulse Modulation for pre-injector systems allows for fast ion switches & simultaneous use of RHIC/EIC and NSRL
6 sec

## Slide 10
NSRL Target Room
Upstream Test Table
Tungsten Collimator
Polyethylene Degrader
Beam Current Detector
Digital Beam Imager
End of Vacuum Pipe
~6 Meter Beam Line Length
~100 Meter Transfer Beam Line
Downstream Test Table
60x60 cm Test Area

## Slide 11: Session Highlights

## Slide 12
Robert Schwartz, M.D. (Weill Medical College of Cornell), Radiobiology
Unfortunately, no slides available Here is my attempt to summarize
Experimental evaluation of simulated microgravity and space radiation exposure in mice with countermeasure drug (Kaempferol, flavonoid compound found in foods) Does countermeasure provide medically observable protection for astronauts?
Yes, it was reported that organ function and oxidative stress was improved in countermeasure-treated group compared to control group
While study is performed in mice, some up-regulated and down-regulated expressed genes are shared in human genetics with slight differences
Further investigation at NSRL is planned

## Slide 13
Andreas Waets (CERN), Microelectronics Testing

## Slide 14
Andreas Waets (CERN), Microelectronics Testing

## Slide 15
Andreas Waets (CERN), Microelectronics Testing

## Slide 16
Andreas Waets (CERN), Microelectronics Testing

## Slide 17: Machine Learning Assisted Tuning and Diagnostics of NSRL Beams
EIC–BeamAI collaboration
E. Hamwi, K. Brown, L. Hajdu, G. Hoffstaetter, W. Lin, M. McCarthy, T. Olsen
Eiad Hamwi (BNL), ML/AI Accl. Phys

## Slide 18
SciBmad slow extraction sim. from the AGS booster
Eiad Hamwi (BNL), ML/AI Accl. Phys

## Slide 19
Eiad Hamwi (BNL), ML/AI Accl. Phys

## Slide 20
Eiad Hamwi (BNL), ML/AI Accl. Phys

## Slide 21
Patrick Peplowski, Nuclear Data

## Slide 22
Patrick Peplowski, Nuclear Data

## Slide 23
Patrick Peplowski, Nuclear Data

## Slide 24
Patrick Peplowski, Nuclear Data

## Slide 25: NSRL is a multi-disciplinary, fixed target beam line hosting user experiments at the RHIC/EIC complex We will operate for the foreseeable future as demand for high energy heavy ion beam continues to grow