## Slide 1: Making the EIC possible: machine perspectives
May 15, 2026
Sergei Nagaitsev
EIC Technical Director

## Slide 2: Compelling EIC Science Case
How do quarks, gluons, and orbital angular momentum contribute to proton spin?
Spin is a fundamental property of matter.
All elementary particles,
but the Higgs, carry spin.
Spin cannot be explained by a static picture, rather the interplay between the properties and interactions of quarks and gluons inside
the proton.
Does the mass of visible matter emerge from quark-gluon interactions?
Atom: Binding/Mass = 0.00000001
Nucleus: Binding/Mass = 0.01
Proton: Binding/Mass = 100
The EIC will determine an important term contributing to the proton mass, the so-called quantum chromodynamics (QCD) trace anomaly.
How can we understand QCD dynamics and the relation to confinement?
EIC will image quarks and gluons in 3D in space and momentum inside the nucleon and nuclei and uncover how the nucleon properties emerge from quarks and gluons and their interactions.
How do quark-gluon interactions create nuclear binding?
Is the structure of a free and bound nucleon the same?
How do quarks and gluons, interact with a nuclear medium?
How do the confined hadronic states emerge from these quarks and gluons?
Does gluon density in nuclei saturate at high energy?
How many gluons can fit in a proton?
How does a dense nuclear environment affect the quarks and gluons, their correlations and interactions?
=
?
gluon
splitting
gluon
recombination
National Academies of Sciences, Medicine, and Engineering, 2018 Consensus Study Report)

## Slide 3: EIC Accelerator Performance
wide center-of-mass energy √s: 20 – 140 GeV :
map the out nucleon and nuclei structure from high to low x
polarized electron and hadron (p, He-3) beams:
access to spin structure of nucleons and nuclei
Spin vehicle to access the spatial and momentum structure of the nucleon in 3d
Full specification of initial and final states to probe q-g structure of NN and NNN interaction in light nuclei
nuclear beams: p to Uranium
accessing the highest gluon densities  saturation
quark and gluon interact with a nuclear medium
high luminosity 1033-1034 cm-2s-1 :
mapping the spatial and momentum structure of nucleons and nuclei in 3d
access to rare probes, i.e. Ws
large acceptance (0.2 – 1.3 GeV) through forward focusing IR magnets
spatial imaging of nucleons and nuclei
gluon emission
?
=
gluon recombination

## Slide 4: EIC Accelerator Performance Requirements
EIC peak luminosities (CDR)
5x41
5x100
10x100
10x275
18x275
Bunch charges: 28 nC (10 GeV, e) and 11 nC (275 GeV, p)
Center-of-mass energies: Ecm = ~20 – 100 GeV (upgradeable to 140 GeV)
High degree of beam polarization: ~70%
Availability of ion beams: from proton to Uranium
Luminosity: 1033 – 1034 cm-2sec-1
Possibly more than one IR
Based on the 2015 US NSAC Long-Range Plan
Figure of merit: to

## Slide 5: EIC concept

## Slide 6: Luminosity performance
ESR fill
Detector Off
“Flat” proton bunches allow for high initial luminosity
Optimal store duration
~4 hours
CoM Energy (GeV) | Average Lumi (x1033 cm-2s-1) (per 4-hour store)
105 | 3
63 | 1.2
45 | 1
140 | 0.44
29 | 0.13
Average
Lumi
EIC peak luminosities (CDR)
5x41
5x100
10x100
10x275
18x275
10x275
Upgrade

## Slide 7: HERA (1992 – 2007)
920 GeV protons (unpolarized)
27.5 GeV electrons (self-polarized by the Sokolov-Ternov effect)
HERA peak luminosity: ~5x1031 cm-2s-1
at ECOM = 318 GeV
The EIC is an electron – ION collider (HERA was an e-p collider)
Variable CoM energy
EIC beams are polarized, starting from the source
New modern particle detector
EIC luminosity is a factor of ~200 higher

## Slide 8: HERA vs EIC: key parameters
HERA EIC FACTOR
Circumference (km) 6.3 3.8 1.7
Number of bunches 174 1160 6.7
Proton bunch charge (nC) 11.7 11 1
Electron bunch charge (nC) 5.3 28 5.3
Bunch length (cm), p/e 16/0.9 6/0.7
Beta at IP (cm), proton H/V (cm) 245/18 80/7.2
Beta at IP (cm), electron H/V (cm) 62/26 45/5.6
Proton emittance, (nm, rms) 4/4 11/1
Electron emittance, (nm, rms) 20/3 20/1.3
Energy (COM), GeV 320 105
Luminosity, x1031 cm-2s-1 5.3 1000 190
60
~3

## Slide 9: Key EIC accelerator concepts
Ribbon-like (flat) hadron beam (11:1 transverse emittance/size ratio)
Large crossing angle (25 mrad)
Operating at beam-beam limits for both beams (0.1 e/ 0.01 p)
Spin preservation from source to collisions (protons and electrons)
Very high bunch intensities and circulating beam currents (1 A (p), 2.5 A (e))
Upgrade path: high-energy hadron cooling at collisions, 2nd detector
These are the key concepts that allow to attain luminosity of ~1034 cm-2s-1 and maintain high polarization at collisions over a broad range of CoM energies

## Slide 10: Key EIC Accelerator Technology Areas
Hadron Beam Cooling
Spin-transparent optics
  High polarization for both beams from source to collisions
  Swap-out injection for electron bunches (at 1 Hz) to maintain high polarization in the ESR
SRF (Crab and elliptical) cavities
  Large-size, complex geometries;
  High-power; HOMs
  Very tight phase and amplitude noise requirements
IR magnets (large aperture, one-of-a-kind SC magnets)
Instability and impedance control;
  Maintain low impedance budget for vacuum chambers, beam screens, kickers, SRF cavities

## Slide 11: Hadron beam cooling
Experimental
demonstration of electron cooling
at NAP-M
(Novosibirsk, 1974).
S. Nagaitsev, et al. “Experimental Demonstration of Relativistic Electron Cooling”, Phys. Rev. Lett. 96, 044801 (2006)
LEReC was designed to operate at electron energies up to 2.6 MeV
(using single-cell SRF accelerating cavity).

## Slide 12: Low-energy Cooler Concept
DC Gun
400kV
e-
Laser
197 MHz
900 kW Beam Dump
16x 197 MHz
NCRF LINAC
extraction
injection
cooling
HSR
4x 591 MHz
NCRF correction Cavities
180° Dipole
Spectrometer
Quad
Cathode transport
Mu-metal shielding
24MHz
RF cavity
SC Quad
130 kW Beam Dump
Extraction line
Injector/linac
Test line
Solenoids
LEReC Cooling Solenoids
180°Dipole
(U-turn)
transport
PM
PM
PM
RF diagnostics line with Deflecting cavity
Injector test
e-
HSR
hadron
hadron
hadron
e-
RF diagnostic
Not to scale
IR2 layout
(all within the
existing RHIC
Tunnel)
150 m cooling section
24 GeV protons
12.5 MeV electrons
Compatible with future beam cooling upgrades at the collision energies

## Slide 13: EIC Low Energy Cooler Parameters
 | electrons | protons
gamma | 25.4 | 25.4
RHIC RF frequency, MHz | 197 | 24.6
Cooling section length, m | 168 | 168
Cooling sections beta function, m | 150 | 100-200
Hadrons Dy, Dy’, m, rad |  | <1, <0.02
Total charge per proton bunch, nC | 3 | 45
Electrons kinetic energy, MeV | 12.46 | 
Electron average current, mA | 74 | 
Normalized emittance, rms, um | <1.5 | 2
rms bunch length, cm | 4 | 100
rms dp/p | <5e-4 | 6e-4
Angles in cooling section, urad | 20-30 | 20
electrons
4-5
704 MHz (9 MHz)
20 m
30 m
3 nC
1.6-2 MeV
30 (60 mA in tests)
<2 um
5 cm
<5e-4
<150 urad
LEReC (2019-2025) key
parameters for reference
A. V. Fedotov et al., Phys. Rev. Lett. 124, 084801 (2020)

## Slide 14: Flat Beam Acceleration Experiment in RHIC
Maximum transverse beam emittance ratio 13:1 was obtained with stochastic cooling at 31 GeV/nucleon
Transverse emittance ratio 11:1 was well maintained during acceleration from 31 GeV/nucleon to 100 GeV/nucleon
Flat beam was stored at 100 GeV/u with EIC/HSR tunes for ~2 hours, 11:1 emittance ratio was well maintained too
Emittance Ratio
Emittance Ratio
Horizontal Emittance
Vertical Emittance
Emittance ratio
100GeV
31 GeV
Emittance ratio
Horizontal Emittance
Vertical Emittance
During Acceleration
Entire store duration
Acceleration
IBS growth
31 GeV
100GeV
July 23, 2025

## Slide 15: Electron beam polarization

## Slide 16: Electron polarization loss in the ESR
Frequent swap-out injection of bunches with high initial polarization of 85%
  Bunch spacing is ~10 ns
Initial polarization decays towards P∞
At 18 GeV, every bunch is replaced (on average) after 2.2 min with RCS cycling rate of 1Hz
Polarization Pav = 70%
The HSR will also have polarized
protons and light ions; RHIC experience
will be key to polarization performance.

## Slide 17: SRF cavities
Hadron bunch length (rms): 6 cm
Electron bunch length (rms): 6 mm

## Slide 18: EIC - RF Systems
Crab Cavities (per IR) | HSR (Cavities/CMs) | ESR (Cavities/CMs)
197 MHz | 8/4 | –
394 MHz | 4/4 | 2/2
Bunch Splitting
3 49.2 MHz NCRF
4 98.5 MHz NCRF Capture & Accel
8 197 MHz NCRF
Low-Energy Cooler, IR02 -
16 197 QWR NCRF,
4 591 NCRF,
1 24 MHz NCRF,
And 1 591 MHz Deflecting Cavity
RHIC – 28 MHz acceleration cavity
4 24.6 MHz Capture & Accel Cavity, IR04
The Project is pre-CD2 and in the design phase.
Many systems are still developing.
IR06
EIC LLRF DAC Clock for Crab Cavities
400 kW Solid State Amplifier
RCS
591 MHz 5-Cell Cavity Cryomodules
2 CMs
HSR NCRF – IR04
Electron Storage Ring & Hadron Storage Ring – IR10
591 MHz 800 kW 2 K
1-Cell Cavity Cryomodules
ESR = 8 CMs, 16 Cav
HSR = 2 CMs, 4 Cav

## Slide 19: IR6 (Crab Cavities)
Facilities
HPRF Amplifiers and Distribution
Crab Cavity Cryomodules
RF Controls
Crabbing System | Quantity
197 MHz HSR | 4 & 4
394 MHz HSR | 2 & 2
394 MHz ESR | 1 & 1
c/o: Karim Hamdi
Notes: Add extra verbiage on issues

## Slide 20: EIC IR layout
9 cryostats housing 11 cold masses (2 K)
  15 magnets (dipole, quadrupole, and combined-function)
    6 “cos-theta” magnets with Rutherford cables, 9 magnets fabricated with Direct Wind technique (DW)
RC-1
RC-2
RC-3
B0pF
FC-1
FC-2
FC-3
FC-4
B2pF
8 cryostats (4 per side) which contain the spin rotators (solenoids 8.5 T, 2K)
  2 long and 2 short per side
Interaction Region - Forward
Interaction Region – Rear
Interaction Region – Rear
Interaction Region - Forward

## Slide 21: EIC IR Superconducting Magnets
B2pF
Q1BpR-Q2eR
Q2pR-eDrift
Q1BpF-Q1eF
Q1ApF-eDrift
Q1ApR-Q1eR
B0ApF-eDrift
Q2pF-eDrift
Spin rotator
B0pF-Q0eF
B1pF-eDrif
B1ApF-eDrift
View from the IP
1 m
All magnets to the same scale

## Slide 22: From RHIC to EIC
Protons: ~40 – 275 GeV
Electrons: 5 – 18 GeV
RHIC
RHIC
EIC
Ion species:
proton – Uranium
60% p polarization

## Slide 23: From RHIC (yellow ring) to EIC HSR
EIC HSR to be composed of existing arcs of the Yellow RHIC ring (remove unused magnets)
Insert sleeves coated with copper and amorphous carbon into superconducting magnet beam pipes to improve conductivity and reduce secondary electron yield (-> electron cloud)
Add new RF cavities
Add hadron cooling to create flat beam
Add crab cavities, new IR SC magnets
Add a collimation system
Add extra ‘snakes’
Actively Cooled Beam
Screen Material procurement
Tripled beam current, shorter bunch length, shorter bunch distance, ‘flat’ beams with small vertical emittance

## Slide 24: Beam Energy and Average Orbit Radius in the HSR
Since the electron revolution frequency is fixed, the hadron orbit must be adjusted with energy to keep the collisions in sync.
70 mm beam pipe
20 mm
275 GeV
100 GeV
store
130 GeV

## Slide 25: The 41-GeV ‘bypass’
Sector 1 without and with the 41-GeV bypass line
This bypass provides access to the lowest EIC CoM energy, 29 GeV

## Slide 26: EIC Electron Storage Ring
Electron Storage Ring (ESR) consists of six FODO-cell arcs, and six straight sections (IRs)
High-intensity (28 nC), short (7 mm) bunches
add many interesting accelerator challenges
Circulating beam current ~2.5 A and the synchrotron
radiation power of ~10MW
EIC needs nearly constant (20 to 24 nm) emittance from
5 to 18 GeV for optimum luminosity, but equilibrium
emittance in an electron storage ring depends on beam energy.
We will use ‘super bends’ (reverse bends) for emittance
control below 10 GeV
36mm
80mm
Heater wire groove
BPM mount
Pump port

## Slide 27: ESR Beam Intensity Parameters
 | 5 GeV | 10 GeV
Num. of electrons per bunch, | 1.72x1011 | 
Bunch Charge, | 28 nC | 
Number of Bunches, | 1160 | 
Single Bunch Current, | 2.2 mA | 
Bunch Length, | 22.7 ps | 25.4 ps
Peak Bunch Current, | 484 A | 433 A
Average Current, | 2.5 A | 2.5 A
 | 5 GeV | 10 GeV
 | 1.72x1011 | 
 | 28 nC | 
 | 1160 | 
 | 2.2 mA | 
 | 22.7 ps | 25.4 ps
 | 484 A | 433 A
 | 2.5 A | 2.5 A

## Slide 28
EIC IR Layout
High Luminosity:
  25 mrad crossing angle
  Small β* for high luminosity
  with limited IR chromaticity contributions
  Large final focus quadrupole aperture
  Machine Detector Interface
  Large detector acceptance
  Forward spectrometer
  No magnets within - 4.5 / +5 m from IP
  Space for luminosity detector, neutron detector, “Roman Pots”

## Slide 29: Electron Injector

## Slide 30: Electron Injector
Function: Deliver electron bunches of up to 28 nC at a 1 Hz repetition rate for injection into the ESR at various energies of 5 – 10 GeV (upgradeable to 18 GeV).
RCS magnet assembly
Vacuum chamber: stainless steel, copper coated (50 um)
Polarized Electron Gun
1-nC, 30 Hz
RCS SRF Cavity, 591 MHz
Beam Accumulator Ring
750 MeV, 40 m
S-band linac, 750 MeV, 30 Hz, 1 nC single bunch
RCS
750 MeV – 18 GeV
28 nC, 1 Hz
85% polarization
1.4 km
Concept modeled after the ANL APS-U injector

## Slide 31: Present EIC Concept (2026)
Accelerator Status at a glance:
Polarized ion/proton source
Ion injection and initial acceleration systems – Linac (200 MeV), Booster (1.5 GeV), AGS (25 GeV)
Hadron Storage Ring (40-275 GeV) – HSR
Electron Pre-Injector (750 MeV linac)
Beam Accumulation Ring (750 MeV) – BAR
Electron Rapid Cycling Synchrotron (0.75 GeV – top energy) – RCS
Electron Storage Ring (5 GeV – 10 GeV) – ESR
Interaction Region(s) – IR
Hadron Cooling System
Ultimate EIC Performance Parameters:
High Luminosity: L= 1033 – 1034cm-2sec-1
Highly Polarized Beams: 70%
Large Center of Mass Energy Range: Ecm = 28 – 140 GeV
Large Ion Species Range: protons – Uranium
Large Detector Forward Acceptance and Low-Background Conditions
Possibility to Implement a Second Interaction Region (IR)
Protons: ~40 – 275 GeV
Electrons: 5 – 10 GeV

## Slide 32: EIC Project: Critical Decisions and Plans
2019
2021
CD-3A, Long-Lead Procurement, approved March 2024. Excellent use of IRA funding.
CD-3B, Long-Lead Procurement, approval planned for 2025.
CD-2 and CD-3 in Preparation
CD-4 EF = 2034

## Slide 33: Summary
EIC is a unique, high-energy, high-luminosity, polarized beam collider that will be one of the most challenging and exciting accelerator complexes ever built – the only new collider in the next decades.
EIC design has converged. The EIC scope is stable and supports the Global Requirements and the DOE Mission Need Statement.
Some project scope is well developed, designs are mature, and is being executed as Long-lead procurements (DOE CD3A and CD3B)
We understand what we need to build to deliver the EIC!