## Slide 1: Variable Rate Neural Compression for TPC Data
RHIC annual user meeting workshop
05-11-2026

## Slide 2
The outer layer group of TPC
249 timesteps on each side along beam direction
16 layers along the radial direction
2304 channels along the azimuthal direction (192 per sub module)
Data from GeV Au+Au collisions with 170 kHz pileup collisions.
Input to a compression algorithm

## Slide 3
Compressed data
(a spatially small tensor with more channels.)
Compression Algorithm
(The encoder part of an Autoencoder model)
Input (a spatially big but flatten tensor)
Spatial dimensions
Spatial dimensions
Channel dimensions
(1 for TPC since it has only one value)
Compression by Size
The vector for one location in the compressed data can be considered as a semantic summary of the receptive field of the location in the input data.

## Slide 4
input
Reconstruction by the compression-by-size approach
Difference
Bruised Reconstruction of the Compression-by-Size approach
Red: reconstruction > ground truth
Blue: reconstruction < ground truth

## Slide 5
Problems of the Compression-by-Size Approach
Inaccurate reconstruction
Fixed size output, even if there is no signals in the input
Fixed time compression, even if there is no signals in the input

## Slide 8
Then, I determined to be lazy
I let the encoder do nothing but to drop signals randomly…
What if the encoder can choose which voxels to keep?
220
Mean squared error of the reconstruction
220
19
With 50% randomly selected signals
90
With 25% randomly selected signals
Best performance of the compression-by-size approach.
And train the decoder to reconstruct the input with remaining signals

## Slide 9
Locate the most important signals

## Slide 10
1
2
3
4
5
6
7
8
9
10
Voxels:
Encoder (importance score assigner)
.42
.35
.93
.01
.57
.88
.71
.89
.95
.99
Scores:
Now, we need to determine voxels to keep, but how?
By choosing a threshold, of course!
Threshold = 0.815484548538
Compression by Importance

## Slide 11
3
6
8
9
10
Voxels
.93
.88
.89
.95
.99
Scores
Decoder
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
Reconstruction accuracy
Back propagation
Ground truth
reconstruction
.42
.35
.93
.01
.57
.88
.71
.89
.95
.99
Minimize total importance score to achieve compression
Compression by Importance
Threshold = 0.815484548538

## Slide 12
Compression by Importance
Threshold = 0.815484548538

## Slide 13
1
Threshold
Density
1
Random Threshold
1
.42
7
.71
Kept:
10
.99
Random Thresholding

## Slide 14
1
Threshold
Density
1
Random Threshold
viv
.71
Now, we get rid of absolutely arbitrary nonsense! But will it work?
Random Thresholding
1.0
Random thresholding can push very important voxels, and very important voxels only, to high scores.

## Slide 15
The BCAE Family – Compression by Size
Bicephalous Convolution Autoencoder
BCAE-2D
BCAE-HT (3D)
BCAE++ (3D)
Code here is a smaller tensor

## Slide 16
Sparse
Convolution
BCAE-VS – Compression by Importance
Variable ratio Compression for Sparse input
Code here is a subset of the input signals

## Slide 17
Sparse Convolution Engines

## Slide 18
Reconstruction Accuracy—regression

## Slide 19
Reconstruction Accuracy—classification

## Slide 20
Performance Comparison
BCAE-VS Reconstruction Performance

## Slide 21
Newest Result of BCAE-VS on proton-proton Collision
type |  | PSNR | precision | recall
Au + Au | 0.0284 | 26.0 | 0.996 | 0.988
p + p | 0.0073 | 28.7 | 0.994 | 0.985
p + p (scaled) | 0.0329 |  |  | 
type |  | PSNR | precision | recall
Au + Au | 0.0284 | 26.0 | 0.996 | 0.988
p + p | 0.0073 | 28.7 | 0.994 | 0.985
p + p (scaled) | 0.0329 |  |  | 
When comparing and compression ratio, the number should be scaled by ratio of occupancy of the two datasets (0.108 / 0.024 = 4.5).
type | Retention ratio | occupancy | CR
Au + Au | 0.133 | 0.108 | 34
p + p | 0.109 | 0.024 | 185
p + p (scaled) |  |  | 41

## Slide 22
Performance Comparison
When we attack the problem from the correct angle, we may not need large model.

## Slide 23
The average throughput of BCAE-VS is smaller than that of the fastest BCAE variant. However, BCAE-VS’s throughput is a function of occupancy. For low occupancy (< 5%), the throughput of BCAE-VS outperforms even the fastest BCAE.
The sparse convolution engine we used for BCAE-VS is not optimized for the state-of-the-art hardware. We can hope for a significant speed-up when there is more hardware support for the sparse convolution engine.

## Slide 24
Compare to Cuda-Enabled Learning-Free Algorithms
Cuda-Enabled Learning-Free
ZFP is a lossy compressor designed for floating-point scientific data. It compresses small independent blocks, making it ideal for simulation data storage with random-access capability.
cuSZ is the first error-bounded lossy compressor on GPUs for scientific data, significantly improving SZ's throughput in GPU-based heterogeneous HPC systems.
cuSZp is an ultra-fast error-bounded GPU lossy compressor that fuses massive computation into one kernel via hierarchical parallelism, drastically improving end-to-end throughput.
Notes: The power of adaptability comparing to smart crafting.

## Slide 25
cuSZp throughput vs batch size
cuSZp throughput at batch size 1
Compare to Cuda-Enabled Learning-Free Algorithms
Have to concatenate a lot of TPC wedges before compression to achieve optimal speed. The compressed data cannot be separated by individual wedge.
72 TPC submodules
Current BCAE-VS implementation needs help with throughput to compete with learning-free compressions

## Slide 26
Summary
For sparse data, we can compress by importance for
More accurate reconstruction
A variable compression ratio
A higher throughput with proper software support
Dataset: https://zenodo.org/records/14064045
GitHub repo: https://github.com/BNL-DAQ-LDRD/NeuralCompression_v3
The current hardware support is still lacking