## Slide 1
FEMC, Calibrations. Initial assessments. (O.Tsai, A.Ogawa)
FEMC – 18320 towers.
Expected initial non-uniformity +/- 10% (sampling fraction variation, calibration of SiPM boards, variations in coupling LG to towers, SiPM boards to LG, calibration of electronics chain…)
Energy resolution - 12%/(E) + (2%-3%)
Requirements from inclusive – 1% energy scale for hadronic states (https://indico.bnl.gov/event/30818/). This will be dominated by calibrations of LFHCAL.
We see requirement as calibration(s) should not add more than ~ 1% into the constant term.
Primary calibration method - pi0 calibration.
Stability monitoring - LED system.
Validation linearity - TBD, may be LED system. (calibration with pi0 limited reach in energy)

## Slide 2: Forward ECAL pi0 calibration
Akio Ogawa 2025 Dec 17 EPIC Calorimeter meeting
Radius [cm] | # of towers | # of >5GeV pi0 / day / tower | # of >2GeV pi0 / day / tower
20<R<100 | ~4800 | 37k | 108k
100<R<150 | ~6200 | 43 | 2.6k
150<R<190 | ~6800 | 4 | 390
PYTHIA6 Q2=0~1GeV DIS events
No decay, no detector MC, just counting PYTHIA pi0 towards FEMC
Assume 20kHz. (12.5kHz ?) DIS events in 1st year of EIC (5 GeV x 41 GeV)
Assume 60% uptime
→ 1B DIS events / day
At this low energy, opening angle between 2 decay photons are large
May need to combine with photons in BEMC for outer radius
Working on study with decay, detector MC, clustering and pi0 reconstruction including background

## Slide 3
Summary:
Central part of the detector can be calibrated within day or two at 5 GeV x 41 GeV, lumi numbers had to be understood, especially at startup.
Peripheral part of the FEMC (R>150cm) is TBD.
No special running conditions required.
Interdependency – probably none (BEMC+FEMC for peripheral part may be too complicated)
All calibration software for FEMC had to be implemented in EICrecon, right now we have nothing in place.