## Slide 1: Initial Results from HRPPD B-field Campaign at BNL
2026/01/12
ePIC TIC Meeting – HRPPDs in magnetic field
Bob Azmoun, Yifan Jin, Jihee Kim, Alexander Kiselev, Brian Page, Martin Purschke, Cheuk-Ping Wong, Craig Woody (BNL)
Andrew Tamis (Yale), Mark Popecki (Incom)

## Slide 2: Motivation
pfRICH: ePIC PID detector
in the electron-going endcap
Verify HRPPD operation in magnetic fields typical for the pfRICH sensor location in ePIC
  Magnetic field strength up to ~1.3 T
  Field-to-HRPPD window normal angles up to ~13°
Conduct a systematic study over (HV, magnetic field, inclination angle) parameter space
Goal: Produce publishable-quality results
Two measurement campaigns @ Superconducting Magnet Division at BNL
  Nov 17–26* (installation and dry runs included)
    *Nov 20–21 (CERN Director-General Visit SMD at BNL)
  Dec 11–12

## Slide 3: Facility and Experimental Area
Superconducting
Magnet Division (SMD)
at BNL
warm dipole
10’ long rails
HRPPD enclosure mounted on a sled
DAQ PC
rack with HV, digitizers, NIM logic
PiLas laser; Hall probe controller
Notes: 10′: 10 feet

## Slide 4: Team
Alexander
Andrew (Yale)
Bob
Brian
Craig
Jihee
Mark (Incom)
Martin
Ping
Yifan
Participated remotely: Alexey Lyashenko (Incom), Yordanka Ilieva (South Carolina)
Local support @ SMD: Vikas Teotia, Chris Tamagro, Ray DeSalvo

## Slide 5: Experimental Setup details
HRPPD assembly
Hall probe and fiber port at the bottom
Retractable sled with an optically tight HRPPD assembly
Protractor with pin holes (2.5° step) to fix a tilt angle
Assembly can be rotated around XY-axes and flipped upside down
PiLas laser is SM-fiber coupled to the enclosure
3D Hall probe attached (rotates together with the assembly)
Readings are included in the event file headers
A single 88 pad spot equipped with MCX adapter cards
Remember, HRPPD anode has a 3232 uniform pixellation
10’ long RG-174 cables to V1742 CAEN digitizer(s)
Most part of the data taken with a single digitizer (66 - 4 pad area)

## Slide 6: Optical configuration details
mirror
diaphragm
lens
ND filter inside
fiber adaptor
Use F=20mm plano-convex lens in a 2F-2F configuration
OD4 filter, diaphragm fully open
At a 40% laser tune get 5-7 % useful events
Beam spot size ~1.5mm diameter
See backup slides
CAD model
Bottom half of the HRPPD enclosurel

## Slide 7: Data Taking and Online Monitoring
RCDAQ-based data acquisition by Martin Purschke, VNC, elog, HV control, online display
Fully automated data taking in a batch mode (except for magnet ramp-up and ramp-down)
~1.5 kHz on tape, typically 100k events per setting, ~1500 runs, ~7.5TB of data
A typical “beam test” environment (and a very useful exercise before going to a pfRICH beam test @ CERN)
Near-online data analysis, with subsequent data productions on BNL SDCC
Online Monitoring VNC display
Data Summary Google sheet
A 6x6-4 instrumented pad area

## Slide 8: Typical Waveforms (Single Event)
~200 ns full range (1024 samples @ 5 GS/s); few dozens of mV signals (gain-dependent of course)
Charge sharing between channels 17 and 18, with an afterpulse observed in channel 18
ch10
ch11
ch12
ch13
ch16
ch17
ch18
ch19
ch22
ch23
ch24
ch25
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]

## Slide 9: Typical Accumulated Waveforms
Charge sharing between channels 17 and 18, with afterpulsing observed in channel 18
Other channels also show some activity when several waveforms are accumulated (stray photons?)
ch10
ch11
ch12
ch13
ch16
ch17
ch18
ch19
ch22
ch23
ch24
ch25
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]

## Slide 10: Run Configuration Parameters
Tilt axis: +/-X, +/-Y, +/-X with assembly flip imitating B-field sign change
High voltage (HV): MCP symmetric, MCP asymmetric, PC HV variation
Magnetic field: 0–1.86 T (magnet current 0–2000 A)
Inclination angle (θ): -30° to +30° (actual range tilt axis dependent)
Only a fraction of results will be shown today; also see the backup
Laser repetition rate: 600 Hz, 1 kHz, 1.6 kHz (default), 2 kHz, 10 kHz
A NIM trigger pulse signal gets digitized by the V1742 along with the HRPPD pad signals
Laser tune: 30 %, 40 % (default)
Single photon mode: typically, ~5-7% of “useful” events out of 100k events / run
Notation: 200 – 675 – 200 – 675 – 200V
anode photocathode

## Slide 11: HRPPD assembly rotation axes
x
y
z
HRRPD facing down, +/-X rotation (“main” axis)

## Slide 12: HRPPD assembly rotation axes
x
y
z
PC
HRRPD facing down, +/-X rotation (“main” axis)

## Slide 13: HRPPD assembly rotation axes
x
y
z
HRRPD facing down, +/-X rotation (“main” axis)

## Slide 14: HRPPD assembly rotation axes
x
y
z
Back: anode, readout, PCB
PC
Front: fused silica
PiLas
x
y
z
HRRPD facing down, +/-X rotation (“main” axis)
Yet MCP#1 & MCP#2 chevron capillary orientation needs to be clarified
+12.5° rotation around X axis
is when MCP#1 pores
are aligned with the B-field (?)
Capillary orientation
MCP #1
MCP #2

## Slide 15: Hall probe orientation / misalignment
Tilting Along X axis
  X axis avg. offset: -1.4° (Protractor error)
  Y axis avg. offset: -0.4° (Hall probe misalignment)
Tilting Along Y axis
  Offset has small dependence on nominal angle due to slight misalignment
Absolute field values
are reproducible within ~0.3 % throughout the whole data taking period
Use mounted Hall probe readings to measure magnetic field components on a run-by-run basis to correct the “nominal” angles
ANDREW TAMIS

## Slide 16: Example charge Spectra vs Magnetic Field
With a 0T Spectrum included
Zoomed in non-zero B-field data
Charge calculation: a sum of 34 neighboring pad signals in a 4ns wide window (20 time bins)
Gain reduction with increasing magnetic field (see backup: full magnetic field set)
Units: 1600 fC is equivalent to a gain of 107
JIHEE KIM

## Slide 17: Mean Charge Extraction (Gain)
1-photon
2-photon
1-photon
2-photon
Fit pedestal (Gaussian) alone
Apply a 4σ cut to remove the pedestal
Mean charge =
Histo→GetMean()
Mean charge error =
Histo→GetRMS()
Currently it is based on an average over 1-photon & 2-photon contributions
Eventually, will account for 0-photon, 1-photon & 2-photon Poisson statistics and also go down to a ~2s cut
Polya fit does not work well anyway (see backup: gain saturation, no large amplitudes)
JIHEE KIM

## Slide 18: Gain vs Magnetic Field at various tilt angles
Time Window Based Analysis
Threshold Based Analysis
Two independent analyses were conducted: time-window–based and threshold-based event selection
The mean charge values from both methods are consistent
JIHEE KIM, YIFAN JIN

## Slide 19: HRPPD Gain in a “pfRICH tilt angle” range of interest
One can easily achieve >106 gain of few times 106 the whole tilt angle range of interest
Which may mean that all 68 HRPPDs can be oriented the same way
At these HV settings an HRPPD would not trip even at a zero field
We’ve taken this type of data in a range of a photocathode and transfer voltages, for a sake of completeness
~1.3T
~1.3T
~1.3T
pfRICH sensor plane location in ePIC: up to ~1.3T field, tilt angles up to 13°

## Slide 20: HRPPD Gain vs Tilting Angle
X-axis: a minimum in gain is observed at approximately +15° nominal angle (B-fieldis roughly aligned with MCP#1 pores)
X-axis: there is also a small dip at −12.5° nominal angle (B-field is roughly aligned with MCP#2 pores)
Gain slightly decreases at large negative tilting angles (around −30°)
Y-axis: a smaller angular dependence is observed

## Slide 21: Repetition rate dependency
Gain can be rate-dependent, especially in a high magnetic field, due to the electron avalanche focusing when only few of the MCP#2 pores are involved and can therefore saturate
One can indeed see a substantial rate dependency, however under the conditions we took data (1.6 kHz repetition rate, ~5-7% useful event fraction) a respective correction will be very small
Laser 1.6 kHz
Signal fraction ~5%
YIFAN JIN
Signal rate = laser repetition rate * fraction of signal events in a run.
200-675-200-675-200V
1.3 T, 0° tilt angle

## Slide 22: After-pulsing example: accumulated waveforms
+X tilt axis, = 0.37T, , laser tune 40 %, laser rep rate 1.6 kHz
HV 200-650-200-650-200
HV 200-675-200-675-200
HV 200-700-200-700-200
ch18
ch18
ch18
An increase in MCP bias voltage leads to more pronounced after-pulses
Which presumably means a faster photocathode aging
As a rule of thumb, the after-pulsing rate should be kept <1% or so

## Slide 23: After-pulse rate
For different HV setting, after-pulse rate ranges from O(1)% - O(10)%
For “reference” pfRICH settings (200-675-200-675-200V @ 1.3 T and 0o tilting angle), after-pulse rate is ~1.3% in a 70ns window past the primary photoelectron pulse
B field: 1.3 T
B field: 1.3 T
Set 1
Set 2
YIFAN JIN
H+ ions
After-pulse rate (for about the same gain)
strongly depends on MCP#1 voltage

## Slide 24: Dark count rate
Using 11 runs, each run has 100k events, 32 channels, first 500 bins in the waveform (laser shots around bin 600), with HV setting 200-675-200-675-200, 1.3 T magnetic field, 0o tilting angle: 10 dark count events are found.
Thus, dark count rate (1.3T) = ~30 Hz/cm2
With HV setting 200-675-200-675-200, 0 T magnetic field, ~5700 dark count events are found in one run
Thus, dark count rate (0 T) = ~170 kHz/cm2
LASER
mV
Bin [0.2ns]
YIFAN JIN
dark counts
after-pulses
primary
photo-electrons
pfRICH case
Compare to a zero-field case:

## Slide 25: Detection efficiency
YIFAN JIN
~1.3T
HV setting 200-675-200-675-200, 0o tilting angle
More studies needed (in a range of tilt angles and HV settings), but first impression is that there is no critical detection efficiency loss in a “typical pfRICH configuration”

## Slide 26: Timing resolution with a DRS4 readout
In “typical” pfRICH conditions (1.3 T magnetic field, 0o tilting angle), with HV settings 200-675-200-675-200V (gain ~3*106), we observe ~52 ps timing distribution core Gaussian width
PiLas laser contribution, effect of DRS4 timing calibration and NIM trigger jitter not unfolded
Weak dependence on a B-field is observed
YIFAN JIN
no idea why
don’t ask

## Slide 27: Timing resolution using a 50 GS/s scope
Data taken at 0, 0.374, 1.138, and 1.509 T
Zero field HV: MCP = 650, PC = 200 V
Non-zero field HV (left to right):
  MCP = 675, PC = 200
  MCP = 675, PC = 400
  MCP = 700, PC = 200
Crystal Ball
Gaus Core
Zero Field
1.5 T (first point)
0.15
0.05
BRIAN PAGE

## Slide 28: Outlook
Need to perform a gain uniformity scan and other calibration measurements
A thorough data analysis and paper drafting will take a couple of more months
  All materials are available under this Indico category
The setup has been left intact and turnkey ready
Would therefore like to come back and repeat the timing measurements using a femtosecond laser and a fast scope, some time in February
  Eliminate PiLas laser timing jitter, DRS4 calibration contribution and NIM trigger jitter
  Come up with a definitive statement about the expected HRPPD timing resolution in a pfRICH-like configuration
BNL SMD welcomes other ePIC groups to use the facility (but be aware about a 6” gap and <1.8 T field limitations)

## Slide 29: Backup Slides

## Slide 30
IMG-4449.jpg
Small spot, vacuum side of window
No. of mm width: 1.5
MARK POPECKI

## Slide 31: Example – Mean Charge Extraction (Gain)
Fit pedestal (Gaussian) alone
Apply a 4σ cut to remove the pedestal
Fit polya function
Define pedestal using Gaussian fit and apply a 4σ cut to remove the pedestal
Remaining distribution using polya fit to estimate mean charge. Not always works (case-by-case)

## Slide 32: Example – Mean Charge Extraction (Gain)
Fit pedestal (Gaussian) alone
Apply a 4σ cut to remove the pedestal
Fit polya function
Define pedestal using Gaussian fit and apply a 4σ cut to remove the pedestal
Remaining distribution using polya fit to estimate mean charge. Not always works (case-by-case)

## Slide 33: Example – Mean Charge Extraction (Gain)
Fit pedestal (Gaussian) alone
Define pedestal using Gaussian fit and signal using Polya fit.
Apply a combined fit (Gaussian + Polya)
Fit combined Gaussian + Polya

## Slide 34: Example – Mean Charge Extraction (Gain)
Fit pedestal (Exponential) alone
Define pedestal using Exponential fit and signal using Polya fit.
Apply a combined fit (Exponential + Polya)
Fit combined Exponential + Polya

## Slide 35: Charge Spectra VS Magnetic Field
Charge calculation: 34 neighboring pad selection.
Peak shifts toward lower charge values.
Gain reduction with increasing magnetic field.
With 0T Spectrum
Without 0T Spectrum

## Slide 36: Charge Spectra VS Inclination Angle
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
  case shows behavior different from other angles
Takeaway:
  Overall angular dependence is weak

## Slide 37: Charge Spectra VS Inclination Angle (+θ)
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
  and cases show behavior different from other angles
Takeaway:
  Overall angular dependence is weak

## Slide 38: Charge Spectra VS Inclination Angle (-θ)
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
Takeaway:
  Overall angular dependence is weak

## Slide 39: Charge Spectra VS Inclination Angle
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
  and cases show behavior different from other angles
Takeaway:
  Overall angular dependence is weak

## Slide 40: Gain VS Magnetic Field (w/ HV)@ θ=-1.4°
Measured mean charge as a function of magnet current at different bias voltage
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge reduces as higher magnet current
  Mean charge increases as higher bias voltage
Takeaway:
  Gain partially recovered by increasing bias voltage

## Slide 41: Gain VS Magnetic Field (w/ HV)@ θ=+11.6°
Measured mean charge as a function of magnet current at different bias voltage
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge reduces as higher magnet current
  Mean charge increases as higher bias voltage
Takeaway:
  Gain partially recovered by increasing bias voltage

## Slide 42: Charge Spectra VS Magnet Current
JIHEE KIM
Measured charge spectra with different magnet current
Charge calculation:
  34 channel selection
  Channels: 10–13, 16–19, 22–25
Observations:
  Clear peak shift with increasing magnetic field
  Peak shifts toward lower charge values
  Higher magnetic field narrower spectra
Takeaway:
  Gain reduction with increasing magnetic field
Data used: 200197, 200198, 200199, 200200, 200201, 200202, 200203, 200204, 200205 (11/19/2025)

## Slide 43: Charge Spectra VS Magnet Current
JIHEE KIM
Measured charge spectra with different magnet current
Charge calculation:
  34 channel selection
  Channels: 10–13, 16–19, 22–25
Observations:
  Clear peak shift with increasing magnetic field
  Peak shifts toward lower charge values
  Higher magnetic field narrower spectra
Takeaway:
  Gain reduction with increasing magnetic field
Data used: 200197, 200198, 200199, 200200, 200201, 200202, 200203, 200204, 200205 (11/19/2025)

## Slide 44: Charge Spectra VS Inclination Angle
JIHEE KIM
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
  and cases show behavior different from other angles
Takeaway:
  Overall angular dependence is weak
Data used: 200171, 200185, 200194, 200203, 200217, 200227, 200236, 200245, 200254 (11/19/2025), 200267, 200280, 200289, 200298, 200307, 200316 (11/24/2025)

## Slide 45: Gain VS Magnet Current (w/ θ)
JIHEE KIM
Data used: 200332, 200336, 200338, 200341, 200351, 200356, 200390, 200395, 200398, 200402, 200409, 200413, 200450, 200455, 200458, 200462, 200469, 200473, 200540, 200545, 200548, 200552, 200559, 200563 (11/24/2025), 200934, 200939, 200942, 200946, 200953, 200957, 200969, 200974, 200977, 200981, 200988, 200992, 201049, 201068 (11/26/2025), 201452, 201457, 201525 (12/12/2025)
Measured mean charge as a function of magnet current at different inclination angles
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  At 0 A, gain remains the same regardless of angles
  Overall gain follows exponential slope across angles
Takeaway:
  Overall angular dependence is weak
  Gain dependence on magnet current can be parameterized as:
See backup slides for results from measurements taken on different dates

## Slide 46: Gain VS Magnet Current (w/ θ=0°, ±12.5°)
JIHEE KIM
Measured mean charge as a function of magnet current at different inclination angles
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  At 0 A, gain is nearly identical for all inclination angles
  Overall gain follows exponential slope across angles
  Measurements taken on different dates are consistent with each other
Takeaway:
  Overall angular dependence is weak
  Gain dependence on magnet current can be parameterized as:
Data used: 200450, 200455, 200458, 200462, 200469, 200473 (11/24/2025), 200934, 200939, 200942, 200946, 200953, 200957, 200969, 200974, 200977, 200981, 200988, 200992, 201049, 201068, 201085, 201091, 201099 (11/26/2025), 201412, 201414, 201417, 201421, 201425, 201429, 201435, 201437, 201440, 201444, 201448, 201452, 201457 (12/12/2025)

## Slide 47: Gain VS Magnetic Field (w/ θ=0°, ±12.5°)
JIHEE KIM
Measured mean charge as a function of magnet current at different inclination angles
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  At 0 A, gain is nearly identical for all inclination angles
  Overall gain follows exponential slope across angles
  Measurements taken on different dates are consistent with each other
Takeaway:
  Overall angular dependence is weak
  Gain dependence on magnetic field can be parameterized as:
Data used: 200450, 200455, 200458, 200462, 200469, 200473 (11/24/2025), 200934, 200939, 200942, 200946, 200953, 200957, 200969, 200974, 200977, 200981, 200988, 200992, 201049, 201068, 201085, 201091, 201099 (11/26/2025), 201412, 201414, 201417, 201421, 201425, 201429, 201435, 201437, 201440, 201444, 201448, 201452, 201457 (12/12/2025)

## Slide 48: Gain VS Magnet Current (w/ θ=0°)
JIHEE KIM
Measured mean charge as a function of magnet current at different inclination angles
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  At 0 A, gain is nearly identical for all inclination angles
  Overall gain follows exponential slope across angles
  Measurements taken on different dates are consistent with each other
Takeaway:
  Overall angular dependence is weak
  Gain dependence on magnet current can be parameterized as:
Data used: 200197, 200198, 200199, 200200, 200201, 200202, 200203, 200204, 200205 (11/19/2025), 200450, 200455, 200458, 200462, 200469, 200473 (11/24/2025), 201085, 201091, 201099 (11/26/2025), 201457 (12/12/2025)

## Slide 49: Gain VS Magnetic Field (w/ θ=0°)
JIHEE KIM
Measured mean charge as a function of magnet current at different inclination angles
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  At 0 A, gain is nearly identical for all inclination angles
  Overall gain follows exponential slope across angles
  Measurements taken on different dates are consistent with each other
Takeaway:
  Overall angular dependence is weak
  Gain dependence on magnetic field can be parameterized as:
Data used: 200197, 200198, 200199, 200200, 200201, 200202, 200203, 200204, 200205 (11/19/2025), 200450, 200455, 200458, 200462, 200469, 200473 (11/24/2025), 201085, 201091, 201099 (11/26/2025), 201457 (12/12/2025)

## Slide 50: Scope Timing resolution: Pedestal Cut Only
BACKUP

## Slide 51: Scope Timing resolution: Amplitude Correction
BACKUP

## Slide 52: Scope Timing resolution: 2-Gaus Fit
Zero Field
Full Fit
1st Gaus
2nd Gaus
1.5 T Field
MCP = 675 V
PC = 200 V
BACKUP

## Slide 53: Scope Timing resolution: Laser Contribution
In B-Field setup with PiLas laser and scope, measure time resolution of ~40 ps at zero field and ~50 ps at 1.5 T
With femtosecond laser and scope in lab, measure time resolution of ~16 ps
PiLas laser contribution to timing resolution = = ~37 ps
HRPPD timging resolution @ 1.5 T = = ~34 ps
Many assumptions and hand waving, but we could be seeing ~ a factor of 2 degradation in intrinsic HRPPD timing performance from 0 T to 1.5 T
BACKUP

## Slide 54: Gain VS Magnetic Field (w/ HV)@ θ=-12.5°
JIHEE KIM
Alexander’s
Yifan’s
Large difference was shown at 1900 A measurement especially at HV = 650 V and 725 V.

## Slide 55
Complimentary documents for timing VS B-Field.