## Slide 1: Team Photo
JIHEE KIM

## Slide 2: Data Taking and Online Monitoring
RCDAQ-based data acquisition @ ~1.5 kHz on tape, VNC, elog
Fully automated data taking in a batch mode (except for magnet ramp-up and ramp-down)
Real-time tabulated data summaries generated during data taking
Express online data quality analysis
Online Monitoring DAQ PC
Data Summary Google Sheet
https://docs.google.com/spreadsheets/d/1YWhTMTupEhW2SHGdD-VX3CkcM7VUVixBggy1QHezrBc/edit?usp=sharing
JIHEE KIM

## Slide 3: Typical Waveforms (Single Event)
Main charge sharing occurs between channels 17 and 18, with afterpulsing observed in channel 18.
ch10
ch11
ch12
ch13
ch16
ch17
ch18
ch19
ch22
ch23
ch24
ch25
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
JIHEE KIM

## Slide 4: Typical Accumulated Waveforms
Main charge sharing occurs between channels 17 and 18, with afterpulsing observed in channel 18.
Additional channels also show signal activity when up to 10k waveforms are accumulated.
ch10
ch11
ch12
ch13
ch16
ch17
ch18
ch19
ch22
ch23
ch24
ch25
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
Amplitude [mV]
Time Sampling Bin [200ps]
JIHEE KIM

## Slide 5: Mean Charge Extraction (Gain)
Currently it is based on combined 1-photon & 2-photon contributions (first-order approximation)
Eventually, will be extracting 1-photon event charge
Polya fit does not work well (see backup: gain saturation, no large amplitudes)
1-photon
2-photon
1-photon
2-photon
Fit pedestal (Gaussian) alone
Apply a 4σ cut to remove the pedestal
Mean charge =
Histo→GetMean()
Mean charge error =
Histo→GetRMS()
JIHEE KIM

## Slide 6: Charge Spectra VS Magnetic Field
Charge calculation: 34 neighboring pad selection.
Peak shifts toward lower charge values.
Gain reduction with increasing magnetic field (see backup: full magnetic field set).
With 0T Spectrum
Without 0T Spectrum
JIHEE KIM

## Slide 7: Gain VS Magnetic Field (w/ θ)
Time Window Based Analysis
Threshold Based Analysis
Two independent analyses were conducted: time-window–based and threshold-based.
The mean charge values from both methods are consistent.
JIHEE KIM

## Slide 8: Afterpulsing: Accumulated Waveforms
+X tilt axis, = 0.37T, , laser tune 40 %, laser rep rate 1.6 kHz
HV 200-650-200-650-200
HV 200-675-200-675-200
HV 200-700-200-700-200
ch18
ch18
ch18
Primary signal channel is 18.
An increase in MCP bias voltage leads to more pronounced afterpulses and higher signal amplitude
JIHEE KIM

## Slide 9: Backup Slides
JIHEE KIM

## Slide 10: Example – Mean Charge Extraction (Gain)
Fit pedestal (Gaussian) alone
Apply a 4σ cut to remove the pedestal
Fit polya function
Define pedestal using Gaussian fit and apply a 4σ cut to remove the pedestal
Remaining distribution using polya fit to estimate mean charge. Not always works (case-by-case)
JIHEE KIM

## Slide 11: Example – Mean Charge Extraction (Gain)
Fit pedestal (Gaussian) alone
Apply a 4σ cut to remove the pedestal
Fit polya function
Define pedestal using Gaussian fit and apply a 4σ cut to remove the pedestal
Remaining distribution using polya fit to estimate mean charge. Not always works (case-by-case)
JIHEE KIM

## Slide 12: Example – Mean Charge Extraction (Gain)
Fit pedestal (Gaussian) alone
Define pedestal using Gaussian fit and signal using Polya fit.
Apply a combined fit (Gaussian + Polya)
Fit combined Gaussian + Polya
JIHEE KIM

## Slide 13: Example – Mean Charge Extraction (Gain)
Fit pedestal (Exponential) alone
Define pedestal using Exponential fit and signal using Polya fit.
Apply a combined fit (Exponential + Polya)
Fit combined Exponential + Polya
JIHEE KIM

## Slide 14: Charge Spectra VS Magnetic Field
Charge calculation: 34 neighboring pad selection.
Peak shifts toward lower charge values.
Gain reduction with increasing magnetic field.
With 0T Spectrum
Without 0T Spectrum
JIHEE KIM

## Slide 15: Charge Spectra VS Inclination Angle
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
  case shows behavior different from other angles
Takeaway:
  Overall angular dependence is weak
JIHEE KIM

## Slide 16: Charge Spectra VS Inclination Angle (+θ)
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
  and cases show behavior different from other angles
Takeaway:
  Overall angular dependence is weak
JIHEE KIM

## Slide 17: Charge Spectra VS Inclination Angle (-θ)
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
Takeaway:
  Overall angular dependence is weak
JIHEE KIM

## Slide 18: Charge Spectra VS Inclination Angle
Measured charge spectra at different inclination angles with magnetic field ~ 1.4 T
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge remains consistent across most angles
  and cases show behavior different from other angles
Takeaway:
  Overall angular dependence is weak
JIHEE KIM

## Slide 19: Gain VS Magnetic Field (w/ HV)@ θ=0°
Measured mean charge as a function of magnet current at different bias voltage
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge reduces as higher magnet current
  Mean charge increases as higher bias voltage
Takeaway:
  Gain partially recovered by increasing bias voltage
JIHEE KIM

## Slide 20: Gain VS Magnetic Field (w/ HV)@ θ=+13°
Measured mean charge as a function of magnet current at different bias voltage
Charge calculation:
  Major signal channel selection by accumulated signals
Observations:
  Mean charge reduces as higher magnet current
  Mean charge increases as higher bias voltage
Takeaway:
  Gain partially recovered by increasing bias voltage
JIHEE KIM