## Slide 1: Global Support Structure (GST) and interfaces
Andreas Jung
Covers both GST and interface mechanics
Purdue University
Physicist

## Slide 2: Charge Questions Addressed
Is the progress and design maturity for all detector systems, support structures, and moving mechanisms technically sound, feasible, and sufficiently mature to advance toward final design and aligned with being baselined in June 2026 (>60% maturity is required)?
Have the required building and facility modifications (floor loading, rails, crane capacity, utilities, service routing, etc.) been adequately analyzed, addressed, or planned?
Have ES&H and QA considerations been adequately incorporated into the designs at their present stage?
Do the designs and installation plans for the Outer Detectors (Barrel HCAL, Barrel EMCAL, Magnet), Inner Detectors within the GST (DIRC, MPGD, TOF, Silicon, EEEMCAL, pfRICH), and the Endcaps (Forward EMCAL/HCAL) meet support, alignment, movement, access, and integration requirements within building/rail constraints?
Are preliminary cooling schemes adequately developed and documented, do they meet thermal and reliability requirements, and are interfaces across subsystems and to facility cooling/HVAC clearly defined?
Is the project team ready to proceed to final design for the scope under review, and what recommendations should be addressed beforehand?
Have the recommendations from previous reviews been adequately addressed?

## Slide 3: Outline
Introduction
TOF-LGAD mechanics
  LGAD-TOF Barrel and Discs
  TOF tray Integration
Global Support Tube
  Design
  Envelopes & Loads
  FEA simulations
Integration & Assembly
  Inner Detectors + GST
  For PST+SVT: see Ben’s talk
QA/QC, ES&H
Summary
Charge 1, 4

## Slide 4: Introduction to Support Structure
Global Support Tube (GST) supports all inner detectors: DIRC, MPGD, TOF, Silicon, EEEMCAL, pfRICH
Time-of-Flight (TOF) aka AC-LGAD
  Detectors and services supported by Global Support Tube (GST)
Images from Roland Wimmer, BNL
6.5m
9.5m
TOF
GST
Charge 1, 4

## Slide 5: Inner Detector Support Hierarchy Y-Z View - Oct 2025
OMPGD
HP DIRC
OMPGD
GST
GST
e-
p
PST
Beam Pipe
p
f
R
I
C
H
TO
F
M
P
G
D
M
P
G
D
Sector Trays to GST
E
E
E
M
C
A
L
Services Support
Services Support
Beam Pipe Break
Supports that act as load transfer paths
All masses are on slide 20 of this talk, details on SVT mass are in B. Denos talk
Total Weight: 5675 kg
LGAD - TOF
MPGD
MPGD
M
P
G
D
M
P
G
D
PST Feet to Rails
PST Feet to Rails
LGAD - TOF
MPGD
MPGD
L4
L3 L2
L1, L0
HD0 HD1 HD2 HD3 HD4
ED4 ED3 ED2 ED1 ED0
Electron Beam
(East, Forward, Z+, hadron-going)
Hadron Beam
(West, Backward, Z-, electron-going)
Z
Y
X o
HP DIRC
Outer MPGD on the outside of GST
Charge 1, 4
NOT TO SCALE

## Slide 6: Inner Detector Support Hierarchy X-Y View - Oct 2025
NOT TO SCALE
Key:
Beam Pipe
SVT Inner
Outer Barrel
SVT Disks
Inner MPGD
TOF Barrel
Composite Support Tube/s
Support
Rail
GST
Detector View at Z=0
PST
GST supports (provides adjustability)
Beampipe support plates via PST (Details in B. Denos’ talk)
Barrel connection radial “cone” attachments seen in gray
3 connections per SVT half-disk to PST
To ease maintenance and integration the inner detectors (TOF, i- and o-MPGD) follow a 30 degree segmentation!
Key:
hpDIRC Prism
hpDIRC & oMPGD
Services
Barrel TOF
iMPGD
Support tubes
- GST & PST
Charge 1, 4

## Slide 7
Presentation Section 1:
Brief Overview of Sub-detector Mechanics
(all supported by GST)

## Slide 8: pfRICH Design
Vessel
Sensor Plane
Mirrors
Aerogel Wall
Major Components:
Shape: 1/2” thick cylinder (12.7 mm)
Outer Diameter: 1300 mm
Length: 491 mm
Precision: < 1 mm radius and length
Technology: Carbon-fiber composite material with nomex honeycomb core
Chosen as a technology baseline for ePIC in April 2023

## Slide 9: EEEMCAL Detector Design
Dimensions:
Outer diameter = 1346 mm (R673 mm)
Inner diameter = 120 mm
Length max (with electronics and cables) = 800 mm
Crystal ≈ 700g / Nb of crystals ≈ 2750 → 2 Tons
Total mass ≈ 2,5 Tons (with mechanics & electronics)
Major components:
PWO crystals
External structure (Cooling, FSW coldplates)
Internal structure (Cooling, copper tubes)
Front copper plate (Passive cooling)
Electronics (SiPM + Front end)

## Slide 10: hpDIRC Detector Design
Forward
Backward
Bar Box
Prism Box
Support Ring
Connection to ePIC Barrel
Readout Box
Box shell
  Current Material: CFRP with thickness 5 mm
Contains expansion prism, calibration laser
Supports sensors, readout electronics, and associated services
Bar Boxes:
CFRP Shell
  Approximately 4.6m Long
  Thickness: 1.5 mm – 3 mm (thicker at times)
Contains Quartz Radiator Bars, Mirrors, and Lenses
  10 long bars each formed by 3 short bars and a Light Guide section

## Slide 11: Outer MPGD (μRWELL-BOT) and Inner MPGD aka CyMBaL
New design for inner MPGD (CyMBal): 12 sectors with fish scale overlaps
New design with 12 sectors for better integration, installation and maintenance together with the barrel time of flight detector
  48 tiles: 12 in ϕ × 4 in z
GST (and TOF trays) provides 4 mount points to inner MPGD (cymbal) per z-side
  All services route within iMPGD envelope to outside, TOF is outermost radii and iMPGD is below that as far as services go
Module
Module
µRWELL-BOT layout
Module design
24 planar detector modules
12 sectors in r*φ × 2 modules in z  No overlaps
Rmin = 72.5 cm; Rmax = 75 cm

## Slide 12: MPGD discs (μRWELL-ECT)
16 Quadrant modules
GEM- Rwell hybrid configuration guarantees gain higher than 104
2D strip read-out a “COMPASS-like” scheme
<150 𝜇m intrinsic spatial resolution for perpendicular tracks
Time resolution
Material Budget <1 % X0
On-detector Front End Boards (FEBs) based on SALSA chips
Two MPGD Endcap Tracking (ECT) disks both in the hadronic and in the leptonic regions increase the number of hits in the |η| > 2 region to improve pattern recognition.
Lepton Endcap
Disks
Hadron Endcap
Disks
μRWELL-ECT

## Slide 13: TOF Sub-Systems
To ease maintenance and integration the
inner detectors follow a 30 degree segmentation!
TOF detector provides particle ID for EPIC
Consists of AC-LGAD’s
Barrel “stavelet” base unit
  60mm wide, 160mm long
  2 x 8 stavelets per half-stave of 1270mm (z+) and 1370 (z-) length
    Includes space for portcards and patchpanel on z-
   288 half staves yields 4608 stavelets
Forward TOF (disc)
Sandwich structure with cooling pipes
Kinematic mount to PST - GST
Charge 1, 4

## Slide 14: Barrel TOF & inner MPGD supports
2mm overlap
Tray mounts via top rails to GST
  Thin line “tracks” a TOF tray, open space inside is for services of TOF
  Designed for 2mm overlap
Other solidly filled areas are “reserved” for service of SVT+oMPGD and TOF+iMPGD
Updated drawing for support of inner MPGD:
Example from CMS “trays”
Charge 1, 4, 6
GST and TOF trays provide 4 mount points to inner MPGD (cymbal) per z-side
All services route within iMPGD envelope to outside, TOF is outermost radii and iMPGD is below that as far as services go

## Slide 16
Presentation Section 2:
Global Support Tube (GST)

## Slide 17
GST supports the 2 “outer” detector systems (hpDIRC & oMPGD) and all inner detectors, all supported by the Global Support Tube
  Total weight GST + inner and outer detectors + services: ~ 5600kg
  For comparison: CMS is similar!
“Double-decker” sandwich structure with internal beams and I-beam cells
  Made from honeycomb core and two face sheets on either side bonded to it + 5mm skin further out
  2mm face sheets +6mm core
  ~425kg self weight
Two Inner detector support rails:
  5.3m long (or 2.65m x 2); ~14x20mm cross section
  Support ~3100 kg inner detectors
Face sheets:
“Carbon Fiber Reinforced Polymer” or CFRP
Global Support Structure (GST)
Dimensions:
Structure is 5050 mm long; with the outer being shorter 4600 mm
Sandwich tube: 1430mm ID, 1450mm OD
Outer tube: 5mm skin between 1610mm and 1620mm
Charge 1, 4, 6

## Slide 18: GST – internal rip structure
Charge 1, 4, 6
Internal rip structure to stiffen GST as needed to support >5t
End rings to provide support for GST bracket and to distribute load, more rings in EEEMCal area
GST support rails for PST feet
Electron direction
(EEEMCal direction)
Massive CFRP
20 x 14mm, full length

## Slide 19: GST tolerances/constraints and mount points
Envelope inner radius is 715 to 725mm
Inner installation clearance is 710 to 715 mm
Inner cylinder (sandwich) is z= -1900 mm to +3125mm
Envelope outer radius = 805 to 810 mm
Outer installation clearance = 810 to 820 mm (this is the clearance between GST and the barrel EMcal (BIC)
Outer Cylinder (CFRP) z= -1900 to +2700 mm
Variety of support rails are provided by GST to support
  PST feet
  Mountpoints for pfRICH, EEEMCAL
  GST itself is mounted to HCAL and EMC
  End rings (50mm massive CRRP) to distribute load of “brackets” for GST support
Adjustability of PST mm and of GST 10mm
Charge 1, 4, 6

## Slide 20: Periphery interface mapping
Best existing design via CMS, adopted for EPIC as needed
The four Tracker brackets support the GST in its final position inside EPIC
The spherical joint allows the tracker to ”settle” without overconstraining
BTST
BTST
Banana
TK Bracket
Connection Plate
Spherical joint assembly
M10
Belleville Springs
Preload spacer
Cover
M8
Connection Block
Coupler

## Slide 21: Periphery interface mapping
The four Tracker brackets support the GST in its final position inside EPIC
The spherical joint allows the tracker to ”settle” without overconstraining
The mechanism on the right allows “alignment” by set screws which then gets “mounted” in position with the below mechanism
Adjusting the orange spacer or amount of Belleville washers on one or both ENDs adjusts the Z position of the Tracker
-Z END
+Z END
Z=0mm
BTST (~6m)
Z position can be measured / surveyed from the protruding part of the cup
Z
X-Y –position is adjusted
by position of the hole

## Slide 22: Detailed drawings on GST adjustment & support
Bracket Spherical Connection
GST Banana
GST Bracket Spherical Joint
Periphery interface mapping

## Slide 23: Support of the Global Support Tube
Mechanism to support GST is in final design adjustments
Connector on GST end ring supported by “bracket”
Bracket allows for adjustability as presented on previous slides
Charge 1, 4, 6
Support bracket via C-channel of EMC

## Slide 24: HPDIRC and oMPGD support by GST
2mm clearance on installation of the trays into the 12 sectors between the GST inner and outer skins
GST support “Cavities”
  GST consists of supports for HP-DIRC and outer MPGD in between inner sandwich and outer skin
  Provide a temporary mounting plate for interfacing to external rails for integration of hpDIRC and oMPGD
Inner beams for Insertion trays for barrel TOF and iMPGD (CyMBal)
  See details on sl 14
Rails to support hpDIRC & oMPGD
Pin holes for interfacing temp rails

## Slide 25: FEA: Loads of detector systems supported by GST
Total weight is 5,675 kg
  Comparable to CMS timing layer + all of the tracker
Services are included in the respective detector subsystem
  Additional service mass outside the respective detector volume is added in addition
GST properties:
  weight is ~ 420 kg
  CFRP rails are 5 kg
  For comparison if made in stainless steel GST weight is 3082 kg (7x GST), and in Al it would 1040 kg (2x GST)
 |  | z-coordinate | Mass (kg)
1 | EEEMCal Crystals | 1842.5 | 2000
2 | EEEMCal Electronics | 2212.5 | 500
3 | HPDIRC Bars | 425 | 1400
4 | HPDIRC Prisms | 3060 | 400
5 | oMPGD | 125 | 100
6 | AC LGAD TOF | -212.5 | 150
7 | Cymbal | -212.5 | 150
8 | SVT | -100 | 285
9 | pfRICH | 1500 | 97
10 | pfRICH Services | 2437.5 | 13
11 | SVT Services Zp | 2187.5 | 50
12 | SVT Services Zm | -1725 | 15
13 | Cymbal TOF Services Zp | 2150 | 50
14 | Cymbal TOF Services Zm | -1725 | 15
15 | EEEMCal Services Zp | 2815 | 30
16 | GST self weight | xx | 420
 |  | TOTAL | 5675
Load distribution

## Slide 26: Finite element analysis of GST
BCs in z-
The current GST design of a composite “double-decker” Carbon Fiber tube can support all inner detector masses within 2.5mm deflection
Currently assumed: HM63 + EX1515 matrix (fairly stiff, other choices exist) – Material properties are in backup
Sufficient within the envelope!
To come: Alternative materials and alternative sandwich

## Slide 27: GST envelope and constraints
Expected deflections, tolerances, geometric tolerances:
  Deflections in final operation setup: 2.5 vs 2.0 mm
  Manufacturing: 1.5mm, Core: 0.5mm & Cylindricity of mm
    Face sheets: 0.1mm + Core yields 0.7mm max deviation
  Geometric to fit within envelope in worst case: mm
Envelope is mm for insertion
  Worst case: mm /2.0mm = / mm
  Can consider more local add. stiffening structures
Key:
hpDIRC Prism
hpDIRC & oMPGD
Services
Barrel TOF
iMPGD
Support tubes
- GST & PST
Adjustability of PST mm in x-y and mm in z
  Tolerance is mm
Adjustability of GST 10mm in all directions
  Tolerance is mm

## Slide 28
Presentation Section 3:
Integration and Insertion/Assembly
See also talk by Dan Cacace

## Slide 29: ePIC Detector Support Hierarchy Y-Z View
Details are on the next slide
Two large sub-assemblies independently integrated
  PST-SVT sub-assembly staying in one physical location
  GST with subdetectors installed in EPIC ready to receive SVT sub-assembly
Side remarks:
Substantial amount of temporary supports needed for beam-pipe, service, cooling, etc
Temporary structures needed to “slide” / integrate sub-assemblies together and also for final step into EPIC GST structure
Charge 6

## Slide 30: Assembly sequence
GST gets integrated with outer MPGD and hpDIRC
Moved inside assembly hall and mounted
pfRICH and EEEMCal installed without services to measure deflection
Remove pfRICH and EEEMCal
Install PST and SVT package with beam pipe and align
Install TOF and inner MPGD (cymbal)
Put PST front feet in the GST rails
  Back of PST rests on external supports
  See Dan Cacace for details
⁠Install pfRICH
⁠Install EEEMCal
⁠TOF disc
Charge 3, 6
EEEMCal
GST TOF
pfRICH
SVT
EMCAL

## Slide 31: Assembly sequence
GST gets integrated with outer MPGD and hpDIRC
Moved inside assembly hall and mounted
pfRICH and EEEMCal installed without services to measure deflection
Remove pfRICH and EEEMCal
Install PST and SVT package with beam pipe and align
Install TOF and inner MPGD (cymbal)
Put PST front feet in the GST rails
  Back of PST rests on external supports
  See Dan Cacace for details
⁠Install pfRICH
⁠Install EEEMCal
⁠TOF disc
Charge 3, 6
EEEMCal
GST TOF
pfRICH
SVT
EMCAL

## Slide 32: 2nd sub-assembly for Beampipe + SVT
SVT + inner MPGD disc assembly
Temporary supports for beam pipe and services
Sub-assembly slides into GST rails
  4 support feet of PST in PST end ring region are supported by GST rails
Next integration steps:
Follow PST subassembly with pfRICH, than EEEMCAL
  Needs temporary support for cables & beam pipe of PST subassembly, e.g. “antlers”
  Needs installation jigs to slide pfRICH and EEEMCAL into GST
Install outer MPGD barrel and hpDIRC with GST in place
  Needs rails & kinematic mounts to avoid stress on either one of them
Charge 6
See Talk by Ben Denos

## Slide 33: QA/QC and installation metrology
Charge 3, 6
Metrology and loading case scenarios based on realistic EPIC parameters
  Rely on existing experience with CMS HL-LHC projects: ITST, SC & BTST projects
  Large area metrology system “Creaform MetraScan” (received!)
    Best circular fit and deviations point-by-point from expected one
Metrology and deformation studies
  Deformation only studies (safe loads)
  Adjust FEA to match deformation only
  Compare to FEA to reproduce data
Predict behavior of full structures in all aspects & measure all
  Deformation only + FEA match
  Loading scenarios + FEA match
  Predict and extrapolate to CMS conditions

## Slide 34: QA/QC procedures informed by CMS experience
Charge 3, 6
Following best practice and lessons learned from CMS upgrade projects
  Iteration of FEA of manufacturing method, performance under load, metrology
  QA/QC during and at end of the process  repeat!
Prototyping using non-final materials
  Smaller prototypes with final material, FEA driven
Met tolerances – we typically achieve:
  1 – 2mm cylindricity (~ 6m length & 2.4m diameter)
  < 500 cylindricity (Solid skin tube)
  50-100 parallelism (Rail/Track alignment)
Best fit cylinder = 340.13mm
Nominal radius = 339.6mm
Curve A
Curve B
Curve C
Curve D
Target: -0.35 Target: -0.85 Target: -0.25
Actual: -0.40 Actual: -0. 75 Actual: -0.30
Target Diameter | 606 mm
Measured dry assembled diameter | 605.47 mm
ITST track alignment:
CMS IT tube end section cylindricity:
Pixel Service Cylinder cylindricity:
Tube transition
to mid section:

## Slide 35: ES&H
No specific ES&H risks in this area
Standard lab practices are being observed
Purdue Radiological and Environmental Management
  Safety officer Purdue CMSC: Johnathan Goodsell
  REM contact at Purdue University: Eric Butt
  Recent walk-through and inspection by REM – went well
  DOE site visit by Project Office & Fermilab ESH – went well
Charge 7
https://www.purdue.edu/ehps/rem/index.html

## Slide 36: Next steps
Mature design for GST adjustment mechanism
Carry out FEA to study material choice vs deflection
Prototype & load test to confront FEA vs reality
Failure mode FEA
Finalize envelopes for GST and adjustment mechanisms
GST

## Slide 37: Summary
The current designs for support structures are well developed for the current phase of the project
The designs are all integrated into the larger central detector model
The current procedure and approaches for the installation of the inner detectors and their support structures are well developed for the current phase of the project
  Separation of inner detectors and outer detectors ease separations!
Adjustments and optimizations are quickly worked into the larger integrated model
Next steps:
  FEA to determine material choice for GST
GST

## Slide 38
Backup

## Slide 39: GST Bracket Spherical Joint
GST Banana
Spherical joint assembly
Bracket Connection Plate
Work in progress

## Slide 40: BTST Banana
M16 x 80mm
OD15mm x 100mm Shear Pin
Z spacer
M16 x 120mm
Banana
Circlip
SS Spherical Bearing
Bearing sleeve

## Slide 41: Bracket Spherical Connection
M10 x 40mm
Connection Block
Coupler
Belleville Springs
Preload spacer
Cover
M8 x 20mm
Survey Reference

## Slide 43: Envelope Overview / CAD
HM63-EX1515
and Nomex Honeycomb

## Slide 44: GST – additional drawings
Detailed drawings

## Slide 45: Beampipe support
Charge 3, 6
Example of the CMS permanent beam pipe support at z = 1.6m
For the arm we want to bond a curve-to-flat adapter with inserts 4x M3 inside the ITST.
  At the moment, precise z-locations are yet to be determined, not critical
Ribbon operating
mechanism
M3-0.5 (x4)
Arm with curve-to-flat adapter and M3-0.5 (x4)
Vertical BP supports at 1.6m

## Slide 48: Scope Definition
MPGD trackers use MicroMegas for the inner barrel and µRWELL technology for the outer barrel and endcaps
In the barrel, each tracker is segmented in 12 sectors in Phi
  Micromegas (CyMBaL) has 4 modules in the z direction and total of 48 modules, whereas µRWELL has 2 modules in z direction with a total of 24 modules
  µRWELL Disks have 2 layers in each direction of Z and 4 modules in Phi, adding to 16 modules
Each MPGD detector readout with SALSA frontend electronics and equipped with all services, including cooling and gas system
Outer Barrel MPGD Tracker
Endcap MPGD Tracker
MicroMegas
μRWELL
μRWELL

## Slide 49: Support of the barrel TOF staves: 12 trays
Orange = mostly SVT + inner MPGD discs
Blue = TOF + inner MPGD barrel ("Cymbal")
EEEMC = gray outline indicates the constraints for services further out
Tray mounts via top rails to GST
  Thin line “tracks” a TOF tray, open space inside is for services of TOF
  Designed for 2mm overlap
Other solidly filled areas are “reserved” for service of SVT+oMPGD and TOF+iMPGD
10mm clearance is closest distance
Doable, still add cover plate for any sensitive parts such as wire bonds

## Slide 50: TOF – Design considerations
2mm overlap
Detector modules need to overlap to guarantee coverage in r-phi
  Designed for 2mm overlap
Integration/Assembly
  10mm clearance is closest distance
  Doable, still add cover plate for any sensitive parts such as wire bonds

## Slide 51: GST CAD Drawings

## Slide 52: Closest clearance is 10mm

## Slide 53: Detector Integration Layout
Charge 3, 6