## Slide 1: MPGD SALSA based Readout
Review of powering scenarios
  Likely increase of expected power consumption of Salsa (important uncertainty at this stage of the dvpt)
  3 options are considered (SALSA current of 1A, 1.5A and 2 A)
The power chain is as follows
  LV power supply – cable plant – DCDC power board – Salsa carrier and communication boards
  The last actors in the power chain are LDO regulators producing clean power for ASICs
    Salsa, lpGBT, VTRX+
  Salsa requires high current 1.2V
  lpGBT requires low current 1.2V
  VTRX+ requires low current 2.5V and 1.2V
Specific MPGD integration
constraints & card electronics
design will define the final card(s)
form factors
Salsa
Connector
Salsa
Connector
Salsa
Connector
Salsa
Connector
ComBrd
PwrBrd connector
ComBrd
VTRX+
lp GBT
LDO
ComBrd
ComBrd
PwrBrd connector
DCDC
DCDC
LDO
LDO
Power board
Salsa carrier board
Communication board
For illustration only : just to show component types
based on recent studies of Irakli.mandjavidze@cea.fr

## Slide 2: Power distribution : Shared power board (option 1.5 A SALSA current)
 | Salsa 1.5A |  |  |  |  |  | Salsa 2A | 
 | Power | Pwr/ch |  | Power | Pwr/ch |  | Power | Pwr/ch
 | W | mW |  | W | mW |  | W | mW
Salsa | 1.8 | 28.1 |  | 1.8 | 28.1 |  | 2.4 | 37.5
Salsa carrier | 9.0 | 35.2 |  | 9.0 | 35.2 |  | 12.0 | 46.9
Salsa carrier + ComBo | 10.8 | 42.2 |  | 10.8 | 42.2 |  | 13.8 | 53.9
Power board | 13.1 |  |  | 13.1 |  |  | 17.1 | 
3 x (Salsa carrier + ComBo) + PwrBrd | 45.5 | 59.2 |  | 45.5 | 59.2 |  | 58.5 | 76.1
Power supply | 48.5 | 63.1 |  | 48.5 | 63.1 |  | 62.4 | 81.2
DCDC 1V5
SalsaCarrierBrd
ComBo
DCDC 1V5
SalsaCarrierBrd
ComBo
DCDC 1V5
SalsaCarrierBrd
ComBo
PwrBrd
PS
11W
13W
46W
63 mW / ch
59 mW / ch
An important uncertainty coming from the consumption of Salsa
LV powering options laid – the power consumption and heat dissipation figures estimated
  Safety factor is not applied
  Varying the Salsa current gives the idea
An Excel file exists that checks several hypotheses
  Several parameters can be changed such as Salsa current, DCDC efficiencies, voltage drops, etc
Total power dissipation for CyMBaL (current new baseline scenario) :
59 mW/ch x 768 x 48 = 2.3 kW
based on recent studies of Irakli.mandjavidze@cea.fr

## Slide 3: Backup slide

## Slide 4: CyMBaL Power distribution : Shared power board
Shared power board for the 3 FEBs of a tile
Example for 1.5 A total Salsa current
SalsaCerrierBrd
lpGBT
1.2V / 0.5A / 0.6W
1.5V LDO
1.2V / 0.5A / 0.156W
15V LDO
2.5V / 70mA / 0.875W
ComBo
15V DCDC 60%
1.5V / 6.5A / 4.4W
PS
16V / 3A / 48.5W
PwrBrd
VTRX+
1.2V / 20mA / 25mW 2.5V / 70 mA / 175 mW
Salsa
1.2V / 1.5A / 1.8W
1.5V LDO
1.2V / 1.5A / 0.45W
Salsa
1.2V / 1.5A / 1.8W
1.5V LDO
1.2V / 1.5A / 0.45W
Salsa
1.2V / 1.5A / 1.8W
1.5V LDO
1.2V / 1.5A / 0.45W
Salsa
1.2V / 1.5A / 1.8W
1.5V LDO
1.2V / 1.5A / 0.45W
16V
15V
1V / 3 A / 3W
20m – 2.1 mm2
1.8W
9W
15V DCDC 60%
1.5V / 6.5A / 4.4W
SalsaCerrierBrd
ComBo
15V DCDC 60%
1.5V / 6.5A / 4.4W
SalsaCerrierBrd
ComBo
1.8W
9W
1.8W
9W
13.1W
50mV / 6.5 A / 0.3mW
30cm – 1.3 mm2
based on recent studies of Irakli.mandjavidze@cea.fr