## Slide 1: ECT Overview
WEST
ELECTRON
BACKWARD
SIDE
EAST
HADRON
FORWARD
SIDE
IP
× 2 DISKS
Complying with the envelope released on 03/03/2025
BEAM PIPE
× 2 DISKS
4 | Disks
16 | Quadrant modules
24576 | Data channels

## Slide 2: ECT Overview
WEST
ELECTRON
BACKWARD
SIDE
EAST
HADRON
FORWARD
SIDE
IP
× 2 DISKS
Complying with the envelope released on 03/03/2025
BEAM PIPE
× 2 DISKS
4 | Disks
16 | Quadrant modules
24576 | Data channels
R450
R450
9-22-2025
1235
1485
20480

## Slide 3: Quadrant Concept
6 FEBs per quadrant located in the service rim
4x SALSA ASICs per FEB
2x Hirose FX20-140P Connectors per FEB
Cutouts for services
At 0°, 90°, 180°, and 270°
Fiber-reinforced epoxy frames define the gas gap and reinforce the outer support panels
Lightweight sandwich-structured composites for anodes/cathodes’ structural supports
Variable cutout to cope with the asymmetric beam pipe (Ø 100, 130, and 180)
5

## Slide 4: PCB and AA after the Redesign
PREVIOUS DESIGN
CURRENT DESIGN
6 FEB
Slots
5 FEB
Slots

## Slide 5: New FEB Model
FE1:
4x SALSA
2x LDO
FE2:
1x lpGBT
2x LDO
1x VTRx+
DC/DC Conv.
HEATSINK

## Slide 6: Cooling Strategy
All 5 heatsinks in a module connected in series with pipes running close to the outer rim
No. 2 Ø6x4 PU pipe per module as inlet/outlet for the cooling chain
All major heat sources are mounted on the top/bottom face of FE1/FE2 to face the heatsink

## Slide 7: Heatsink
Preliminary proposal, no simulation has been run yet
Quite bulky and difficult to manufacture → We will be working on alternative cooling solutions
4x3 machined groove
Ø6x4 PU Pipes
Welded
Barbed Tube Connectors

## Slide 8: Services Estimates