## Slide 1: The RHIC to EIC Transition
RHIC to EIC and Working Safely
9 February 2026
Wolfram Fischer Deputy Associate Laboratory Director for Accelerators, NPP Chair, C-AD
Notes: 15 min => 10 slides

## Slide 2: Goals for today

## Slide 3: Contents
RHIC in review
EIC in preview
From RHIC to EIC – what changes
  RHIC Removal & Repurposing (R&R) – Dave Chan
  Safety during the transition – Ray Fliller
  Tunnel Access and Work Authorization – Paul Sampson

## Slide 4: Relativistic Heavy Ion Collider (RHIC)

## Slide 5: Relativistic Heavy Ion Collider
1984 began to think about heavy ion collider
~100 GeV/nucleon, dipoles ~3.5 T (5 T for ISABELLE/CBA)
transfer line from Tandem, develop heavy ion beams in AGS, with heavy ion experiments
1991 construction begins
2000 first collisions
[Ernest D. Courant, “Accelerators, colliders, and snakes”, Annu. Rev. Nucl. Sci. 2003. 53:1-37]
Satoshi Ozaki
Mike Harrison
Tom Ludlam

## Slide 6: Relativistic Heavy Ion Collider – main parameters
RF
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
(s)PHENIX
(PHOBOS) Electron lenses
Polarized Jet Target
(BRAHMS) Electron cooling
EBIS
BLIP
TPL
Start operation : 2000
Circumference : 3.8 km
Max dipole field : 3.5 T Energy : 255 GeV polarized p : 100 GeV/nucleon Au
Species : ph to U (incl. asymmetric) Experiments : BRAHMS, PHOBOS, pp2pp, AnDY, RHICf, PHENIX, STAR, sPHENIX

## Slide 7: RHIC Design Manual
reached Lavg = 88×1026 cm-2s-1 (44x design)
reached Lavg = 24.8×1031 cm-2s-1 (25x design) with Pavg = 57%

## Slide 8: RHIC Design Manual (July 1998)
IR design with beam splitting DX dipoles first
DX dipole
D0,Q1—Q3
DX dipoles
Lmag = 3.7 m, Bmax = 4.3 T
large aperture (18 cm coil ID)
only magnets that need training (~5 for IR6/8 only)
 Interaction Point
Notes: MAKE REAL CALCULATION FOR DX MOVE

## Slide 9: Transition crossing – with sc magnets
[M. Harrison, S. Peggs, and T. Roser, “The RHIC accelerator”, Annu. Rev. Nucl. Sci. 2002. 52:425-369]
Did limit intensity for some time:
Initially no gamma-t quads
Electron clouds
Instabilities

## Slide 10
Claudia Ratti,
University of Houston
RHIC CDR, 1986

## Slide 12: Configuration Manual Polarized Proton Collider, 2006
reached Lavg = 2.5×1032 cm-2s-1
reached Pavg = 57% (avg. over 3D distribution and time)
Notes: A little sloppy with 10% effects

## Slide 13
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper
Special devices for polarized protons: source, polarimeters, snakes, rotator, flipper

## Slide 14: RHIC performance evolutions
Au+Au luminosity at 100 GeV/nucleon
p+p luminosity and polarization (100 and 255 GeV)
Medium heavy (Cu+Cu, O+O)
Asymmetric collisions (p+Au, d+Au, h+Au, Cu+Au)
U+U (non-spherical), Zr+Zr / Ru+Ru (same A = 95, max different DZ = 4)
Au+Au luminosity at 3.85 to 9.8 GeV/nucleon (Beam Energy Scan, including a fixed target program)
New detector for 2023 to 2025: sPHENIX
only ion combination shared between
RHIC and LHC are O+O and p+p (polarized in RHIC)

## Slide 15
RHIC Au+Au / U+U operation at full energy
Could be done later in 1/2 day (200x faster)

## Slide 16: Performance limits – RHIC ions, high energy
Bunch intensity Nb, limited by injectors EBIS, bunch merges in Booster and AGS transition instability luminosity lifetime
Intrabeam scattering => stochastic cooling
Lattice with small b* and large off-momentum dynamic aperture with hourglass factor ≈0.5 at end of store, need large b* reduction any lattice change must not result in additional beam losses dynamic b* reduction after emittance decreased by cooling
Goal is to have burn-off as the dominant beam loss mechanism.

## Slide 17: RHIC Run-14 Delivering RHIC-II luminosity
2007, Beginning of RHIC-II upgrade
2014, End of RHIC-II upgrade
Increase in initial luminosity result of larger bunch intensity
Increase in luminosity lifetime result of 3D bunched beam cooling, >90% burn-off

## Slide 18: 3D stochastic cooling for heavy ions
M. Brennan, M. Blaskiewicz, F. Severino, PRL 100 174803 (2008); K. Mernick PRSTAB, PAC, EPAC
longitudinal kicker cavity (half side with waveguides)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Notes: Frequency range: 5-8 GHz transverse, 6-9 GHz longitudinal

## Slide 19: Operation at burn-off limit in U+U
97% of intensity burned off at Lmax
Burn-off dominated operation allows for determination of total U+U cross section – and comparison with calculation (mostly QED) (published in Phys. Rev. C) =>

## Slide 20: Au bunch intensity evolution
main limits: - injectors output - e-cloud in RHIC
- transition instability in RHIC
Run-25
AGS 12g6g2 merge
EBIS, Booster 4g2g1, AGS 8g4g2 merge
scrubbing with protons
111 bunches
43 bunches
gt-jump, octupoles at transition

## Slide 21: Run-18 Zr+Zr/Ru+Ru – same A, different Z (CME) Zr-96/Ru-96
Extraordinary help from DOE, ORNL, RIKEN for source material and preparation
Ru isotopes

## Slide 22: Run-18 Zr+Zr/Ru+Ru at 100 GeV/nucleon
Run Coordinator: Greg Marr paper: IPAC 2019
Zr+Zr
Ru+Ru
Zr+Zr
Ru+Ru
Ru+Ru
Zr+Zr
Ru+Ru
Zr+Zr
CeC PoP dedicated
scheduled maintenance
Store-by-store species change and flat luminosity of 21.5×1026 cm-2s-1
20 h nominal store length (WEEK: 30-Apr-18 to 07-May-18)

## Slide 23: How did stochastic cooling change heavy ion collider operation?
Increased in luminosity lifetime from ~2.5 h Au+Au up to infinite
Allowed for increase in bunch intensity L ~ Nb2
Increased optimum store length from 4 to 8 h for Au+Au, resulting in more time in collision, less time refilling
Can tolerate emittance growth during acceleration (from IBS, transition instabilities) as long as no intensity is lost
Operation close to burn-off limit, full use of accelerated intensity
Allowed flat luminosity for alternating species (Ru+Ru/Zr+Zr)

## Slide 24: Low-Energy RHIC electron Cooling (LEReC) for the Beam Energy Scan I and II (BES-I, II)
[2015 NSAC Long Range Plan for Nuclear Science]
BES-I in 2010/11/14
BES-II: 10x increase in the number of events
Au+Au collisions down to 3.85 GeV/n (40% of CoM energy at nominal injection)
Luminosity really low
  Space charge
  Intrabeam scattering
  Magnetic field errors (also time dependent)
  Large beam with losses
BES-II goal of 4x luminosity over 3.85 – 9.8 GeV/n (highest energy is nominal injection)
Designed cooler for 2 lowest energies
Notes: Picture from 2015 NSAC long-range plan

## Slide 25: LEReC Accelerator (100 meters of beamlines with the DC Gun, high-power fiber laser, 5 RF systems, including one SRF, many magnets and instrumentation)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
ERL solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity

## Slide 26: Low Energy RHIC electron Cooler
A.V. Fedotov et al., “Experimental demonstration of hadron beam … “, PRL 124, 084801 (2020)]
LEReC operational electron cooler:
  utilizes RF-accelerated electron bunches
  uses non-magnetized electron beam (no magnetization at the cathode and no continuous solenoidal field in cooling section)
LEReC approach to cooling is directly scalable to high-energies – pre-cooler in EIC at injection

## Slide 27: BES-I vs BES-II luminosity
Run Coordinator: Chuyu Liu (Run-19 to 21)
3rd year
1st year
2nd year
Goal was
Lavg (BES-II) = 4x Lavg (BES-I)

## Slide 28
RHIC p+p operation at 100 / 255 GeV
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper

## Slide 29
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper
Special devices for polarized protons: source, polarimeters, snakes, rotator, flipper

## Slide 30: p bunch intensity and polarization
FOM = LP4 ~ Nb2P4
main limits: - injectors output - polarization - e-cloud in RHIC - beam-beam in RHIC
beam-beam compensation
polarized source upgrade with Atomic Beam Source
AGS tune jumps, RHIC 9 MHz RF
AGS cold snake
polarized source upgrade with sc solenoid
AGS warm snake
A. Zelenski, H. Huang, K. Gardner, K. Zeno, RF, et al.
(double-spin experiments)

## Slide 31: Head-on bb compensation
tune distribution measured with BTF and p+Al collisions proton beam: (Qx,Qy) = (.685,.695); Al beam: (Qx,Qy) = (.685,.695); DQx, DQy >> x => no coherent modes
no bb
2x bb
DQ reduction from e-lens
Can only reduced BB tune spread (black curve is limit)
Tune footprint compression with a Gaussian electron beam
[W. Fischer, et al., ”Operational head-on beam-beam compensation with electron lenses in the Relativistic Heavy Ion Collider", Phys. Rev. Lett. 115, 264801 (2015).]

## Slide 32: Run-25 Au+Au
[mb-1]
damaged 69 kV power line
repair shut off Central Cryo Plant
required managing helium inventory
15 days
unsynchronized beam abort
Yellow abort vacuum repair
14 days
Run Coordinator: Travis Shrey
short in superconducting bus
repair required partial warm-up
opened several cryostats
65 days

## Slide 33: Run-25 STAR and sPHENIX event rates
Maintenance day
STAR 0 mrad crossing angle
sPHENIX 1 mrad crossing angle
Oct/Nov 2025
Run Coordinator: Travis Shrey

## Slide 34: Run-25 p+p O+O
Run Coordinator: Travis Shrey

## Slide 35
L design
nominal injection
L design
Used stochastic or electron cooling in 1 or 2 beams

## Slide 36: RHIC: The World’s Most Versatile Collider
High-intensity, high-brightness ion and proton sources
49 different combinations of energy, ions, and collision configurations
10 different ion species
18 center-of-mass energies
Innovative accelerator technologies
Gold-gold collision rates 44 times higher than design
Only polarized proton collider in the world
Abhay Deshpande, RHIC Capstone Event, MCR, 6 Feb 2026
Notes: RHIC is the most versatile particle collider in the world… [highlight one or two things and end with the polarization being essential to the future EIC.

## Slide 37: RHIC’s 25 years of physics …
Good design – allowed for significant upgrades
Evolving physics program, strong community and funding agency support – DOE NP
Full energy Au+Au Lavg = 44x design New: bunched-beam stochastic cooling
Only p+p collider, Lavg = 1.3x design, P ~ 57% (70% design) New: p polarization preservation to high energy
12 species combinations (incl. asymmetric), 18 center-of-mass energies, low-abundance isotopes New: built-in flexibility, high-intensity high-brightness ion/p sources
Extended energy range slightly above; and significantly below nominal injection New: electron cooling with RF accelerated e-beam
RHIC operation ended 6 February 2026 Most of RHIC complex will be re-used for the Electron-Ion Collider Hadron injectors, RHIC tunnel, Yellow ring (part of Blue), Technical Infrastructure, New technologies listed above
Nominal injection
[APS DPB Newsletter on RHIC: https://engage.aps.org/dpb/resources/newsletters/25-newsletter/2025-f7]

## Slide 38
DOE Undersecretary for Science Dario Gil ending the last RHIC store on 6 Feb 2026, 09:08:44
Red button created by Patricia Moore.

## Slide 39: Following RHIC: The Electron-Ion Collider (EIC)

## Slide 40: HERA (1992 – 2007)
920 GeV protons (unpolarized)
27.5 GeV electrons (self-polarized by
the Sokolov-Ternov effect)
HERA peak luminosity: ~5x1031 cm-2s-1
The EIC is an electron – ION collider HERA was an e-p collider
Variable CoM energy HERA was a fixed-energy collider
Both EIC beams are polarized, starting from the source (HERA only electrons)
New modern particle detector
EIC luminosity is a factor of ~200x higher
[Sergei Nagaitsev, EIC Technical Director, NAPAC’25]

## Slide 41: From RHIC to EIC
Protons: ~40 – 275 GeV
Electrons: 5 – 18 GeV
RHIC
RHIC
EIC
Ion species:
proton – Uranium
60% p polarization
[Sergei Nagaitsev, EIC Technical Director, NAPAC’25]

## Slide 42: EIC Accelerator Performance Drivers
wide center-of-mass energy √s: 20 – 140 GeV :
map the out nucleon and nuclei structure from high to low x
polarized electron and hadron (p, He-3) beams:
access to spin structure of nucleons and nuclei
Spin vehicle to access the spatial and momentum structure of the nucleon in 3d
Full specification of initial and final states to probe q-g structure of NN and NNN interaction in light nuclei
nuclear beams: d to Pb
accessing the highest gluon densities  saturation
quark and gluon interact with a nuclear medium
high luminosity 1033-1034 cm-2s-1 :
mapping the spatial and momentum structure of nucleons and nuclei in 3d
access to rare probes, i.e. Ws
large acceptance (0.2 – 1.3 GeV) through forward focusing IR magnets
spatial imaging of nucleons and nuclei
gluon emission
?
=
gluon recombination
[Sergei Nagaitsev, EIC Technical Director, NAPAC’25]

## Slide 43: HERA vs EIC: key parameters
HERA EIC FACTOR
Circumference (km) 6.3 3.8 1.7
Number of bunches 174 1160 6.7
Proton bunch charge (nC) 11.7 11 1
Electron bunch charge (nC) 5.3 28 5.3
Bunch length (cm), p/e 16/0.9 6/0.7
Beta at IP (cm), proton H/V (cm) 245/18 80/7.2
Beta at IP (cm), electron H/V (cm) 62/26 45/5.6
Proton emittance, (nm, rms) 4/4 11/1
Electron emittance, (nm, rms) 20/3 20/1.3
Energy (COM), GeV 320 105
Luminosity, x1031 cm-2s-1 5.3 1000 190
60
~3
[Sergei Nagaitsev, EIC Technical Director, NAPAC’25]

## Slide 44: Key EIC accelerator concepts
Ribbon-like (flat) hadron beam (11:1 transverse emittance/size ratio)
Large crossing angle (25 mrad)
Beam-beam limits for both beams (0.1 e/ 0.01 p)
Spin preservation from source to collisions (protons and electrons)
Very high bunch intensities and circulating beam currents (1 A (p), 2.5 A (e))
Upgrade path: high-energy hadron cooling at collisions
These are the key concepts that allow to attain luminosity of ~1034 cm-2s-1 and maintain high polarization at collisions over a broad range of CoM energies
[Sergei Nagaitsev, EIC Technical Director, NAPAC’25]

## Slide 45: Key EIC Accelerator Technology Areas
Hadron Beam Cooling
Spin-transparent optics
  High polarization for both beams from source to collisions
  Swap-out injection for electron bunches (at 1 Hz) to maintain high polarization in the ESR
SRF (Crab and elliptical) cavities
  Large-size, complex geometries;
  High-power; HOMs
  Very tight phase and amplitude noise requirements
IR magnets (large aperture, one-of-a-kind SC magnets)
Instability and impedance control;
  Vacuum chambers, beam screens, kickers, SRF cavities
[Sergei Nagaitsev, EIC Technical Director, NAPAC’25]

## Slide 46: From RHIC to EIC What changes?

## Slide 47: New directorate – EIC+NPP+SMD

## Slide 48: From RHIC to EIC – what changes?
Last 25 years:
RHIC is running, or
Preparing for the next RHIC run
Also supporting
  Accelerator Research & Development
  Industrial and academic users at Tandem
  Isotope production at BLIP
  Space radiation studies at NSRL

## Slide 49: From RHIC to EIC – what changes?
The future:
Decommission RHIC (retire Accelerator Safety Envelope)
RHIC Removal & Repurposing (R&R)
Maintain/upgrade the hadron injectors for EIC
Maintain/upgrade the technical infrastructure for EIC
Accelerator Readiness Reviews (ARR) for Linac/Booster and AGS
=> All DOE Nuclear Physics funding must support the EIC

## Slide 50: Large Upgrade Projects in Order of Priority
Central Cryo Plant Upgrade
SRF Test Facility in 912
AGS Cooling Water System Upgrade
LINAC RF Power Amplifier Upgrade Phase => will delay, but need a reliability upgrade
Notes: Should removal of legacy infrastructure

## Slide 51: From RHIC to EIC – what changes?
The future:
Also supporting
Accelerator Research & Development – DOE NP, LDRD, NOFO, other key areas: sources, beam cooling, polarization and polarimetry, AI
Tandem – self-supporting, users pay for beam time
Isotope production at BLIP – funded by DOE IP expect R&D focus, less production (ie <6 months running time/year)
Space radiation studies at NSRL – funded by NASA, electronics testers expect increasing demand for space electronics testing HEET proposal (PI Kevin Brown)

## Slide 52: BNL Collider-Accelerator Complex with the proposed HEET facility location
Space Effect Test Facilities

## Slide 53: RHIC–to–EIC Transition and Working Safely
With RHIC operations successfully concluded last Friday, our work now shifts to a new phase
Safety remains our highest priority — new activities across many areas bring different hazards and risks
Primary focus is EIC — R&R and maintaining/upgrading injectors and technical infrastructure
Will continue isotope production (BLIP), space-radiation studies (NSRL) and advance the HEET proposal for space-electronics testing using the AGS

## Slide 54
DOE Undersecretary for Science Dario Gil ending the last RHIC store on 6 Feb 2026, 09:08:44
Red button created by Patricia Moore.