## Slide 1: TOF Test Beam Campaign 2026
Satoshi YANO
Hiroshima University

## Slide 2: Challenge of AC-LGAD Test Beam
AC-LGAD requires high-precision waveform measurement
  Rise time for timing
  Height for hit position reconstruction
High performance digitizer or oscilloscope must be used
  High band-width, high sampling rate, data-taking rate: ~1GHz, 10 GS/s, O(100) Hz data taking
    CAEN DT5742: 500 MHz, 5GS/s, 16ch
    LeCroy WaveRunner8204HD: 2 GHz, 10GS/s, 8ch
    LeCroy WavePro804HD: 8 GHz, 20GS/s, 4ch
  Digitizer rise-time is ~850ps but Oscilloscope is ~600ps
Three sensors or fast device are used for the timing reference
  E.g. Photek PMT240 (MCP-PMT): σT ~ 10ps

## Slide 3: Test Beam Campaign in 2025
Strip-type sensor has been tested at JLab in July
  First full-size sensor test (variable pitch sensor)
  Unfortunately, only 30um strip-type sensor has been tested
  CAEN DT5742: 500 MHz, 5GS/s, 16ch
  MCP-PMT timing reference
Full-size strip-type and pixel-type sensor have been tested at DESY in December
  First real full-size strip-type sensor (BTOF sensor) has been tested
  Full-size pixel-type sensor (variable pitch) has been also tested
  Data was taken with several HV configuration (HV-scan)
  CAEN DT5742: 500 MHz, 5GS/s, 16ch
  NO MCP-PMT timing reference, but DC-LGAD for Pixel sensor data timing reference
FCFDv1.1 test at DESY in August
  First FCFDv1.1 with strip-type AC-LGAD test
  Small prototype sensor (50um) with FCFDv1.1 (6ch analog block)
  LeCroy WaveRunner8204HD: 2 GHz, 10GS/s, 8ch
  MCP-PMT timing reference

## Slide 4: Results From 2025
Strip-type sensor has been tested at JLab in July
  30um thickness result has been presented
  σt~63 ps and σx~32 um
Full-size strip-type and pixel-type sensor have been tested at DESY in December
  Analysis is on going
FCFDv1.1 has been tested with small-size strip-type sensor (eRD112 FY23 sensor) at DESY in August
  σt~40 ps and σx~15 um
    Sensor + PCB board was ~35 ps

## Slide 5: Test Beam Campaign in 2026
KEK-PS, electron @ ~6.5 GeV (Fortunately obtained by chance, parasite)
  Fixed: Feb. 19th ~ 25th
  Primary Goal
    20um and 30um pixel-type sensor test
Tohoku-RARiS, electron @ 800 MeV (main)
  Fixed: Mar. 3rd ~ 6th
  Primary Goal
    New geometry strip-type sensor (20um, 30um, 50um) test
    Homework of previous beam tests
CERN-SPS, proton @ 120 GeV (main)
  May/Eary June (Requested)
  Primary Goal: Test of EICROC1 with full-size pixel sensor (under discussion)
KEK-PS, electron @ ~6.5 GeV (main)
  Oct. to Dec (We will request the beam-time)
  Primary Goal: BTOF sensor + FCFDv1.2 and the first full-chain test
Using oscilloscope (8 GHz, 20GS/s)
MCP-PMT timing reference
Using oscilloscope (8 GHz, 20GS/s)
MCP-PMT timing reference