## Slide 1: Overview of AstroPix Performance
Daniel Violette
4th BIC Workshop, Argonne National Lab

## Slide 2
Overview
Discussion Topics:
AstroPix Version 3
AstroPix Version 4
SW/FW Development

## Slide 3
AstroPix v3 Quad Chip Test Board
AstroPix v3 is the first 2x2 cm2 chip implemented.
Last version with OR’d Row/Column Hit Buffers
First version of AstroPix tested in “quad-chip” design.
Testing with AstroPix v3 is still providing lots of important feedback on how to operate the AstroPix daisy-chain readout.
AstroPix Version 3 : Overview

## Slide 4
AstroPix Version 3 : Overview
New hardware has been developed to interface with AstroPix v3, moving away from the Nexys Video + GECCO board readout.
AstroPix Sounding Rocket Technology Demonstration Payload (A-STEP)
Compton-Pair (ComPair-2) Segment

## Slide 5
AstroPix Version 3 : Single Chip Performance
Single Pixel Source Spectra
Credit: Yusuke Suda, Hiroshima U. (https://arxiv.org/abs/2408.12891)
AstroPix v3 detector testing: mean 6.4 keV FWMH at 59.5 keV.
44% of pixel meet target (<10% FWHM at 60 keV)
60 keV
31 keV
22 keV
88 keV
122 keV

## Slide 6
AstroPix Version 3 : Quad Chip Performance
Credit: Kavic Kumar, UMD College Park, Adrien Laviron NASA\GSFC
Hit-map of four AstroPix chips on one SPI bus
Recorded 580 events/s after row/col hit matching
Am-241 source
0
1
2
3

## Slide 7
Bus bar photon attenuation
PMOS comparator test columns disabled
?
Interrupt Line
AstroPix Version 3 : Quad Chip Performance

## Slide 8
AstroPix Version 3 : Thermal Testing
Credit: Carolyn Chinatti, Carleton College

## Slide 9
AstroPix Version 3 : Thermal Testing
Attempted a linear scaling of the shifted ToT spectrum as a function of temperature.
Some noted energy dependent shifts remain, bimodality of the amplifier, other effects?
Credit: Carolyn Chinatti, Carleton College

## Slide 10
AstroPix Version 3 : Sub-Pixel Scans
We want to understand AstroPix’s subpixel detection efficiency.
Is depletion uniform? What does charge collection look like at pixel boundaries?
Norito Nakano designed experiment to collimate x-rays for a 2-D scan using Cd-109.
Credit: Norito Nakano, Hiroshima U.
Best spot size: ~220 um

## Slide 11
AstroPix Version 3 : Sub-Pixel Scans
Showed change-over in count rate from one pixel row to the next while scanning across a column. Compared simulations.
Credit: Norito Nakano, Hiroshima U.

## Slide 12
AstroPix Version 4
Credit: Yusuke Suda, Hiroshima U
Reduction in pixel capacitance!

## Slide 13
Credit: Grant Sommer, GW University.
AstroPix Version 4: Performance

## Slide 14
Credit: Grant Sommer, GW University.
Credit: Grant Sommer, GW University.
AstroPix Version 4: Performance
Slightly above goal 10% FWHM at 122 keV!

## Slide 15
AstroPix Version 4: Injection Calibration + Depletion
Credit Yusuke Suda, Hiroshima U.
Methods: https://www.sciencedirect.com/science/article/pii/S0168900224006880?via%3Dihub
Work in Progress!

## Slide 16
Software Development
As the AstroPix user group grows we are attempting to adjust from an R&D mindset.
Looking for feedback!
https://github.com/AstroPix

## Slide 17
Software Development
Single-Chip (v3,v4) Running
Quad Chip (v3) Running, Daisy Chain Readout
ComPair Segment Running (380 Detectors)!
How HW agnostic can this be?
AstroPix v3, Quad-Chip, v4 Decoding

## Slide 18
Software Development
low-level firmware
*Adjustable # of AstroPix daisy-chains
Register File Map
Use-specific firmware/logic
Software
Mostly design agnostic? HW change, # daisy chains just update Register File Map references

## Slide 19
https://astropix.github.io/astep-fw/
Great firmware/software documentation by Richard Leys
Software Development

## Slide 20
Thank You!