## Slide 1: ESR and RCS Compton DAQ
Dave Gaskell
2/26/2026

## Slide 2: ESR Compton Layout
Crab cavity
Photon Detector
(30 m from Laser IP)
*
D4EF
qB=1.5 mr
Q9EF
D5EF
qB=1.5 mr
D6EF
qB=12 mr
Q10EF
Q8EF
Q7EF
Q6EF
Q5EF
Q4EF
Q3EF
D3EF
qB=13 mr
D2EF
Electron Detector
Laser IP​
74 m upstream of IP-6
Three key interfaces with electron ring:
Laser-electron beam interaction region
Backscattered photon exit and transport to detector
Electron detector
Key requirement: bunch-by-bunch measurement:
Implies 100 MHz “readout” at 5 and 10 GeV
25 MHz at 18 GeV

## Slide 3: Electron Detector
10 ns
Signals from CALYPSO/FLAT32 prototype
Hall C diamond strip detector
Will use 4 planes of diamond strips to detect scattered electrons
Active area = 6 cm, segmentation = 0.4 mm  150 channels per plane
Total number of channels = 600

## Slide 4: Photon Detector
Will use a Forward EMCAL module for photon calorimeter
  Block of W/SciFi, subdivided into 4 towers
  2 cm light guide from block to PMT
  Expected resolution
Would like to read out in threshold-less, energy integrating mode  this is easiest with a single PMT
 Some subset of full waveforms also desireable
Will use also need to use diamond strips for transverse polarization measurement
  Size = 5 cm, segmentation = 0.1 mm  500 channels per plane
  2 planes  1000 total channels

## Slide 5: ESR Compton Readout summary
Detectors
  1600 channels for diamond strip detectors  LVDS pulses, < 10 ns wide
  LVDS repeater will likely be required to propagate signals to DAQ
  1 channel for photon calorimeter  FADC
Other signals
  BPM from laser IP (for each bunch)
  Beam intensity measurement (for each bunch)
  Laser signals (photodiodes, power, position measurements)  slow ok
  Laser helicity
Various slow signals from epics

## Slide 6: RCS Compton Polarimeter
RCS polarimeter similar to ESR Compton
No electron detector
Will use same detectors for photon detector
Calorimeter
Diamond strips

## Slide 7: RCS Operation Mode
Property | Value
Injection energy | 0.75 GeV
Bunch train repetition rate | 1 Hz
Charge per bunch | Up to 28 nC
Max. current | 5.9 mA
Circumference | 1421.26 m
RCS properties
RCS must accelerate electrons from 0.75 to nominal ESR beam energy  5, 10 , 18 GeV
Racetrack design: 2 accelerating linacs with recirculating arcs
Designed to maintain (vertical) polarization through acceleration
Ramp time < 500 ms at 10 GeV
ESR fill time @10 GeV 19.33 minutes
  1160 buckets at 1 Hz
RCS Compton will operate in “multi-photon” mode
thousands of backscattered photons per collision
average over several bunches at a given energy

## Slide 8: RCS Readout Summary
Detectors
  1000 channels for diamond strip detectors  analog pulses (not LVDS)
  1 channel for photon calorimeter  FADC
Other signals
  BPM from laser IP (for each bunch)
  Beam intensity measurement (for each bunch)
  Laser signals (photodiodes, power, position measurements)  slow ok
  Laser helicity
Various slow signals from epics