## Slide 1: Detector readout for HJET polarimeter
E. Shulga for Polarimetry Effort

## Slide 2: Measurement
Interference between electromagnetic (Coulomb) and strong (nuclear) forces at small scattering angles creates a spin-dependent asymmetry.
Measurement of recoils in one direction versus the other, can determine the beam polarization using the known analyzing power of the reaction.
CNI region (0.001<-t<0.03 (GeV/c)2) has a large, calculable analyzing power (AN), the beam polarization (P) is directly proportional to this asymmetry (𝜀)
Detectors are registering recoil target particles (p, C) and provide direct 𝜀 measurement
proton Beam
proton/Carbon
Target
Left detector
Right detector

## Slide 3: HJET polarimeter detectors: Current setup
Present setup: L-R detectors and guide field By
Only vertical component Py measurable near
8 Si-strip detectors:
12 vertical strips
3.75mm pitch
500 μm thickness
Beam
Proton beam passes through target of polarized H atoms of known polarization Q
L/R
R/L

## Slide 4: HJET polarimeter detectors: Holding field effects
Strong transverse holding field required to suppress beam-induced depolarization Bx, By, Bz
Work in progress
Toy MC recoil p results for HJET:
Colored points represent endpoints of recoil protons
Charges #1, 3

## Slide 5: HJET polarimeter detectors: Possible upgrade
97 mm
97 mm
512 ch
512 ch
× 2
Requirements:
Time resolution < 2ns to separate 10 ns
Large 𝞿 coverage for Px, Py, Pz
Punch-throughs selection for background rejection (no material between layers)
Detector Solution S13804:
Hamamatsu 1024-strip 300 um thick SSD
97mm by 97 mm
2 detectors, 2 layers each @ 22 cm
Readout:
Combine 8 strips ➔ 256 per detector
Exploring ePIC ECAL analog readout
mini-DAQ system to be synchronized with EPIC data stream and accelerator cycle
Charges #1, 3
Work in progress

## Slide 6: HJET polarimeter detectors: Simulation results
Charges #1, 3
Hits in the detectors with 8 strips interconnected:
L
R
10 ns
Requirements:
Time resolution < 2ns to separate 10 ns
Large 𝞿 coverage for Px, Py, Pz
Punch-throughs selection for background rejection (no material between layers)
Energy deposition in 2 layers

## Slide 7: HJET polarimeter detectors: Readout
Original Muon g-2 / EDM readout design with Slit128D
SilTerra 180 nm CMOS technology

## Slide 8: HJET polarimeter detectors: Readout
Forward and Backward ECALs (suggested by Elke)
LED pulser 1.8 ns
FWHM optical pulse
Seams to be suitable for our needs
Needs upgrade for 256 channels per detector

## Slide 9: HJET polarimeter detectors: Readout
Current thoughts
Detector capacitance (1 layer) | ~17 [pF]
Charge deposit (MIP) | ~12 [fC]
Charge collection | 5-10 [ns]
Time resolution | <1 [ns]
Max. channels per detector | 260
Max. Data rate | 15 [Mbit/s]
ASICs to consider
What is your experience with this ASICs ?
Suggestions are very welcome

## Slide 10: HJET polarimeter detectors: Readout (Claude)
Claude thoughts (must be thoroughly checked)

## Slide 11: HJET polarimeter detectors: Readout (Claude)
Claude thoughts (must be thoroughly checked)

## Slide 12: HJET polarimeter detectors: Readout (Claude)
Claude thoughts (must be thoroughly checked)

## Slide 13: HJET polarimeter detectors: Readout (Claude)
Claude thoughts (must be thoroughly checked)

## Slide 14: Summary
We need fast (<1 ns) Silicon Strip detector readout
Detailed simulation is required
Various ASICs available, need additional work and studies
Can we utilize ePIC readout?

## Slide 17: HJET polarimeter detectors: S13804

## Slide 18: HJET polarimeter detectors: S4114-35Q

## Slide 19: pC polarimeter detectors: Current setup
Provide fast measurements and depolarization evolution and scan polarization structure in the beam
1
3
4
5
6
2
18cm
C-target holder
Ultra-thin ribbon targets: ≈ 10 μm × 50 nm
Target holder inside beam pipe
Provides fast monitoring for Depolarization and Polarization profiles
In sweep mode, a polarization of ±2% measurement can be done by p-Carbon polarimeter in about 30sec.
H. Huang Existing spin manipulators at RHIC 2024
6 Si strip detectors

## Slide 20: pC polarimeter detectors: Possible upgrade
Requirements:
fast, relative
transverse profiles of Polarization
  per scan
Second detector layer installed in pC polarimeter
Included in DAQ since start of Run22 operations
Data from RHIC Run 22
with a match in second layer
TOF vs. 𝐸𝑘𝑖𝑛 in layer 1
H. Huang Existing spin manipulators at RHIC 2024
Detector Solution for upgrade S12858:
Hamamatsu 16-strip 200 um thick Si
6 detectors, 2 layers each
Readout:
32 channels per detector
The same ePIC ECAL analog readout should be suitable
Charges #1, 3

## Slide 21
Components requiring quality control:
  Upgraded 2-layer Si-detector systems
  Electronics readout with preferred <2 ns time resolution
ESH and Quality Assurance
Charge #7
Hadron Polarimeters:
ESH and QA-related issues:
  After 20 years of operating experience at RHIC, ESH and QA-related issues for the pC and HJET polarimeters are well established.
Described in Quality Control Plan: → https://eic.jlab.org/Documents/DET/Quality/References/Detector-6.10-QualityControlPlan.pdf

## Slide 22: Summary
HJET Polarimeter:
Current L-R detector setup measures only vertical polarization component (Py)
Strong holding field effects require detector geometry optimization
Two detectors with dual layers will enable full 3D polarization measurement (Px, Py, Pz)
Time resolution <2ns meets requirement for 10ns bunch separation
pC Polarimeter:
Current 6-detector system provides fast polarization monitoring (~30s for ±2%)
Second layer successfully commissioned in Run22 for improved background rejection
Proposed upgrade: Hamamatsu S12858 detectors (16-strip, 300 μm)
Dual-layer configuration (6 detectors, 2 layers) enhances measurement precision
Target: ΔP/P < 1% per scan for transverse polarization profiles
Readout: 100s of channels per system, exploring using ePIC ECAL analog electronics
Overall Status:
Overall concept is based on current system, needs to be upgraded to EIC conditions
Both systems address critical EIC polarimetry requirements
Integration with ePIC electronics provides unified readout approach
Ready to proceed to next project phase