## Slide 1: EICROC update
F. Bouyjou, H. Chanal, F. Dulucq, M. El Berni, S. Extier, M. Firlej, T. Fiutowski, K. Guillossou, F. Guilloux, M. Idzik, N. Kachkachi, B.-Y. Ki, C. de La Taille, J. Moron, D. Marchand, L. Royer, N. Seguin-Moreau, L. Serin, A. Shama, A. Soulier, K. Swientek, D. Thienpont, A. Verplancke

## Slide 2: EICROC prototypes
EICROC0 : 4x4 pixels with simple readout (2022)
EICROC OA/0B 1/1B fabricated in 2025 « ATLAS/ EIC » engineering run TSMC 130n
  EICROC0A/B : 4x4 with improved blocks and testability
  EICROC1/1A : 32x32 and 4x32
EICROC2 will be fabricated Q1 2027
  Should be the final chip…

## Slide 3: EICROC0
Analog frontend similar to ATLAS ALTIROC
  Cd = 1 pF (max 3 pF)
Need ADC instead of ToT for charge measurement : 8bit 40 MHz from AGH Krakow
TDC taken from HGCROC by CEA Saclay
Simple digital readout but SEE-proof I²C slow control
~2 mW/pixel
Fabricated in spring 2022 in TSMC 130nm

## Slide 4: First measurements of EICROC0A (ASIC alone)
Only partial configuration is possible : look at ADC data and s-curves
  Improved ADC baseline, similar minimum threshold (3 fC)

## Slide 5: EICROC0A + sensor : S-Curves
S-Curve with 0 DACu
S-Curve with 10 DACu (5 fC)

## Slide 6: EICROC0A + sensor : S-Curve 50% vs charge
Lowest charge detected with discriminator around 5-6 fC.
Results are consistent between simultaneous and separate injections.

## Slide 7: EICROC0A + sensor : ADC Signal reconstruction
Signal reconstruction at lowest charge
Same signal as ASIC alone
Signal reconstruction at highest charge
Same signal as ASIC alone
Tests done with no threshold writing to avoid ADC signal errors (probably a software issue)

## Slide 8: EICROC0A + sensor : ADC linearity
Non-linearity is similar to ASIC alone + cD = 11; difference to linear regression between +/- 2.5%
Zoom on channel 5, RMS of 1.8 ADCu

## Slide 9: EICROC0A + sensor : TDC ToA
Injection only in channel 5
Injection only in channel 5 with all other discriminators disabled
Range is 1 charge value smaller than plot on the left

## Slide 10: EICROC0A + sensor : TDC Jitter
Injection only in channel 5
Injection only in channel 5 with all other discriminators disabled
Proper TDC calibration is needed...

## Slide 11: EICROC1
32x32 chip : final dimensions
Goal :
  test full-scale chip analog performance (IR drops)
  Allow final sensor characterization
  Test interface with DAQ : fast commands and 320 Mb/s data output
  Progress on module/front-end boards
Caveats :
  Not (yet) zero-suppressed data
  Still 2mW/ch
  Still analog-on-top

## Slide 12: First measurements of EICROC1 ADC&TDC

## Slide 13: EICROC0 measurements : ADC linearity
8 bit 40 MHz SAR ADC [Krakow]
  Noise ~1 UADC but large common mode noise (here substracted)
  Signal 50 UADC ~500 um => 1 UADC ~10 um
ADC mean & residuals – no sensor
ADC mean & residuals – BNL Flipchip sensor

## Slide 14
EICROC1 linéarity ADC pixel 0 vs 31 [Kinann]

## Slide 15: EICROC1 TDC TOA and jitter pixel 0 vs 31

## Slide 16: TDC uniformity
Random injuection : should be flat !
=> Leakage current in 1000 pixels is degrading the charge pump performance

## Slide 17: Next steps
Continue test bench measurements on EICROC1 ASIC alone
  Understanding TDC misconfiguration
Start laser tests with EICROC0A and sensor at IJCLAB
Study TSMC130 replacement
Proceed with EICROC2 digital design at Clermont (relatively techno independant)

## Slide 18: summary
EICROC now reached full scale 32x32 with EICROC1
  Important for analog performance and sensor test
  Also allows to progress on system design
Small scale EICROC0s 4x4 still under test to improve performance and reduce power
  Tests to start soon with sensors
EICROC2 now needs its digital design DoT : ~6 months design time from now
  Responsibility of Clermont Ferrand lab
  Main driving specification is power minimization and low hit rate (< 100 Hz/pixel)
  Submission in Engineering run in TSMC130n Q1 2027
System tests will be (as always) an important input for chip(s) finalization

## Slide 19: backup

## Slide 20: Technology choice
TSMC130 | TSMC65 | UMC110 | XFAB130 | VIS130
5M 1T 1U RDL C4 | 5M 2T 1U RDL C4 | 5M 1T 1U no C4? |  | As TSMC130
Radhard 200 Mrad | Radhard 200 Mrad | Bump @ 5 Mrad | N/A | Which fab ?
ER : 300 k$ | ER : 750 k$ | ER : 300 k$ ? |  | 
EIC | EIC, LHCb | EIC, LHCb, ALICE |  | 
AGH, Lisbon,SLAC | FNAL,BNL,CERN | Torino |  | 
Discontinued | Perenity ? | Low volume | 6-9 months fab | Available when ?
 | ADC |  |  | 
DNW, HiR, CMIM | DNW, HiR, CMIM |  |  | 

## Slide 21: PCB1 – 10/04/2026 : Test results
ADC signals
External inj.
Internal Inj.
Test with external injection used no command pulse, no ctest was wired to the front ends.
Internal injection was obtained with FPGA cmdpulse, no ctest was wired to the front ends and 0 DACu as input charge.
Only 1 event could be captured with the external injection, but the waveform doesn’t show the linear decreasing behavior seen in the plot with the internal injection. We might be seeing some internal cmdpulse interference in the signal?

## Slide 22: PCB1 – 27/04/2026 : Test results - ADC
ADC linearity (all channels injected sim.)
ADC linearity is very similar between channels. The range also seems to be quite similar between all channels.
We can see two different “parts” to the linearity, with 2 different slopes.
Slope 1 (from 0 to 32 fC) is around 2.6 ADCu / fC
Slope 2 (from 32 to 38 fC) is around 3.2 ADCu / fC
Slope 3 (from 38 to 62 fC) is around 4.4 ADCu / fC

## Slide 23: PCB1 – 27/04/2026 : Test results - Hit
S-Curve 50% vs charge
Minimum charge detected is around 4 fC.
The noise enveloppe at 1 fC is around 40 DACu (20 mV), as seen on plot (see plot under).
Slope from 4 fC to 9 fC is around 12.2 DACu / fC, or 6.1 mV / fC

## Slide 24: PCB1 – 07-09/04/2026 : Test results
TDC ToA for cD = 00 and cD = 11
cD = 00
cD = 11
There is a visible effect of cD on ToA results, with the ToA being higher when the capacitance is enabled. The range is different on the plots because of the additional capacitance which restricted the “usable” charge range in the results to a smaller interval.
In our restricted range, we find a ToA range around 500ps for cD = 00 and 850ps for cD = 11.

## Slide 25: PCB1 – 07-09/04/2026 : Test results
TDC jitter for cD = 00 and cD = 11
cD = 00
cD = 11
Jitter plots exhibit a very good jitter floor, which indicates better performance with regards to EICROC0. The “bumps” seen in the TDC values could be from an incorrect TDC configuration.

## Slide 26
A. Sharma & D. Marchand
Pixelated AC-LGAD read-out characterization
Preliminary results with Infrared Laser (1/2)
ADC waveforms (8 time samples = 8 points/event): BEFORE & AFTER pedestal subtraction (based on « far » pixel evt by evt)

## Slide 27: EICROC0 Coupling investigation
Large coupling seen on the ADC data which was completely hiding the signal up to 20 fC
Large coupling capacitance between local (pixel) digital block and preamp / shaper bias lines
Layout improved by adding exclusion zones and a shield between bias lines and digital
Bias / digital block layout in new EICROC ASICs

## Slide 28: EICROC1 description
Designed as 8 blocks of 4x32
  Read out sequentially, like EICROC0
  Pixel similar to EICROC0A
  8 CLPS outputs at 40 MHz
  Clock tree for isochronous calib_pulse distribution
Common balcony (End of column)
  Biases and slow control
  New : fast command decoder (clock, calib_pulse, enable_acquisition, start_readout)
  Backup clock and cmd_pulse inputs available
  320 MHz serializer for 1 CLPS output : to be used for systèm tests

## Slide 29: next EICROC2 (2027)
What is missing in EICROC1 ?
  Larger rate compatibility ?
  Derandomizer for successive events (how many ?)
  Digital on Top (DoT) design for digital power reduction and timing verification on large area : more powerful tools available (UVM)
  Auto-trigger and zero_suppressed data
  Power reduction if possible below 2 mW/ch
Clermont Ferrand lab has joined to take responsibility for the DoT
  Already participated in ATLAS ALTIROC
  The design and verification should take ~9 months from now
Technology choice
  Seems to converge to 130n provided rate remains low enough

## Slide 30: ePIC AC-LGAD detectors

## Slide 31
Goals
  Less digital logic possible inside pixel/matrix
  Less signals possible between matrix and periphery
  Triplication of sensitive circuits (configuration registers for example)
    No triplication on data path
  Complexity on periphery side, simple logic inside pixel
Proposal : Based on clusters of 4 pixels, controlled by the periphery
  Some logic shared at cluster level
  Shared data bus between 2 columns
First iteration of this architecture is ready at RTL level, some debug in progress
 Physical implementation can reveal new constraints, architecture may change
Triggered Pixel (TP)
Neighbor pixel (TL1)
Busy cluster
Cluster waiting for hit
Architecture proposal [A. Soulier et al.]

## Slide 32
First physical implementation done in 130nm
  Check if we manage to fit digital readout inside pixel
Preliminary layout of the cluster of 4 pixels and the column
Triplication of cluster (probably need some refinement)
Using a pixel_analog_dummy macro, not the real analog front-end
Need more time to validate that this architecture can fit using 130nm technology
Double column
Cluster of 4 pixels
Physical implementation

## Slide 33: Path towards production and QC
For roman pots ~500 chips would be needed (500 k ch) = 6 wafers
For FToF 10k chips ~100 wafers
EICROC2 should be a final version (all features implemented)
  Schedule accomodates a possible EICROC3 to fix bugs in EICROC2
  ~1 year after EICROC2 tests and system tests complete
Wafer probing station and test setup will be needed
  Can be inspired from ALTIROC setup

## Slide 34: EICROC0 measurements : S-Curves
6-bit DAC for channel-wise threshold alignement
Correction of channels for a charge of 5 fC (ASIC alone)

## Slide 35: EICROC0 measurements : TDC ToA
Time walk measurement :~400 ps
TDC ToA – no sensor
TDC ToA – BNL Flipchip sensor
500 ps

## Slide 36: EICROC0 measurements : TDC jitter
TDC jitter – no sensor
TDC jitter – BNL Flipchip sensor
Charge range degraded with sensor, still need to properly calibrate the TDC for each channel and remove correlated noise
30 ps
30 ps

## Slide 37: ePIC experiment far-forward region
Roman Pots for ePIC experiment
          Used in the far forward tracking of particle collisions, mandatory for exclusive reactions
2 stations ~2m apart
  2-3 layers of sensors per station
  Square pixels of (500µm)²
Stringent requirements
  AC-LGAD sensors will be used because of their capability to provide excellent resolution in timing and spatial resolution.
EIC Conceptual Design Report, 2021

## Slide 38: EICROC0 performance on testbench
Charge #3
500 ps
30 ps
Qin = 5 fC
Noise ~1 LSB
More in backup