## Slide 1: GTU updates
ePIC DAQ introduction
ePIC GTU design
The ePIC DAQ setup
Some test results
Works to do

## Slide 2
1. ePIC DAQ introduction - general structure
GTU: Global Timing Unit
  control encoding, status decoding.
  The interface for machine clock source,
  Data acquisition control and monitor etc.
DAM: Data Aggregation Module: (FLX155)
  The clock/control fan out, and status/busy accumulation.
  local control over the RDO boards connected, though the main function of the DAM is for Data Acquisition.
RDO: optical interface of detector ReaDOut
  control decoding, status encoding.
  The clock/control interface to the frontend electronics.
  Data collection from Frontend boards, and data transmission to the DAM
FEB:
  Detector dependent Front End / ASIC carrier boards.
GTU
Clock
Control
Status
DAM
DAM
RDO
RDO
RDO
RDO
Data Acquisition
DAM
(O)100
RDO
(O)1000
GTU (O)1
ePIC
EIC
Common
Platform
Online computer
4
FEB
FEB
FEB
System Clock: 19.7 MHz

## Slide 3
1. ePIC DAQ Introduction - Detailed signal implementations
1.1 Clock Distribution
EIC
common platform
GTU
RunControl computer
System clock
(98.5MHz in, 19.7 MHz out)
two-level fanout
Beam orbit
Ethernet
DAM
Clock reconstruct
(& jitter cleaner)
DAQ
PCB and fanouts:
Additive Jitter <1ps
Phase: fixed
Fiber cable (one per DAM):
Additive Jitter <1ps
Phase: fixed
PCB and fanouts:
Additive Jitter <1ps
Phase: fixed
RDO
Clock recovery
(iitter cleaner)
Clock fanouts
Control
Config
DAQ
Optic fiber cable:
Additive Jitter <1ps
Phase: fixed
GTY REC Clock:
Or LpGBT rec clock
RunControl: Run_Start/Stop, Run_type, config, Reset, Synchronization, SRO time_start/stop, Throttling…
Status: Buffer busy, out of sync …
GTY
Control config, status
Host PC
TX/RX
RefClk
Beam Orbit synchronized RunControl
GTY
TX/RX
RefClk
RecClk
FEB/ASIC
1.2 RunControl and DAQ
RunControl: forward or ‘hijack’ the GTU control;
DAM, RDO, FEB/ASIC configuration, readout backpressure
Status: Buffer, sync, etc.
Config synchronized with beam orbit, FEB/ASIC readout and control
Status: Buffer, sync, etc.
Beam Crossing phase aligned
(two fibers per DAM):
control/Downlink, Data_Status/uplink
(two fibers per RDO):
control/Downlink, Data_Status/uplink
DAM to PC: 2xPCIe5x8, DAM to switch: 100 GBE
DAQ time slice/window aligned

## Slide 4
2. ePIC GTU Design - The ePIC clocks:
Single clock source, distributed to the whole system
1 2 3 4 5 6 7 8
3 4 5 6 7 8 9 0 1 2 3 4
5 5 5 5 5 5 5 6 6 6 6 6
1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
1 2 3 4
1160 (all or 1/4 with beam)
100 (no-beam /gap)
* * * * * * * *
* * * * * * * *
* * * * * * * *
EIC_BX_Clock, 98.5 MHz
GTUDAM, 19.7 MHz
(Frequency divided by 5)
ePIC system clock
EIC_beam_orbit
Fixed delay (divider, cable, PCB delays)
The phase (divider) is determined by the orbit information
DAM rec. Clock
39.4 MHz
98.5 MHz
others
252 clock_cycles per Orbit
n*252 clock_cycles per Orbit
All the reconstructed clocks are synchronized (same frequency, fixed phase)
Beam crossing: 98.5MHz
Orbit period: 12.7886 µs

## Slide 5
2. ePIC GTU Design - run-control (downlink) and Data/status (uplink)
ePIC system clock
(19.7 MHz)
GPN, Five 64-bit words, 8b/10b encoding,  7.88 Gbps, 320-bit per ePIC system clock cycle
GPN1
GPN+1
GPN-1
GPN5
GPN4
GPN3
GPN2
DAM  LpGBT (39.4 MHz)
DgPN1
DgPN2
DgPN+1
DgPN-1
DgPN
LpGBT and VTRx+ dictated package format, extracted (repackaged) from GPN
DAM  RDO (non-LpGBT) (98.5 MHz for example)
DrPN1
DrPN+1
DrPN-1
DrPN5
DrPN4
DrPN3
DrPN2
DrPN
RDO dictated package format, extracted (repackaged) from GPN
GTUDAM

## Slide 6
2. ePIC GTU Design - DAQ partition (multiple run-control support)
Hardware: Each MGT transceiver corresponds to one DAM. It can be ‘controlled’ independently.
Firmware: supports 32 run-control processes, (ID#0-31), with ID#0 and #31 reserved for global run.
Software: to be developed
Run-control-N requests for a new system ID (1 to 30) by reading the sub-system (bookkeeping) register (32-bit, offset 0x200) from GTU, and set the bit#ID to ‘1’ (means that subsystem#ID is being used);
Run-control loads the corresponding DAM/MGT with the sub-system ID. (the DAM/MGT with the same ID numbers belong to the same sub-system, and controlled by the run-control-N, N and ID can be different);
The ID will be propagated from the GTU_MGT to the corresponding DAM via the GTU_DAM downlink;
The DAM remembers its sub-system ID, and direct the data to run-control-N;
At the end of run-control-N, release the DAM/MGT by unloading the sub-system ID (reverse the step#2 above), release the subsystem ID (set bit#ID to ‘0’ in sub-system bookkeeping register, reverse the step#1 above).
Maximum sub-system can be running simultaneously: 30
Number of DAMs per sub-system: min: 1, max: 148 (not to overlap with other sub-systems)

## Slide 7
2. ePIC GTU Design - DAQ partition (multiple run-control support)
Firmware implementation:
One 32-bit sub-system (bookkeeping) register (offset 0x200) in GTU;
One set of Beam-crossing counters (64-bit, up to 4000 years), beam-crossing number within the orbit (11-bit, from 0 to 1159), and the first beam-crossing signal (BX0) in the orbit;
32 (sub system ID#0~31) sets of: orbit counters (32-bit, up to 14 hours), streaming time intervals (or windows, 14-bit at 19.7 MHz, up to 800 µs), streaming START/STOP/PAUSE etc.
Sub-system ID tagged run control command (8-bit code, run-start, run-stop, various resets etc.), which affects the DAM with the specific ID only.
RUN_CONTROL_USER_1
RUN_CONTROL_USER_2
RUN_CONTROL_USER_31
GTU_FPGAs
CROSS-POINT
switch
MGT/DAM_1
MGT/DAM_2
MGT/DAM_148
RUN_CONTROL_USER_0

## Slide 8
protoGTU
opticPlugInGTU
FADEonAXU15
FLX155a
Si5344H
JTAGcables
GTU02.phy.bnl.gov
GTU01.phy.bnl.gov
3. The ePIC DAQ setup - at BNL (510_1-231)

## Slide 9
Axu15DAM on GTU02 xcau15p firmware
Flx155DAM on GTU02 xcvp1552 firmware
protoGTU
opticPlugInGTU
FADEonAXU15
GTU01.phy.bnl.gov
FLX155
Si5344H
AlmaLinux 10
/tools/Xilinx/Vivado & Vitis 2024.1 license @maia.phy.bnl.gov
/data/PCIeControl/Axu15DAM on GTU02 xdma software/driver
/data/fpga_v2024/GTUzu19 on GTU01 xczu19EG firmware
USB
JTAG
USB
UART
GTU02.phy.bnl.gov
USB
JTAG
USB
(JTAG)
PCIe3x4
Clock
PCIe4x8
PCIe4x8
MTP fibers
RDOs
RDOs
3. The ePIC DAQ setup - at BNL (510_1-231)
Implemented
To be implemented

## Slide 10
protoGTU
opticPlugInGTU
FADEonAxzu5
gu-pc2.jlab.org
FLX182
Si5394A
JTAGcables
3. The ePIC DAQ setup - at JLAB (to be moved to CC/F109)
UART
GBE

## Slide 11
4. Some test results - Clock distribution
Measurement @ Mar. 27, BNL
Oscilloscope 5 GS/s  200 ps sampling
EIC clock
SI5344H
CH#1
ePIC Clock
GTU
CH#2
DAM clock
FLX155a
CH#3
DAM clock
FADE
CH#4

## Slide 12
4. Some test results - Clock distribution
Measurement @ July 15th, Jlab
Oscilloscope 25 GS/s
‘EIC’ clock
SI5394A
CH#1
Clock divider AD9510 output:
  CH#2: 44.288 ns ± 1.7 ps, FWHM: ~4.5 ps
GTU Jitter cleaner and clock synthesizer SI5395 output:
  CH#3: 21.0162 ns ± 1.36 ps, FWHM: ~4 ps
Single ended
50 Ω clock receiver
Differntial
100 Ω clock receiver
Mux and fanout
Clock divider
AD9510
Jitter cleaner MGT clkRef
SI5395A
Clock fanout
SI53302/GTU
SI53302/optic
98.5M
98.5M
98.5M
19.7M
19.7M
19.7M
(40/60)
(50/50)
CH#2
CH#4
CH#3
DAM
(FLX155a,
FADE…)
ePIC system clock (19.7 MHz) from GTU (to DAM):
CH#4: TIE: σ = 1.9 ps, FWHM: 4.5 ps
Latency of CH#4 vs CH#1: Phase stability:
  45.328ns ± 2.1 ps, FWHM: ~6 ps
The system clock divider (98.5 MHz/5) works
CH#3
ePIC system clock (19.7 MHz) recovered on (FADE) DAM:
CH#3: TIE: σ = 0.9 ps, FWHM: ~2 ps
Latency of CH#3 vs CH#1: Phase stability:
  6.2015ns ± 1.3 ps, FWHM: ~4.5 ps

## Slide 13
4. Some test results - GTU  DAM communication (Downlink)
packet | One packet at 19.7 MHz, (or five 64-bit words at 98.5 MHz) |  |  |  |  | 
Word# | 1 | 2 | 3 | 4 | 5 | five words per package
Bit(7:0) | K28.1_3C 0011111001 | K28.2_5C 0011110101 | K28.3_7C 0011110011 | K28.4_9C 0011110010 | K28.5_BC 0011111010 | Bit alignment, word alignment, and packet alignment
Bit(15:8) | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | Synchrnous Run_control codes
Bit(31:16) | BX(15:0) | OrbitC(31:0) |  | SRO_T(13:0) | BX(63:16), Orbit(47:16), etc. Global and subsystem counters | 
Bit(36:32) | subSysID | subSysID | subSysID | subSysID | subSysID | Partition this DAM to subsystem (ID) run-control
Bit(63:37) | USER | USER | USER | USER | USER | Extras
GTU_RC: 8-bit codes for BX_0, Data Acquisition START, STOP, Sync_RESET, SRO_TIME etc.
This is tested with the fiber loopbacks : port_A_Tx  port_A_Rx;
                port_A_Tx  port_B_Rx, port_B_Tx  port_A_Rx;
The data are 8b/10b encoded, which results in 7.88 Gbps downlink,

## Slide 14
4. Some test results - GTU  DAM communication (Downlink)
ePIC system clock
(19.7 MHz)
GPN+1
GPN-1
GPN5
GPN4
GPN3
GPN2
GTU_Tx
DAM_Rx (7.88 Gbps)
GPN1
GPN+1
GPN-1
GPN5
GPN4
GPN3
GPN2
GPN1
DAM_Parallel (19.7 Mbps)
GPN-1
GPN+1
GPN1
GPN5
GPN3
GPN4
GPN2
DAM to LpGBT (2.56 Gbps)
DAM to non-LpGBT (RDO) (6.4 Gbps)
LpGBT_GPN-1
LpGBT_GPN+1
LpGBT_GPN1
LpGBT_GPN2
RPN-1
RPN+1
RPN2
RPN3
RPN4
RPN5
RPN1
* To be implemented and tested (98.5 MHz instead of 40 MHz  6.4 Gbps)

## Slide 15
4. Some test results – GTU, zynqMP
Gigabit Ethernet: DHCP to Jlab’s DAQ network;
UART: serial port terminal emulator;
JTAG: ZU19EG, KU15P firmware loading, logic analyzer;
USB2.0 with type A connector;
32 GB EMMC;
SD (TF) card reader;
PS-QSPI, PS-SPI (clock divider AD9510 setting)
PS_I2C-0, PS_I2C-1 (GTU thermistor readout, QSFP status readout, EEPROM R/W…)
Character display with I2C control
ARM-cortex-A53, quad core with 4/5 GB DDR4 memory
All these features are tested, and working

## Slide 16
5. Works to do
5.1: to test/debug the chip-to-chip communication between the zynqMP (zu19eg) and the KU15p FPGAs;
5.2: to implement the GTU downlink receiving firmware in DAM (flx155a, flx182, FADE, etc.);
5.3: DAQ software development (on the two hardware setups);
5.4: sub-system run-control test;
5.5: to connect with real RDO (with or without LpGBT chip);
5.6: to make a clock phase monitoring board.

## Slide 17
Thank you

## Slide 18
Up to 144
GTU
DAM
4U tall, 19” rack mounted
DAQ Room-air cooling
GTU base board
Optic transceiver adaptor boards
Clock monitor board

## Slide 19
ProtoGTU

## Slide 20
GTU functional requirements
GTU required:
EIC common platform interface;
Run Control;
~150 DAM interface
Risk mitigation:
Beam vs clock phase monitoring;
Dedicated clock fanout
Between GTU and DAM (Quad LTI)
Same-length Multimode fibers: 4 Tx/4 Rx (inexpensive, standard, commercially available)
Dest#1
Dest#2
Dest#600

## Slide 21
DAM control link (downlink/uplink)
XCZU19EG
XCKU15P
XCKU15P
1 x MGT
40 x IO
1 x MGT
40 x IO
52 x MGT
104 x d_IO
52 x MGT
104 x d_IO
40 x MGT
80 x d_IO
Plugin Cards for 144 DAM
2 x MGT
4 x d_IO
4 x MGT
40 GBE
Or 4 x RDO
2 x DAM
2 x DAM
2 x MGT
4 x d_IO
Supports:
148 DAM
4 RDO (or 40GBE)

## Slide 22
KU15P_A
FPGA
The actual implementation of DAQ partition (multiple subsystem run-control)
RUN_CONTROL_USER_1
RUN_CONTROL_USER_31
MGT/DAM_95
MGT/DAM_96
MGT/DAM_148
RUN_CONTROL_USER_0
ZU19EG
zynqMP SoC
KU15P_B
FPGA
RUN_CONTROL_USER_1
RUN_CONTROL_USER_31
RUN_CONTROL_USER_0
RUN_CONTROL_USER_1
RUN_CONTROL_USER_31
RUN_CONTROL_USER_0
MGT/DAM_55
MGT/DAM_56
MGT/DAM_94
MGT/DAM_1
MGT/DAM_2
MGT/DAM_54

## Slide 23
Clock monitoring (another GTU plugin module)
Clock
Fanout
Clock
Fanout
QSFP opticTRx
FireFly opticTRx
Fiber loopback, either the spares between GTU and DAM, or the spares between DAM and RDO
FPGA (SOM)
Clock phase measurement
Clock_A
Clock_B
Clock_C
Clocks from the GTU base board, and the phase measurement results to the GTU base board
Clocks’ phases
(4)
(10)
(1)
(2)
(2)
(1)
(12)

## Slide 24
Beam pickup signal: stand alone PCB design
e- Beam pickup
RDO(area) Clock
Phase#1
Phase#2
Phase#1160
Phase#1
PhaseOrbit (average)
GTU: Phase Correction
RF-SoC (?)
Phase adjustment:
Si5395 (I2C) : ~70 ps steps
AD9510 (SPI) : ~25 ps steps

## Slide 25
FLX155a – without the Firefly modules and front panel

## Slide 26
DAM (FLX155) clock interface
Dedicated Clock input,
up to three MGT lanes (Tx/Rx)
MTP multimode 850µm optical
* These two diagrams are from FLX155 presentations
NB7VQ14M (and 2:1): not on FLX182, FLX712
* DAM implementation

## Slide 27
FADE on Axau15p
With this FMC adaptor ( 20 pieces in hand ), the Axau15P can be GTU, DAM, or RDO.
Platform For DAQ software development
Platform for firmware development
Mini-daq for detector/FEB/ASIC test