## Slide 1
ePIC MPGD Trackers Test beam Plans & Other ongoing R&Ds
Kondo Gnanvo, Surabhi Tarafdar, Annalisa D’Angelo, Stefano Gramigna, Francesco Bossu, Fabien Jeanneau
7th DRD1 Collaboration Meeting - February 23 – 27, 2026, CERN

## Slide 2
Outline
Overview of ePIC MPGD Trackers & Test beam
  CyMBaL: Module description – Test beam plans, goals & requirements
  MPGD-BOT: Module description – Test beam plans, goals & requirements
  MPGD-ECT: Module description – Test beam plans, goals & requirements
Double-side Thin-Gap GEM-μRWELL Prototypes
  R&D goals and test beam plans, goals & requirements
μRWELL-PICOSEC Prototypes
  R&D goals and test beam plans, goals & requirements

## Slide 3: MPGD Trackers in ePIC Central Tracker @ the EIC
MPGD-BOT
CyMBaL
Lepton MPGD-ECT
Hadron MPGD-ECT
Barrel Trackers
CyMBaL: Cylindrical Micromegas Barrel Layer​
    Micromegas based​
MPGD- BOT: Barrel Outer Tracker​
    Thin gap GEM-µRWELL hybrid based​
​End cap trackers
  MPGD- ECT: End Cap Tracker​
    GEM-µRWELL based​

## Slide 4: CyMBaL: Cylindrical Micromegas Barrel Layer

## Slide 5: CyMBaL: Setup and Goals and requirements
Goals
Test of the scale 1 prototype (see previous slide)
Spatial resolution and efficiency studies
Time resolution?
Inclined tracks reconstruction
1 mm and 3 mm drift gaps
Reqiruements
Trigger from DRD1
Ar/CO2/ISO (93/5/2
Silicon pixel reference
Readout with DREAM electronics
Test bench like in November 2025
DESY table desirable for position scan

## Slide 6: ePIC MPGD Endcap Trackers: MPGD-ECT
MPGD-ECT disks
GEM- µRWELL hybrid configuration guarantees gain higher than 104
2D strip read-out a “COMPASS-like” scheme
600 µm pitch guarantees a spatial resolution better than 150
time resolution~10 ns
On-detector Front End Boards (FEBs) based on SALSA chips
Two MPGD Endcap Tracking (ECT) disks both in the hadronic and in the leptonic regions increase the number of hits in the |η| > 2 region to improve pattern recognition.
GEM – µRWELL technology
X-Y readout
×1000
Light weight CATHODE
DRIFT
6 mm
GEM
50 µm Kapton
TRANSFER
3 mm
µ-RWELL
Readout
2D strip layout, 600 µm pitch
×20
NOT IN SCALE
-3.5
1.93.2
Lepton Endcap
Disks
Hadron Endcap
Disks

## Slide 7: MPGD-ECT: Setup, Goals & Requirements
QUAD×2
CS×2
TRG + 2×TRK
TRG + 2×TRK
H = 1112 mm
L = 1927 mm
W = 1000 mm
Objectives:
Performance studies with different gas mixtures
Performance mapping with standard gas mixture (position scan)
Angle of incidence scan with standard gas mixture
Time performance studies
Requests:
5 gas lines (4 IN, 1 OUT)
Gas needs
  Ar, CO2, CF4, N2
  Premix Ar:CO2:CF4 (45:40:15) or Ar:CO2 (80:20)
  Premix to test Ar:CO2:iC4H10 (93:2:5) + TBD
Large red moving table!!! (For position scans with our large setup)

## Slide 8: MPGD-BOT: Overview & PED test article
Working detector
MPGD-BOT module: Full scale test article (aka prototype)
1700 mm
330 mm
FEBs
1800 mm
360 mm
MPGD Barrel Outer Tracker (MPGD-BOT)
Right module
Left module
FEB
Heatsink with tubing
MPGD chamber
cooling tubing for the 2nd module behind
Service Area
Mounting Frame
Detector Envelope
MPGD-BOT module cross sectional view
https://www.jlab.org/sites/default/files/eic_rd_prgm/files/2023_Proposals/20230714_eRD_tgMPGD_Proposal_FY23_Final_EICGENRandD2023_16.pdf
drift
induction
Thin-gap GEM-μRWELL Hybrid Detector

## Slide 9: MPGD-BOT: Setup, Goals & Requirements
MPGD-BOT prototype beam test goals
HV scans for spatial resolution & efficiency studies
Performance in magnetic field up 1.5 T field (pions beam)
Gas mixtures studies: stability vs. performance
Setup: MPGD-BOT prototype inside GOLIATH magnet
  MPGD-BOT support frame: ~200 cm × 40 cm × 40 cm (in GOLIATH)
  Upstream & downstream GEM frames: Two ~40 cm × 40 cm × 20 cm
  Readout with APV25+SRS with JLab CODA DAQ
  Scintillator / PMT coincidence trigger
Requirements
Access to GOLIATH magnet (all beam time if possible)
Two fixed stands upstream & downstream GOLIATH magnet for the GEM trackers
Gas needs:
  Ar:CO2 80/20, Ar:CO2:iC4H10 93:2:5 (or 93:5:2 if flammable or availability concerns)
  Will use gases from INFN mixing system if operational for performance studies in gas
Layout of beam test setup
Scint / trig1
Scint / trig2

## Slide 10: Generic R&D: Double Thin-gap GEM-μRWELL
https://www.jlab.org/sites/default/files/eic_rd_prgm/files/2023_Proposals/20230714_eRD_tgMPGD_Proposal_FY23_Final_EICGENRandD2023_16.pdf
1 mm
1 mm
1 mm
1 mm
Medium prototype with X-Y strip readout
30 cm
30 cm
ASACUSA pattern X-Y-strip
X-strips
Y-strips
1.2 mm
Double-sided thin-gap GEM- µRWELL hybrid detectors with capacitive-sharing readout.
Two prototypes in beam test
  Position resolution & HV scan
  Performance in B-field
Share setup and gas needs with MPGD-BOT
Small prototype with pad readout
Pad readout PCBs
3.2 mm pitch
4 quadrants with pad patterns
S. Tarafdar - PI (JLab)

## Slide 11: µRWELL-PICOSEC Technology @ the Future FCC-ee: Precision Muon Timing and ToF-based PID
Motivation (dual use):
Detection of delayed charged particles from long-lived particle decays in muon system, e.g.
Particle identification using time-of-flight (ToF) detector outside central tracker (“barrel timing wrapper”)
Concept: µRWELL-PICOSEC detector (MPGD with Cherenkov radiator)
First beam test results with single-pad μRWELL-PICOSEC prototype
Approach:
Design, construction, & test of 10cm×10cm prototype with 100 channels
Photocathode:
  non-hygroscopic Diamond-like Carbon (DLC) instead of CsI
Beam test at CERN in summer 2026
M. Hohlmann - PI (FIT) & K. Gnanvo (JLAB)

## Slide 12: µRWELL-PICOSEC Prototypes: 2026 beam test plans
Large prototype: (preferably in CERN PICOSEC Telescope)
New prototype with some minor modifications (HV contacts)
Test primarily with DLC photocathode
Single & Multi-channels with SAMPIC
Voltage and Position scans for response uniformity
Drift gap studies
Single-pad prototypes: (JLab PICOSEC-MM Telescope)
50 µm and new 75 µm μRWELL prototypes
Primarily with DLC photocathode
Voltage and Position scans for response uniformity
μRWELL hole geometry and sizes
Drift gap studies
Single-pad prototype
DLC HV
1 cm
Active area
Ground ring
10 cm
10 cm
Large prototype (100-pads readout)
JLab PICOSEC telescope

## Slide 13: Summary of July 2006 beam test requests
Physics Scope and planned measurements: Characterization of ePIC MPGD tracker full scale 1:1 PED test articles
  MPGD-BOT setup: Standalone telescopes (include Generic R&D double thin-gap protos)  thin gap hybrid GEM-μRWELL test article
  MPGD-ECT setup: Standalone telescope for hybrid GEM-μRWELL full scale engineering test article + 46 cm × 40 cm prototypes
  CyMBaL setup: Standalone telescope for curved full size Micromegas + small prototypes
Measurements: Efficiency, timing and position resolution studies through
  HV scans, position scan, angle scan, gas mixture studies (timing)
  performance in magnetic field (GOLIATH Magnet for MPGD-BOT setup)
Beam requirements when relevant (muons, pions, electrons, momentum, polarity, rate – high/low/scan)
  High momentum muons, narrow pions and (electrons?) all OK  rate scan desirable at the beginning of the test beam campaign
Required gas (mixtures and approximate amount – important to know asap)
  Ar-CO2 (80/20) for the reference trackers (2 -3 bottles) & Ar-CO2-CF4 45/10/45 (existing bottle)
  Ar-CO2-iC4H10 93/2/5 (3 bottles) or 93/5/2 (2 bottles)
  Alternatively: Ar ( 3 bottles) , CO (2 bottles), iC4H10 (2 bottles) for the INFN 3-gas mixing system  will benefit JLab and Saclay as well
Required infrastructure:
  Two DESY tables (if possible) for MPGD-ECT and CyMBaL setups
  DRD1 Trigger signal for CyMBaL setup
  Two stands upstream & downstream GOLIATH magnets for MPGD-BOT setup

## Slide 14: BACKUP

## Slide 15
μRWELL / CapaSh readout PCB: Front view
GEM foil
Detector major components are ready
GEM foil, μRWELL / CapaSh-X-Y strip readout PCB and detector support frames are all in hand at JLab
Clean room infrastructure and equipment at JLab almost complete
Assembly start week of Oct.13th  Completed by December 15th
Plan to test performance in beam in Spring-Summer 2026
Test article validation in 2026  Pre-production modules in 2027
Capacitive sharing readout with X-Y strips @ 45o
MPGD-BOT Test Article: Project Engineering Design

## Slide 16: ePIC MPGD Endcap Trackers: µRWELL-ECT
Strips routing
X/Y strips
600 µm pitch
(X, Y) readout
no FEB in the active area
PED Test Article Module to be delivered and characterized in November Test Beam at CERN-SPS NA H4

## Slide 17: DAQ
HIROSE to Panasonic
Transition Board
Trigger Signal
Injection Board
Detector
APV25
SRS
Corryvreckan
mmDAQ3
Data Pipeline

## Slide 18: Trigger
Also provides a time reference (t0) to selected APVs for µTPC reconstruction
Onsemi J-Series 30020
3x3 mm2 SiPM Area
×9 Ø1 mm wavelength shifter fibers
Bundled and embedded in the groove
Non-amplified signal output
from cosmic rays

## Slide 19: Preliminary Results from TB-2025 Data
* WELL = 550 V
TRSF = 4.5 kV/cm
DRFT = 2.5 kV/cm
Residuals’ σ VS GEM Voltage *
PRELIMINARY
2D Efficiency [1x1 cm2] VS GEM Voltage *
PRELIMINARY
Highest charge cluster position QUAD1 (w/ grids)
PRELIMINARY
PRELIMINARY
Preliminary performance satisfy requirements @ HV GEM = 350V
Generous leeway for safe detector operation and optimization

## Slide 20: Residuals Distributions
Upper view
90 μm strip width
Lower view
520 μm strips width
Lower view
520 μm strip width
Upper view
90 μm strip width
The two quadrants are rotated by 90 degrees with respect to each other, hence the X-Y exchange
PRELIMINARY

## Slide 21: Size and Charge of the Signal Clusters
Cluster Size VS GEM Voltage *
Cluster Charge VS GEM Voltage *
Cluster Charge
Cluster Size
Charge sharing visibly skewed in favor of the wider strips of the lower view
QUAD1
QUAD2
* WELL = 550 V
TRSF = 4.5 kV/cm
DRFT = 2.5 kV/cm
PRELIMINARY
PRELIMINARY