## Slide 1
Electronics and DAQ WG Meeting (3/26/2026)
DAM Board & Test Setups
Announcements, Schedule, News
dRICH DAQ Backend – Alessandro Lonardo
FLX-712 Test Stand – Martin Purschke
GTU / FLX-155 Test Stand – William Gu
Next steps & discussion

## Slide 2: Schedule
Electronics & DAQ Meetings:
  3/26 – E & DAQ WG: Felix Test Development / Test Stands
  3/30 - TIC Meeting – data rates
  4/2 – No meeting
  4/9 – ASIC Updates
Scheduled Reviews
  Peer Reviews - https://indico.bnl.gov/category/720/
    4/1 – EICROC
    4/22 – ALCOR
    5/6 – SALSA
    5/13 – CALOROC
    4/20 – FCFD
    4/27 - Discrete
  DOE Independent Project Review of the EIC Project Status: 4/28-5/1, 2026
  PDR  Peer Review for Slow Controls (~June 2026)

## Slide 3
DAM Board: Next Steps: Technical Questions to be resolved
Data Readout Chains:
  TOF / AC-LGAD: Direct connection lpGbt VTRX+  DAM (using lpGBT protocol, need 48 ports)
  Calorimeters/MPGDs: Generic RDO  DAM (Need to define protocol)
  Si Tracking: lpGbt  Generic RDO (aggregating)  DAM (Need to define ?Aurora 64B/66B?)
  Astropix: End Of Stave Card  DAM (?)
  LowQ Tagger: Spyder 4  DAM (?)
Transport of Fast Commands:
  Same protocol as uplink?
Transport of Slow Control Information:
  ASIC / FEB Configuration
    Fast Commands
    I2C
    Fast Configuration Protocols
Transport of FPGA programing information:
  Assume separate mode, needs specific defininition
Firmware Triggering Protocol:
  Interaction between detectors likely requires GTU involvement to communicate results synchronously

## Slide 4
DAM Board: Next Steps: DAQ Group Support to be resolved
Actions being taken:
  Test stands as per Martin / William – we will have development systems in place
  A few more FLX-155 to be procured this year, FLX-712 to become available when sPHENIX finished with them
What we need to regarding the DAM conection:
  Give guidance to detector groups, and front end developers
    Specify protocols
    Specify / Document commands and command arguments
    Specify / Document mode switching
    Define document headers
      Need to be capable of untangling 40 MHz vs 100 MHz clocks, and mapping local ASIC timing to EIC rf clock
      Need to identify time frames
      Need global scheme for identifying detectors/components/channels
  Give Technical support to detector groups and front end developers
  Develop expertise in the Felix
How to do this:
  Specify an individual(s) to work on the Felix firmware development