## Slide 1: IP6 – ePIC Detector Subsystems
electron beam
p/A beam
Luminosity
System
Low-Q2 Taggers
Zero Degree Calorimeter
B0 Magnet
Spectrometer
Roman Pots (RPs) and
Off-Momentum Detectors (OMDs)
26 Total Detector Subsystems: Bunch crossing : ~100MHz Interaction rate : ~500kHz

## Slide 2
Detectors and Electronics
WBS
DAQ/Computing
WBS
Off Project
Hardware interface with Front-End electronics: ~120 Data Aggregation and Management boards – DAM
Roughly 8000 data path fibers connecting DAM boards to the detector readout electronics
COTS computing: Echelon 0 ~140 computing nodes interconnected with a 100/400Gb ethernet network.
Electronics racks for mounting all components in the experimental areas and for Echelon 0 computing (roughly 25-30 total racks).
ePIC Detector

## Slide 3
Splitting of Echelon 0
ePIC DAQ and computing will require network connectivity at BNL between resources in IP-6, SCDF as well as development labs that is bandwidth guaranteed and minimizes routing.
SCDF
Lab
Lab
Lab
IP-6
DAQ Room
(~70 computers)
To JLAB
ePIC (Echelon 1)
BNL ePIC
Echelon 1
ePIC DAQ
Enclave
( ~70 computers)
ESNET
4Tbps
(10x400 Gb/s)
Up to
100Gbps
400 Gb/s
400
Gb/s
Early DAQ & Electronics development will be in labs (Physics, starting early 2026).
Initial computing needs for development would best be placed in a central location (SCDF, initially one rack, by Q1 FY27).
DAQ production and interface with Echelon 1 can be worked out with test beds in labs and the SCDF. (Q2 FY27 – Q1 FY30)
When beneficial occupancy at IP-6 is attained, additional Echelon 0 computing resources can be placed in both sites (5-6 racks total at SCDF, Q2 FY30).
For production running it is important to all network infrastructure in place (Q2 FY33) and have equal and transparent network access from SCDF to both Echelon 1 sites (BNL and JLAB)
Physics
Green indicated network & computers owned/administered by ePIC.
34
~2km BNL Campus